## Slide 2: Contents
Acceleration and Speed of Light
Evolution of proton/ion acceleration
Pulsed SRF becomes a major actor
Back to CW

## Slide 3: Contents
Acceleration and Speed of Light
Evolution of proton/ion acceleration
Pulsed SRF becomes a major actor
Back to CW

## Slide 4: Particle Acceleration
Particle accelerators accelerate particles to speeds very close to that of light.
At low energies, the velocity of the particle increases with the square root of the kinetic energy (Newton).
At relativistic energies, the velocity increases very slowly asymptotically approaching that of light (Einstein).
It is as if the velocity of the particle ‘saturates’.
One can pour more and more energy into the particle, giving it a shorter De Broglie wavelength () so that it probes deeper into the sub-atomic world.
What does special relativity tell us,
e.g. for an electron?
The speed increases, but not as spectacularly as the mass. In fact, it would be more correct to speak of the momentum () increase .

## Slide 5: Energy and Mass
Electron rest energy: E0 = 0.511 MeV
Proton rest energy: E0 = 938 MeV
Speed of light: c ≡ 2.99792458  108 ms-1
Energy unit: 1 eV = 1.6021  10-19 J
Momentum
Kinetic energy
When

## Slide 6: Properties of some charged particles
The electronvolt, eV, is the amount of (kinetic) energy gained by one elementary charge e moving across an electric potential difference of one volt.
C
J

## Slide 7: Speed Increase and its Saturation
b = v/c
E0, electron
E0, proton
E0, electron = 0.511 MeV
E0, proton = 938 MeV

## Slide 8: RF acceleration: Synchrotron at
Cyclotron: constant B
Synchrotron: constant r
Accelerating cycle
Strong focusing concept
For v ≈ c
E [GeV] ≈ 0.3 B [T] ·r [m]
The LEP Example

## Slide 9: RF Acceleration - Electrons
For electrons the life is easier. A few MV are sufficient to stabilize their speed, close to the speed of light.
The particles of the beam need to be localized in bunches and properly phased with respect to the field so that the beam is gaining energy
TM010 mode
Standing Wave

## Slide 10: RF Acceleration – Protons (and ions)
With protons, and even worst with ions, a lot of voltage, some GV, must be integrated by the particles before their speed is becoming stable, i.e. close to the speed of light.
The RF accelerating structures must be designed for different particle speed, from the speed at the source exit (Wk of the order of one hundred keV, i.e. ) to the speed of light (.
For ions the situation is the same but worst. For the same energy/nucleon the number of cavities must be multiplied by the factor Z/A.
For a CW beam of protons at moderate energy and power the cyclotron is still a valid solution. Several tenth of cyclotrons are used and still built every year for isotope production, and a few for hadron therapy.

## Slide 11: Cyclotron for moderate Energy
Folded Wideroe Linac in a constant magnetic field
For m and B = constant
also frev = constant
Ec /A [MeV] = Kcycl. (Z/A)2
= q v B

## Slide 12: The Big Ones: PSI & TRIUNF
accelerating cavity sector magnet
PSI: K=590 Cyclotron,
2.5 mA, 590 MeV, Pbeam > 1MW
TRIUNF: K=500 Cyclotron,
0.2 mA, 500 MeV, Pbeam > 100 kW

## Slide 13: Contents
Acceleration and Speed of Light
Evolution of proton/ion acceleration
Pulsed SRF becomes a major actor
Back to CW

## Slide 14: French Linear Accelerators in 1946
Historical examples: a Wideroe type structure
(ALICE heavy ion injector, IPN Orsay)
A drift tube linac (DTL – Alvarez type)
(Saturne, CEA Saclay)
p mode
2p mode

## Slide 15: Since seventies RFQ is a main actor
From the exit of the source and up to a few hundreds of MeV, the proton (ion) beam is slightly relativistic, its speed practically follows the classical mechanics lows and it’s proportinal to the square root of the energy.
In a DTL (Drift Tube Linac) to maintain the synchronism with a certain frequency, the length of the drift tubes should doubles each time the beam energy change by a factor of four.
It turns out that a DTL is not performing efficiently when the injection energy is too low (50-100 keV). The non-trivial effort of developing sources at higher voltage (200 kV and above) was partially overcoming this problem.
The invention of the Radio Frequency Quadrupole, RFQ, gave a bright solution to this problem, smoothly transforming the CW, low energy, beam from the source to a few MeV bunched beam, ready for the injection into the DTL.

## Slide 16: About the RFQ - 1
From SNS CDR
RFQ invented by:
I. M. Kapchinsky and Vladimir Teplyakov
1970

## Slide 17: About the RFQ - 2
From SNS CDR

## Slide 18: About the RFQ - 3
From SNS CDR

## Slide 19: RFQ Technological Problems for CW
RFQ is great but to be efficient needs very high electric field to have adequate focussing forces and to reduce the length
For several years RFQ have been designed and built just for pulsed operation with a modesf duty factor < 1%.
As a consequence RFQs were mainly develotted for low energy proton and ions accelerators for nuclear physics, Good alternative to Tandem and Van der Graaf DC accelerators
First CW RFQ, called LEDA, developped at Los Alamos for the APT/ATW projects at the end of past century. Nominal parameters:
LEDA was switched off after ca. 100 hours of succesfull operation !!!
Since then a few CW RFQs have been designed and operated with currents of tenths of mA. The best examples are the two RFQ developped by IHEP and IMP for the CADS project
  H- Injection energy: 75 keV
  Output Energy 6.7 MeV
  CW current >100 mA
  Beam Power >670 kW
  Total RF power > 2 MW
  Cooling power 1.5 MW

## Slide 20: The LEDA RFQ at Los Alamos

## Slide 21: Normal Conducing Linac until mid-nineties
A part of a few CW, low current, ion accelerators, SRF was not considered until mid nineties for high power, non-fully relativistic, proton beams.
Up to mid-nineties all the high intensity proton linacs that have been built were pulsed and normal conducting.
Their scope was substantially that of injecting moderate energy beams (few hundreds of MeV) into large synchrotons (as PS, SPS, TEVATRON, etc.) for high energy collisions.
SRF ion accelerators

## Slide 22: In parallel a few SRF CW Linacs for Ions
  New Projects in the nineties
    Stony Brook
    JAERI,
    Washington University
    Argonne upgrade,
    Legnaro
  Improved cavity designs
  Higher accelerating fields, limited by:
    Microphonics
    No beam vacuum separation
Group of four Quarter-wave cavities for the JAERI Heavy-ion Linac

## Slide 23: Contents
Acceleration and Speed of Light
Evolution of proton/ion acceleration
Pulsed SRF becomes a major actor
Back to CW

## Slide 24: Pioneering Proposal for SRF above 100 MV
b = 0.85 done with CERN

## Slide 25: The TRASCO Project as in 1998

## Slide 26: European ADS: EUROTRANS conclusion
The conceptual design of ADS accelerator once frozen: a highly-modular SC linac
Several R&D activities have been successfully performed, leading to design choices & recommendations

## Slide 27: Elliptical Cavity Issues for b < 1
elliptical cavities have seen designs starting at β  0.5 for cw application (β  0.6 ffor pulsed for high energy acceleration (SNS, ESS)
Elliptical cavities have intrinsic problems for lower velocity acceleration – in  mode the cell to cell distance is β/2 but the diameter is ~0.9  so cell length/diameter~ β/2 and the cavity starts to look like a bellows – mechanical stability, multipacting and low RF efficiency are all issues
Bob Laxdal - Non Elliptical Cavities
SRF 2017

## Slide 28: European ADS pushed other projects
Proton SRF Activities in Europe
Carlo Pagani INFN Milano-LASA & University of Milano
ISTITUTO NAZIONALE DI FISICA NUCLEARE
SEZIONE DI MILANO
Brookhaven National Lab
December 6-8, 1999
SNS – ASAC Meeting

## Slide 29: SNS and RIA acknowledged our contribution

## Slide 30: SNS b = 0.61 6-cell, 805 MHz

## Slide 31: SNS RFQ & Drift Tube Linac (DTL)
RFQ
DTL
NC
SC

## Slide 32: SNS CCL: Coupled Cavity Linac
CCL
NC
SC

## Slide 33: EU Spallation Neutron Source, ESS
ESS Parameters | 
Max Energy | 2 GeV
Average beam power | 5 MW
Peak beam power | 125 MW
Peak beam current | 62.5 mA
Pulse length | 2.86 ms
Repetition rate | 14 Hz
Energy from SC sections | 96 %

## Slide 34: INFN LASA Contribution to ESS
INFN LASA In-Kind contribution
  Design and qualification of the 6-cell cavities for the Medium b Section
  Fabrication of 36 complete cavities in the industry, following a build-to-print strategy
  Cavities delivered ready for the cold test.
    Analogous strategy as for the XFEL
  Cold test in a qualified infrastructure (DESY).
  Delivery at CEA ready for the cryomodule assembly.
  First cavity, ready for the cold test by November 2018
  Delivery rate: 2 cav/3 weeks
INFN-LASA contribution
NC
SC

## Slide 35: From Design to Prototypes and Production
F=1742.4 MHz
Max R/Q=23Ohm
Qext=9.6×10^5
LFD from cavity simulator
Cell shape design
HOM analyses
Dynamical analyses: natural modes
Dumb-Bells
RF measures

## Slide 36: About the Transit Time Factor
The energy gain of the particle depends on:
The accelerating field
The operating synchronous phase
The velocity mismatch between the particle velocity and the synchronous velocity in the cavity
For high N values the Transit Time Factor is too narrow, i.e. The cavity works efficiently in a small velocity range
Compromise between space efficiency and velocity acceptance
Eacc is limited by peak fields!

## Slide 37: Low beta designs start to be considered
Multiple gaps (n) will increase the total voltage gain since Veff = Eacc* Lact and Lact =. n* β /2
But the velocity acceptance of the transit time factor is reduced as n increases
At the RFQ exit and its variation with energy is less dramatic
2 gaps SRF cavities can be a good choice
RF frequency can be higher and cavities with efficient and stable geometries can be developped
Cavities either for pulsed and CW operation are then designed and fabricated in different labs
Transit Time Factor

## Slide 38: A few of the many cavities for low beta
Others designs that I don’t like because of fabrication problems

## Slide 39: Contents
Acceleration and Speed of Light
Evolution of proton/ion acceleration
Pulsed SRF becomes a major actor
Back to CW

## Slide 40: CADS asks for CW: ADS project in China
Injector II, 162.5 MHz - IMP
Y2011-2016, 1.78 B CNY
“Strategic Technology Pilot Project” of CAS
Key technology R&D
Injector I, 325 MHz - IHEP
IMP is the leading institute to carry out the research in cooperation with a number of participants.
Stage 1 - 10 MWt
Stage 2 - 500 MWt

## Slide 41: Injector I at IHEP
5 MeV
5 MeV
3.2 MeV
35 keV
Ion soure, 35 keV
RFQ
  frequency 325 MHz, 3.2 MeV,
RF power 280 kW, four couplers
SRF cryomodules
  Frequency 325 MHz, 2 K operation
  Spoke beta = 0.12, Epeak = 32 MV/m, Vacc = 0.78 MV
  7 Spokes and 7 solenoids per modulez

## Slide 42: CADS Injector II at IMP
SRF cryomodules
  Frequency 162.5 MHz, 4.5 K
  HWR beta = 0.1, Epeak = 25 MV/m, Vacc = 0.78 MV
  6 HWRs and 6 solenoids per module
RFQ
  frequency 162.5 MHz, 2.1 MeV,
  RF power 100 kW, 2 couplers

## Slide 43: PIP-II at Fermilab
An 800-MeV superconducting H- Linac; CW-compatible
Beam transport of 800-MeV H- from the SRF Linac to the Booster
Modifications to the Booster, Main Injector, and Recycler Ring to enable >1MW power on LBNF target
Associated conventional facilities
SRF Linac
Transfer Line
Booster
Main Inj/Recycler

## Slide 44: PIP-II SRF CW Linac, 2mA, 800 MeV
Five Types of Cryomodules
2.1 MeV
10 MeV
32 MeV
177 MeV
516 MeV
833 MeV
H- Ion source
RFQ
PIP-II Linac, state of the art SRF accelerator.
The highest energy and highest power CW proton linac.
Cryoplant
CDS
HWR
8 Cavities
162.5 MHz
Single Spoke
SSR1 X 2
16 Cavities
325 MHz
Single Spoke
SSR2 X 7
35 Cavities
325 MHz
Elliptical
HB650 X 4
24 Cavities
650 MHz
Elliptical
LB650 X 9
36 Cavities
650 MHz

## Slide 45: The PIP-II Superconducting RF Systems
2021-22
2023
2023
2022
5.9 m
5.3 m
6.5 m
5.5 m
9.9 m
Half Wave Resonator
=0.11 Q0 =0.85x1010
Single Spoke
SSR1
=0.22 Q0 =0.82x1010
Single Spoke
SSR2
=0.47 *Q =0.82x1010
0
Elliptical
LB650
=0.61 *Q0 =2.4x1010
Elliptical
HB650
=0.92 *Q =3.3x1010
0

## Slide 46: INFN contribution to PIP-II
INFN firstly provided a novel RF design for the LB650 cavities, fully plug compatible with the Fermilab technical interfaces and performances specifications.
Cavity design meets the CW RF performance requirements
INFN contribution aims to cover the needs of LB650 section, and this includes:
38 SC cavities required to equip 9 cryomodules with 2 spares, delivered as ready for string assembly.
Qualification via vertical cold-test provided by INFN through a qualified cold-testing infrastructure acting as a subcontractor
Compliance to the PIP-II technical management plans and interfaces: System Engineering, Project Review, Quality Assurance and Risk Management.
PIP-II LB650 Project Specifications | 
Acc. Gradient | 16.9 MV/m
Q0 | 2.4 1010
RF rep rate | 20 Hz to CW
Beta | 0.61
Cryomodule picture is a courtesy of Nicolas Bazin, CEA, France
Low-Beta (LB650, b=0.61) cryomodule
RT
SC

## Slide 47: INFN LB650 cavity challenges
The successful cavity design from INFN-LASA is the result of an interplay of multiple, state-of-the-art competences in electromagnetic, mechanical and technical domains.
PIP-II LB650 cavities are among the key scientifical challenges of the project:
an unprecedented quality factor is required for these resonators.
Accelerating and High-Order Modes must be assessed so that neither instabilities nor additional cryogenic losses are posing critical issues.
PIP-II operational scenario is an uncharted territory in terms of detuning control, and this requires deep understanding of Lorentz Force detuning, pressure sensitivity and mechanical leading parameters as rigidities, yield limits, stresses.
Detailed finite element analysis to evaluate compliancy to ASME codes.
INFN LB650 for PIP-II, cold cavity | 
βgeometric | 0.61
Frequency | 650 MHz
Number of cells | 5
Iris diameter | 88 mm
Cell-to-cell coupling, kcc | 0.95 %
Frequency separation π-4π/5 | 0.57 MHz
Eq. diameter - IC | 389.8 mm
Eq. diameter - EC | 392.1 mm
Wall angle – Inner-End cells | 2 °
Effective length (10*Lhc) | 704 mm
Optimum beta βopt | 0.65
Epeak/Eacc @ βopt | 2.40
Bpeak/Eacc @ βopt | 4.48 mT/(MV/m)
R/Q @ βopt | 340 Ω
G @ βopt | 193 Ω
Inner cells stiffening radius | 90 mm
External cells stiffening radius | 90 mm
Wall thickness | 4.2 mm
Longitudinal stiffness | 1.8 kN/mm
Longitudinal frequency sensitivity | 250 kHz/mm
LFD coefficient kext at 40 kN/mm | -1.4 Hz/(MV/m)2
Pressure sensitivity kext at 40 kN/mm | -11 Hz/mbar
Maximum Pressure VM stress at 50 MPa | 2.9 bar
Maximum Displacement VM stress at 50 MPa | 1.5 mm
High Order Modes analyses.
Last mode in 3rd monopole passband, -6.5 MHz away from 10th ML
Monopoles under cut-off and Machine Lines. For ref. accelerating mode: 20 W ~ (R/Q)QL2 ~ 3e16

## Slide 48
Thank you for your attention