## Slide 1
Experience in KAGRA Construction with Japanese Companies
Prof. Takayuki TOMARU
National Astronomical Observatory of Japan @ Osaka Expo. 2025, Italian Pavillion

## Slide 2
KAGRA
2.5th Generation GW telescope
in Japan

## Slide 3
Underground
Cryogenic Mirror
Reduce Thermal Noses
Reduce Vibration Noises

## Slide 4
1. Tunnel Excavation
Contractor: Kajima Corporation
From 2012 to 2014
Total cutting length: 7,697 m
NATM method
+ new Austrian Tunneling method

## Slide 5
Not including experiment rooms.
Xarm
3000m/14month=210m/month
2013/9/1-30
Xarm: 359.4m
Yarm(down slope): 301.2m
Total: 660.6m
Maximum Drilling Speed
359 m/month
Japan Record
Notes: this figure shows progress of the excavation except for the experiment rooms.
this purple line indicates the progress of Xarm. According to this result, excavation speed of one party is about 200m/month.
i like to emphasize the progress in the last september, they achieved more than 300m both arm and Yarm. according the company, this values are Japanese record using natm method.

## Slide 6
2. Ultra-High Vacuum System
Manufacturer: Mirapro Co. Ltd.
Applying accelerator vacuum technology
Design Vacuum Pressure: 10-7 Pa
• 3km x 2 Beam Tubes,
Φ800mm x L12m, 500 tubes
• 10 Major Vacuum Tanks
• 4 Main Cryostats
Total Inner Volume：
~ 3,000 m3
Total Surface Area：
~ 15,000 m2

## Slide 7
tube forming; SS304L, 8 mm thick, Rmax 8 mm finished
hydro-formed bellows;
SS316L, 0.6 mm thick, chemical polished
TIG-weld Assy
Electrolytic Polishing (EP) and Rinsing
with ultra pure water; Rmax 2.5 mm
removing 25 mm of outermost layer
flange; SS F304, Rotary forging
vacuum baking
at 200°C for 20 hrs
storage in the tunnel of
Kamioka mine railway
Outgassing Rate:
~ 10-9 Pa m3 s-1 m-2
for pumping time
of 100 hrs.
@ Factory

## Slide 8
Upper Floor
Bottom Floor
Arm tunnel
14m
Vibration Isolator @ room temperature
Cryogenic part
Main mirror positions
3. Cryogenic System

## Slide 9
Cryogenic Payload
Ultra-small Vibration Cryocooler
Heat-Link
& its Vibration Isolator
Black Coating on
Wide-Angle Baffle
TOSHIBA
VIC International
Asahi Precision
Sumitomo Heavy Industries
Jecc Torisha
Sumitomo Chemical
Etc.

## Slide 10
Main Cryostat
Manufacture: Toshiba Energy Systems
Ultra-low Vibration Cryocooler
Manufacture: Sumitomo Heavy Industries
& Jecc Torisha
nm level vibration
was realized
Joint research btw
KEK and SHI
Φ2.6m, H3.6m
Aug, 26, 2017
@KAGRA

## Slide 11
Heat Link
Manufacture: Sumitomo Chemical
+ Arai + Noge Elec. + Furukawa Power Sys.
Black Coating (Solblack)
Coater: Asahi Precision
6N ultra-pure Al: Joint research btw
KEK and Sumitomo Chemical
Non-magnetism
Solblack coatings

## Slide 12
3. Sapphire Mirror (ITM) Reproduction
ITM
Birefringence Map
Optical Absorption Map
Unexpectedly, large birefringence and optical absorption were found
in the sapphire single crystal, and KAGRA decided to recreate ITM.
Φ22cm x L15cm, 23kg
With the cooperation of the Korea Astronomy and Space Science Institute,
we were able to obtain large, high-quality crystals (Aztec, Korea).
However, there are many challenges involved in ultra-precise polishing of
large sapphire crystals, so we began looking for a new polishing company.

## Slide 13: KAGRA ITM High Precision Polishing
Initial
In the middle of polishing
Scratch Removal
Sapphire Mirror
Measurement
Surface Accuracy
Power
In the middle of polishing
W/O Power
4.9λp‐v
0.01λrms
Diameter: Φ220
Effective Diameter: Φ200
Surf1:
Curvature radius 1.9km(Concave)
Surf2:
Curvature radius nominal flat
Surface Measurement Configuration
Zygo TF(12inch)
ITM
by Nikon

## Slide 14
Towards Einstein Telescope
10km arms
Underground
Triangle Shape
3 High Freq. Telescope
+ 3 Low Freq. Telescope
Cryogenic Mirror
Maximum Observable Distance for BH-BHs
from Big Bang
After
We can see the edge of Universe…
The experience of KAGRA and that of Japanese companies will be of great value to ET.