## Slide 1: ATLAS
Abritta Costa Igor, Albicocco Pietro, Antonelli Mario, Arcangeletti Chiara, Battisti Marco, Beretta Matteo Mario, Buadze Beka, Capitolo Emilio, Chubinidze Zaza, Croce Antonio, Dané Emiliano, Gardini Alessia, Gargana Riccardo, Gongadze Levan, Ligi Carlo, Liedl Andrea, Mancini Giada, Pileggi Giuseppe, Ponzio Bruno, Pudzha Dennis, Rosatelli Filippo, Testa Marianna, Tinti Gemma, Vilucchi Elisabetta, Gianmario Cesarini
Si ringraziano i tecnici del servizio vuoto e della metrologia della DA, e tutti i tecnici e progettisti della DT

## Slide 2
LNF still involved in operation and maintenance activity. Several responsibilities covered during the construction and installation phases
NSW Operation in ATLAS
Data Taking & Performance
DAQ stability very much improved: stable efficiency >95%
Track reconstruction is >99%
NSW in Level-1 Trigger chain included: all sTGC Pad and MM sectors in since May 28th 2024
Fakes rate rejection ~11 kHz and Tigger efficiency up to 98%
M. Antonelli, G. Mancini, C. Arcangeletti
E. Capitolo, B. Ponzio, G. Pileggi
Micromegas HV status
Gas mixture with Isobutane → Only 1-2% channels are not working

## Slide 3
LNF activity on H→ZZ*→4l decay channel
LNF contribution
HZZ group convenership
  Focusing on performing measurements of the Higgs boson properties in the H→ZZ* decay channel at 13.6 TeV
    Differential and STXS measurements and BSM interpretation
  First ATLAS evidence of the H→µµ decay channel!
  Study of Quantum Entanglement in the Higgs decay in two vector bosons
*
C. Arcangeletti, G. Mancini
H→µµ observed significance: 3.4𝜎 (exp. 2.5𝜎)
First Run2+Run3 combined result!
2507.03595 (submitted to PRL)
ATLAS-CONF-2025-002
Notes: Starting from the analysis, the Higgs to four lepton decay channel is called the golden channel since it has a fully leptonic final state and high lepton reconstruction efficiency allowing to be one of the main channel to perform precision measurements of the Higgs properties. And despite the low decay rate it has a very good signal over background ratio around 2, making the signal clearly identifiable over the main backgrounds. My work on this topic is dated back to 2017, so in the last years I gave several contributions in different analyses to probe the various Higgs boson properties, from the mass to the CP up to the cross-section and coupling measurements, covering leading roles as Analysis contact and paper editor, and now I am the current coordinator of the HZZ group in the ATLAS collaboration which aim to study the Higgs boson in this specific final state.
I will start the overview of my main contributions…

## Slide 4: HL-LHC
The LHC will be upgraded to the High Luminosity-LHC (HL-LHC) to produce up to 4000 fb-1 of integrated luminosity until 2040
Requirements for pixel detector at HL-LHC
Instantaneous conditions: pile-up, luminosity
High trigger rate: 1 MHz
High granularity: occupancy at 1 %
Integrated effects
Integrated luminosity x10
Radiation hard technologies
up to 2·1016 neq/cm2
LHC: Inner Detector (ID) system, TRT (gas detector) + Strips + Pixels
HL-LHC: New all-silicon Inner Tracker (ITk), Strips + Pixels
Luminosity
= 5-7.5 x 1034 cm2 s-1
A replacement of the current ID detector is by far not enough!

## Slide 5: ITk : The New Inner Tracker
All-silicon tracker
Improved tracking
  Coverage up to |η|<4 (ITk) from |η|<2.5 (ID)
  Finer segmentation:
    50x50μm2 or 25x100μm2
    ID: 50 × 400 μm2 or 50 × 250 μm2
  Reduced material: Carbon Fibre structures, CO2 cooling with thin Ti tubes walls, advanced serial powering, data link sharing
Radiation hardness:
  n-in-p pixel sensors (n-in-n for ID)
  Thinner sensor 100-150 m (200-250 m in ID)
ITk (ID) | Area (m2) | # Modules | # Channels (M)
Pixels | 13 (1.6) | 9164 (2000) | 5100 (92)
Strips | 165 (61) | 17888 (4088) | 60 (6.3)
Italy will build one
Outer Pixel
Endcap

## Slide 6: ITk Performances
Important LNF contribution to design and simulation,
for |η|<4 coverage and pixel size decision
ATL-PHYS-PUB-2019-014
ITk Pixel TDR
ITk Strip TDR
>9 silicon hits per track
M.Testa

## Slide 7: ITk Pixel Detector
Local supports: Different designs to support flat and inclined module mounting
L1 L0
L4 L3
L2
Outer Barrel
IS to be replaced after 2000fb-1 to reduce radiation damage.
L0 placed 34 mm from beam pipe.
Outer Endcap
Inner System
Modules: two main module types, quad & triplet.
Layer | Module type | Sensor type | Sensor thickness [um] | Pixel size [um2]
L0 barrel | Triplet | 3D n-in-p | 150 | 25x100
L0 rings | Triplet | 3D n-in-p | 150 | 50x50
L1 | Quad | Planar n-in-p | 100 | 50x50
L2-4 | Quad | Planar n-in-p | 150 | 50x50
Triplet
Quad

## Slide 8: ITk Pixel Outer Endcap
Three layers of half-rings (HR) loaded into carbon fibre half- cylinders
HR are strategically placed in z to provide hermeticity in η
Modules on both sides of HR ⟂ to beampipe → Φ hermeticity
>= 5 pixels overlap in φ.
Each HR side holds one serial-powering chain:
  16/22/26 Modules for Layer2/3/4
SI modules
Cooling lines, data and electrical cables, run between outer rims of rings and inner surface of cylinder
IP
Half-rings are C-foam / C-fibre “sandwiches” with embedded cooling pipe and fixation lugs

## Slide 9: ITk Pixel Outer Endcap
L2 HR: 11 per HS
L3 HR: 8 per HS
L4 HR: 9 per HS
Dimensions:
L4 diam: 750,2 mm
L3 diam: 528.1 mm
L2 diam: 408 mm
Length: 1888 mm
IP FLANGE
(Low-z)
SERVICE FLANGE
(High-z)

## Slide 10: Sensor, Front-End Chip and Modules
Planar Sensor n-in-p
Front-End Chip by RD53 collaboration
  Read out trigger frequency at 1 MHz
  4 data lines at 1.28 Gbps
  Uplink sharing
  Rad-hard up to 500 MRad
  65nm technology
  Chip size: 400 x 384,
50x50 μm2 pixels, 2.0 x 2.1 cm2
  Shunt-LDO regulator for serial powering
  8912 data links / endcap from modules to off-detector electronics
Modules: 4 FE chips bump-bonded to sensor
Cu-Kapton flex hybrid glued to sensor
for connection to power, slow controls and data distribution
  Wire bonds connect the flex to the FE chip(s)
  “pigtails” connecting modules to power / data
1172 modules/endcap

## Slide 11: Schedule from the last statusing

## Slide 12
Sistema supplementare di essiccamento aria
Camera Climatica
Impianto CO2 Luckacsz
Camera Pulita ATLAS ITk
Welding Machine
M.Testa
E. Dané
G. Cesarini

## Slide 13
0
Dry air with dew point down to -70°C
CO2 cooling LUCASZ
Light Use Cooling Appliance for Surfaces Zone
Climatic Chamber
Constructed and commissioned in 2021 at DESY
Successful test with merging lines at LNF
 20 g/s CO2 flow
Successful Integration with interlock system
Orbital Welding Machine

## Slide 14: OVERVIEW OF THE SYSTEM
RIGHT CRADLE
LATERAL RAILS
FLOATING FLOOR
T-TROLLEY
LEFT CRADLE
y
x
z
3 SUBSYTEMS:
BASEMENT UNDER THE FLOATING FLOOR (PILLARS AND LATERAL RAILS)
T-TROLLEY
CRADLES
Filippo Rosatelli
Bruno Ponzio
Marco Battisti
Emilio Capitolo
Lorenzo Roscilli
Giuseppe Pileggi
Antonio Croce
Beka Buadze
Sandro Tomassini
Dario orecchini

## Slide 15
Material from Naples shipped to LNF, ready to be mounted
Missing the part of the service, the material is just arrived and some other parts are produced in LNF so we can start to add this part. The idea is to mount already closed the upper part of the cradle and then connect it to the bottom part. Missing the part of the connection between the cradles and carriages. Arriving these parts soon to perform some test.

## Slide 16
PIPE INSERTION TOOL
Detector Manifold
Pipes
by Milan group
Assembly tool

## Slide 17
FIRST PP1 MANIFOLD WELDING
Once the pipes are in position the first welding for connecting the exhaust and inlet PP1 manifolds is performed
PP1 Manifold Exhaust
Inlet
L2 Rear Flange
Part of the detector manifold emerging in PP1 Area
First PP1 Manifold welding
T part of the PP1 manifold
Temporary fitting o Fred fitting
S. Coelli slides for welding details

## Slide 18
The position of the cable harness is adjustable on the cradle. The plate at either end can slide on a low-friction interface
Horizontal position is adjusted by screws
CABLE HARNESS INSERTION TOOL
Support of cables in order to transfer to the integration tooling
by UK group

## Slide 19
Horizontal rails are positioned on the rotating cradle for movement along z axis. A vertical rail is devoted to move down the HR.
HALF RINGS INSERTION TOOL
by Lecce group
TILTING TABLE
RAILS
Y MOVEMENT
HR Orientation Tool

## Slide 20: Half-ring test after insertion
QC: measure the isolation resistance between the GND pad of bus-tape and the HS
Connect HR to pwr and data type-1 cables
Bus tape is grounded
Canbus shield |  | 

## Slide 21
Half-ring welding
Three weldings per HR
Leak test, Pressure test 162 bar, Leak test
Temporary ground the pipes nearby HR to protect modules
Re-test connectivity one HR at the time after welding to check no damage to module or services
1° exhaust welding 2° exhaust welding
1° inlet welding
After welding
After welding LS is grounded through pipes

## Slide 23: HALVES SHELLS MATING: ASSEMBLY PROCEDURE
The 2 HS are mated by mean the 2 rotating cradles
Interlinks are connected: 6+6 pairs on upper and bottom side of the HSs
STEP 2
STEP 1

## Slide 24: HALVES SHELLS MATING: ASSEMBLY PROCEDURE
Exploiting the spherical joint and the linear stages the cross-flange is oriented and adapted to the low-z flange position
The Low-z flange is connected to the L2 mated
cross flange
spherical joint
STEP 3
STEP 4

## Slide 25: STATUS OF T-TROLLEY
"HEADS"
SERVICE TROLLEY

## Slide 26
Integration Heads
Low Z flange (A)
High Z flange (B)

## Slide 27: HALVES SHELLS MATING: ASSEMBLY PROCEDURE
As can be seen in the figure there is no clash between the PP1 manifold and the detector support. By taking advantage of the 2 springs present in the lower arms of the cross-flange and the movement along the z axis allowed by the bearing, the detector support can be connected to the rear flange.
STEP 5
Also the Head in High-z position is connected
cross flange
System of springs (not in the pic)
Z-axis shift
No clash between the PP1 Manifold and the cross flange
PP1 EhxuastManifold

## Slide 28: HALVES SHELLS MATING: ASSEMBLY PROCEDURE
STEP 6
The part of the services is connected to the "Totem"
Totem
Cables
In this position the load is still on the cradles. Exploiting the spherical joints of the head the detector is the first load transferred to the T-trolley, and after the services.

## Slide 29: Test on complete Layer
Optopanel
Twinax
Extentions
Optopanel
Climate chamber
or external box
Low impedance connection of the two HS
Ground layer to floor
Connectivity Test for complete layer
Use Lowe Power mode
Cooling through climate chamber
  Demonstrated with prototype
with Tair ~ - 35 C ( in bkp)
Helping with CO2 cooling is still possible
LV lines:
chip register reading
MOPS reading of module V and T
Tlock
Data transmission:
  Uplink: digital scan and BERT
Downlink: Configure a FE in each module
HV lines:
PS will have not enough sensitivity
Open point: strategy to be defined
CO 2
plant ground
GND
GND
PP2
Low impedance connection from HS to floor
braid
electrical break

## Slide 30: Connectivity Test on full endcap pre-shipping
Final test in the climate chamber
  Low power mode
  Cooling demonstrated with prototype with Tair ~ - 35 °C
  Helping with CO2 cooling is still possible
Harness not present in picture
By mean the lifting system under the floating floor, the T-trolley is positioned on wheels and then can be moved into the Climatic Chamber for the final test.

## Slide 31
Switch load system
Rail support
Solution with a smaller box
1660mm
4200 mm
Optoboxes

## Slide 32
The idea is to have the whole detector in a prototype/mockup version in in order to test the mating (empty), then the insertion of the piping, the insertion of the cables and the Half Rings, and then the mating with the populated HS and the PP1 manifold (see tomorrow talk) for each layers. Some HRs could have the piping to perform some welding test.
What we have so far:
Half Shell: we have one Half L4 (from Liverpool) and 2 L2 (from Aviacompositi).
Lugs: all printed in ULTEM (by Naples)
In production the tool for the positioning the lugs of the HS (by Giuseppe Pileggi LNF)
Half rings: 2 HRs per type (6 in total) made in LNF (E. Paoletti, R. Tesauro)
Lz flange: already printed (ABS)
Hz flange: Printed for L2 (ABS)
"Spider" Flange: Produced (F. Rosatelli)
Prototypes

## Slide 33
6
QA Tests are foreseen to check the functionalities of the system:
Thermal Cycling on the HS connected to the rotating cradle
Thermal Cycling and functional test on the HS equipped with HRs
Climatic Chamber
Cradle with HS

## Slide 34
We performed some test for the mating of the cradles but problems raised up. Each part has not bad cylindrical shape but the mating of some part does'nt match, so we decide to simplify the system and check the alignment of the cradles once they are built. The rails now are one part instead being 2 parts in order to gurantee a better alignment.
Alignment test are scheduled to prove the position precision of the system

## Slide 35: System Test
Single and multi-module setup
High Speed data adapter board designed and
produced for Pixel community
DAQ with optical readout
Data Transmission test
Develop interlock logics
  NTC, cooling, power, environmental sensors
Develop of scalable DCS system
6
Z. Chubinidze
Z. Chubinidze, M. Gatta, M. Beretta, M. Testa

## Slide 36: ITk Services
Power/DCS cables:
Design, Prototypes and Production
  Quality Control
  Thermo-mechanical cycles
Extension twinax data cables
  Design Prototypes and Production
  Data transmission test
6
P. Albicocco, M. Testa, Z. Chubinidze

## Slide 37: Attività e assegnazioni CIF II Semestre 2025
Servizio | Reparto | Assegnato (m.u.)
SEM | Progettazione | 4,5
SEM | Costruzioni Meccaniche | 10
Supporto Esperimenti | Support Unit | 3
SPCM | Progettazione | 0,5
SPCM | Meccanica | 2
Attività nel II semestre 2025:
Finalizzazione dei disegni delle parti mancanti
Finalizzazione del sistema di sollevamento
Produzione di alcune parti del tool di assemblaggio
Montaggio del tool di assemblaggio e test
Progettazione del sistema di Trasporto

## Slide 38
Richieste 2026
 |  | Richieste (kEUR)
apparati | ATLAS Tier-2 | 212
consumo | ATLAS | 21
missioni | ATLAS | 162
consumo | Phase II - ITk | 34.5
apparati | Phase II - ITk core | 563
ATLAS FTE Totali: 11.25 (Fisici + Tecnologi)
Servizi | Richieste stimate 2026 (person months)
Electronics and Automation Service (DR) | 12
Mechanics Service (DR) | 8 months x 4 persons
Detector Development and Experimental Activities Support Service (DR) | 10 months x 2 persons
Servizio Progettazione e Costruzioni Meccaniche (DT) | 4
Cryogenic System (DA) | 3
Vacuum (DA) | 5
Notes: Starting from the analysis, the Higgs to four lepton decay channel is called the golden channel since it has a fully leptonic final state and high lepton reconstruction efficiency allowing to be one of the main channel to perform precision measurements of the Higgs properties. And despite the low decay rate it has a very good signal over background ratio around 2, making the signal clearly identifiable over the main backgrounds. My work on this topic is dated back to 2017, so in the last years I gave several contributions in different analyses to probe the various Higgs boson properties, from the mass to the CP up to the cross-section and coupling measurements, covering leading roles as Analysis contact and paper editor, and now I am the current coordinator of the HZZ group in the ATLAS collaboration which aim to study the Higgs boson in this specific final state.
I will start the overview of my main contributions…