## Slide 1: 4DSHARE – INFN CSN5
DC-coupled resistive readout in silicon sensors with internal gain:
signal sharing for future 4D tracking
Coordinatore: Roberta Arcidiacono Iniziato nel: Gennaio 2023 (3 anni)
Anagrafica indicativa (frazione di FTE) in 2025
INFN - Sezione di Torino: R. Arcidiacono 0.3 - N. Cartiglia 0.3 - M. Ferrero 0.2 – L. Menzio 0.5 – F. Siviero 0.2
INFN - Sezione di Perugia: A. Morozzi 0.4 - D. Passeri 0.3 - F. Moscatelli 0.2 – T. Croci 0.1
TIPFA : M. Centis Vignali 0.4 - M. Boscardin 0.1 - G. Pepponi 0.1 - S. Ronchin 0.1 - O. Hammad Ali 0.3
Obiettivo del progetto: migliorare il disegno dei “resistive AC-LGAD” (prestazioni e scalabilità per dispositivi di grandi dimensioni)
Punti chiave:
ottenere un “signal sharing”controllato;
drenare la “leakage corrente” in ogni pixel

## Slide 2: Obiettivi
Thin LGAD with a resistive DC-coupled read-out. Signals are DC-coupled, unipolar and contained within a grid of resistors.
DC-RSD
Main objectives of the 4DShare project
Finalize the concept of DC-coupled resistive read-out sensors via simulations to drive the design
Design and produce the first “proof-of-concept” prototype run, exploring multiple technological options and electrodes layouts
Perform full characterization of the production, with static and dynamic measurements in the laboratory (new/irradiated devices), and detailed performance measurements of most promising DC-RSD layouts
Develop in parallel analytical reconstruction code for estimating the position and time of the hit
Iterate the simulation process for an optimized DC-RSD design
Produce a second prototype run of DC-RSD, followed by a similarly detailed characterization of the production (if time permits)
Siamo qui!
ongoing…

## Slide 3: Attività dell’ultimo anno
completed the definition of mask layout/process split table and manufactured the first prototype run of DC-RSD
performed the full on-wafer characterization of the prototype run
pre-tested a small subset of sensors in the laboratory to be studied with an electrons test beam, using high resolution tracking station (DESY- December 2024 and March 2025).
At higher gains (higher reverse bias voltage), we obtained:
500-micron pitch: 𝝈𝒙,𝒚~ 𝟐𝟎 𝝁𝒎
1000-micron pitch: 𝝈𝒙,𝒚~ 𝟒𝟖 𝝁𝒎
detailed analysis of testbeam data ongoing
Optimization of the analysis codes (analytic method and ML technique method) for extracting the position and time resolution of DC-RSD devices, ongoing.
detailed studies of all designs ongoing in the LAB with TCT setup.

## Slide 4: Sinergie con PRIN 4D-Share
PRIN 2022 4D-Share protocollo 2022KLK4LB
Coordinator: Roberta Arcidiacono
Team: due unità
UPO e INFN (Firenze/Torino - RL: Lorenzo Viliani)
PRIN finanziato con 209 kEuro in PE2 – Iniziato a Settembre 2023 – fine a 02/2026
Overlap con il programma 4DSHARE gr V (per i primi due anni):
nel PRIN e’ data piu’ enfasi alla parte di software di ricostruzione (con Machine Learning) per cui si richiede anche un contratto di ricerca (INFN – Firenze)