## Slide 1
NeuProX - Neutron Production Cross Sections (Young Researcher Grant Proposal)
Goal: Assess the feasibility and reliability of measuring double differential neutron production cross-sections using a dedicated TOF multi-detector system
1. TOF from single particle data acquisition.
2. Combinatorial background rejection.
3. Neutron TOF distributions.
4. Neutron kinetic energy spectra.
5. Incoming neutrons per kinetic energy and angular direction.
Methodology:
Beam
t0
td
TOF = td - t0
Iram B. Rivas Ortiz (irambarbaro.rivasortiz@to.infn.it)

## Slide 2
8-strip silicon detector, FBK
(Time Resolution: 50 ps)
Beam Monitor Sensors
Secondary Detectors
LaBr3:Ce + SiPM, Luxium
(Time Resolution: < 200ps)
Beam
Veto plastic scintillators
Signal read-out by a DT5742 digitizer (16 channels) by CAEN at a sampling frequency of 2.5 GHz
DAQ
Conceptual Design (WP1) activities:
- Define appropriate materials and layout of crystal scintillators, veto plastic scintillators, target thickness and beam sensor for optimal TOF resolution (M1 - M6).
Mechanical and Electronic Assembly (WP2) activities:
- Design and build a system for rotating and/or translating the detectors for data acquisition at different angles and distance from the target (M6 - M16).
- Assemble scintillators with photodetectors and connect to readout electronics (M6 - M16).
NeuProX - Neutron Production Cross Sections (Young Researcher Grant Proposal)
NeuProX - Neutron Production Cross Sections (Young Researcher Grant Proposal)
Iram B. Rivas Ortiz (irambarbaro.rivasortiz@to.infn.it)
Beam sensor
Secondary Detectors