## Slide 1: R&D activities @ LNGS
Davide Fiorina – GSSI & INFN LNGS

## Slide 2: Tests foreseen
Check Primary Scintillation light with PMT instead of camera
  Through the camera hole removing the GEM
  Easy test to crescheck and thest the feasibility
CYGNO04 optimization
  Absolute saturation measurement
  Fields optimization
  Fine pitch GEMs
NID
  Fine-pitch GEMs to crosscheck diffusion behviour
  Better alpha alogment and repetibility
  MMThGEM
Polarimetry
  Incredibly promising result, ready for grant proposal
  Overview of R&D

## Slide 3: NID alignement
Detector space
Lack of alignement ~mm
Lack of repetibility (placement by hand)
Detector space
Actuator
Actuator
Source holder
3D printed base for detector and actuator aligment ~100um
Alpha collimation as much as we want
Trasparent catode (mesh)
Gain space for 1 additional hole
Try to see primary scintillation with SiPM
Shoot alpha perpendicular to GEM

## Slide 4: Saturation
Direct measurement of absolute saturation
Low energy X-rays peaks spectrum (charge+light)
Peak positions wrt real ratios gives the Absolute saturation
Alpha source shooting to a 45° inclined target emitting fluorecence
Rotating holder already printed and integrated in MANGO DAQ
Target procured!
Only testing is needed ;)
alpha
target
fiorotto8/LinearMovementArduino

## Slide 5: Polarimetry
The Imaging X-ray Polarimetry Explorer (IXPE) was launched in December 2021
3 Photoelectric detectors (GPD) in the optics of 3 mirror telescopes (reduces background, focuses sources)
Onboard calibration system with polarized and unpolarized sources
DME gas @ 0.8 bar (diffusion of ~90-100 )
50 µm thick Be window (transparent to X-rays)
Single GEM amplification (50 µm pitch)
Hexagonal custom ASIC pixelated charge detector (105 channels)
Energy resolution 15% @ 6.4 keV
Position resolution less than 120 µm @ 2 keV
A
B
Polarization Angle
Polarization Degree
Modulation Factor

## Slide 6: Angular resolution to electrons
‘MIMAC-like’ measurement
Electrons emitted parallel to the GEM
Angular resolution from 30° to 10°
No strong dependence on the gas used
 Upper limit for angular resolution!!!
Efficiencies are quite low (we are gaseous) and change of gas impacts it strongly
Geant4 simulation to estimate the efficiency to photons
 Fully contained photoelectron in a 10 cm side cube

## Slide 7: Polarimeter quality factor
𝝁√𝜺
IXPE values: 0.11 @ 2.6 keV
0.074 @6.4 keV
He/CF4 60/40
ORCA Fusion
200ms
Ar/CF4 60/40
ORCA Quest2
10ms
@ 17keV
ε≈8%
𝝁√𝜺≈12%
@ 17keV
ε≈1%
𝝁√𝜺≈3.7%
Upper limits!!

## Slide 8: Next steps
New Geant4 to study and tune digitized signals
Reproduce measured modulation factor
  Need CYGNO infrastructure and expertice (I know a certain Melba who is expert in this)
Plug fluxes and background from space to estimate sensitivites to sources
New detector Prototype (sealed)
3 month-person request to LNGS
Play with gases and higher pressures
Play with different amplification structures
  GEM+MM
  >3 GEMs or <3 GEMs
Garfield simulation to optimize the amplification structure and WP
Money+People! The idea is to submit for a CSN5 mini-grant
N.B. Every development for electron tracking is a step forward for a neutrino observatory ;)

## Slide 9: BACKUP