## Slide 1
TIMEPIX4
G.Collazuol
INFN Padova Gr5 2025/6/25
Acronym: TIMEPIX4 Project duration: 3 years (2025, 2026, 2027) Research area: Interdisciplinary / Detectors Principal Investigator: Massimiliano Fiorini (INFN Sezione di Ferrara) Participating Units: Ferrara, Laboratori Nazionali del Sud, Napoli, Padova, Pisa, Trieste Ambito: DRD4 - WG1 (Gaseous) / WP2 (Vacuum Based)
Sinergia: HYPER-K (CNS1) per charge & optical readout in gaseous detectors
Aims: exploiting TIMEPIX4 chip => to develop detector systems beyond State-of-the-Art
Applications:
  Ultra-fast, high granularity MCP based photon detector => HEP
  X-ray, gamma ray and particle imaging w/ semiconductors => Medical Physics
  Photons detection and Tracking w/ gas detectors => Padova proposal
Staff: G.Collazuol, S.Levorato
Post-Doc: M.Feltre
Notes: 1

## Slide 2
Hybrid vacuum photon detector - MCP / TIMEPIX4
TIMEPIX4

## Slide 3
Aim
Proof of principle of coupling gas multiplication gap to TIMEPIX4 chip in a simple way
Target applications high-resolution & low material budget tracking detectors with PID capabilities for charged particles down to very low momenta
Method
building MicroMegas Resistive Embedded Anode gap by standard technique at CERN
(stainless steel mesh supported by pillars on DLC resistive layer on Kapton)
to be tensioned and over-imposed on top of TIMEPIX4
TIMEPIX4 gas detector – WP2 rimodulated
TIMEPIX4 chip
DLC resistive layer
on 50 um of Kapton
128 um gap with SD45/18
woven stainless steel mesh
Gas multiplication gap
Chip Support and gap tensioning system
TIMEPIX4

## Slide 4
History of TIMEPIX gas detectors

## Slide 5
TIMEPIX gas detectors – issue #1 = discharges
Protection layer
High resistivity

## Slide 6
When the Timepix chip was used with a Micromegas the grid was first stretched over the chip surface and set on top of the chip using pillars
The grid holes were not aligned to the chip pads/pixels
and the distance between the chip and the grid was
not constant along the surface
This misalignment resulted in spatial inefficiency
and gain variations with patterns resembling
Moiré optical effect
TIMEPIX gas detectors – issue #2 = alignment
To solve this issue a 1um thick Al grid was integrated on top of the TIMEPIX3 chip (InGrid)
The grid was perfectly aligned to the TIMEPIX3 pads thanks to lithographic based technique carried on during the chip post-processing phase

## Slide 7
A much simpler approach based on ERAMs
(Encapsulated Resistive Anode Modules)
development for the T2K Near Detector TPCs

## Slide 8
Charge spread on low resistivity foil
Charge Spreading 2D telegraph eqn. solution
in O(RC) time scale
Gaussian spread
RC ~ O(100ns/mm2 )
Final ERAM layout choice for series production:
Considering pads of 11x10 mm2 parameters
400 kΩ/□ DLC resistivity – low resistivity
150 mm thickness glue – Cdlc-pad/gnd ~ O(20pF)
Trade-off optimal charge spread VS spark protection
Gain not affected by resistivity
(transparency to induced signals is guaranteed)

## Slide 9
Coupling ERAM gaps to TIMEPIX4 chip => ERAMPIX
TIMEPIX4 chip
DLC resistive layer
on 50 um of Kapton
128 um gap with SD45/18
woven stainless steel mesh
Note
A) need (simple) system for tensioning the gap and to lay down it on the chip
B) must tune DLC resistivity to avoid charge spread too much (all over chip !)
=> easy development at CERN MPGD lab. – agreement with Rui de Oliveira
C) testing GAP coupling to chip by simple contact (no gluing) has advantages
- does not affect induced signal
- does allow testing on the same chip various GAPs with different
configurations (mesh geom, DLC resistivity, gap distance mesh to DLC, …)
GAP
Chip Support and gap tensioning system
Proof of principle of simple coupling of TIMEPIX4 with ERAM-like multiplication gap
1) DLC (Diamond-like-Carbon) resistive layer = chip protection against discharges
2) DLC layer with low resistivity = charge spread against efficiency non uniformity
3) Micromegas principle allowing low ion feedback

## Slide 10
Coupling ERAM gaps to TIMEPIX4 chip => ERAMPIX
TIMEPIX4 chip
DLC resistive layer
on 50 um of Kapton
128 um gap with SD45/18
woven stainless steel mesh
Proof of principle of simple coupling of TIMEPIX4 with ERAM-like multiplication gap
1) DLC (Diamond-like-Carbon) resistive layer = chip protection against discharges
2) DLC layer with low resistivity = charge spread against efficiency non uniformity
3) Micromegas principle allowing low ion feedback
GAP
Chip Support and gap tensioning system
TIMEPIX4 on NIKHEF carrier board
Readout based on FPGA
Xilinx AMD Kintex UltraScale KCU105-G

## Slide 11
Developments 2024/25 at CERN
TIMEPIX4

## Slide 12
Developments 2024/25 at CERN
TIMEPIX4

## Slide 13
Developments 2024/25 at CERN
TIMEPIX4

## Slide 14
Developments 2024/25 at CERN
TIMEPIX4

## Slide 15
Developments 2024/25 at CERN
TIMEPIX4

## Slide 16
Activities 2025
TIMEPIX4
Activities 2026
Acquired RO system and start development of TIMEPIX4 readout (based on INFN FE FW)
Production of ERAMPIX structures fror simple coupling with TIMEPIX4
Development TIMEPIX4 readout fast links
Production and test of ERAMPIX structure to embed with TIMEPIX4
Development of gas photon-multiplier layer for TPC optical readout
Resistive Micromegas detector - Panel of 4 detector (2 guaranteed): production Panel P2 (330X254) Thickness 200um - 77mm x 97 mm (Based on DFS 3192 uRwell layout but adapted to MM) - 25mm x 41mm active area, 150um gap amplification (Dynamask) - DLC resistivity from 5 to 10M Ohm - 2 external connexions for Mesh and DLC
Xilinx AMD Kintex UltraScale FPGA KCU105 thanks to INFN-PD-Dtz1
Eager to move our “gas detector”
activities from LNL to new Lab. “dell’Universo” in via Luzzatti

## Slide 17
Development TPC Optical Readout
Synergy  DRD1/4 / INFN Gr5 TIMEPIX4
Development new Digital-SiPM
Synergy  DRD4 / INFN Gr5 ASPIDES
Development new Back Side illuminated SiPM
Synergy  DRD4 / INFN Gr5 IBIS-Next (C.Forza - PhD)
Readout of Water-based liquid scintillator
SiPM => low noise & high PDE
 Readout of very fine grained sci-fi detector
1. Downstream TCP under study
- Optical readout of avalanche gas multiplication
- Extended drift regions - Transparent conductive anodes - Advanced timing solutions
2. “Thin” top and bottom TCPs under evaluation
Further upgrade Hyper-Kamiokande Near Detector (2030)
 Optical Readout of TPC

## Slide 18
Development TPC Optical Readout
Synergy  DRD1/4 / INFN Gr5 TIMEPIX4
Development new Digital-SiPM
Synergy  DRD4 / INFN Gr5 ASPIDES
Development new Back Side illuminated SiPM
Synergy  DRD4 / INFN Gr5 IBIS-Next (C.Forza - PhD)
Further upgrade HK Near Detector
Requests to ASPIDES: optical instrumentation & parts
for Photo-detector characterization
Requests to TIMEPIX4: gas multiplier structures
DTZ-Gr1 Padova: provided FPGAs for Readout systems
Requests to HK for R&D = optical parts for imaging anode
(Lenses, Mirrors, Quartz windows …) needed also for TPC laser data taking Request  O(15kE) including MM structures (prev. slide)

## Slide 19
Courtesy
E.Radicioni G.Catanesi

## Slide 20
Resources @ INFN Padova
FTE Padova 2025/7 => 40%
G.Collazuol 10 %
S.Levorato 10 %
M.Feltre 20%
Richieste 2026 in Sezione PD
Servizio Elettronica
programmazione FPGA TimePix4 (collaborazione con INFN FE) ~ 3m.p.
(overlap – con richiesta ADA-5D)
Servizi Tecnici ed Elettronici
Servizio Progettazione Meccanica
Servizio Officina Meccanica
Preventivi 2026
Consumo (new ERAM structures) per circa 10kEuro
Missioni (CERN) per 4kEuro
TIMEPIX4

## Slide 21
Additional Material
TIMEPIX4

## Slide 22
Courtesy
E.Radicioni G.Catanesi

## Slide 23
Aim
Implementation of Optical and Charge readouts of gas multiplication structures
based on resistive and capacitive micro-pattern gas detectors (MPGD)
Target sensitivity - for optical readout => VUV and DUV light
- for primary charge readout => single electron
Methods
Coupling Embedded Resistive Anode MicroMegas (ERAM) with TIMEPIX4 (DLC for resistive layer)
Coupling nano-diamond / DLC photo-cathodes to ERAM (later stage)
Applications
Imaging detectors exploiting charge and light
Robust x-ray & VUV & DUV gas-based detector
Padova Interests & contribution
TIMEPIX4

## Slide 24
TIMEPIX gas detectors – issue #1 = discharges

## Slide 26
History of TIMEPIX gas detectors

## Slide 27
Very compact electronics
ERAM module for T2K TPCs
8 + 8 ERAMs per HATPC
ERAMs used for the new TPC of T2K
ERAMs are built at CERN MPGD Lab

## Slide 28
TIMEPIX4
ERAMs used for the new TPC of T2K
ERAMs are built at CERN MPGD Lab

## Slide 29
TIMEPIX4

## Slide 30
TIMEPIX4

## Slide 31
TIMEPIX4

## Slide 32
TIMEPIX4
Coupling ERAMs + TIMEPIX4 chip
Resistive layer (DLC)
Key points addressed (simulation and measurements) by TIMEPIX4
Choice of Diamond-Like-Carbon (DLC) resistivity
and thickness of insulator layer (between pads and DLC)
R x C => charge spread velocity
Geometry and dimension of grid/mesh with respect to pad
  Geometry in order to avoid Moire`- like effect
 Build prototype
Insulating layer
Applications
very fine grained tracker
and X ray detector

## Slide 36
TIMEPIX4
Coupling H-ND cathode + ERAMs + TIMEPIX4 chip
Resistive layer (DLC)
Key points addressed (simulation and measurements) by TIMEPIX4
behavior of the hydrog. nano-diamond photo-cathode withT2K gas
study HV configuration and detector geometry for optimizing photo-electron collection and drift
 Build prototype
Insulating layer
Applications
very fine grained photo-det
VUV-DUV imaging
Photo
Cathode

## Slide 37
TIMEPIX4
TIMEPIX4 – WP2 timeline and milestones