## Slide 1: Medical Applications of Plasma Accelerators
October 6, 2025
Chair of Experimental Physics – Medical Physics
Laser-Ion Acceleration Group, Prof. Dr. Jörg Schreiber
Sonja Gerlach

## Slide 2
What is medical physics?
Definition:
[…] physics principles, methods and techniques in practice and research for the prevention, diagnosis and treatment of human diseases with a specific goal of improving human health and well-being.
Fields:
        Imaging (ionizing & non-ionizing)
  Radiation therapy
  Nuclear physics
  Radiation protection
  …
This talk: Ionizing radiation for imaging and cancer therapy
International organization of medical physics

## Slide 3
Cancer
Some numbers (Germany, rounded):
≈ 50% get cancer in the course of life
≈ 60% 5-year survival rate (1980: 50%)
Second likely cause for death (Most likely: Cardiovascular disease)
Reason (USA): Food (35%), Tobacco (30%), Infections (10%)
 | ♀ | ♂
Incidence | Breast Colorectum Lung | Prostate Lung Colorectum
Mortality | Breast Lung Colorectum | Lung Prostate Colorectum
Cardiovascular disease
Cancer
Respiratory disorder
Psychological diseases
Digestive system
Mortality per 100 000 inhabitants
Ref.: Health report German government

## Slide 4
Cancer therapy
 | All patients (N = 1,029,569) | Patients survived less than 5 years (N = 491,599) | Patient survived at least 5 years (N= 537,970)
Modality | % of patients | % of patients | % of patients
Surgery | 64% | 46% | 80%
Radiotherapy | 35% | 31% | 39%
Chemotherapy | 31% | 34% | 29%
Surgery and/or Radiotherapy and/or Chemotherapy | 79% | 66% | 90%
Other options: Immunotherapy, Hormon therapy, Laser therapy…
Mee et al, British Journal of Radiology, 2023
British study, treatment 2009:

## Slide 5
Radiation therapy
Options: X-rays, Ions, Electrons (Neutrons)
Hughes et al Int Journal of Molecular Science, 2020
Gal et al, Journal of Neuro-Oncology, 2024
Comparison of depth dose curves:
Comparison of treatment plans:
A: Protons B: X-rays
Protons seem to have beneficial properties, but physical dose is not everything!

## Slide 6
Radiation therapy
Clinical practice:
X-rays dominant
Few % receive ion therapy: Pediatric cases, skull base tumors, spinal cord, pediatric…
Internal X-ray therapy: Brachytherapy
Current research topics:
Flash
Biological effectiveness
Motion control
Treatment verification
Mini/Micro beam therapy
---
Fig: Oh PFM 2019, adabed from PTCOG
Drawbacks ions:
Expensive
Robustness to inhomogeneities & movements
Clinical evidence not always clear
Excursus FLASH: The FLASH effect refers to the observation that delivering radiation at ultra-high dose rates (≥40 Gy/s, compared to ~0.03–0.1 Gy/s in conventional therapy) can spare normal tissues while still being equally effective (or more effective) at killing tumors

## Slide 7
Radiation therapy
Radiobiology – RBE as an exemplary research field:
Assessment through clonogenic cell survival, modelled by ‘linear quadratic model:
Radiobiological effectiveness: RBE =
RBE clinically assumed to be 1.1 for protons
Fig: Amaldi et al, CERN reports, 2019

## Slide 8
Medical physics & plasma based accelerators
Current research topics:
Laser-driven proton therapy
Laser-driven proton sources for isotope production
Laser-driven proton sources for preclinical research in radiobiology, including FLASH
Laser-driven electron therapy
Plasma based X-ray sources for imaging
This talk: Laser-driven proton acceleration for therapy and research

## Slide 9
Outline
Introduction to laser-driven proton acceleration
State of the art & limitations
Research at CALA in Munich
Three examples for medical physics with plasma-based accelerators

## Slide 10
Laser-driven ion acceleration
Difference to Electron Acceleration:
Short focal length parabola
High sensitivity to laser contrast
Overcritical target (solid/liquid)
‘younger field’
…
Acceleration mechanism:
Target normal sheet acceleration (TNSA)
Radiation pressure acceleration (RPA)
More advanced concepts (…)
Fig: Macchi, 2016

## Slide 11
Laser-driven ion acceleration
Thick target (TNSA)
‚Target normal sheet acceleration‘
R
Thin target (RPA) ‚Radiation Pressure Acceleration‘
Mass limited targets
µ-plasma in Paul trap
transverse confinement
Hilz+,
Nat Comm. 9, 423 (2018).
Optimization strategy during last 20 years: laser-pulse energy ­, pre-pulses ¯, target thickness (size) ¯, repetition rate ­, reproducibility ­

## Slide 12
Laser-driven ion acceleration
Laser-plasma acceleration | Non-laser (Radio frequency, RF) acceleration
Single bunch every second (large particle number ≈1012 per bunch) | Continuous beam (micro-bunch train)
Broad energy distribution (100%) yet short bunch (fs…ps…ns) | Mono-energetic (ns…µs bunches)
Spray (10° divergence) yet small source (µm) | Beam
Intrinsically synchronous to multiple radiation modalities | Non-trivial in sub-ns
Source and acceleration combined (high field, high temperature, high density) | 
New application possibilities
Topics in medical physics
Probing ultrafast processes
Research in nuclear astrophysics

## Slide 13
Laser-driven ion acceleration
State of the art (rough numbers):
 | Laser-driven | Conventional
Energy | 150 MeV record, 70 MeV reproducible | 70-230 MeV
Energy spread | 100% without beamline | 0.1 %
Avg. Dose rate | 0.5 Gy/s | 0.1 Gy/s
Peak Dose rate | Up to 109 | Continuous beam
Stability | Poor | Solved
Diagnostic | Challenging | Solved
Costs | $ 40M (1 PW) | $ 40M
Literature:
Schreiber et al: “Hands-on” laser driven ion acceleration: A primer for laser-driven source development and potential applications (2016)
Linz et al: What will it take for laser driven proton accelerators to be applied to tumor therapy? (2016)
Linz et al: Laser-driven ion accelerators for tumor therapy revisited (2016)
Notes: Accelerator hardware: only around 20% of 40 Million

## Slide 14
Centre for Advanced Laser Applications (CALA)
Fig: Google maps
ATLAS3000
https://www.pulse.physik.uni-muenchen.de/
Broadband IR Diagnostics
Electrons+xrays
Prot+carbons
Heavy ions
Light-Light scatter
ZEUS (R&D)
PFS (kHz)

## Slide 15
ATLAS 3000 Laser
Experimental areas
Homebuilt frontend
Thales main amplifier
Ti:Sa
Pulse length: 25 fs
Repetition rate: 1 Hz
Energy: 60 J (13 J)
3 Deformable mirrors
Focus size: 4.5 μm
Bachreflex Suppression via PC
Temporal Contrast:

## Slide 16
Laser-ION Acceleration (LION)
Target positioning system
Permanent magnet quadrupoles
Wide angle spectrometer
f/5 off-axis parabola
Application plattform
Laser

## Slide 17
Laser-ION Acceleration (LION)
Target positioning system
Permanent magnet quadrupoles
Wide angle spectrometer
f/5 off-axis parabola
Application plattform
Some specifics:
Extensive control system based on Tango
Water leaf target
Operation w/o beamline
---------------------------------------------
University based system!

## Slide 18
Laser-ION Acceleration (LION)
Target positioning system
Permanent magnet quadrupoles
Wide angle spectrometer
f/5 off-axis parabola
Application plattform
Current performance:
Typically 20 MeV (42 MeV max)
With beamline: ≈ 1 mm lateral focus size, ≈ 5 % energy spread
1 Hz operation (mostly) possible
Online characterization of individual ion bunches

## Slide 19
Laser-ION Acceleration (LION)
Application plattform at LION
Protons
Subtitle:
From single shot experiments towards a machine
High repetition rate
Reproducibility
…
Goal:
Providing particle bunches with reproducible & tunable parameters at 1 Hz for various applications

## Slide 20
Machine control via ‚Tango controls‘
Requirements:
Operation at 1 Hz
Correlation between laser- and ion-parameters
Intelligent feedback loops
ATLAS-3000
Diagnostics (energy, spectrum, profile)
Dispersion manipulation (Dazzler)
Attenuator + filters
Experiment
Motion (Phytron, PI, Owis, Thorlabs, …)
Cameras (Basler, IDS, Grasshopper, …)
Diagnostics (Picoscope, …)
Others (Arduino, power supplies, …)
User control
Scripted control
Many device servers available open source!
Weiße et al, HPLSE 2023
https://gitlab.lrz.de/ cala-public

## Slide 21
Liquid Leaf Target System
FRONT VIEW
1 mm
fused silica nozzles: 50 and 25 µm
Ø1 mm catcher: heated to approx. 110° C
45° collision angle
Setup:

## Slide 22
Chromatic focusing lens
Permanent magnet quadrupoles
Dublet / quadruplet available
Magnets motorized in x/y position & rotation
PMQ position defines transported proton energies
Lateral FWHM: ≈ 1 mm
Energy spread: ≈ 5 % (calculated & experimentally confirmed)
Range (mm)
Normalized Dose (a.u.)
1 cm
18 MeV
Target: formvar foils
Target: liquid leaf
Other options: Solenoids, plasma lens

## Slide 23
Particle Bunch Characterization @ 1Hz
Working Principle
Ions deposit their energy in a water reservoir
Energy deposition leads to localized heating
A pressure wave originates from gradients in thermal expansion
Ultrasonic signal is recorded by a transducer
Gerlach et al, 2023 & Haffa et al, 2019
I-BEAT 3D
Measures particle bunch properties such as energy, position & particle number at the ion focus
Electromagnetic pulse resistant & cheap
1 Hz compatible

## Slide 24
Particle number & mean energy characterized at 1 Hz @ LION
Particle Bunch Characterization @ 1Hz

## Slide 25
Example 1: First in-vivo studies
Zebrafish irradiation (CALA, Munich)
Rösch et al, Rev Sci Instrum, 2020
Feasibility of irradiating zebrafish embryos with laser-driven proton bunches
Biologically relevant doses (up to ~15 Gy photon-equivalent)
Challenges: dose inhomogeneity, precise dosimetry, and reproducibility

## Slide 26
Example 2: First in-vivo studies
Mouse irradiation (HZDR, Dresden)
Kroll et al, Nat Phys, 2022
Demonstration of a laser-driven proton plattform delivering controlled, homogeneous tumour doses
Irradiated mouse ear tumours with 4 Gy & ultrahigh dose rates (~10⁹ Gy/s)
Challenge: beam stability and precision for radiobiology studies

## Slide 27
Example 3: Imaging
Ostermayr et al, Nat Com, 2020
Bi-modal imaging: X-ray phase contrast & proton projection (Texas Petawatt Laser)
Co-emitted x-ray and proton micro-sources from micrometer tungsten needles.
Micrometer-scale source sizes and ultra-short proton and x-ray bunches (generation < ps)
Opens prospects for integrated imaging and irradiation in radiobiology and therapy.

## Slide 28
Summary
Conclusion
Medical physics is a broad yet specialized field with major impact
Plasma-based accelerators hold promise for addressing questions motivated mainly by imaging & radiotherapy
Technology is maturing, but improvements in stability and instrumentation remain crucial
First in-vitro & in-vivo studies are ongoing
Outlook: novel applications on the horizon?

## Slide 29
Acknowledgements
Tel Aviv University (Israel): I. Pomerantz+ Queens University Belfast (UK): B. Dromey+
GSI Darmstadt (Germany): B. Zielbauer, V. Bagnoud+
TU Darmstadt (Germany): M. Roth+, G. Schaumann,
HZDR Dresden (Germany): U. Schramm, M. Bussmann+ FSU Jena (Germany): M. Zepf, P. Hilz, +
Peking University (China): W. Ma+
SIOM (China): J. Bin
LBNL (US): T. Ostermayr
Funding: DFG, BMBF, Bavarian state
Ludwig Maximilians University Munich:
AG Schreiber, AG Karsch, AG Döpp, AG Thirolf
K. Parodi+, P.R. Bolton, J. Bortfeldt, G.Dedes, W. Assmann, F. Krausz+, H. Ruhl+, A. Friedl, M. Groß, J. Szerypo, H. Wirth, O. Gosau, N. Gjotev, F. Saran, G. Schilling