## Slide 1
1
Development of the L2-DUHA dual output front end at ELI-ERIC
Alex Whitehead, Lukáš Indra, Jonathan T. Green
The Extreme Light Infrastructure ERIC - ELI Beamlines Facility, Dolní Břežany, Czech Republic
Czech Technical University, Prague, Czech Republic
This project has received funding from the European Union´s Horizon Europe research and innovation programme under grant agreement no. 101073480.

## Slide 2: ELI-ERIC – ELI Beamlines facility
Located in Dolní Břežany (Czech Republic)
ELI Beamlines explores the interaction of light with matter at intensities 10 times higher than previously achievable.
4 High power laser systems: From mJ kHz to PW 1shot/min systems
7 Secondary sources – EUV - X-rays, Electron and Ion Accelerators
10 User stations
2

## Slide 3: ELI-ERIC – ELI Beamlines facility
L1 ALLEGRA
6 TW, 1 kHz
L2 DUHA
100 TW, 50Hz
L3 HALPS
1.5 PW, 10Hz
L4 ATON
10 PW, 1shot/min
X-ray generation
Electron acceleration
Proton/ion acceleration
L4 compressor
Material & biomolecular applications
Plasma physics
3

## Slide 4
Compact laser driven incoherent source
4
LUIS beamline
L2 DUHA
100 TW, 50Hz

## Slide 5: Laser driven soft x-ray free electron laser
5
Photon beamline
LP-Accelerator
Electron Beamline
Undulator line
User 2-3 Stations
Pump-probe set-up
Host of the EuPRAXIA 100 Hz laser driven plasma accelerator

## Slide 6: L2 DUHA
Parameters | Target
Central wavelength | 820 nm
Peak power | 100 TW
Energy | 3 J (aiming 4 J)
Pulse duration | 25 fs
Repetition rate | 20 - 50 Hz (aiming 100 Hz)
Beam size (diameter) | 120 mm
Contrast | at 10 ps
Output laser beam RMS pointing stability | < 1 µrad
Intensity on target | 
Parameters | Target
Central wavelength | 820 nm
Peak power | 100 TW
Energy | 3 J (aiming 4 J)
Pulse duration | 25 fs
Repetition rate | 20 - 50 Hz (aiming 100 Hz)
Beam size (diameter) | 120 mm
Contrast | 
Output laser beam RMS pointing stability | < 1 µrad
Intensity on target | 
High energy, high repetition rate, OPCPA system
3
25
6

## Slide 7: Dual output front-end
7
Seeded by a fiber oscillator (Orange model, 80 mW output power, 80 MHz, 1030 nm).
In-house developed diode-pumped Yb:YAG thin-disk amplifier delivers 75 W average power at a 2 kHz, generating pulses compressed to 3 ps.
Single pump laser for both outputs

## Slide 8: Near IR OPCPA
8
Seed for high power OPCPA used for laser-plasma acceleration.
2 OPA stages reaching over 1 mJ
Stretched to 3 ns, and repetition rate reduced to 50 Hz for the high power OPCPA

## Slide 9: Near IR OPCPA – supercontinuum generation
9
Seed created via supercontinuum generation in a 13 cm long YAG crystal
Stable, and high contrast method for broadband beam generation*
*Lukáš Indra, and al., "Picosecond pulse generated supercontinuum as a stable seed for OPCPA," Opt. Lett. 42, 843-846 (2017)
*Alexandr Špaček, and al., "Stability mechanism of picosecond supercontinuum in YAG," Opt. Express 28, 20205-20214 (2020)
Supercontinuum output

## Slide 10: Near IR OPCPA – OPA stages
10
2 OPA stages reached over 2 mJ with fluctuations around 1% rms
Output of stretcher

## Slide 11: Near IR OPCPA - stretcher
11
Spectrum between 760 and 900 nm
Pulse stretched to 3 ns
Output of stretcher

## Slide 12: Mid IR OPCPA
12
Usage for high harmonics generation for seeding the FEL of the LUIS beamline, and drive a laser plasma X-ray source in L2 hall
Mid-IR beam generated in DFG crystal
3 OPA stages reaching 5 mJ at 2 kHz
Compressed to 30 fs with a long suprasil rod

## Slide 13: Mid IR OPCPA – OPA stages
13
Spectrum between 1800 and 2400 nm
Output of OPA 3 reached over 3.5 mJ with fluctuations around 1% rms
Output of SHG generated in OPA 3

## Slide 14: Mid IR OPCPA - compressor
14
Work in progress to compress to 30 fs
Compression in bulk using a suprasil rod
Dazzler for high order dispersion optimization

## Slide 15: Conclusion
15
Offering a dual output source capable to run simultaneously
N-IR: > 2 mJ achieved after 2 OPA stages
Mid-IR: > 3 mJ achieved after 3 OPA stages
Summary
Next steps
N-IR: High power OPCPA amplification
Mid-IR: Amplification to 5 mJ and compression to < 30 fs

## Slide 16: Thank you for your attention
16
This project has received funding from the European Union´s Horizon Europe research and innovation programme under grant agreement no. 101073480.

## Slide 17
Pump laser