## Slide 1: TECH-PFA PhD Program Admission to II year presentation Multi-parametric thermal-mechanical modeling and analysis of high order active mirrors for space telescopes
Candidate: Chiara Scandaglia
Supervisors: Runa Briguglio, Marco Xompero
INAF - O.A. Arcetri
XL Cycle
23 September 2025

## Slide 2
  Educational requirements
Attended courses
  Adaptive Optics for Astronomy I - Dr. Carmelo Arcidiacono - Passed
  Adaptive Optics for Astronomy II - Dr. Kalyan Radhakrishnan - Attended
  Fundamentals of system engineering and project management for large scientific projects - Dr. Marco Xompero and Dr. Runa Briguglio - Passed
  Coupled electrical-thermal-structural Finite Element Analyses - Dr. Michele Ballan, Prof. Giovanni Meneghetti and Prof. Mattia Manzolaro - Passed
  Methodologies and techniques for the analysis of experimental data - Prof. Alexis Pompili - Attended
  Random excitations and response of structures - Prof. Giuseppe Petrone and Prof. Francesco Franco - Ongoing lectures
12 total credits (10 credits required from educational obligations)
Missing exams will be taken by the end of 2025

## Slide 3
  Educational requirements
Planned schools and conferences
  Workshop on Innovative Technologies for Space Optics (WITSO) 2025 - ESA/ESTEC, Noordwijk, The Netherlands - 13-17 October 2025 - Workshop - Poster accepted
  SPIE Astronomical Telescopes + Instrumentation 2026 - Copenhagen, Denmark - 5-10 July 2026 - Conference
  Observing with Adaptive Optics 2026 - Observatoire de Haute-Provence, Saint-Michel-l'Observatoire, France - October 2026 - School
A period of study and research abroad during the second year is foreseen, but not yet defined. The ESA OSIP program is one of the proposed options.

## Slide 4
  Scientific context
SCIENCE CASES
REQUIREMENTS
TECHNOLOGIES
High resolution
High contrast
Ultra-stable wavefront
Risks and costs mitigation
  Large primary apertures
  Deformable mirrors (w/ contactless actuators)
  Wavefront sensors
  Active optics control loops
Earth-like exoplanets
characterization
Cosmological structures
observation

## Slide 5
  Why adaptive optics in space?
Features
  Stable wavefront control
  Large primary aperture achievable
    and correction directly on the primary
  Support vibration rejection through the use of particular actuators (e.g. voice coil)
    Decoupling from the mirror
    Use of lighter materials -> mass reduction
    Looser tolerances
  Thermal load deformation correction
  High contrast imaging (e.g. if combined with
coronagraph instruments)
Challenging topics
  New studies on adaptation of ground-based technologies in the space context
  New mission profiles taking into account deformable mirrors
  Cost effectiveness assessment

## Slide 6
  Main research activity
  An active mirror system parametric integrated model
In what does it consists?
Telescope opto-mechanical model
  w/ variable mirror configuration parameters
Thermal-mechanical simulator
  w/ variable orbital environment parameters
You are here
TO
Calculate deformations and displacements
Compute wavefront correction
Estimate mirror performance (fitting error)
Set trade-offs and optimize
  mission profiles
  mirror configurations
Evaluate the system behaviour in different scenarios (i.e. costs)
Part of the ULAOPS project, funded by ASI and in collaboration with PoliMi and industrial partners
Leading question: with regard to typical space mission profiles, costs and requirements, what could make this technology more attractive than others?

## Slide 7
  Simulation pipeline
Simulation train meant to be as automatized as possible, to autonomously switch between the environmental condition and mirror configuration parameters and re-run the analysis

## Slide 8
  First implementations: structural parametric model
Configuration parameters
Deformable mirror support model with 7 modules
Single actuator cell model
Deformable mirror segment (module) support model with 7 actuator cells

## Slide 9
  First implementations: thermal inputs on FEM model
Telescope optical drawing
Telescope dummy mechanical model + mesh
Telescope thermal model (inside a dummy spacecraft for thermal boundary conditions)
Selected orbit

## Slide 10
  First implementations: thermal inputs on FEM model
FEM mesh imported in the telescope thermal model and temperature distribution mapped onto it
Imported temperature distribution in the Ansys Mechanical model
Out-of-plane displacements (WFE from deformations) calculated by Ansys and exported as python maps

## Slide 11
  First implementations: thermal inputs on FEM model
FEM mesh imported in the telescope thermal model and temperature distribution mapped onto it
Imported temperature distribution in the Ansys Mechanical model
DM correction loop
Out-of-plane displacements (WFE from deformations) calculated by Ansys and exported as python maps
+sensitivity matrix∙displacement vector

## Slide 12
  Other activities: introducing LATT
Deformable segment of a primary mirror prototype
40 cm thin Zerodur deformable shell (mirror)
Aluminium honeycomb reference body (support)
Low mass density
19 voice-coil actuators and 19 capacitive sensors (contactless technology)
  When set, the shell floats at a given gap from the reference body
  Decoupling between mirror and support!

## Slide 13
  Other activities: LATT thermal tests
Goal: assess effects of reference body deformations and resulting actuator commands on mirror correction
Reference body
Mirror shell
Vacuum chamber
Heaters placed on reference body
Reference body back w/ actuator electronics
Thermostat
Connectors
Sensed temperature dataloggers
Notes: Thermal tests in vacuum chamber to assess the deformations of the reference body and how they propagate to the mirror shell
Objective: verify how the mirror deformations are the result of an ‘incorrect’ actuator command, caused by the greater distance measured by the capacitive sensors due to the reference body thermal deformations
Being the deformations caused by an actuator command, an equal and opposite command would be sufficient to restore the shell original surface: corrections with zero fitting error

## Slide 14
  Roadmap for the next years
 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3
Opto-mechanical model finalization |  |  |  |  |  |  |  | 
Python automatization architecture finalization |  |  |  |  |  |  |  | 
Simulations on actual model and performance evaluation |  |  |  |  |  |  |  | 
Laboratory activities |  |  |  |  |  |  |  | 
Thesis writing |  |  |  |  |  |  |  | 
2025
2026
2027
WITSO
KM1
SPIE
KM3
KM2
MILESTONES
WITSO @ ESA - Simulation scheme finalized
KM1 - Model completed
KM2 - Architecture code completed
SPIE @ Copenhagen - Paper ready
KM3 - Activities completed
KM4 - Thesis completed
KM4

## Slide 15
  THANK YOU FOR YOUR ATTENTION!