## Slide 1
Introduction to JUNO/TAO, My Contributions and Research Activities
Presented by: Ammad Ul Islam
For: Admission to the III year
Supervisor: Dr. Andrea Fabbri
Co-Supervisor: Dr. Fabrizio Petrucci

## Slide 2
INTRODUCTION
Taishan Antineutrino Observatory (TAO), a satellite experiment of JUNO.
  Taishan Nuclear Power Plant, 30 –35 m from one of the 4.6 GW the reactor cores
Measure reactor neutrino spectrum
Ton scale Gd-doped Liquid Scintillator (Gd-LS)
Full coverage of SiPM
Operate at -50 ℃ (reduce SiPM dark noise)
Water tanks and plastic scintillator for shielding
Water Tank (WT)
1.2 m thickness of water Cherenkov detector
300, 3 inch PMTs, same with sPMT in JUNO
GdLSAcrylicvessel SiPM/support  Tank Insulation  1.2 m water or HDPE shielding
Reference: TAO CDR arXiv:2005.08745

## Slide 3
TAO Electronics
Key features (refer to CDR):
8048 readout channels, 12.5 cm2/ch
Timing resolution: ~1ns

## Slide 4
TAO Electronics Scheme
FEB
  2 channel 1 tiles
  Total 8048 channels
  Tile and FEB are connected
  Analog signals from FEB will be transferred to FEC via differential pairs, 3-4 m inside the SS tank, ~10 m outside the tank
FEC
  ADC is on FEC, used to digitize analog signals from FEB
  FPGA & Power boards in MicroTCA.4 crate
  Q/T information is extracted with FPGA (waveform analysis)

## Slide 5
Study Abroad at TNNP/IHEP
The Language Barrier
Working in a Controlled Environment
Working Underground in a Noisy Environment
Safety, Access, and Logistical Hurdles
System Integration and Interdependence
Custom/Prototype Hardware
Troubleshooting Unforeseen Failures

## Slide 6
Water
My Contribution
Water
PS Testing, Configuration, Pair Testing
Interface Board Issue
Cabling of LV to all flanges
Testing Dryrun initial 1
Troubleshooting of Faulty Channels
DryRun Initial test 2
Troubleshooting
Dryrun Initial Test 3
Troubleshooting of faulty channels
Documentation of all Initials and Troubleshooting
Notes: Final Signal Cable Mapping [Final one] - HedgeDoc

## Slide 7
Water
My Contribution
Water
Dementaling of LV, HV and Signal Cables
Cleaning of the tank and Internal parts with ethanol
Shifting and setting of new Cleanroom
Bottom Shielding with Lead
HDPE bottom
ACU(Automatic Calibration Unit)
Cable Loop Systems(CLS)
Air Purging
Thermal Insulation
HDPE

## Slide 8
Water
My Contribution
Water
Troubleshooting Resistance Issue
JUNO Workshop
Collaboration Meeting
Resistance Testing
GUI development for LV
Water Leakage Issue
Dismanteling Everything From Racks
Flange Boxes
Putting Everything on Racks
Commissioning

## Slide 9
Current Status of TAO
Installation work almost done
CD installation done
LS filling was done on Aug. 30
Started cooling on Sep. 2, now at ~-50
TVT installation done
WT filling done
Detector Commissioning
TAO Goals Achieved
Reconstruction algorithm works with reasonable accuracy
Backgrounds are understood
Detector response is understood, and energy response is obtained
First IBD signals are obtained by analyzing the commissioning data
Notes: European community for future accelatror

## Slide 10
Remaining Tasks
Delivery remaining ADC boards [Rome Tre]
Overshoot optimization, Sep. 15 Guofu Cao + 1 PhD from NJU
LV control software improvement, [Rome Tre]
Grounding, Sep. 11 Guofu Cao]
1 mTCA crate commissioning (~1300 channels), Sep. 11 Sep. 22 [Elec. + TDAQ]
Cabling in cabinets, Sep. 22 Jie Zhang +
Q/T algorithm optimization based on waveform data, < Sep. 22 Guofu Cao, Jiayang Xu]
Firmware, < Oct. 13 Fengfan Yang]
Address issues found during the commissioning
Smooth data flow from FEC to TDAQ
Implement optimized Q/T algorithm, reasonable Q/T accuracy
Firmware for TVT
Complete the full detector commissioning and performance optimization, < Oct. 27
Notes: European community for future accelatror

## Slide 11
Roma Tre Tasks
Delivery remaining ADC boards [Rome Tre]
Testing and Troubleshooting of the LV issues with proposed solutions at INFN Roma Tre
Setup LV system controls to DCS(Remote Control is already implemented)
Notes: European community for future accelatror

## Slide 12
Courses and Conferences
Courses
  Programmable System on Chip (SoC) for Data Acquisition and Processing(Passed)
  High Energy Particle Physics Detectors in Space(Passed)
  Management of Scientific Projects(Passed)
  Machine Learning For Physics(Project in Development)
  Advanced scientific Programming in MATLAB(Attended)
Conferences and Workshops
  The 26th JUNO Collaboration Meeting, Kaiping, China
  JUNO Analysis Workshop, Dongguan University of Technology(DGUT) July 2025
  PhD meeting at the Gran Sasso National Laboratories February 2025: Poster Presentation
  2nd ECFA-INFN Early Career Researchers Meeting, 2024
Notes: European community for future accelatror

## Slide 13
Publications
Published
  As Corresponding Author: “Real-Time Monitoring and Control of Renewable Energy Systems Using Wireless Telecommunication and Signal Processing Techniques for Smart Grids with Energy Storage”, Spectrum of Engineering Sciences (2025)
In Writeup
  Development and Performance of Silicon Photomultipliers Readout System and Front-End Electronics for Reactor Neutrino Detection at the JUNO-TAO Experiment (writeup)
Talks
  TAO LV System Talk in TAO Meeting
Notes: European community for future accelatror

## Slide 14
Water
Planning for III Year
Final Version of GUI for LV and its Deployment on DCS
Optimization of Noise Issues on I2C of LV System
Data Analysis and Pre-processing:
  Analyze the real-time data acquired from the TAO which is expected to be available at the end the year.
  Cleaning, pre-processing, and organizing
AI Algorithm Development:
  Develop and train the AI-based pattern recognition technique.
  Machine learning model, optimizing its architecture, and training
FPGA Implementation:
  AI model will be developed on an FPGA(KU15P).
System Validation and Benchmarking:
  Benchmarking the speed, accuracy, and efficiency of proposed method against traditional methods.
Thesis Writing:
  Writing the thesis, systematically documenting the research methodology, results, and conclusions.
Water

## Slide 15
THANK
YOU

## Slide 16
Supporting Slides

## Slide 17: Electronics Update

## Slide 18: Over shoot

## Slide 19: Pending Actitivies since last meeting
Low Voltage Control system
  Splitter boards give some insulation issues when several PSU are connected
ADC Production
  It was scheduled during the last spring

## Slide 20: LV system
A second version of the splitter board is currently running @ NPP. All the insulation issues are solved.
The control software for the LV system is currently under final deployment by Ammad directly at NPP.
It will be included in the DCS software in the next weeks.

## Slide 21: ADC Board
Production done at the end of May
AD9083 (16 channel each)
Input connector
FPGA Connector
PLL
E2PROM
Voltage Regulators
Level shifters

## Slide 22
Test Procedure
Test JIG generates 32 signals that feed all the ADC board input.
Signal amplitudes can scan the input dynamics starting from below half of a single p.e. up to ~300 p.e.
Test JIG
#32

## Slide 23: QA / QC results

## Slide 24: QA / QC results
Several boards (~ 100) didn’t pass the first steps of the QA / QC:
  odd resistance values on the DC/DC outputs.
  Reduced voltages on the ADC pins also with the right resistance values.
Data cannot be acquired by the DAQ system (discontinuous transfer or totally absent)
After several iteration with the assembly company we found there was a big issue with the soldering oven,
the temperature was not homogeneus during the process and was below the soldering threshold on some of
boards.

## Slide 25: QA / QC results

## Slide 26: Current activities
Currently ~16 boards were recovered.
Fifty-four reworked boards will be delivered next Wednesday, we will be able to test them the day after and ship them as soon as possible.
We have 6 board in China right now, thanks to Fabrizio, to test the same reworking there trying to speed up the process.
The last board batch should be ready for mid-september (take into account italian company summer break.)

## Slide 27
Physics Requirments
RequirementsENC < 0.1 p.e.
Negligible impacts on energy resolution and allowed us to perform photon counting
ASIC Readout Scheme
Discrete Readout Scheme

## Slide 28
Timing Resoultion
Requirements: 1 ns
It’s not essential to have a ~ns level timing resolution for PSD
However, a good timing resolution (~1 ns) can help to improve the resolution of reconstructed position
ASIC scheme
200 ps TDC bin size, timing resolution of SPE is under investigation
Discrete scheme
~1.5 ns at 1 p.e., measured with a 6 x 6 mm square SiPM
ASIC
Discrete

## Slide 29
Energy Non Linearity
ASIC scheme:
  The large non-linearity is expected for KLauSchip, which is similar with that in DYB.
  The non-linearity based on charge depends on event positions, but this dependence can be significantly reduced by using p.e.counting, which is one of main features of SiPMs.
  Can be corrected during energy calibration.
Discrete scheme:
  No electronics non-linearity is expected for discrete readout.

## Slide 30
Pulse Shape Discrimination(PSD)
Due to fine granularity of ASIC readout scheme, it shows very powerful PSD discrimination
The sensitivity of mass ordering determination is improved with Δχ2increased by 0.05 (Doc-6568) (JUNO budget ~300 M$ for Δχ2= 9, so Δχ2= 0.05 is corresponding to 1.7 M$)
The potential risks on fast neutron background are almost eliminated
If the number of channels in discreate readout scheme is increased by a factor of 2, the similar PSD power with ASIC one can also be achieved
IBD Efficiency 100%
Discrete
ASIC
Discrete
ASIC

## Slide 31
Muon Induced Fast Neutron Findings
The spallation neutron from muon can mimic IBD signal.
Fast neutron
  High energy neutron deposited energy(proton recoil)+neutron capture
Double neutron:
  Two neutron capture
Using about 22days’ data
Muon
Water
Muon

## Slide 32
Water
In the real case, the fast-n background is an untagged muon-induced background.
Here use the tagged WP muon to study the fast-n properity.
The preminary trigger select WP muon(nHit>450);
CD muon [-20us,20us](total PE>40000);
Select WP only event(no CD muon)
Cut:
  After muon:[0, 500]us, find the CD event；
  Sub-event PE>3000
[0,500us] sub-event mulitiplicity
Water
Muon
Outside from the veto
Event Selection

## Slide 33
Water
Sub event Time vs Charge after WP-only muons
Since select the WP-only muon:
Still see before 60μs, there were a lot of events;
Caused by the flasher/PMT after pulse?
Sub-events time:
Prompt Time，the time of first signal after muon
Delayed Time，the time of second signal after muon
The time of third signal after muon
Time n：The time of (n+1)th signal after muon

## Slide 34
Water
Fast-neutron/Double neutron Finding
Water
Fast neutrons:
  Multiplicity =2;
  Prompt signal : within <2us after WP-only
  Delay signal: [60,500]us, neutron capture signal
Double neutron
  Prompt(neutron capture), [60,500]us
  Delay(neutron capture), [60,500]us
For sub-event
Add Cut :[0,500us], sub-event multiplicity =2;

## Slide 35
Water
Sub-event multiplicity =2 event feature
Water
– Time distribution of prompt signals
– Time distribution of delayed signals
– Time timediff distribution
There is a distinct pulse between 0 and 60 microseconds
The Event generated by the inherent properties of the PMT

## Slide 36
Water
Time vs Charge without Cut
Water