## Slide 1
Integrated Waveguide Source of Squeezed Vacuum for Quantum computation and Gravitational-Wave Detection
Hamza Hasnaoui
Integrated Quantum Photonic Laboratory
Hamza.hasnaoui@unitn.it

## Slide 2
1
Squeezed state of light
Squeezed states are non-classical states of light that enable measurements below the shot-noise limit, providing a fundamental resource for quantum computing, quantum communication and quantum metrology.
Notes: The squeezed vacuum state is created inside a non linear medium PPLN. When a strong laser beam at frequency 𝜔_𝑝 passes through it, due the light matter interaction the pump photon is splited into pairs of weaker photons that share quantum correlations — this process reduces the noise in one property of light, which is what we call squeezing.”

## Slide 3
2
CV-cluster model quantum computation
(2025) 3D cluster state (time-frequency multiplexing)
https://arxiv.org/abs/2309.05437
TMSV (EPR) states
CV- Measurement based quantum computation (CV-MBQC)
(2019) 2D cluster state (time domain multiplexing)
https://doi.org/10.1126/science.aay4354

## Slide 4
3
Fault-tolerant quantum computation
Gottesman–Kitaev–Preskill (GKP states)
(2025) https://doi.org/10.1038/s41586-025-09044-5

## Slide 5
4
Aasi, J., Abadie, J., Abbott, B. et al. Enhanced sensitivity of the LIGO gravitational wave detector by using squeezed states of light. Nature Photon 7, 613–619 (2013). https://doi.org/10.1038/nphoton.2013.177
Gravitational wave detection
Frequency range of GW 
Quantum noise in interferometric GWD:
  shot noise
  radiation pressure noise (due to the high power)
m
Notes: One of the most successful applications of squeezed light is in optical interferometry, where the goal is to detect tiny changes in phase or length.
A prime example of this is the LIGO gravitational wave observatory, which uses a large-scale Michelson interferometer to measure distortions in spacetime as small as 10^(−19)meters.
The sensitivity of an interferometer is limited by quantum noise, particularly the shot noise that arises from vacuum fluctuations entering the unused port of the interferometer. By injecting a squeezed vacuum state into this port, we can reduce the noise in the relevant quadrature — effectively improving the signal-to-noise ratio and pushing the sensitivity beyond the standard quantum limit.
But to To fully exploit squeezing, we need to control them wich means we precisely manipulate their phase and amplitude. I another word set the squeezed light at the squeezing level over time and across the detector’s full frequency bandwidth.
To ensure that we use Coherent control technique
Click ***

## Slide 6
Interaction Hamiltonian
5
nonlinearities based on SPDC interaction
Squeezing strength depends strongly on:
    Pump intensity
    Phase matching condition
    Nonlinear susceptibility
    Spatial mode overlapping
    Material losses
Direction of squeezing is determined by the phase of pump
Signal idler 
Two Mode Squeezed Vacuum
Signal idler 
Single Mode Squeezed Vacuum
How to generate Squeezed light ?
Notes: A common approach to generate squeezed light relies on on second-order, nonlinearities, typically through spontaneous parametric down-conversion. When a strong laser beam at frequency 𝜔_𝑝 passes through non linear medium, the pump photon is splited into pairs of weaker photons that share quantum correlations. In the general case, the signal and idler are distinguishable, typically at different frequencies or polarizations. Each mode individually may look thermal state, but the two modes in reality are correlated. And Squeezing emerges in joint quadratures of the signal and idler fields, leading to two-mode squeezing and entanglement. In the other hand when the signal and idler occupy the same optical mode, the nonlinear interaction directly produces a single-mode squeezed vacuum, where the noise of the field quadrature is reduced below the shot-noise limit, while the orthogonal quadrature is amplified.
The general formula of the squeezing operator is given by the time evolution of the interaction Hamiltonian, where the strength of squeezing depends on the pump power, phase matching condition and optical losses.
Squeezing can also be generated using third-order, χ³ nonlinearities, such as the Kerr effect or four-wave mixing. However, these processes are generally weaker per pass compared to χ² interactions.

## Slide 7
6
Integrated optical squeezed vacuum sources
 | Integrated source | Bulk source
Nonlinear medium | Thin-film LN ,PPLN waveguides | Bulk nonlinear crystals (e.g., PPKTP, PPLN,…)
Nonlinear interaction strength | High (tight optical confinement) | Moderate (limited by beam focusing and crystal length)
Optical losses | Higher propagation and coupling losses | low propagation loss
Squeezing levels | Up to~10 dB https://arxiv.org/abs/2511.15082 2016 | Up to ~15 dB http://dx.doi.org/10.1103/PhysRevLett.117.110801 2025
Bandwidth of squeezing | Broad (typically GHz to THz) | Tens of MHz; (limited by the cavity bandwidth)
Other properties | Compact, High passive stability, hight scalability, | Large setup, sensitive to mechanical vibrations, poor scalability
Optical parametric oscillator (OPO)
Integrated source (Single pass PDC )

## Slide 8
7
Squeezing experiment @ UNITN
Waveguides
Pump (775 nm)
Local oscillator (1550 nm)
Squeezed vacuum (1550 nm)
Integrated Quantum Photonic Laboratory

## Slide 9
8
Diced ridge waveguides in : (PPLN)
High optical confinement
Low optical losses
Squeezing source
Optical parametric amplification
(OPA)

## Slide 10
9
Quantum efficiency : 99%
Homodyne detector:
HD, key to observing squeezed states !!
CMRR
Bandwidth

## Slide 11
10
- Squeezing level of
- Anti-squeezing level of
Squeezing measurement
Non perfect spatial overlap  Visibility 90 % 
Improving visibility and external losses, estimate
Signal
Local oscillator

## Slide 12
Demodulation
Error signal QCF-Pump :
lock-in the phase of the pump (squeezing)
11
1
1
Coherent control
Seed
Pump
Coherent control is an active techniques to stabilize the phase of the squeezed light and ensure that the measurement is always performed on the quadrature with reduced quantum noise.
: Quadrature Control Field

## Slide 13
12
1
Coherent control
Demodulation
Error signal QCF-LO :
Lock in the relative phase between the squeezed states and local oscillator
2
2

## Slide 14
12
Challenging work for low frequencies, due to electronic noise, scattering, environment vibrations
squeeze lock-in
Zoom-in
13

## Slide 15
14
Developing integrated sources of squeezed vacuum for gravitational wave detection
will significantly reduce costs, improve ease of implementation, and open the door to next generation of GW detectors
Future efforts will emphasize scalable generation of high squeezing, reconfigurable on-chip control, and hybrid integration with non-Gaussian resources, enabling fault-tolerant continuous-variable quantum computing and deployable quantum technologies.
Future perspective

## Slide 16
Thank you
Mirko Lobino Alberto Quaranta Matteo Leonardi Massimo Cazzanelli Hamza Hasnaoui
Acknowledgment