## Slide 1: Test di precisione del modello standard ai collider
M. Diemoz - INFN Roma – RaRa occasione 20/10/2025 - MiB

## Slide 2: LEP – Test Standard Model (include top & Higgs)+?
C = 27 km
LEP Gestation 1975 -1980
CERN Council approval in 1981 – First beams JUL 1989 – Stopped NOV 2000
Probing SM at the quantum loop level
Discovery of W and Z 1983 (during LEP construction)
Overall  25 y: 15 y +10 y physics

## Slide 3: LEP- test di precisione dello SM (1989-2000)
INPUT
Total Luminosity: 1000 pb-1
20 Million Z’s
40,000 W+W-
Precision: 0.1%
Energy: 88  209.2 GeV
1989-2000 LEP Run
1989-->2000
Largest discrepancy (-2.9s) well inside
statistical expectation;
2 probability = 8%. Just fine.
Consistenza interna dello
Standard Model
N osservabili misurabili il cui
valore nello Standard Model
è funzione di Mhiggs (e Mtop)
W
W
top
bottom
Higgs
MW = MW0 + C1 Mtop2 + C2 ln(MHiggs2)

## Slide 4: LEP – Standard Model in ottima salute!
Predizione su mtop verificata
dall’osservazione diretta!
mH (GeV)
SM Global Fit (misure di precisione LEP, Tevatron, e altri esperimenti):
mH < 193 GeV (95% CL)
Limite diretto LEP:
mH > 114.4 GeV (95% CL)

## Slide 5: LEP: il progresso è straordinario!
Figure 1.15: The neutrino scattering and e+e− annihilation data available in 1987 constrained
the values of gVℓ and gAℓ to lie within broad bands, whose intersections helped establish the
validity of the SM and were consistent with the hypothesis of lepton universality. The inset
shows the results of the LEP/SLD measurements at a scale expanded by a factor of 65
CERN-PH-EP/2005-041
SLAC-R-774
hep-ex/0509008
7 September 2005
Precision Electroweak Measurements
on the Z Resonance

## Slide 6: LEP -DELPHI
Stefano è entrato in DELPHI con Tonino Pullia fin dall’inizio (1985) - INFN e Uni MI

## Slide 7: LEP (i calorimetri)

## Slide 8: DELPHI - I calorimetri possono muoversi…
Stefano risolve la crisi dell’ageing anomalo dell’HPC riducendone drasticamente il guadagno.
Nel 1992 (DELPHI week a Roma)
diventa responsabile dell’HPC.

## Slide 9: L3 – Sempre un calorimetro (molto preciso)
7680 EB + 3640 EC BGO crystals
PIN diode read-out (no gain)
Noise level around 1 MeV

## Slide 10: L3 – I calorimetri possono muoversi…
Results on 45GeV Bhabha electrons
(after continuous refinement of methods)
1.25% (0.8 from calibration)
1999 1.06% (0.5 from calibration)
Test beam calibration (2-50 GeV e-)
Xe monitor once per day
Cosmic rays (20 MeV)
Bhabha events (45 GeV e)
RFQ calibration (17 MeV g ) LEP2
Lezione: i metodi di calibrazione non sono mai troppi

## Slide 11: Secondo capitolo: Large Hadron Collider
Machine luminosity 1034 cm-2 s-1
inel  100 mb 109 events/s
higgs  10-50 pb 0.1/0.5 events/s
1 bunch crossing every 25ns 50 collisions/crossing 2000 tracks
Extreme conditions for detectors
Granularity (105 107 channels)
Speed of response
DAQ + trigger (4107   103 ev/s)
High radiation resistance
27 km ring
CERN Lab
CMS
ATLAS
LHCb
ALICE
p
p
Council approval in DEC 1994, TDR OCT 1995, First Collisions 2010.
HL-LHC project approved by Council in 2016, foreseen to run 2029-2040
CERN Council’s unanimous December 1991 vote that the LHC machine, to be installed in the existing 27 km LEP tunnel, is ‘the right machine for the advance of the subject and for the future of CERN’.
LHC Gestation 1984-1993
Overall  45y: 15 y + 30 y physics&UPGR

## Slide 12: LHC: caccia all’Higgs (e a tutto il resto)
LEP
H
® gg
H
®
ZZ
®
4 leptons
*
H
®
ZZ
®
4 leptons
H
®
WW or ZZjj
LHC
Natural width (GeV)
Higgs Mass (GeV)
0
50
100
200
400
800
0.001
0.004
1.4
30
250
L3
LEP observed an
excess of events
around 115 GeV
Only precision
in g detection
will tell a peak
(H gg signal)
from a huge
background
m, e, g

## Slide 13: ECAL @ CMS
barrel
Super Module
(1700 crystals)
endcap
supercystals
(5x5 crystals)
Pb/Si preshower
barrel cystals
EndCap “Dee”
3662 crystals
Barrel: || < 1.48
36 Super Modules
61200 crystals (2x2x23cm3)
EndCaps: 1.48 < || < 3.0
4 Dees
14648 crystals (3x3x22cm3)
Previous
Crystal
calorimeters:
max 1m3
PWO: PbWO4
about 10 m3, 90 ton
Precision electromagnetic calorimetry: 75848 PWO crystals
Con la lezione di LEP chiara
in testa, Stefano e io ci troviamo
in CMS ECAL.
Roma entra in ECAL nel 1994:
R&D su xl a APD
Struttura Meccanca
HV per APD
Costruzione ½ barrel
Milano (poi MiB) nel 2002.

## Slide 14: ECAL – Il cooling del calorimetro
dLY/dT = -2%/°C
dM/dT = -2.3%/oC
Milano arriva in un momento molto complesso per ECAL: progetto del cooling ancora
non ben definito, cambio radicale dell’elettronica e cambio di management in vista.
Temperature stability:
  negligible contribution to the energy resolution constant term if temperature of the Barrel/Endcap stable within 0.05 °C/0.1 °C (VPT are stable in temperature).
Temperature stability of the ECAL Barrel
and Endcap detectors.

## Slide 15: ECAL - Il cooling del calorimetro
This result shows that the cooling system fully complies
the requirements for the thermal stability of CMS ECAL.
Therefore, taking into account that it also provides good
integration with the electronics and allows for a feasible
mounting procedure, we can conclude that the test performed
at CERN in 2003-2004 has successfully validated the cooling
system of CMS ECAL.
CSN1: ok finanziamento al sistema di cooling 09/2003 a Lecce
Stefano diventa il coordinatore del gruppo di Milano-Bicocca in CMS a partire dal 2003, circa 1 anno dopo l’ingresso nell’esperimento.

## Slide 16: ECAL – La calibrazione
Non c’era tempo per calibrare su
fascio di elettroni tutti i Super
Moduli. Quindi è stato fatto un
enorme sforzo per arrivare in situ
conoscendo al meglio possibile
la risposta dei cristalli con misure
di laboratorio e cosmici.

## Slide 17: ECAL – La calibrazione
Published by IOP Publishing and SISSA
Received: September 15, 2008 Accepted: October 24, 2008 Published: October 30, 2008
Intercalibration of the barrel electromagnetic calorimeter of the CMS experiment at start-up
The CMS Electromagnetic Calorimeter Group
Si comincia l’avventura con una intercalibrazione
al 1.5%. Fondamentale per la comprensione del
calorimetro e dei metodi sviluppati per la calibrazione
in situ.

## Slide 18: ECAL - I muoni in situ
S. Ragazzi corresponding author
(si diverte anche…)

## Slide 19: ECAL monitoring della trasparenza
Inject fixed amount of light to monitor transparency loss
Response loss up to 10% in EB and up to 90% in EE (50% in the electron acceptance region |η| < 2.5)
Radiation Wavelength-dependent loss of light transmission (w/o changes in scintillation)
Crystal Transparency drops within a run by a few percent but recovers in the inter-fill periods
Lasers
PN
APD
(VPT)
crystal
reference diode
Cycle of response loss during irradiation and recovery in beam-off periods

## Slide 20: ECAL intercalibrazione dei cristalli
Combining all calibration methods
  φ-symmetry calibration: limited by systematic uncertainties
  π0 and η calibration: limited by systematic uncertainties
  high energy electron: statistically limited for |η|>1
Barrel: <1% (~0.3% for |h|<1)
Endcaps: ~2% (almost everywhere)
Barrel
p0gg

## Slide 21: ECAL stabilità della risposta
Stability of the energy scale after monitoring corrections with We events (Run1).
Barrel: average signal loss ~5% RMS stability ~0.1%
Endcaps: average signal loss ~25% RMS stability ~0.3%
Stability of the ECAL resolution from Zee invariant mass peak.
Barrel: resolution stable within errors.
Endcaps: worsening of ~1.5% in quad. (residual PU effect)

## Slide 22: ECAL con e senza correzioni
Zee invariant mass distribution applying :
  channel Inter-Calibration
  IC and Laser Monitoring corrections
Questo lavoro su cui in particolare giovani milanesi e romani hanno speso molto è stato un investimento
che ha ripagato con la scoperta che è valsa il premio Nobel per la fisica nel 2013 (ATLAS e CMS menzionati).

## Slide 23: CMS – La scoperta!

## Slide 24: ECAL la risoluzione in evoluzione
Ricostruzione “pronta” entro 48h dalla presa dati
Ricostruzione al meglio
delle condizioni
1% alla massa dell’Higgs!

## Slide 25: Higgs con i dati del Run 1 (2010-2012)
Observation in the  decay channel alone
5.7 σ significance with Run1 data
March 2014
Run1 Paper

## Slide 26: ECAL continua a funzionare...
Ad oggi 33 pubblicazioni con stato finale gg
Scoperto l’Higgs il più era fatto:
Stefano è diventato Direttore della Sezione INFN-MIB (dopo i primi tre anni di Direzione di Tonino) da fine 2009 a fine 2012, quando è stato chiamato a dirigere i laboratori al Gran Sasso.

## Slide 27: LHC continua a funzionare alla grande!
EPS 2025 Highlights

## Slide 28: Alcuni risultati dai dati di Run2 e Run3
Low mass resonances:
the invariant mass distribution for pairs of oppositely charged electrons originating from a common vertex. CMS PAPER EXO-23-007

## Slide 29: Lo Standard Model continua ad essere in ottima forma…
Misure di precisione!

## Slide 30: Sezioni d’urto di produzione (selezione)
Stairway to discovery: a report on the CMS programme of cross section measurements from millibarns to femtobarns
Figure 1: Cross sections of selected high-energy processes measured by the CMS experiment.

## Slide 31: Per il momento nulla di nuovo nelle ricerche dirette
See talks by Livia Soffi and Marumi Kado, ICHEP 2024
Un’enorme “pulizia” dello spazio dei parametri Beyond-SM: un risultato forse un po’sottovalutato…

## Slide 32: Il futuro (prossimo): HL- LHC (fino al 2041)
MIP Timing Layer
zRMS ~ 4-5cm
HL-LHC  fino a 1.9 vertici/mm
LHC  fino a 0.3 vertici/mm

## Slide 33: Mip Timing Detector: 4D vertexing for HL-LHC
33
Thin layer between tracker and calorimeters
MIP sensitivity with time resolution of 30-50 ps
Hermetic coverage for |η|<2.9
ENDCAPS
Surface ~ 15 m² Number of channels ~ 8000k
Radiation level ~ 2x1015 neq/cm²
Sensors: Low gain avalanche diodes
BARREL
Surface ~ 40 m²
Number of channels ~ 332k
Radiation level ~ 2x1014 neq/cm²
Sensors: LYSO crystals + SiPMs
Un nuovo rivelatore vede in posizione trainante i gruppi italiani di ECAL

## Slide 34: Un vero evento (MD) in CMS!
206 reconstructed primary vertices (orange circles) amongst the 9381 reconstructed tracks (yellow lines)
Per realizzare il programma di fisica con HL-LHC il rivelatore MTD sarà cruciale!

## Slide 35: CMS: upgrade indispensabile!
The current detectors were designed for 10 years running and L=500 fb-1. End of HL-LHC: 30 years of data-taking and 3000-4000 fb-1 → ageing and irradiation
    The ECAL barrel on-detector electronics will undergo an accumulated irradiation of ~6 kGy at the end of the HL-LHC
The average number of proton-proton interactions per bunch crossing (pileup) will increase up to 4 times w.r.t. phase1 (140-200): critical for vertex identification in Hγγ.
The CMS L1 trigger rate will be increased up to ~750 kHz with the latency increased from 4 μs to 12.5 μs → ECAL electronics to be changed.
Moreover, on the electromagnetic calorimeter:
With the legacy system the L1 trigger bandwidth would be saturated by the ECAL anomalous signals (spikes), the rate of which is proportional to the amount of pileup.
APD dark current will critically increase the noise term of the ECAL energy resolution.
Il vecchio rivelatore rinnovato deve continuare ad essere trainato dai gruppi italiani di ECAL. Il know-how (oltre che la performance) deve essere preservato:
le misure di fisica accessibili a HL-LHC sono fondamentali, e.g. produzione HH.
Upgrade sostanziale di tutti I rivelatori per mantenere l’attuale performance anche nelle condizioni estreme di HL-LHC

## Slide 36: Doppio higgs: una delle motivazioni più forti per HL-LHC
Highlights of the HL-LHC physics projections
by ATLAS and CMS
The ATLAS1 and CMS2 Collaborations
ESPP update

## Slide 37: FCC, un progetto integrato per il futuro lontano
https://home.cern/science/accelerators/future-circular-collider
Rende Steernberg, ICHEP 2024
LEP+LHC+HL-LHC: un progetto integrato di 60 anni. Dal 1981 (LEP approval) al 2041 (end HL-LHC). FCC: 2028+60  2088

## Slide 38: Il capitale da coltivare con progetti challenging!
3564
New accelerator (@ CERN)
gestation: discussions going on since 2006 (EU strategies)
In 2014 FCC CDR – in 2021 FCC Feasibility study committed
in 2025 FCC Feasibility study completed
Potential start in 2041/5 if approved by Council in 2028
(coupling)-1
or
(uncert.)-1
more statistics ➔
more energy ➔
Today we are in exploratory mode,
accelerators for the future are needed!
HL-LHC is granted, FCC?

## Slide 39: Ognitanto Stefano si fa fotografare…

## Slide 40: In conclusione
Trovare persone come Stefano con cui lavorare è un privilegio:
profondità di pensiero e conoscenza scientifica
fermezza nelle convinzioni (ma non testardaggine)
riservatezza
affidabilità
A me è capitato e la ritengo una fortuna!