## Slide 1: Artificial Intelligence–Driven Optimization of Light and Heavy Ion LINAC Design and Operation
Istituto Nazionale di Fisica Nucleare
The Italian National Institute for Nuclear Physics
Ysabella Kassandra Ong
Dottorato in Fisica degli Acceleratori: Seminari di passaggio al III anno (39 ciclo) 20 October 2025

## Slide 2: Outline
Artificially intelligent algorithms
How are we using AI for accelerators?
ANTHEM MEBT line
TAP accelerator complex
European Spallation Source
ML algorithm generalization
Conclusions

## Slide 3
What is Artificial Intelligence (AI)?
Artificial Intelligence (AI)
Enables computers and machines to simulate how a human mind works which allows them to learn, comprehend, solve problems, make decisions
Notes: "Let’s take a quick look at what Artificial Intelligence, or AI, really is. At its core, AI is about enabling machines to think and act like humans — learning from experience, solving problems, and making decisions.
Now, within AI, we have Machine Learning — this is where we teach machines to learn from data, so they can make predictions or decisions without being explicitly programmed for every task.
And deeper within that, we have Deep Learning, a subset of Machine Learning. Deep Learning uses complex, multilayered neural networks that try to mimic how the human brain processes information — allowing AI to tackle more sophisticated problems, like image recognition or natural language understanding.
So, in simple terms: AI is the big picture, Machine Learning is how we teach, and Deep Learning is the brain-like structure doing the heavy lifting."

## Slide 4
What is Artificial Intelligence (AI)?
Machine Learning (ML)
Artificial Intelligence (AI)
Enables computers and machines to simulate how a human mind works which allows them to learn, comprehend, solve problems, make decisions
Creates models by training an algorithm to make prediction or decisions based on data
Notes: "Let’s take a quick look at what Artificial Intelligence, or AI, really is. At its core, AI is about enabling machines to think and act like humans — learning from experience, solving problems, and making decisions.
Now, within AI, we have Machine Learning — this is where we teach machines to learn from data, so they can make predictions or decisions without being explicitly programmed for every task.
And deeper within that, we have Deep Learning, a subset of Machine Learning. Deep Learning uses complex, multilayered neural networks that try to mimic how the human brain processes information — allowing AI to tackle more sophisticated problems, like image recognition or natural language understanding.
So, in simple terms: AI is the big picture, Machine Learning is how we teach, and Deep Learning is the brain-like structure doing the heavy lifting."

## Slide 5
What is Artificial Intelligence (AI)?
Machine Learning (ML)
Artificial Intelligence (AI)
Deep Learning (DL)
Enables computers and machines to simulate how a human mind works which allows them to learn, comprehend, solve problems, make decisions
Creates models by training an algorithm to make prediction or decisions based on data
Uses multilayered networks to simulate complex human decision making
Notes: "Let’s take a quick look at what Artificial Intelligence, or AI, really is. At its core, AI is about enabling machines to think and act like humans — learning from experience, solving problems, and making decisions.
Now, within AI, we have Machine Learning — this is where we teach machines to learn from data, so they can make predictions or decisions without being explicitly programmed for every task.
And deeper within that, we have Deep Learning, a subset of Machine Learning. Deep Learning uses complex, multilayered neural networks that try to mimic how the human brain processes information — allowing AI to tackle more sophisticated problems, like image recognition or natural language understanding.
So, in simple terms: AI is the big picture, Machine Learning is how we teach, and Deep Learning is the brain-like structure doing the heavy lifting."

## Slide 6
Examples of AI algorithms
Particle Swarm Optimization (PSO)
Genetic algorithm (GA)
GIF from https://en.wikipedia.org/wiki/Particle_swarm_optimization
Genetic algorithm (GA)
Particle Swarm Optimization (PSO)
Machine Learning (ML)
Artificial Intelligence (AI)
Deep Learning (DL)

## Slide 7
Examples of AI algorithms
Bayesian Optimization (BO)
Bayesian Optimization (BO)
Trust Region Bayesian Optimization (TuRBO)
Adaptive Region Bayesian Optimization (ARBO)
Adaptive Region Bayesian Optimization (ARBO)
Machine Learning (ML)
Artificial Intelligence (AI)
Deep Learning (DL)
Particle Swarm Optimization (PSO)
Genetic algorithm (GA)

## Slide 8
Examples of AI algorithms
Bayesian Optimization (BO)
Trust Region Bayesian Optimization (TuRBO)
Adaptive Region Bayesian Optimization (ARBO)
Neural Networks (NN)
Neural networks (NN)
Machine Learning (ML)
Artificial Intelligence (AI)
Deep Learning (DL)
Particle Swarm Optimization (PSO)
Genetic algorithm (GA)

## Slide 9
How are we using AI for accelerators?
AI help in the following aspects of accelerator design and operations:
Automation & adaptivity
  reduce operator workload in tuning and calibration
  Real-time adjustment to environmental or system changes
Optimization
  Improve beam quality, stability, and efficiency
Virtual diagnostics
  Surrogate model of destructive or broken diagnostic
Online modelling / Simulations
  Fast beam transport model
Fault detection & prediction
  Identify anomalies before they occur, interlock prediction
Bayesian Optimization (BO)
Trust Region Bayesian Optimization (TuRBO)
Adaptive Region Bayesian Optimization (ARBO)
Neural networks (NN)
Machine Learning (ML)
Artificial Intelligence (AI)
Deep Learning (DL)
Particle Swarm Optimization (PSO)
Genetic algorithm (GA)
Notes: We see the practical benefits of AI in different aspects of accelerator design and operation: AI reduces operator workload through automation and adaptivity, making real-time adjustments to changing conditions. It enhances optimization for better beam quality and efficiency. AI also supports virtual diagnostics, modeling systems when direct measurements are destructive or unavailable. Furthermore, it accelerates online simulations, and enables fault detection and prediction, spotting anomalies before failures occur.

## Slide 10
LNL accelerators
TAPA – Tandem ALPI PIAVE ADIGE
accelerator complex
Anthem BNCT facility
European Spallation Source

## Slide 11
Anthem BNCT facility
AGATA
High-intensity CW proton machine 150 kW beam power
Space-charge → non-linear effect
MEBT matching critical → beam shaping at the target (uniform power deposition)
Objective: High beam transmission and beam uniformity at the target → optimal neutron yield
  Controlled losses in cooled collimators (for shaping)
MEBT
Target
TRASCO RFQ
Notes: Because of this complexity, optimizing their performance is a major challenge — and that’s where AI can play a crucial role."

## Slide 12
Offline Activities – ARBO
Shaping the target beam uniformity at ANTHEM high intensity MEBT line
Algorithm: Adaptive Region Bayesian Optimization (ARBO)
Parameters optimized: MEBT last three quadrupoles, two octupole magnets (Total: 5)
Goal: obtain good beam uniformity at the target with an area of 12×12 cm2 to maintain the beam power deposition at around 1 kW/cm2, transmission > 85% to maintain necessary neutron production yield (multi-objective!!)
Uniformity x | Uniformity y | Transmission
± 10.76 % [-55 mm, 55 mm] ± 16.68 % [-60 mm, 60mm] | ± 12.19 % [-55 mm, 55 mm] ± 17.58 % [-60 mm, 60mm] | 92.16 % [-60 mm, 60mm]
Target
Optimization lasted about 500 iterations
Beam uniformity obtained through tail-folding technique of the octupole magnets
Asymmetry in the x-plane → uncorrected dispersion from the dipole
Octupoles inactive,
No collimator
Beam distribution at the target
Octupoles active,
With collimator,
After BO
ANTHEM MEBT
Result: Nominal MEBT optics achieved with desired beam characteristics

## Slide 13
ANTHEM MEBT – Diagnostics definition
ANTHEM MEBT layout with diagnostic boxes and main components

## Slide 14
Offline Activities – CNN
Virtual diagnostics for the ANTHEM high intensity MEBT line
Algorithm: Convolutional Neural Network (CNN)
Goal: train a CNN to serve as a virtual diagnostic for determining the beam uniformity at the target position
Projections @ DBOX4
Predicted projections @ target
CNN SEM Grid predictions
DIAG BOX 4
SEM grids
Slits
ACCT
TARGET
CNN
ANTHEM MEBT line
Result: Applicable model for predicting beam distribution @ target position

## Slide 15
Offline Activities – ARBO + CNN
Virtual autotuning of the ANTHEM high intensity MEBT line with applied errors
Algorithm: Convolutional Neural Network (CNN) and Adaptive Region Bayesian Optimization (ARBO)
Parameters: Steerers (beam centering (oct off)); Steerers, last three quadrupoles, octupoles (uniformity + transmission (oct on))
Goal: Applying beam/magnet errors to the line, rematch the line by first centering the beam at DBOX3 and DBOX4 (oct off), then optimize the target uniformity (using the trained CNN model) and transmission (oct on)
Beam distribution @ target position
 | Uniformity X | Uniformity Y | Transmission
Worst case | ± 73.81 % | ± 30.71 % | 89.94 %
TraceWin opt. (Steerers only) | ± 29.25 % | ± 19.31 % | 92.11 %
ARBO + CNN | ± 16.84 % | ± 19.77 % | 92.10 %
Worst case
TraceWin opt.
ARBO + CNN
Result: Autotuning procedure will be applied in online operations

## Slide 16
TAPA accelerator complex
ALPI
Tandem-XTU
PIAVE
ADIGE
SPES
Users
PIAVE SRFQ
ALPI QWR
TANDEM-XTU
AGATA
SPES RFQ
SPES MRMS
SPES CB
SPES TIS
A heavy ion accelerator facility
~300 control parameters (transport and acceleration)
  Parameters vary depending on the species, mass/charge ratio and the injector used
Two main objectives: beam energy and transmission

## Slide 17
TAPA accelerator complex
ALPI
Tandem
PIAVE
ADIGE
ADIGE (being installed)
Stable +1 ion source
Charge breeder SPES-CB
MRMS (R = 1/1000, HVP -120 kV)
SPES RFQ (up to 727.3 keV/u for A/q=7)
3.5 < A/q < 7
ALPI
20 cryostats (each with 4 superconducting QWR cavities)
Eacc: 3MV/m (designed), up to 5 MV/m (improved)
Two types of QWR: 80 MHz and 160 MHz
1 triplet per 2 cryostats
3 stable ion injectors (2 active, 1 under installation)
Tandem (active)
Electrostatic accelerator
Terminal voltage: 14.5 MV
28 MeV/u for 1H up to 1.5 MeV/u for 197Au.
Can provide beams w/o ALPI
PIAVE (active)
ECR source LEGIS (HV platform 250 kV to 300 kV max)
Superconducting RFQ (@ 80 MHz), external bunching
RFQ output energy of 587.5 keV/u
Notes: Ions are generated inside an external source and are extracted with a weakly positive charge state (q = +1). Before entering Tandem ions cross a charge-exchange region in which, by playing on the relative electronic affinity, they receive two electrons from the gas which they interact with (cesium, Cs). The first electron makes the atom neutral again, while the second gives the atom a weakly negative charge (q = -1).
For nuclei with an atomic number larger than A~100, at the beam current levels usually injected inside the Tandem, the stripper foils average life-time is so short to make it unsuitable in practice. When all the 250 stripper foils, available in a special, remotely operated carrier, are exhausted, a Tandem opening is indeed required, in order to replace them.
PIAVE-ALPI Energy: from 13.6 MeV/A with 14N to 6.0 MeV/A with 238U
Tandem-ALPI Energy: from 22.5 MeV/A with 12C to 5.5 MeV/A with 96Zr
MRMS of 1/1000, which removes the CB contaminants.

## Slide 18
TAPA accelerator complex
TAP Performance in 2024 | Time [hours]
Beam on target | 3277
Beam preparation | 850
Accelerator Division test | 480
Unscheduled maintenance | 481
Working time | 4607
ALPI
Tandem
PIAVE
ADIGE
Almost 20% of the accelerator operation is utilized for beam preparation.
Data from Fagotti, E. (2025, April 3). LNL accelerator activities: Status and perspectives [Conference presentation]. 4ᵃ Giornata Acceleratori (National Accelerator Day), INFN Laboratori Nazionali di Legnaro, Padova, Italy. https://agenda.infn.it/event/43957/
Users

## Slide 19
Online Activities – Tandem ALPI PIAVE Problem
ALPI lattice
20 mm diameter aperture of cavities
E0 increased 4 times the initial design → unstable longitudinal phase advance 𝜎0𝑙
-20 -20 -20 -20 – -20 -20 -20 -20
-20 -20 +20 -20 – -20 -20 +20 -20
deg
deg
Nominal Sync. Phases: Not stable!
APF: the beam can be accelerated and transported but still suffers from low transmission
Manual set-up of the accelerator → time-consuming (~ 6-8 hours)
  Every ion beam type → optics need to be optimized, cavities independently tuned
Poor transmission (max 35% vs expected 93%)
  Active injectors suffer low transmission to ALPI due to its aggressive transverse focusing → sensitive to beam misalignment
Frequent need for reoptimization due to beam and hardware instabilities (every few hours)
Small transverse and longitudinal acceptance
  Nominal → beam not fully covered by acceptance
  Small oscillations of input beam → beam losses
Transverse acceptance
Longitudinal acceptance
TAP accelerator facility operation problem
From PIAVE injector

## Slide 20
Online Activities – ARBO
Longitudinal acceptance optimization of ALPI (2024)
Algorithm: Adaptive Region Bayesian Optimization (ARBO)
Beam: 129Xe25+
Parameters Optimized: ALPI Cryostats 1-6 (Total: 24)
Goal: Improve the beam transmission and acceptance of ALPI
ALPI
PIAVE
BO
inital
Synchronous phases along the linac
Longitudinal acceptance
BO range φ⁡ss ±3.5 deg on the ALPI cavity phases (allowed to expand)
Algorithm had a total of 120 iterations (~ 5 mins.)
BO distorts the shape of the acceptance to increase the coverage towards +𝜙 → input beam phase offset from ALPI by a few degrees
No significant change in beam output energy
BO
inital
 | Initial | BO
Current | 122 nA | 180 nA (+47.54 % wrt initial)
Time taken | - | ~ 5 min
Result: Almost 9% increase in longitudinal acceptance

## Slide 21
Online Activities – ARBO vs TuRBO
ARBO achieved the highest relative transmission of 23.1% in less than 20 iterations.
Moreover, although ARBO began with a smaller region 𝑅 than TuRBO, its adaptive region feature allowed it to eventually explore beyond TuRBO’s fixed global bounds, giving ARBO a potential advantage in discovering better solutions.
Transmission optimization of PIAVE (2024)
Algorithm: Adaptive Region Bayesian Optimization (ARBO) and Trust Region Bayesian Optimization (TuRBO)
Beam: 129Xe25+
Parameters Optimized: PIAVE Steerers (Total: 16)
Goal: Improve the beam transmission and acceptance of PIAVE
Result: ARBO achieved better transmission efficiency and explored a larger search region
PIAVE

## Slide 22
Online Activities – ARBO
ARBO achieved maximum transmission of 63.9 % more than doubling the initial value in less than 20 minutes.
Against the «best operator» (~60 % trans. in one hour)
Changes in quadrupoles are fine-tuning (ΔG < 10%)
63.9 % transmission
Transmission optimization of full PIAVE optics (2024)
Algorithm: Adaptive Region Bayesian Optimization (ARBO) and Trust Region Bayesian Optimization (TuRBO)
Beam: 129Xe25+
Parameters Optimized: PIAVE Steerers, Quadrupoles (Total: 37)
Goal: Improve the beam transmission and acceptance of PIAVE
Result: Achieved higher transmission efficiency than the best operator in one-third of the time
PIAVE

## Slide 23
Online Activities – ARBO
Full optics optimization of PIAVE-ALPI (2024)
Algorithm: Adaptive Region Bayesian Optimization (ARBO)
Beam: 129Xe25+
Parameters Optimized: Source optics, PIAVE-ALPI steerers, quadrupoles, cavities (Total: 48)
Goal: Improve the beam transmission @ Faraday Cup
Result: Record numbers for the facility reached, closer to expected values
ALPI
PIAVE
Xe
Xe, 3 uA accelerated beam
O, 0.1 uA accelerated beam
Pb, 0.3 uA accelerated beam
Official data and milestones related to PIAVE-ALPI
Sequential optimization
  Source optics (in collaboration with the source group)
  PIAVE-ALPI transverse optics
  Longitudinal optics
Reached 85% of ALPI transmission (cavities on)
  Record since its construction, roughly 20 years ago
  Max theoretical transmission of 93%
Maximum current reached at 3 μA
  Record, limited by uncooled diagnostics

## Slide 24
European Spallation Source (ESS)
MEBT
DTL
High-intensity machine (protons, 5 MW ave. beam power, 2 GeV energy, 62.5 mA current)
  Even at low duty cycle (50 μs, 1 Hz) → 300 W ave. beam power at end of DTL (enough to damage the linac!!)
Testing the ML algorithm on the normal conducting linac NCL (MEBT, DTL)
Many diagnostics available (hundreds), compared to TAP accelerator (Faraday cup)
  Beam Current Monitors (BCMs)
  Beam Position Monitors (BPMs)
  Beam Loss Monitors (BLMs)
Our approach:
Start from a working solution
Restrict the parameter search range
Tune the hyperparameters of the ML optimization algorithm
Optimization challenge?
Collapsing the objective function (diagnostic measurements) to a single value
Optimize the objective function to control of the losses along the line
Full beam transmission with the correct energy at the target
Notes: Because of this complexity, optimizing their performance is a major challenge — and that’s where AI can play a crucial role."

## Slide 25
Offline Activities – ARBO
Result: Tuned the ML parameters and search range for online tests
ESS NCL transverse transport optimization
Algorithm: Adaptive Region Bayesian Optimization (ARBO)
Beam: Protons @ 62.5 mA, low duty cycle (50 μs, 1 Hz)
Parameters Optimized: MEBT Quadrupoles, Steerers, Bunchers, DTL Steerers (Total: 69)
Goal: Optimize beam transmission and trajectory until the end of the DTL (multi-objective!! → 23 diagnostics BPMs, BCMs)
Nominal w/ induced losses
Bayesian optimized line
DTL
MEBT
Nominal w/ induced transmission loss
Bayesian optimized line
Beam transmission

## Slide 26
Online Activities – ARBO
ESS NCL transverse transport optimization (June 2025)
courtesy and fundamental support of ESS team
Algorithm: Adaptive Region Bayesian Optimization (ARBO)
Beam: Protons @ 6 mA current, 1 Hz repetition rate
Parameters Optimized: Steerers, quadrupoles (Total: 56)
Goal: Optimize beam transmission and trajectory until the end of the DTL (multi-objective!! → 52 diagnostics BPMs, BCMs)
ESS MEBT
Control parameters tuned for
transmission & trajectory optimization
Beam stop
Starting condition → beam misaligned in x-axis, 20-30% beam current loss
Losses minimized with 20 iterations (~3mins, 7-10s per iteration)
Final beam transmission efficiency increased to 99.43%
MEBT
DTL
SPK
MEBT
DTL
SPK
Beam trajectory
Beam transmission
Result: Beam trajectory corrected, beam transmission efficiency increased

## Slide 27
Online Activities – ARBO
ESS NCL longitudinal transport optimization (June 2025)
courtesy and fundamental support of ESS team
Algorithm: Adaptive Region Bayesian Optimization (ARBO)
Beam: Protons @ 6 mA current, 1 Hz repetition rate, SCL active (energy @ Beam Dump ~800 MeV)
Parameters Optimized: MEBT buncher cavities field and phases (Total: 6)
Goal: Optimize beam transmission and minimize beam losses until the beam dump (multi-objective!! → 291 diagnostics BLMs, BCMs)
Control parameters tuned
Optimize transmission and minimize beam losses in the SCL
Effect of frequency jump longitudinal acceptance shrinkage
Measurement of beam loss monitors
BLM signals reduced significantly especially at MBL-HBL interface
  Optimized settings caused only a small beam energy change (a few keV, from simulations)
Improved overall transmission efficiency from 96.27% → 99.12% (measured at the beam dump BCM)
Best point reached in 45 iterations (< 10 mins, 12s per iteration)
Result: Beam loss minimized, beam transmission efficiency increased
Beam Dump zone

## Slide 28
ML algorithm generalization
The code consists of the following:
  BO wrapper
  Configuration file (type of run, iterations)
  Accelerator-specific dictionary (PVs, objective function)
Easily adaptable to different accelerator systems, important things required:
  PVs (magnets, cavities, diagnostics, etc.) required for the optimization
  Objective function (must be collapsed to a single value)
  Starting range (initial set point ± x)
Easily executable in command line → interface currently being developed
  Calling the configuration file and specifying the parameters of the optimization run
We created ML python code based on the Bayesian Optimization (BO) python module from MIT [1] and on EPICS for controlling and reading PVs of different elements (magnets, cavities, diagnostics).
Notes: Transverse obj function:
\textbf{max} $f(x_{RFQ}, x_{DTL5}, o_{i}, ..., o_{n})=\frac{\left [ w_{x}\left ( \frac{-|x_{RFQ}-x_{DTL5}|}{x_{RFQ}} \right )+w_{o}\sum_{i}^{n}\left ( -|o_{i}| \right ) \right ]}{w_{x} + w_{o}n}$
Longitudinal obj. function:
\textbf{max} $f(x_{RFQ}, x_{BD}, y_{i}, ..., y_{n})=\frac{\left [ w_{x}\left ( \frac{x_{BD}}{x_{RFQ}} \right )+w_{y}\left ( \frac{1}{n}\sum_{i}^{n}y_{i} \right ) \right ]}{w_{x} + w_{y}}$

## Slide 29
Conclusions
AI and ML are powerful tools for accelerator operation and optimization
They support both offline tasks (data analysis, modeling) and online tasks (real-time tuning, anomaly detection).
Benefits:
  Improved efficiency, beam quality, and stability
  Reduced operator workload
  Faster simulations and surrogate diagnostics
Accelerator physics knowledge is essential to guide ML application and ensure meaningful results
Early results at LNL and ESS show strong potential for ML-based optimization
Next steps:
  Integrate ML more deeply into control systems
  Develop robust models and optimization algorithms for scientific use
  Scale methods to other future high-intensity machines
  Develop a surrogate model for the ANTHEM MEBT line
AI support
Conventional Theory of Accelerator
Disclaimer:

## Slide 30
References
[1] Ong, Y., Bellan, L., Pisent, A., Comunian, M., Fagotti, E., Bortolato, D., Montis, M., Giacchini, M., Carletto, O., et al. (2025, June). Enhancing ALPI-PIAVE performance at INFN-LNL with advanced optimization algorithms [Conference presentation]. HIAT 2025, Michigan State University, East Lansing, MI, United States. (Paper WEB04, unpublished).
[2] Ong, Y., Bellan, L., Pisent, A., Comunian, M., Fagotti, E., Bortolato, D., Montis, M., Giacchini, M., Carletto, O., et al. (2025, June). Enhancing ALPI-PIAVE performance at INFN-LNL with advanced optimization algorithms. In Proceedings of HIAT 2025 (pp. 250–253). Michigan State University. https://doi.org/10.18429/JACoW-HIAT2025-WEP12
[3] Ong, Y., Bellan, L., Pisent, A., Comunian, M., Fagotti, E., Bortolato, D., Montis, M., Giacchini, M., Carletto, O., et al. (2024). Advanced algorithms for linear accelerator design and operation. In Proceedings of the 32nd Linear Accelerator Conference (LINAC 2024) (pp. 288–291).
[4] Bellan, L., Carletto, O., Comunian, M., Fagotti, E., Giacchini, M., Montis, M., Ong, Y., & Pisent, A. (2024). New techniques method for improving the performance of the ALPI linac. Journal of Instrumentation, 19, T03005.
[5] Pisent, A., Grespan, F., Baltador, C., Bellan, L., Comunian, M., Conte, V., Esposito, J., Ferrari, L., Fagotti, E., Montis, M., Ong, Y., Palmieri, A., & Selva, A. (2024). ANTHEM project: Construction of a RFQ-driven BNCT neutron source. In Proceedings of the 32nd Linear Accelerator Conference (LINAC 2024) (pp. 291–294).
[6] Montis, M. (2025, April 4). AI and accelerators: The pilot experience at LNL as a base for a new INFN-A network [Conference presentation]. 4ᵃ Giornata Acceleratori, INFN-ACC.
[7] Bellan, L., & Montis, M. (2025, January 17). C’è dell’Intelligenza (Artificiale) negli Acceleratori [Conference presentation]. RPF@LNL: Risultati e Prospettive Future 2024, Istituto Nazionale di Fisica Nucleare.JUAS. (2020, February 26).
[8] Machine learning — JUAS-ML [Conference presentation]. JUAS, CERN. Retrieved from https://indico.cern.ch/event/977332/contributions/4116530/attachments/2198314/3717164/20200226JUAS-ML.pdf
[9] Ong, Y. K. (2023). Beam transfer lines design study for high-intensity proton beam (30 and 50 mA) for Boron Neutron Capture Therapy facility (Laurea magistrale thesis, Università degli Studi di Catania). Università degli Studi di Catania.
[10] F. Nogueira, Bayesian Optimization: Open source constrained global optimization tool for Python, 2014–. https://github.com/bayesian-optimization/BayesianOptimization

## Slide 31
Thank you for your attention!