## Slide 1: High Temperature Superconducting Solenoids for the Muon Collider Cooling Section
Giuseppe Scarantino, PhD Candidate in Accelerator Physics,
XXXIX Cycle

## Slide 2: The Muon Collider: Overview
A multi-TeV 𝜇-collider is a promising candidate for a future lepton collider
precision physics and discovery machine.
Due to short 𝜇 lifetime, unique features with respect to p-p / e-e colliders.
Need of steady state superconducting magnets and fast ramped resistive magnets.
produce which decay into muons to be captured
Short protons bunches
Ionisation cooling of muons
Acceleration to collision energies
Collisions
 Magnetic field along the machine: 1.8 T … 40 T.

## Slide 3: HTS Magnet Technology: Motivation
Increase operational temperature to 20 K  one order of magnitude increase in cryogenic system efficiency.
High cryogenic temperature:
  Large enthalpy margin,
  Reduced He inventory,
  Reduced power consumption.
Reach higher fields with respect to LTS magnets in a compact, high current density design.
1.9
Nb-Ti
8T
5T
Nb3Sn
16T
12…14T
HTS
This could be the best range of for future HEP
COP-1
4.5
18-16 T
12-14 T
Cryogenic Efficiency vs. Operating Temperature
Credits: L. Bottura

## Slide 4: 6D Cooling Section
On z-axis Fields: 2…14 T, 90mm…1.5 m
> 700
Challenges:
Large bore derived from RF cavity constraint.
High field gradient: need of high current density at high fields.
Mechanical forces in the order of tens of MN, affecting structural support design, cost and cryogenics.
More than 3000 HTS coils (12 different types) for 1 km string integrating absorbers and RF cavities for muon re-acceleration.
B5-type cells selected as the candidate demonstrator cell
HTS Solenoid
Absorber
RF Cavity
Dipole
z

## Slide 5: B5 Demonstrator Cell
Target field harmonics
Target Field - Longitudinal Harmonics Expansion
Input for the magnet design
10 units cell array for 𝜇 beam testing.
Inter-cell cryostat design: magnet structure decoupled from the cell unit.
Design improved for force intercepting and reduced cryogenic load.

## Slide 6: B5 Demo Magnet Design: Parameter Space and Assumptions
*Tape data from: [University of Victoria Wellington, Robinson HTS critical current database, SuperOx YBCO 2G HTS data. https://htsdb.wimbush.eu]
Parameter Space:
Coil 1
Coil 2
HTS coil
SS Spacer
Conductor Section
Assumptions:
Operating temperature: 20 K.
Conductor layout: 2x HTS tapes + SS tape co-wound (dry winding).
Performance based on industrial production (Faraday Factory Japan tape - SuperOx YBCO 2G HTS*).
Inter-turns contact resistance: .
Stainless steel spacers separating the coil pancakes.

## Slide 7: B5 Demo Magnet Design: Parameter Space and Assumptions
Assumptions:
Operating temperature: 20 K.
Conductor layout: 2x HTS tapes + SS tape co-wound (dry winding).
Performance based on industrial production (Faraday Factory Japan tape - SuperOx YBCO 2G HTS*).
Inter-turns contact resistance: .
Stainless steel spacers separating the coil pancakes.
*Tape data from: [University of Victoria Wellington, Robinson HTS critical current database, SuperOx YBCO 2G HTS data. https://htsdb.wimbush.eu]
Conductor Section
Constraints:
Space available for coils
Geometrical constraints:

## Slide 8: B5 Demo Magnet Design: Optimization Approach
Optimal Design
margin
spatial constraints
Field Obj. – Conductor Cost
Field Obj. – Forces on Coils

## Slide 9: B5 Demo Magnet Design: B5 Demo Mag 2.4
Configuration obtained from single-objective optimization
Obtained Solution Main Parameters | Coil 1 / Coil 2
Coil current (A) | 761.2 1193
SS spacers width (mm) | 7.9 13.7
Axial Force (Total) (MN) | -4.6 / 11.7 (7.09)
Temperature Margin (K) | 13
Mag. Energy Density (MJ/m3) | 152 147
Hotspot Temperature (K) | 142 144
Total HTS tape length | 50.9

## Slide 10: B5 Demo Magnet Design: B5 Demo Mag 2.4
Mechanical stresses within material limits in nominal operative conditions.
Obtained Solution Main Parameters | Coil 1 / Coil 2
Coil current (A) | 761.2 1193
SS spacers width (mm) | 7.9 13.7
Axial Force (Total) (MN) | -4.6 / 11.7 (7.09)
Temperature Margin (K) | 13
Mag. Energy Density (MJ/m3) | 152 147
Hotspot Temperature (K) | 142 144
Total HTS tape length | 50.9
Configuration selected for cell integration studies!

## Slide 11: B5 Demo Mag 2.4: Coil Charging Transient
Ramp rates of the two coils tuned to match the same ramping time.
Assumed 6h charging time: 4h current ramp in Coil 1.
Conduction cooling of the two magnets via cryocoolers.
Critical current fraction during charging
Coil 1
Coil 2
Coil margins and peak stress limits satisfied during charging.

## Slide 12: B5 Demo Cell Design and Integration
Engineering design of the B5 demo cell.
Inter-cell cryostat design: specific solutions for the cell assembly and installation have been considered:
  Soldered flanges for the RF waveguide.
  Custom pillow seals based on elastomers for vacuum connections.
  Girder layout  improved modularity for installation and maintenance.
Credits: M. Castoldi

## Slide 13: B5 Demo Cell Design and Integration
Von Mises Stress
0.32 MN*m bending moment
Credits: M. Castoldi
Mechanical design of the magnet structure
Stress concentration in coil casing. Peak value within material limits.

## Slide 14: HTS Split-Coil Facility for RF Cavity Testing
Coil stack
Cu fins for thermal connections to cryocooler interfaces
60 K cryocooler for thermal shield
Credits: M. Castoldi
First step in the realization of a muon cooling demonstrator:
  Magnet design and system integration.
Target: 400 mm magnet inner bore, 320 mm free-bore. 20 K operation: cryocooled.
Technology validation:
  Breakdown limit of RF cavities (> 704 MHz) under high magnetic field (7 T peak).
  Design, manufacturing and testing of 7 T split-solenoids, with metal-insulated HTS.

## Slide 15: HTS Split-Coil Facility for RF Cavity Testing
Coil stack
Credits: M. Castoldi
Coil Charging Transient Analysis
Cu fins for thermal connections to cryocooler interfaces
60 K cryocooler for thermal shield
Coil margins and peak stress limits satisfied during charging.

## Slide 16: HTS Single-Coil Facility: EU funded EPITA
Credits: M. Castoldi
Coil stack
1 GHz RF cavity
Vacuum and cooling pipes (He gas cooling)
Thermal shield
Scaled-down version of the HTS split-coil facility: single-magnet layout.
Test of RF cavities of > 1 GHz frequency.
Peak field on axis: 7 T. Magnet inner bore: 250 mm, 170 mm free bore.
5 km HTS tape (4 mm width) acquired by INFN-LASA.
Construction and assembly will be part of the EPITA program.

## Slide 17
Fully Soldered - Non-insulated HTS Coils Experimental Campaign

## Slide 18: Soldered Coil Test Campaign
V0.2: 3D printed test stage:
  11 voltage taps (2 mm spacing) upgradeable to 21 per sector
  8 hall-probe positions
  2 slots for alternative instrumentation
Non-invasive and post-mortem characterizations:
  Tomography/microscopy to assess quality and uniformity of soldered layers, and for void fraction measurement.
Analysis on the Manufactured Samples
Coil Measurements at 77 K in LN2 bath

## Slide 19: Current Step Measurements Results
Onset of residual resistance
Coil Transversal Voltage vs Current
Variations of saturation field are expected: 10-15% of Ic variation in self-field.
Center Hall Probe Field vs Current

## Slide 20: First Coil Polishing Test
Polished Coil
Hastelloy Surface
Removing the Cu stabilizer layer on the coil sides significantly reduces the coil time constant.
>3 order of magnitude increase in the turn-to-turn resistance.

## Slide 21: Polished Coil Measurement Results
Center Hall Probe Field vs Current
V-I current ramp test comparison
Coil time constant after polishing: 2 s !
Factor 150 reduction in the coil time constant compared to the non-polished coil.
Behaviour as insulated coil: quenched at 40 A / 75 A depending on the setup.
B-I curve follows the same behaviour of non-insulated in the linear regime.

## Slide 22: Next Steps
Finalize the design of the B5 demonstrator magnets and the magnet of the HTS facility for RF cavities accounting for fault scenarios:
  Quench simulations are critical for the design (unbalanced forces in the MN range)!
Update the 6D cooling section magnets based on the design solutions of the B5 demonstrator.
Manufacture and test prototype metal-insulated coils for the design of the HTS facility.
Construction and commissioning of the single-magnet HTS facility by 2026.

## Slide 23
Funded by the European Union (EU). Views and opinions expressed are however those of the author only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.
Thank you for your attention!