## Slide 1: Beam merging techniques assisted by curved crystals
Ph.D. Candidate: Davide Annucci
Sapienza Università di Roma – INFN Roma – CERN
Thesis Advisor: P. Valente
INFN Supervisor: A. Variola
CERN Supervisor: R. Rossi, W. Scandale
Thesis assessment Ph.D. Seminar – 12/11/2025
Ph.D. in Accelerator Physics
Cycle XXXVIII

## Slide 2: Outline of the Presentation
Beam Merging with bent crystals
  Coherent processes in bent crystal
UA9 Experimental setup design and simulations
  Beam merging Key Performance Indicators
  Merging efficiency after introducing imperfections
Beam merging implementation in H8
  Merged beam horizontal emittance measurement
  Emittance systematic uncertainty determination
Conclusion
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 1

## Slide 3
1
Beam Merging with bent crystals
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 2

## Slide 4: Coherent processes in bent crystals (1/2)
A particle impinging on a crystal behaves differently depending on its alignement wrt crystal structure
  Amorphous or Coherent Behaviour
Particle aligned with the crystal planes
  Critical Angle for Channeling
  capture inside the tunnel if particle impacts Cry with
Bent crystal Particle deflection
If the particle leaves the Channeling condition
  Dechanneling
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 3

## Slide 5: Coherent processes in bent crystals (2/2)
Dechanneling (DCH), Volume Capture (VC) and Rechanneling (RCH)
  No more CH condition DCH can happen (sometimes followed by RCH)
  VC conceptually similar to RCH
Volume Reflection (VR)
  Charghed particles reflected by the crystal potential barrier
Is it possible to exploit Coherent Processes to merge beams?
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 4

## Slide 6: Beam merging Idea
Two beams incoming from different directions, merged by bent crystal
  The beamlet emittance after merging should be comaprable to the emittance of the beamlets before the merging
A bent crystal act as an «Angular Filter», deflecting particles by Channeling
  Beamlet #1 AM/VR wider divergence after crystal Beamlet #2 Channeling
  Main scheme and phase space plots in the ideal case
  How is it possible to implement this merging scheme?
Beamlet #2
Beamlet #1
Merged Beam
Bent crystal
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 5

## Slide 7: Beam merging proposed setups
Problem: A Two-Converging Beamlines setup does not exist
  Solution: Bent crystals create two beamlets which will converge at another point
  Third crystal at the convergence point here the merge will happen!
CERN SPS H8 extracted Beamline is the UA9 experimental site since decades
H8 North Area Beam
Beamlet #1
Beamlet #2
Merged Beam
Bent crystal #1
Bent crystal #2
Bent crystal #3
H8
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Beamlet #2
Page 6

## Slide 8
2
UA9 Experimental setup design and simulations
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 7

## Slide 9: From the idea to the simulations
Geant4 Toolkit used to perform the simulation of the UA9 merging setup
  Channeling implemented by E.Bagli et al (INFN-Fe) since G4 10.05.p01
Simulations campaign to determine max spatial/angular tolerances that can be applied to the Setup
«Baseline» unperturbed Configuration scheme
  Reference frame centered on Cry2 Cry1 and Cry3 placed at -8 m and +10 m
  Bending Angles:
  Realistic H8 Beamline Parameters
  Beam Spot: RMS
  Divergence:
  Energy:
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Cry1
Cry2
Cry3
-13.1 -8.1 -7.9 -0.5 +0.5 +5.0 +10.1 +19.1
H8 Beam
Ch1
Ch2
Merged
Ch2-Am3
Page 8

## Slide 10: Beam Merging Efficiency
Focus only on the Beamlets #1 and #2 and the Cry3
  Beam #1 enters Cry3 in AM/VR Fully passes through Cry3 an go almost straigth
  Beam #2 enters Cry3 in Channeling Some particles will be bent, some other will go in AM
Beamlet #1 and #2 are already in Cry3 Acceptance
  Same crystal entry face width for all the crystals. Beamlets #1 and #2 have
Merging Efficiency
  For the Baseline Configuration
  Which is quite good! Lose only 30% of Beam #2, if assuming
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Beamlet #1
Merged Beam
Cry3
Beamlet #2
Page 9

## Slide 11: Introducing perturbation
What happens if there are Bending errors on the crystal
  Small The and will be reduced
  Big Beam #1 and/or #2 could not impact Cry3 anymore
  Cry3 should be shifted laterally if is too big
How to modify the UA9 setup if bending errors on the crystals are present
How can the baseline configuration be recovered
  Bending errors can be compensated by changing the crystals orientation
  Rotations must NOT be too high
    Otherwise less particles impinging the crystals will be into their Channeling Acceptance
    The Beamlet #1 or #2 or the Merged one would be less populated for big rotation angles
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 10

## Slide 12: Introducing perturbation
Apply Bending errors and rotations to the crystals
    Study how merging efficiency () andmerged beam population () will be reduced
    Quadrature sum of all the source of angular errors
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Bending Errors Only
Bending Errors & Rotation
Ratio of the merged beam population when applying the angular perturbations with respect to the Baseline case (no perturbations applied)
Same but for the merging efficiency
and are still acceptable (30% losses wrt Baseline) only if
Keep crystal BELOW
Page 11
Critical angle

## Slide 13: Recombined beam in the phase space
12/11/2025
Fewer particles in the Merged Beam…
Page 12
Davide Annucci – Beam merging techniques assisted by curved crystals

## Slide 14
3/a
Beam merging implementation in H8
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 13

## Slide 15: Roadmap towards the beam merging
Beam merging achieved in three steps
  (1) Double Extraction (2) Double Channeling (3) Full Merging setup
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
1
2
3
Reco Plane (Gonio 3)
Page 14

## Slide 16: Merging configurations in a nutshell
Beamlet #2 always in Channeling in Cry3
Beamlet #1 experiences Multiple Scattering and/or Volume Refection in Cry3
Three merging schemes possible!
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Cry3
Cry3
Cry3
Channeling + Amorphous
Channeling + Volume Reflection
Channeling + AM/VR Transition
Page 15

## Slide 17: Merged beam identification
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
c
a
a
b
Ch(1)Am(3)
Ch(1)VR(3)
Ch(2)Am(3)
Ch(2)Ch(3)
Merged Beam
Ch + AM/VR Transition
Ch(1)
Ch(2)
Ch(2)Ch(3)
Ch(1)Am/VR(3)
Ch(2)Am(3)
Ch(2)
Ch(1)
(a)
(b)
(c)
Define appropriate spatial/angular cuts
  Spatial cuts defined by Cry3 active region width
  Angular cuts defined by outgoing angle distribution
  Emittance computation for particles in region (b)
Page 16

## Slide 18: Merged beam identification
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
c
a
a
b
Merged Beam
Ch + AM/VR Transition
Ch(1)
Ch(2)
Ch(2)Ch(3)
Ch(1)Am/VR(3)
Ch(2)Am(3)
Ch(2)
Ch(1)
(a)
(b)
(c)
Page 16/b
c
c
d
e
f
d
e
f
Ch(2)
Ch(2)Ch(3)
(d)
Ch(1)
Ch(1)Am(3)
Ch(1)VR(3)
(e)
(f)

## Slide 19
3/b
Merged beam emittance measurements
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 17

## Slide 20: Merged beam emittance computation
Formulas used to compute the emittance and its absolute uncertainty
  Look Pag.183-187 of my Thesis for the full computations
  RMS beam spot ; RMS beam divergence ; Correlation term
  computed for the particles ensemble enclosed within geometrical cuts
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Tracker position resolution
Tracker angular resolution
Page 18

## Slide 21: Merged beam emittance outcome
Different emittance values for the three merging configurations
  Because different coherent/incoherent processes are involved in the different cases
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Ch + VR
Ch + Tr
Ch + AM
Page 19
Geometrical Cuts
Geometrical Cuts
Geometrical Cuts
Geometrical Cuts
Geometrical Cuts
Geometrical Cuts

## Slide 22: Systematic uncertainty determination
Geometrical spatial/angular cuts change Different emittance values
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Ch + Tr
Ch + Tr
Page 20
Spatial cuts: Step = 1/20 of Cry3 width
Range: respect to cuts design values
Angular cuts fixed
Angular cuts: Step = 1/6 of critical angle
Range: respect to cuts design values
Spatial cuts fixed
Critical angle

## Slide 23: Systematic uncertainty determination
Geometrical spatial cuts changed, angular cuts unchanged
of the emittance design value
of the emittance relative error design value
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Ch + Tr
Ch + Tr
Page 21

## Slide 24: Systematic uncertainty determination
Geometrical angular cuts changed, spatial cuts unchanged
of the emittance design value
of the emittance relative error design value
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 22

## Slide 25
4
Conclusions
Now this is not the End
It is not even the Beginning of the End
But it is, perhaps, the End of the Beginning
- W.Churchill 10 Nov 1942
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 23

## Slide 26: Conclusions
The beam recombination scheme with crystals can be implemented in NA H8
  From simulations Merging efficiency is 85% in the unperturbed case
  Maximum tolerance for bending errors and crystal rotation shoud not exceed
Three beam merging configurations (Ch+AM, Ch+VR and CH+AM/VR Transition)
  Careful geometrical cuts ensure menaingful merged beam identification
  Different coherent processes Different merged beam emittance in the three cases
  The merged beam emittance and its statistical error grow monotonically in the considered cuts parameters ranges reasonable to define Systematic error
  Emittance Systematic error is more sensitive to the spatial cuts variation than to the angular ones
Plenty of work (Autocollimator, TimePix3 measurements) not shown
  Autocollimator bending angle characterisation Allows crystals tuneability before putting in H8
  TimePix3 Used standalone to observe Ch and VR Can be used as beam diagnostics tool
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 24

## Slide 27: Ph.D. Timeline
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
2022/2023
Classes and lectures
Geant4 Simulations implementation and debug
2023/2024
Geant4 Simulations with and without imperfections
2024/2025
Double Extraction and double Channeling achieved in October 2024
Test beam activity
Three different merging schemes (Ch+Am, Ch+VR, Ch+AM/VR) implemented and tested in September 2025
First beam merging in June 2025
Test beam activity
Monte Carlo data anaysis and simulated KPIs determination
Page 25

## Slide 28: Mobility and Duty Travel periods
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
2022/2023
10 Weeks (January-March): Joint Universities Accelerator School
2 Weeks (mid June): UA9 Test beam for single-Channeling crystal characterisation
2023/2024
2 Weeks (mid May): UA9 Test beam for single-Channeling crystal characterisation
2 Weeks (mid June): UA9 Test beam for single-Channeling crystal characterisation
1 Week (mid February):Crystal curvatire characterisation with Autocollimator
2 Weeks (mid September): UA9 Test beam for single-Channeling crystal characterisation
3 Months (September-November): Mobility period. UA9 Test beam for double Extraction and double-Channeling assessment
2024/2025
3 Months (May-July): Mobility period. UA9 Test beam for beam merging assessment
2 Weeks (mid September): UA9 Test beam for beam merging assessment and tuning
Page 26

## Slide 29
Thank You for your attention
Author e-mail: davide.annucci@uniroma1.it
Many thanks to my Ph.D. Supervisors for their precious advices, passion and dedication
Many thanks to GC,LS (and DDR former) for the smooth administrative operation of our Ph.D.
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 27

## Slide 30
Backup Slides
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 28

## Slide 31: Single-crystal KPI
Determine Single-crystal Channeling Efficiency
    Beam ; crystal .
    Only 30.7% of the beam in the CH Acceptance
    Deflection efficiency for Cry1,2,3 is in range
Effect of Cry Rotation on
  Even less particles in the Acceptance
  i.e. rotatyng Cry by only 5% of particles in Acceptance
Effect of Cry Bending on
  Sligthly increased Dechanneling if curvature radius get smaller
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Beam
crystal
CH
AM
No rotation
Rotation
Page 29

## Slide 32: Channeling Acceptances (1/2)
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 29/b

## Slide 33: Beam Merging scheme
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Beamlet #1
Merged Beam
Cry3
Beamlet #2
Beamlet #1
AM/VR by Cry3
Cry3
Cry3
Beamlet #2
CH by Cry3
AM
Page 30

## Slide 34: Beams seen by the Tracker P7 (+19.1 m)
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
What does the most downstream Tracker Station observe (X-Y 2d-Plot)
  H8 Circulating Beam
  Merged Beam (Ch1-AM/VR3 + Ch2-Ch3)
  AM componet of B2 after Cry3 (Ch2-AM3)
Cry1
Cry2
Cry3
-13.1 -8.1 -7.9 -0.5 +0.5 +5.0 +10.1 +19.1
H8 Beam
Ch1
Ch2
Merged
Ch2-Am3
Geant4 Setup
  Tracker Stations
  This constrain bending angles
H8 Beam
Ch2-Am3
Merged Beam
Page 31

## Slide 35: Phase Space plot at P7 (+19.1 m)
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
The Circulating Beam goes straight
  and
The Ch1-Am/VR3 Beam goes at
  Impacts Plane6 in
The Ch2-Am3 Beam goes at
  Impacts Plane6 in
H8 Beam
Ch2-Am3
Merged Beam
Cry1
Cry2
Cry3
-13.1 -8.1 -7.9 -0.5 +0.5 +5.0 +10.1 +19.1
H8 Beam
Ch1
Ch2
Merged
Ch2-Am3
H8 Beam
Ch2-Am3
Page 32

## Slide 36: Phase Space plot at P7 (+19.1 m)
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Dch2
Dch3
Dch1
VR3
VR2
VR1
Page 33

## Slide 37: Phase Space plot at different Planes
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 33/b

## Slide 38: Angular distributions at different Planes
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 33/b

## Slide 39: Recovery Strategies
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 33/c

## Slide 40: Recovery Strategies
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 33/d

## Slide 41: Merged beam identification
Define appropriate spatial/angular cuts
  Spatial cuts defined by Cry3 active region width
  Angular cuts defined by outgoing angle distribution
  Emittance computation for particles in region (b)
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
c
a
a
b
Ch(1)Am(3)
Ch(2)Am(3)
Ch(2)Ch(3)
Merged Beam
Ch + AM
Ch(1)
Ch(2)
Ch(2)Ch(3)
Ch(1)Am/VR(3)
Ch(2)Am(3)
Ch(2)
Ch(1)
(a)
(b)
(c)
Page 34

## Slide 42: Merged beam identification
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
c
a
a
b
Ch(1)VR(3)
Ch(2)Am(3)
Ch(2)Ch(3)
Merged Beam
Ch + VR
Ch(1)
Ch(2)
Ch(2)Ch(3)
Ch(1)Am/VR(3)
Ch(2)Am(3)
Ch(2)
Ch(1)
(a)
(b)
(c)
Define appropriate spatial/angular cuts
  Spatial cuts defined by Cry3 active region width
  Angular cuts defined by outgoing angle distribution
  Emittance computation for particles in region (b)
Page 35

## Slide 43: Emittance Systematic error – Full study
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Ch + Am
Channeling + Amorphous recombination scheme
Left: Change spatial boundaries, Right: Change angular boundaries
Page 36

## Slide 44: Emittance Systematic error – Full study
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Ch + VR
Channeling + Volume Reflection recombination scheme
Left: Change spatial boundaries, Right: Change angular boundaries
Page 37

## Slide 45: Emittance Systematic error – Full study
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Ch + Tr
Channeling + Amorphous/Volume Reflection Transtion recombination scheme
Left: Change spatial boundaries, Right: Change angular boundaries
Page 38

## Slide 46
Not Shown/I
TimePix3 measurements for Channeling detection in SPS H8 NA
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Cooperation with M. Garattini
Page 39

## Slide 47: The TimePix3 in a nutshell and its application
Small and portable detector
  14x14 sensitive area, 256x256 pixels, 55 pixel pitch, 100 thick Si sensor
  ToA, ToT, Itot functionalities Beam X/Y Profiles, Time distribution and energy deposit
  Acquisition in «Single Frame» or «Cumulative» mode (stacking more frames per single DAQ)
TimePix3 can be used as online beam monitor
Useful to perform the Angular Scan
  Cumulative mode See how the beam spot size and morphology change over time
  Real time CH/VR peak emerging from the Background when rotating the crystal (June 2024)
  Scheme of the setup
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
H8 Beam
AM
CH
VR
TimePix3
20 m
Bent crystal
Page 40

## Slide 48: TimePix3 angular scan – Compare with Tracker
Angular Scan performed using the TimePix3 and the UA9 Tracker Standalone
  Large impact angle acceptance bigger than Twisted crystal
  At different time, different parts of the crystal are in Channeling
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Angular Scan with the Tracker
Twisted crystal
h 10:47
START SCAN
h 12:06
END SCAN
TimePix Acquisition at different times RAW Data – Twisted crystal
10:53
Amorphous
Lower part in CH
11:03
11:18
crystal in CH
11:33
Upper part in CH
Amorphous
12:03
(a)
(b)
(c)
(d)
(e)
(a)
(b)
(c)
(d)
(e)
Page 41

## Slide 49: Bending Angle measurement with TimePix3
Readout in «Frame» mode Beam X/Y distribution
  Mandatory to record almost 10 Spills, otherwise the SNR is too low and data cannot be analyzed (more spills is better, i.e. 100)
  The two Runs are cleaned, normalized, and then subtracted.
Crystal bending angle: 170 from previous UA9 measurements
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
2d-plot Run Channeling
10 Spills
Subtraction Y-Profile
2d-plot Run Channeling
Subtraction Y-Profile
100 Spills
100 Spills
10 Spills
SPS Page 1 – SFTPRO Supercycle
Page 42

## Slide 50: 100 Spills best CH and VR Runs
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
These two Runs are the best in CH and VR orientation
  TimePix3 can be used to measure precisely CH and VR angle
  In these plot the CH/VR-AM subtraction is applied
  VR Angle measurement:
Best CH Run
Sub Y-profile
Best VR Run
Sub Y-profile
CH Peak
VR Peak
Emptying Area
Emptying Area
Best CH Run 2D Sub
Best VR Run 2D Sub
Page 43

## Slide 51: Crystal Torsion measurement with TimePix3
SPS-Type Crystal with known torsion defect
  measured with UA9 Tracker: (September 2023 – May/June 2024)
Beam impacts on the crystal at different heights
  CH particles are deflected at different angles despite Cry Channeling angle is the same!
  This means there is a Twist effect!
  Key goal: Obtain bending angle slice-by-slice to compute the torsion
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
5 Slices
Slope
Torsion
Center of the i-th slice [Pixel]
Deflection Angle []
Compatible with Tracker
Page 44

## Slide 52: TimePix3 Differential Data Analysis
Necessary Runs to perform the Analysis
  DAQ in «Frame» mode One Run with Crystal in AM and one in CH or VR orientation
  Clean (eliminate frames with spikes) & normalize the two Runs separately
  Subtract the 2d cleaned beam distributions
  Obtain the Y profile Fit the CH or VR peak and the Emptying Region Compute CH/VR Angle
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Raw
Clean
Raw
Clean
Raw and Cleaned data
X/Y Profiles for CH Run
CH–AM Subtraction 2d Plot
CH–AM Subtraction Y Profile
Page 45

## Slide 53: Transition Regions
One Run (-60) is pure VR, the other three Runs (30, 40, 50) are at CH/VR Transition
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Very effective to check the crystal alignment in real time if the Tracker does not work
VR peak lowers
CH peak rises up
Page 46

## Slide 54
Not Shown/II
Autocollimator for optical bending angle measurements
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Cooperation with S. Giroldi and S. Di Gennaro
Page 47

## Slide 55: Autocollimator in a nutshell
Optical device used to measure angles with precision
  Focal length (f) of the lens is known by construction
  Spatial offset (d) with respect to a straight-back reflection is measured
  Angle given by
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Page 48

## Slide 56: Why the Autocollimator?
Beam Merging setup with three Crystals
  Tracker Planes size
  Available space for UA9 setup in H8: 30 m
  mrad-order bending angles
Mandatory to precisely measure Xtals bending angle
  Otherwise merging is not feasible
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
H8
Keep crystal BELOW
Page 49

## Slide 57: Bending angle measurement
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Autocollimator mounted on optical table
Slab Silicon crystal
  Mounted on a 2-axis movable support
  Size:
  Polished surfaces for enhanced reflectivity
Mechanical holder
  Produced by INFN Roma
  Impress tuneable Primary Curvature on the crystal
  This induces a secondary deformation on the crystal
Not shown: Slit-shaped window to narrow the Autocollimator ligth beam spot size
X
Y
Page 50

## Slide 58: Bending angle measurement
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
L/R Move
U/D Move
Measurement strategy
Horizontal Slit
Vertical Slit
Secondary curvature uniformity
Primary curvature uniformity
Page 51

## Slide 59: Primary Curvature
Check Primary Curavature uniformity Move the crystal on the Y axis
  As expected, the Primary curvature remains quite constant
  AlpyX company (crystal manufacturer) has also an optical profilometer to benchark these measurements at AlPyx
  Full compatibility between these measurements
  Nice shape of the «bean» allows to determine correctly the Primary Curvature
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Autocollimator measurements
Page 52

## Slide 60: Secondary Curvature
12/11/2025
Davide Annucci – Beam merging techniques assisted by curved crystals
Check Secondary Curavature uniformity Move the crystal on the X axis
  As expected, the Secondary curvature changes. Max value
  With the optical profilometer at AlpyX
  Full compatibility between these measurements
  Fuzzy and almost spot-like «bean» allows to determine the Secondary Curvature with big error!
Autocollimator measurements
Page 53