## Slide 1: LHC Injection Dynamics for the HL-LHC Era
Longitudinal Beam Dynamics at Highest Intensity in the Super Proton Synchrotron
Supervisors: Prof. M. Migliorati & Dr. H. Timko
Ph.D. candidate: Birk Emil Karlsen-Bæck
XXXVIII Ph.D. School in Accelerator Physics – 3rd Year Final Seminar 12/11/2025

## Slide 2: Contents
Introduction
Optimization and implementation in hardware
Experience with high-intensity beams in the LHC
Projections for HL-LHC operation
Conclusions

## Slide 3: LHC Layout
26.7 km tunnel with two rings [1]
  Beam 1 (clockwise) and beam 2 (counter-clockwise), each with up to 2760 bunches
  Minimum 25 ns spacing between bunches
  Injected at 450 GeV/c and accelerated to 6.8 TeV/c
Eight interaction regions (IRs)
  Four experiements
Superconducting magnets
Injector: Super Proton Synchrotron
  Second largest synchrotron at CERN
  Can deliever up to 288 bunches per injection into the LHC
Notes: Show LHC and SPS as injector

## Slide 4: The High-luminosity LHC Era
The Large Hadron Collider [1]
  Nominal 1.15 x 1011 p/b
  Ultimate 1.8 x 1011 p/b
The High Luminosity Upgrade [2]
  Upgrade and addition for a lot of equipment, e.g. crab cavities, magnets, collimators etc.
  Bunch intensity doubling
    1.15 x 1011 p/b -> 2.3 x 1011 p/b
  Luminosity increase 500 fb-1 to 3000 – 4000 fb-1
  Only additions to RF system were the crab cavities
    No upgrade foreseen for the main RF system
Parameter | Symbol
Particles per bunch | 
# bunches colliding | 
Revolution frequency | 
Horizontal emittance | 
Vertical emittance | 
Geometric reduction factor | 
Parameter | Symbol
Particles per bunch | 
# bunches colliding | 
Revolution frequency | 
Horizontal emittance | 
Vertical emittance | 
Geometric reduction factor | 
Notes: Add color to equation and a table

## Slide 5: Beam Loading and Cavity Controllers
Half-detuning beam-loading compensation scheme [3]
Without beam
With beam
Total gap voltage,
Loaded quality factor,
Cavity detuning,
R upon Q,
Total field in the cavity
Field for a given power
Difference between the resonant frequency and the rf frequency
Accelerating field for a given energy stored in the cavity
Oscillating voltage from an RF cavity
Notes: Introduce external voltage -> figure below with second line of the beam-induced voltage (beam loading)
You need power to counter act this beam-induced voltage.
In the LHC most of the power goes to counteracting this beam-loading
Show voltage and bucket:
No beam loading
With beam loading but with out CC
With beam loading and CC -> higher power

## Slide 6: The LHC RF System
Eight 400 MHz superconducting standing-wave RF cavities per beam
Each cavity is power by its own klystron and has its own cavity controller
  Each klystron can provide maximum 300 kW [4]
  A circulator between the klystron and the cavity
The low-level RF system [5]
  Fast RF feedback
  One-turn delay feedback (OTFB)
  Switch and protect (SWAP) unit
    Prevent feedbacks from requesting too much power from klystron
  Tuner loop
    Controls position of power coupler
    Controls stepper motor that mechanically tunes the RF cavity
Notes: Use colors

## Slide 7: Beam Losses at the Start of the Ramp
Uncaptured beam generated at injection
  Due to errors in energy and timing at transfer
Intra-beam scattering (IBS) [6]
  Small angle scattering of particles inside the bunches
  Lead to a diffusive effect in the LHC in all three planes
  Due to diffusion from IBS and background noise in the RF system [7]
    Particles slowly leak from buckets
Most particles outside the RF buckets at the start of the energy ramp will lost on the collimators in IR3
  Part of the beam outside the RF buckets will be cleaned by the transverse damper
  Losses are less 0.5% of the total circulating beam, but are lost over a few seconds
Notes: Capture losses, IBS losses, and ADT cleaning

## Slide 8: RF Power Limitations at Injection Energy
SPS and LHC bucket, 2018
SPS and LHC bucket, HL-LHC
2018: 7 MV in SPS -> 4 MV in LHC
Relative momentum spread increase
3.74 x 10-4 -> 5.32 x 10-4
HL-LHC: 10 MV in SPS -> 7.9 MV in LHC
84 kW average steady-state RF power in the LHC
265 kW average steady-state RF power in the LHC
Notes: Table with power w/o beam, avg power, peak power

## Slide 9: RF Power Limitations at Injection Energy
Voltage needed calculated simple scaling with momentum spread
  Does not take into account:
    Injection offsets
    Beam loading
    Debunching during flat bottom
  What voltage do we need to have an acceptable amount of losses?
RF power requirements based on steady-state RF power demand
  Does not take into account
    power transients at injection
    peak power when the beam is in steady state
  Significant ±20% spread in RF power has been observed in the past in the LHC
  What is the maximum voltage that can be achieved with HL-LHC beams?
Notes: Table with power w/o beam, avg power, peak power

## Slide 10: Overview of the Project
The HL-LHC
Operational Scenario
RF Hardware
Operation
Measurement
Campaign
Simulation
Campaign
Calibration of
RF parameters
Half-detuning
Optimization
RF Power
Margins
High-intensity
MDs
Minimum RF
Capture Voltage
Beam Losses at
The Start of the Ramp
Modelling of LLRF
Control Loops
Pre-detuning
At Injection
Intra-beam
Scattering
Operational
Beam Evolution
At flat-bottom
Notes: Boxes from this diagram in the different slides to illustrate what the subject belongs to

## Slide 11: Overview of the Project
The HL-LHC
Operational Scenario
Measurement
Campaign
Simulation
Campaign
Calibration of
RF parameters
Half-detuning
Optimization
RF Power
Margins
High-intensity
MDs
Minimum RF
Capture Voltage
Beam Losses at
The Start of the Ramp
Modelling of LLRF
Control Loops
Pre-detuning
At Injection
Intra-beam
Scattering
Operational
Beam Evolution
At flat-bottom
RF Hardware
Operation

## Slide 12: Hardware Optimisations
Optimization of half-detuning [8]
Used to be manual but is now almost automatic
Algorithm developed to detect power in beam segment
Automatic optimization of LHC RF working point in half-detuning
Pre-detuning at injection [8,9]
Pre-detune RF cavities in anticipation of beam loading from first long bunch trains
Scans performed in operation and recreated in simulation using BLonD [10]
Is projected to reduce peak power of first long train injection for HL-LHC by almost 3 times
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters

## Slide 13: Calibration of the RF Voltage
10% uncertainty on RF voltage in the past
Two methods
  Synchrotron frequency from bunch phase oscillations
  Longitudinal phase-space tomography [11,12]
First measurement in 2022 [13]
  Corrections implemented in the LLRF
  Confirmed with measurements in 2024 and 2025
Simulation study using BLonD
  Synchrotron frequency accurate within 3%
  Tomography accurate within 1%
Results for Beam 1
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters

## Slide 14: New Calibration method of the Quality Loaded
Previously calibrated from
  power and voltage
  Open-loop transfer function
Open-loop transfer function is very inaccurate 12% – 25%
New method
  Observe the decay of voltage inside the cavity
  Only fitting a single parameter
  Simulations showed that this method should be very accurate
Participated during month-long LHC hardware commissioning in 2024
vs.
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters

## Slide 15: Available RF Power in the LHC and HL-LHC
Combining calibrated RF voltage and loaded quality factor without beam
Agrees with independent measurement
  Based on calibration of the directional couplers measuring the forward power from the klystron
Some margin is lost when the SWAP is active
Based on the calibrated RF power up to 6.5 MV could be sustained [14]
High efficiency (HE) klystrons will be installed for HL-LHC [15]
  Increase of power from 300 kW to 350 kW by design -> 7.4 MV
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters

## Slide 16: Overview of the Project
The HL-LHC
Operational Scenario
Measurement
Campaign
Simulation
Campaign
Calibration of
RF parameters
Half-detuning
Optimization
RF Power
Margins
High-intensity
MDs
Minimum RF
Capture Voltage
Beam Losses at
The Start of the Ramp
Modelling of LLRF
Control Loops
Pre-detuning
At Injection
Intra-beam
Scattering
Operational
Beam Evolution
At flat-bottom
RF Hardware
Operation
Notes: Boxes from this diagram in the different slides to illustrate what the subject belongs to

## Slide 17: Beam Measurements
Year | Beam type | Bunch Intensity | RF Voltage
2023 | Standard | 1.9 x 1011 p/b | 5 MV
2023 | Standard | 1.9 x 1011 p/b | 7 MV
2024 | BCMS* | 2.0 x 1011 p/b | 7 MV
2024** | BCMS* | 2.3 x 1011 p/b | 6.5 MV
2025 | Standard | 2.3 x 1011 p/b | 6.0 MV
2025 | 8b4e | 2.3 x 1011 p/b | 8.0 MV
*Low transverse emittance beam type
**With the OTFB open, note a few bunches saturated FBCT
Overview of high intensity MDs
MDs in the LHC
  Dedicated beam time to perform measurements and tests
MD milestones
  2022: RF voltage calibration, capture of 1.8 x 1011 p/b [13,16]
  2023: Capture of 2.0 x 1011 p/b [17]
  2024: Capture of 2.3 x 1011 p/b BCMS* beam and direct measurements of start-of-ramp losses
  2025: Capture of 2.3 x 1011 p/b standard and 8b4e beams
In total 9 x 8-hour MDs performed
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters
Say what is BCMS

## Slide 18: Debunching during Run 3 and HL-LHC
Beam measurements [18]
Calculated debunching rate
Debunching and RF Voltage
HL-LHC bunches were found to suffer less from IBS than the operational beams
Using IBS model in BLonD [20]
More particles loss despite less IBS-driven bunch lengthening
Confirmed from theory [19]
  Due to larger transverse emittances
Notes: Say that stars are measurements

## Slide 19: Off-position Beam and Start-of-ramp Losses
Off-momentum beam
Satellite particles
Off-position beam
All particles leaking from the bunches drift off-momentum relative to the main bunches
This can be measured by comparing the DC and fast BCTs
  Off-position beam: estimate the beam lost from the bunches but is still circulating [21]
From operation:
  Linear correlation between off-position beam and start-of-ramp losses
  Start-of-ramp losses correlate with maximum ratio to dump in IR3
Bunch
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters

## Slide 20: Beam Losses during High-intensity MD Sessions
Off-position beam was estimated for high-intensity tests
  Scaled to the full HL-LHC beam spending the a projected 20 – 25 min at injection energy
Operational correlations can be used to
  calculate start-of-ramp losses for fills where the beam was not ramped
  Project the maximum ratio to dump threshold for the beams injected during the MDs
This does not take into account uncaptured beam
  47% of dump threshold has been reach despite 10 - 20 % expected from off-position beam
Beam type | RF Voltage | # Bunches | Ratio to dump, Beam 1 | Ratio to dump, Beam 2
BCMS | 6.5 MV | 2748 | 9.4 % | 29.8 %
Standard | 6.0 MV | 2760 | 23.2 % | 56.4 %
Standard | 6.0 MV | 2760 | 24.0 % | 30.8 %
8b4e | 6.0 MV | 1972 | 14.8 % | 10.8 %
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters

## Slide 21: Uncaptured beam generated at injection
Estimated by comparing BCTs in SPS and LHC for each injection
Tracking model used to calculate uncaptured beam generated at injection
  Detailed model of beam dynamics at SPS flat top and LHC injection [22, 23]
  Benchmarked against operational and MD measurements
Results show that around 1% of the high-intensity trains will be converted to uncaptured particles with present RF voltage
  The bunches near head and tail of trains lose the most
For example, the standard beam
  1% uncaptured would implie 6.3 x 1012 p in total which would need to be cleaned before acceleration
Coupling of control loops for the first time in a tracking code [24]
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters

## Slide 22: Overview of the Project
The HL-LHC
Operational Scenario
Half-detuning
Optimization
Calibration of
RF parameters
Pre-detuning
At Injection
RF Hardware
Operation
Measurement
Campaign
High-intensity
MDs
Simulation
Campaign
Modelling of LLRF
Control Loops
Intra-beam
Scattering
Operational
Beam Evolution
At flat-bottom
RF Power
Margins
Minimum RF
Capture Voltage
Beam Losses at
The Start of the Ramp
Notes: Boxes from this diagram in the different slides to illustrate what the subject belongs to

## Slide 23: The HL-LHC Operational Scenario
Peak power from calibration
  Currently: around 275 kW/klystron
  HL-LHC: around 320 kW/klystron
Voltage for different beam types
  Currently: 6.5 MV (8.0 MV for 8b4e)
  HL-LHC: 7.4 MV (9.5 MV for 8b4e)
Simulated uncaptured beam
  Increase of 3 – 7 times compared to Run 3
  Relative losses of 0.43% to 0.94%
Simulated IBS-driven debunching
  Increase of 0.16 to 0.8 times compared to Run 3
  Relative losses of 0.12% to 0.65%
Expected 4.3 % lost from SPS extraction to collisions at LHC flat top
  Uncaptured particles and IBS-driven leakage could reach up to one third of this budget
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters

## Slide 24: Mitigation Measures
Measures to accept more beam losses
Increasing the BLM thresholds in IR3
  Up to a factor eight can be gained
Slower momentum increase at the start of the ramp
  Spend twice the time amount of time below 460 GeV/c
Inter-train cleaning with the transverse damper
  Promising results from beam tests in 2025
Measures to further reduce beam losses
High-efficiency klystrons
  More voltage for better capture and less debuching
Regular optimization of the operatonal working point
Full-detuning at injection
  Apply a different beam loading scheme at injection to reduce power and increase voltage
Larger transverse emittances to reduce IBS
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters

## Slide 25: Conclusions and Outlook
Hardware
  Maximally optimized performance of hardware to capture HL-LHC beam
  Projected a maximum of 6.5 MV currently and up to 7.4 MV with HE klystrons
  Confirms voltage limits from calibration
HL-LHC projections from simulations and beam measurements
  Debunched beam is predicted to be comparable to operational levels during Run 3
  Predicted uncaptured beam will increase by up to several times compared to Run 3
  With BLM threshold increase the beam could be accelerated this Run
Outlook
  Studies of mitigation measures
    Testing of full-detuning scheme at injection
  LHC heat run to test the full beam at the end of 2026 Run
Notes: BLM systems, Layout, RF system, UX45 sketch, LHC cycle
Start-of-ramp losses, uncaptured beam, debunching, etc.

## Slide 26: List of Publications
H. Timko et al., ‘’Beam longitudinal dynamics simulation studies’’, Phys. Rev. Accel. Beams, vol. 26, 2023
B. E. Karlsen-Baeck et al., “Validation of control loop modelling for power limitation studies with beams for HL-LHC”, in Proc. IPAC’23, Venice, Italy, 2023
H. Timko et al., “Advances on LHC RF Power Limitation Studies at Injection”, in Proc. HB’2023, CERN, Geneva, Switzerland, 2023
M. Zampetakis et al., “Refining the LHC Longitudinal Impedance Model”, in Proc. HB’2023, CERN, Geneva, Switzerland, 2023
B. E. Karlsen-Baeck et al., “Effects of cavity pre-detuning on RF power transients at injection into the LHC”, JINST 19 T04005, Contribution to HB’2023
B. E. Karlsen-Baeck et al., “Correlating start-of-ramp losses with beam observables at flat-bottom in the LHC”, in Proc. IPAC’24, Nashville, TN, USA, 2024
K. Iliakis et al., “Machine learning-based extraction of longitudinal beam parameters in the LHC”, in Proc. IPAC’24, Nashville, TN, USA, 2024
M. Zampetakis et al., “Modelling intra-beam scattering in the LHC for longitudinal beam loss studies”, in Proc. IPAC’24, Nashville, TN, USA, 2024
B. E. Karlsen-Baeck et al., “LHC MD 6944: RF Voltage Calibration”, technical report CERN-ACC-NOTE-2023-0008, CERN, Geneva, Switzerland, 2024
B. E. Karlsen-Baeck et al., “LHC MD 6945: Injection Power Transients”, technical report CERN-ACC-NOTE-2024-0002, CERN, Geneva, Switzerland, 2024
B. E. Karlsen-Baeck et al., “Optimizing cavity detuning at high beam intensities at LHC injection energy”, in Proc. IPAC’25, Taipei, Taiwan, 2025
B. E. Karlsen-Baeck et al., “Comparison of BCMS and standard beams at LHC injection energy”, in Proc. IPAC’25, Taipei, Taiwan, 2025
H. Timko et al., “Upgrade of the LHC main RF system for HL-LHC”, in Proc. IPAC’25, Taipei, Taiwan, 2025
M. Zampetakis et al., “Benchmarking the LHC impedance model through loss of Landau damping measurements and simulations”, in Proc. IPAC’25, Taipei, Taiwan, 2025
L. S. Thiele et al., “Beam loading for counter-rotating high-intensity beams in the Muon Collider”, in Proc. IPAC’25, Taipei, Taiwan, 2025
S. Morales Vigo et al., “LHC BLM-based beam loss pattern recognition algorithm for off-momentum losses”, in Proc. IPAC’25, Taipei, Taiwan, 2025
B. E. Karlsen-Baeck et al., “LHC MD 9525: Injection Power Transients with Different RF Settings”, technical report to be submitted
B. E. Karlsen-Baeck et al. “Coupling of local and global rf feedback loops for macroparticle tracking simulations”, submitted for peer review
B. E. Karlsen-Baeck et al. “Calibration of the CERN Large Hadron Collider RF system”, to be submitted for peer review
14th International Particle Accelerator Conference (IPAC’23), Venice, Italy, 7-12 May 2023
68th ICFA Advanced Beam Dynamics Workshop on High-intensity and High-Brightness Hadron Beams (HB’23), CERN, Geneva, Switzerland, 9-13 October 2023
Joint Accelerators Performance Workshop 23, Montreux, Switzerland, 5-7 December 2023
I.FAST Workshop 2024 on Bunch-by-bunch Feedback Systems and Related Beam Dynamics, KIT, Karlsruhe, Germany, 3-6 March 2024
14th HL-LHC Collaboration Meeting, Genoa, Italy, 7-10 October 2024
16th International Particle Accelerator Conference (IPAC’25), Taipei, Taiwan, 1-6 June 2025
15th HL-LHC Collaboration Meeting, Geneva, Switzerland, 29 September – 2 October, 2025
Conferences

## Slide 27: References
[1] | O. Bruning et al., “LHC Design Report,” CERN Yellow Reports: Monographs, Rep. CERN-2004-003-V-1, CERN, Geneva, Switzerland, 2004
[2] | O. Aberle et al., “High-Luminosity Large Hadron Collider (HL-LHC): Technical design report,” CERN Yellow Reports: Monographs, Rep. CERN-2020-010, CERN, Geneva, Switzerland, 2020
[3] | D. Boussard, “rf power requirements for a high intensity proton collider; parts 1 (chapters I, II, III) and 2 (chapters IV, V, VI),” Rep. CERN-SL-91-16-RFS, CERN, Geneva, Switzerland, 1991
[4] | O. Brunner et al., “RF Power Generation in LHC”, in Proc. PAC’03, Portland, OR, Unites States, 2003
[5] | P. Baudrenghien et al., “The LHC low level RF” , in Proc. EPAC’06, Edinburgh, Scotland, 2006
[6] | J. D. Bjorken and S. K. Mtingwa, “Intrabeam scattering”, Part. Accel. 13, pp. 115-143, 1983
[7] | T. Mastoridis et al., “Radio frequency noise effects on the CERN Large Hadron Collider beam diffusion”, Phys. Rev. ST Accel. Beams 14, p. 092802, 2011
[8] | B. E. Karlsen-Baeck et al., “Optimizing cavity detuning at high beam intensities at LHC injection energy”, in Proc. IPAC’25, Taipei, Taiwan, 2025
[9] | B. E. Karlsen-Baeck et al., “Effects of cavity pre-detuning on RF power transients at injection into the LHC”, JINST 19 T04005, Contribution to HB’2023
[10] | H. Timko et al., ‘’Beam longitudinal dynamics simulation studies’’, Phys. Rev. Accel. Beams 26, p. 114602, 2023
[11] | S. Hancock, “A simple algorithm for longitudinal phase space tomography”, Rep. CERN-PS-RF-Note-97-06, CERN, Geneva, Switzerland, 1997
[12] | D. Quartullo et al., “RF voltage calibration using phase space tomography in the CERN SPS”, in Proc. IPAC’22, Bangkok, Thailand, 2022

## Slide 28: References
[13] | B. E. Karlsen-Baeck et al., “LHC MD 6944: RF Voltage Calibration”, Tech. Note CERN-ACC-NOTE-2024-0008, CERN, Geneva, Switzerland, 2024
[14] | B. E. Karlsen-Baeck et al., “Calibration of the CERN Large Hadron Collider RF system”, to be submitted for peer review
[15] | N. Catalan Lasheras et al., “High-efficiency klystrons from a dream to a reality”, in Proc. IPAC’24, Nashville, TN, USA, 2024
[16] | B. E. Karlsen-Baeck et al., “LHC MD 6945: Injection Power Transients”, Tech. Note CERN-ACC-NOTE-2024-0002, CERN, Geneva, Switzerland, 2024
[17] | B. E. Karlsen-Baeck et al., “LHC MD 9525: Injection Power Transients with Different RF Settings”, technical report to be submitted
[18] | B. E. Karlsen-Baeck et al., “Comparison of BCMS and standard beams at LHC injection energy”, in Proc. IPAC’25, Taipei, Taiwan, 2025
[19] | S. Nagaitsev, “Intrabeam scattering formulas for fast numerical evaluation”, Phys. Rev. ST Accel. Beams 8, p. 064403, 2005
[20] | M. Zampetakis et al., “Modelling intra-beam scattering in the LHC for longitudinal beam loss studies”, in Proc. IPAC’24, Nashville, TN, USA, 2024
[21] | B. E. Karlsen-Baeck et al., “Correlating start-of-ramp losses with beam observables at flat-bottom in the LHC”, in Proc. IPAC’24, TN, USA, 2024
[22] | B. E. Karlsen-Baeck, “Modelling Control Loops for SPS-LHC Beam Transfer Studies”, Master thesis, Norwegian University of Science and Technology, 2022
[23] | B. E. Karlsen-Baeck et al., “Validation of control loop modeling for power limitation studies with beams for HL-LHC”, in Proc. IPAC’23, Venice, Italy, 2023
[24] | B. E. Karlsen-Baeck et al., “Coupling of local and global RF control loops for macroparticle tracking simulations”, submitted for peer review

## Slide 29: Motivation
Backup

## Slide 30: Longitudinal Dynamics at LHC Injection
5 ns SPS bucket into 2.5 ns LHC bucket
  Matched voltage would lead to particles arriving outside bucket
  LHC operates at a higher-than-matched voltage to reduce amount of uncaptured particles
Voltage mismatch together offsets in timing and energy of the injected bunches
  Excites oscillations of the bunches
  Leads to generation of uncaptured particles
Notes: Capture losses, IBS losses, and ADT cleaning

## Slide 31: Scaling uncaptured beam and debunching to HL-LHC
Beam type | RF Voltage | Uncaptured beam Increase form Run 3 | Relative uncaptured beam | Debunched beam increase from Run 3 | Relative debunched beam | Total relative intensity lost
Standard | 6.5 MV | 5.36 | 0.76 % | 0.92 | 0.69 % | 1.45 %
Standard | 7.4 MV | 4.69 | 0.66 % | 0.42 | 0.32 % | 0.98 %
BCMS | 6.5 MV | 7.82 | 1.08 % | 1.66 | 1.23 % | 2.31 %
BCMS | 7.4 MV | 6.82 | 0.94 % | 0.88 | 0.65 % | 1.59 %
8b4e | 8.0 MV | 3.69 | 0.52 % | 0.44 | 0.33 % | 0.85 %
8b4e | 9.5 MV | 3.09 | 0.43 % | 0.16 | 0.12 % | 0.55 %
Notes: Simplified picture of the LHC with the two rings and the experiments
Table with the main parameters