## Slide 1
Plasma acceleration
Angelo Biagioni
On behalf of the Sparc_lab collaboration
Accelerator Physics and Technology PhD: meeting first year students
Sapienza Università di Roma |Thursday 13 Nov 2025

## Slide 2
  Plasma acceleraiton experiments at Sparc_lab test facility
  Principles of plasma acceleration
  Gas-filled discharge capillaries
  Laser-induced plasma sources
  Plasma properties characterization
  Plasma sources for the EuPRAXIA@SPARC_LAB project
      Long plasma sources
      Material science
      Integrated plasma accelerating module
Outline
Sapienza Università di Roma |Thursday 13.11.2025
Pag. 2

## Slide 3
Particle-driven plasma acceleration
Energy | 6 J
Duration | 25 fs
Wavelength | 800 nm
Bandwidth | 80 nm
Spot@focus | 10 um
Peak power | 250 TW
Contrast ratio | 1010
EuPraxia Betatron
Radiation Source (EuAPS)
Laser-driven plasma
acceleration (ExIn)
High-power laser (FLAME)
SPARC_LAB test facility
Sparc_Lab facility
Sapienza Università di Roma |Thursday 13.11.2025
Pag. 3

## Slide 4
Particle-driven plasma acceleration
EuPraxia Betatron
Source (EuAPS)
High-power laser (FLAME)
3D-printed plasma sources (plastic)
3cmx2mm capillary
Plasma densities 1016 – 1017 cm-3
SPARC_LAB test facility
Sparc_Lab facility
Energy | 6 J
Duration | 25 fs
Wavelength | 800 nm
Bandwidth | 80 nm
Spot@focus | 10 um
Peak power | 250 TW
Contrast ratio | 1010
Sapienza Università di Roma |Thursday 13.11.2025
Pag. 4

## Slide 5
n0 = 1016 cm-3 λp = 300 µm
Wave-breaking field
LWFA Drive beam is a laser pulse
PWFA Drive beam is high energy or proton beam
λp
  Geometry to control density gradient, plasma ramps...
  Reproducibility
  Stability
  Uniformity/ramps
  High repetition rate (heat dissipation, materials)
  Vacuum requirements
Main topics related to the design of a plasma source:
Wakefield
Principles of plasma acceleration
Pag. 5

## Slide 6
6 MeV acceleration in 3 cm long plasma capillary with 200 pC driver/20 pC witness
  Plasma density set to 2x1015 cm-3
  ~200 MV/m accelerating gradient (RF structures in the range 20-60 MV/m)
  Driver decelerated by almost 10 MeV
  During last experiments, accelerating gradient close to 1 GV/m has been reached
Demonstration of energy spread compensation
  Total projected spread from 0.2 MeV to 0.12 MeV
Initial Witness
energy
Driver
Witness
Driver
Witness
Nearly the same energy
with plasma OFF
Discharge in 3 cm long gas-filled capillary
First results at Sparc_lab
Pag. 6

## Slide 7
4/28
Gas inlets
Electrode
HV pulse
Plasma channel
thin capillaries are used to confine a neutral gas (H, Ar, N…), which is injected through several inlets into the plasma channel
OpenFOAM code
for neutral gas distribution
0-5 ms
0 – 5 ms
4.5 ms
2.5E17
6E16
2E16
1 ms
the plasma formation process is triggered by a high voltage pulse at the ends of the capillary
Density profile
x1017
The plasma characterization is based on spectroscopic techniques (Stark broadening effect)
Design of plasma sources – Discharge capillary
Pag. 7

## Slide 8
1.2 mbar
L = 39.75 mm
d = 567.6 um
Intensity [a.u.]
Time [ns]
7 ns Lifetime
Laser pulse: 15 mJ, 100 fs
N2 95% - H2 5%, 1-10 mbar
Tune laser energy, focal spot and gas pressure to change filament size and plasma density
Ne = 1016 - 1017 cm-3
Design of plasma sources – Laser-induced plasma
Laser pulse
Pag. 8

## Slide 9
                Fabrication by machining
                10 increasing diameter
                Density range 1016 -1017 cm-3
                13 kV with 500 A
                100 Hz rep Rate
1017
  V = 13 kV
  Ip = 500 A
Design of long plasma sources for the EuPRAXIA project
Pag. 9
159 m
45 m
Accelerator tunnel
Plasma
module
Undulator tunnel
Experimental hall
Lasers clean rooms
Laser and particle user rooms
Klystron & power supplies hall
Technical rooms
Preparations labs
1.1 GeV (1 GV/m 600 MeV in 60cm long capillary - density 1016 cm-3 )
60-cm long discharge capillary

## Slide 10
Design of plasma sources – High repRate operations
10-150 Hz operation
N2 80-100 mbar in continuous flow
6 kV – 500 A
First prototype of the ceramic capillary
High thermal conductivity
High max operating temperature
Good machinability, cost-effectiveness and availability for large geometries
New materials for electrodes
Stainless
steel
Molybdenum
Shapal
Macor
150 Hz repetition rate discharges
Sapienza Università di Roma |Thursday 13.11.2025
Pag. 10

## Slide 11
Plasma capillary
Plasma capillary
Focusing
lens
Acelerating
section
Extraction
lens
Integrated plasma module
Alinegment issues
Compactness (20 cm)
No motors to move PMQs
Strong current-modulated magnetic field (1 kT/m)
Lens ON Acc ON Lens ON
3 us
Acc-200A
Lens-500A
Current pulses
Plasma formation
Quadrupoles are essential
to achieve plasma acceleration
Active plasma
lens
Compact plasma accelerating modules
Pag. 11

## Slide 12
Driver
Witness
5 MeV/3cm acceleration in 19 cm long integrated plasma module with 200 pC driver/50 pC witness
  3 cm long accelerator with 200 A ionization current
  3 cm long plasma lenses with 500 A ionization current
  Plasma density inside the accelerator set to 2x1015 cm-3
  ~150 MV/m accelerating gradient
  Stability of the accelerated beam
200 consecutive shots taken with accelerated beam
Pag. 12
Compact plasma accelerating modules

## Slide 13
Particle acceleration based on plasma technology involves research across a wide range of subjects related to the overall design of the plasma accelerator module. This includes studies on plasma generation techniques, plasma property measurements, and improvements in the geometric modeling of the plasma source:
    Design and development of plasma sources based on electrical discharge and laser pulses
          Lasers
          High voltage circuits
    Theoretical studies of magnetohydrodynamic models capable of simulating plasma formation from neutral gases
    Theoretical and experimental study of laser–plasma interaction
    Characterization of plasmas for particle accelerators
          Spectroscopy
          interferometry
Pag. 13
Conclusions
Sapienza Università di Roma |Thursday 13.11.2025

## Slide 14
Thank you for your attention
Angelo.Biagioni@lnf.infn.it