## Slide 1: DC trigger
Present DC design
Lab tests and implementation.
Paolo Branchini – INFN Roma 3

## Slide 2: Let’s remember the specs in SuperB
Baseline:
re-implement BaBar L1 trigger with some improvements
  Shorter latency (~6us instead of 12us)
  Higher sampling frequencies (DCH and EMC)
  2-d map for calorimeter
Possible additions
SVT trigger
What about the TOF ? (in DELPHI we used it in the trigger)
Bhabha Veto
Do we need an absolute time stamp at the trigger level?
Challenge
To keep the event loss due to dead time below 1% => a maximum of ~70ns “per-event dead time” is allowed in trigger and FCTS
Other considerations
What goes in L1, what in L3, what’s the optimum?
Luitz 2010
150kHz
Exponential Inter-arrival time pdf.

## Slide 3: DC Architecture

## Slide 4: DC SuperB present design
 | SL1 | SL2 | SL3 | SL4 | SL5 | SL6 | SL7 | SL8 | SL9 | SL10 | TOT
Planes | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 
Type | A | A | U | V | U | V | U | V | A | A | 
#wires | 736 | 864 | 496 | 560 | 624 | 688 | 752 | 816 | 896 | 960 | 7392
#TSF 64 opt | 12 | 14 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 118
#NDCB 64 opt | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 10
Number of wire could change due to internal radius uncertainties.
The 64 TSF layout depends on the form factor of the FE board used at the moment a conservative assumption has been made (i.e. 6U VME form factor)

## Slide 5: What we have done so far
We have profitted of the LNF DC prototype to insert our eltx.
We have built our own RF emulator, clocked discriminators and used them all offline to setup a trigger algorithm (inspired by BaBar).
We have implemented the trigger algorithm on a Virtex 6 demo board.

## Slide 6: Trigger setup
Clocked discriminator
Discriminator
Ring Oscillator

## Slide 7: RF emulator needed @tbeam
We have also built a ring oscillator to emulate RF when a machine trigger occurs.
And a transition board to feed Virtex6 demo board with LVDS signals.

## Slide 8: TSF (Track Segment Finder)
P
P
P
P
4 pattern for a fixed pivot tube. The other 4 pattern can be found via a parity transformation.
So in this example there are 8 patterns per pivot tube and 4 pivot tubes. In total 32 combinations.

## Slide 9: Analog and discriminated signals

## Slide 10
Results (flash adc distribution left side vs discriminated one right side)
Right side DC wave Form distribution left side clocked discriminator distribution
Triggered by scintillators

## Slide 11: DC trigger
It’s based on track segment
The track segment is defined by 4 contiguous
hits in neighbouring layers.
Drift signal is stretched by one drift time (500 ns) in order to allora time coincidences.
When at least a TSF is found a trigger is asserted.
We collect this information using the DC daq
provided by Riccardo De Sangro.

## Slide 12
Serial Track i-th first hit outcome
20 ns + n*20ns
The width of the pulse is proportional to the number of the track n, in which the first hit is detected. If there are simultaneous hits the track with lower value of n has priority.
Start
Track 1
Track 2
Track 3
Track 4
Track 40
i-th tick after the start pulse is fired when i-th look-up table. Simultaneous tracks can be detected.
ID for Serial Track outcome
20 ns
Tracks_pattern
Hit_Tracks
The rising edge of the Hit_Tracks signal is a copy of a synchronized and delayed version of the rising edge of the first hit signal of the track

## Slide 13
Hit 1 from DC
Hit 2 from DC
Hit 28 from DC
Synchronizer
Synchronizer
Synchronizer
Strecher (480 ns)
Strecher (480 ns)
Strecher (480 ns)
Hit 1 stretched
Hit 2 stretched
Hit 1 stretched
Track 1
Hit 9 stretched
Hit 10 stretched
Track 40
Hit 18 stretched
Hit 19 stretched
Hit 27 stretched
Hit 28 stretched
Hit 2 stretched
Hit 28 stretched
Hit 2 stretched
Hit 1 stretched
Track 1 Hits or
Hit 9 stretched
Hit 10 stretched
Track 40 Hits or
Hit 18 stretched
Hit 19 stretched
Hit 27 stretched
Hit 28 stretched
Delay (480 ns)
Delay (480 ns)
Strecher (2240 ns)
Track 1
Track 40
Strecher (2240 ns)
Track 1_first Hit
Track 40_first Hit
Track i-th first Hit has information of the first hit phase of the tracks i-th

## Slide 14
Board 1
Board 2
Board 3
Board 4
Trigger Time
Triggered track
Example 1

## Slide 15
Board 3
Board 4
Board 2
Board 1
Trigger Time
Triggered track
Example 2

## Slide 16
Board 1
Board 2
Board 3
Board 4
Trigger Time
Triggered track
Example 3
Trigger time occurs at about 900 ns

## Slide 17: To be compared with ……
Trigger time occurs at
about 250 ns
TSF latency 750 ns
in this implementation

## Slide 19
Board 1
Board 2
Board 3
Board 4

## Slide 20: Look up tables (cosmic)

## Slide 21: Timing resolution (cosmic)