## Slide 1
Front End Electronic Design
For outer Layers of SVT(L.4 & L.5)
Team: Luca Bombelli, Bayan Nasri, Carlo Fiorini, Paolo Trigilio

## Slide 2: Table of Contents
Update on Noise evaluation
Update on Timing accuracy
  Noise jitter
  Time walk

## Slide 3: Remind of chosen architecture
FE-Block Diagram
Third order complex-pole shaping

## Slide 4: ENC Contributions
Example of ENC evaluation
Tp(ns) | 375 | 500 | 750 | 1000
ENC_FET | 600 | 529 | 444 | 395
ENC_Rs | 468 | 407 | 333 | 290
ENC_RB | 234 | 270 | 329 | 379
ENC_Rf | 579 | 583 | 589 | 590
ENC_Leakage | 149 | 172 | 210 | 241
ENC_others | 539 | 498 | 434 | 408
ENC_Total | 1132 | 1066 | 998 | 978

## Slide 5: FE-Model
Detector Model used in simulation
(including ganging)
  Detectors Parameters (Updated by Luciano Bosisio May 20, 2012):
Strip side | Layer | Type | Strip length (cm) | CD (pF) | RD (Ω) | RB (MΩ) | Ileak at startup (nA) | Ileak 7.5y BK (nA) | Ileak 7.5y 5xBK (nA) | CAC (pF) | Cfanout (pF) | Rfanout (Ω)
Phi | 4 | p | 30.34 | 51.6 | 121 | 2.7 | 6.1 | 102 | 484 | 1213.6 | 1.5 | 3.2
Phi | 5 | P | 38.04 | 64.7 | 152 | 2.5 | 7.6 | 44 | 187 | 1521.6 | 1.5 | 3.2
Z | 4 | n | 15.42 | 26.2 | 46 | 2.7 | 3.1 | 105 | 513 | 925.2 | 21 | 53
Z | 5 | n | 15.42 | 26.2 | 46 | 3.3 | 3.1 | 34 | 156 | 925.2 | 26 | 66
Temperature = 20°C
Distributed RC network

## Slide 6: Connection of the Z-Strip
Distributed R-C network both on detector and on fanout
Moreover the 2 type of networks are interleaved several times for ganged strips!

## Slide 7: FE-Model
Strip side | Layer | Type | Strip length (cm) | CD (pF) | RD (Ω) | RB (MΩ) | Ileak at startup (nA) | Ileak 7.5y BK (nA) | Ileak 7.5y 5xBK (nA) | CAC (pF) | Cfanout (pF) | Rfanout (Ω)
Phi | 4 | p | 30.34 | 51.6 | 121 | 2.7 | 6.1 | 102 | 484 | 1213.6 | 1.5 | 3.2
Phi | 5 | P | 38.04 | 64.7 | 152 | 2.5 | 7.6 | 44 | 187 | 1521.6 | 1.5 | 3.2
Z | 4 | n | 15.42 | 26.2 | 46 | 2.7 | 3.1 | 105 | 513 | 925.2 | 21 | 53
Z | 5 | n | 15.42 | 26.2 | 46 | 3.3 | 3.1 | 34 | 156 | 925.2 | 26 | 66
Detector Model used in simulation
(including ganging)
  Detectors Parameters (Updated by Luciano Bosisio May 20, 2012):
  Model for Phi side
  Model for Z side
Similar ratios

## Slide 8: ENC Estimation before radiations damage
Tp(ns) | 250 | 375 | 500 | 750
ENC_FET | 533 | 463 | 406 | 346
ENC_Rs | 389 | 320 | 280 | 233
ENC_RB | 200 | 249 | 283 | 330
ENC_Rf | 384 | 427 | 425 | 418
ENC_Leakage | 64 | 85 | 97 | 114
ENC_others | 581 | 427 | 396 | 384
ENC_Total | 982 | 866 | 819 | 786
Tp(ns) | 375 | 500 | 750 | 1000
ENC_FET | 496 | 441 | 375 | 336
ENC_Rs | 377 | 330 | 273 | 240
ENC_RB | 222 | 256 | 303 | 351
ENC_Rf | 429 | 428 | 420 | 420
ENC_Leakage | 102 | 116 | 137 | 159
ENC_others | 472 | 429 | 389 | 359
ENC_Total | 925 | 866 | 808 | 790
Tp(ns) | 250 | 375 | 500 | 750
ENC_FET | 596 | 491 | 437 | 376
ENC_Rs | 483 | 392 | 343 | 288
ENC_RB | 207 | 251 | 288 | 345
ENC_Rf | 600 | 644 | 646 | 640
ENC_Leakage | 117 | 141 | 162 | 194
ENC_others | 695 | 638 | 586 | 507
ENC_Total | 1220 | 1140 | 1086 | 1024
Tp(ns) | 375 | 500 | 750 | 1000
ENC_FET | 591 | 525 | 452 | 405
ENC_Rs | 546 | 477 | 401 | 351
ENC_RB | 261 | 300 | 360 | 415
ENC_Rf | 648 | 651 | 653 | 655
ENC_Leakage | 158 | 181 | 217 | 250
ENC_others | 648 | 600 | 505 | 471
ENC_Total | 1257 | 1187 | 1106 | 1083
Phi-Strip
  Layer 4
Phi-Strip
  Layer 5
Z-Strip
  Layer 4
Z-Strip
  Layer 5

## Slide 9: ENC Estimation after 7.5 years (without safety factor)
Tp(ns) | 250 | 375 | 500 | 750
ENC_FET | 533 | 463 | 406 | 346
ENC_Rs | 389 | 320 | 280 | 233
ENC_RB | 200 | 249 | 283 | 330
ENC_Rf | 384 | 427 | 425 | 418
ENC_Leakage | 439 | 583 | 663 | 783
ENC_others | 581 | 427 | 396 | 384
ENC_Total | 1074 | 1041 | 1049 | 1104
Tp(ns) | 375 | 500 | 750 | 1000
ENC_FET | 496 | 441 | 375 | 336
ENC_Rs | 377 | 330 | 273 | 240
ENC_RB | 222 | 256 | 303 | 351
ENC_Rf | 429 | 428 | 420 | 420
ENC_Leakage | 332 | 377 | 446 | 516
ENC_others | 472 | 429 | 389 | 359
ENC_Total | 977 | 937 | 913 | 930
Tp(ns) | 250 | 375 | 500 | 750
ENC_FET | 596 | 491 | 437 | 376
ENC_Rs | 483 | 392 | 343 | 288
ENC_RB | 207 | 251 | 288 | 345
ENC_Rf | 600 | 644 | 646 | 640
ENC_Leakage | 478 | 580 | 665 | 796
ENC_others | 695 | 638 | 586 | 507
ENC_Total | 1353 | 1271 | 1263 | 1282
Tp(ns) | 375 | 500 | 750 | 1000
ENC_FET | 591 | 525 | 452 | 405
ENC_Rs | 546 | 477 | 401 | 351
ENC_RB | 261 | 300 | 360 | 415
ENC_Rf | 648 | 651 | 653 | 655
ENC_Leakage | 381 | 436 | 523 | 603
ENC_others | 648 | 600 | 505 | 471
ENC_Total | 1304 | 1251 | 1204 | 1214
Phi-Strip
  Layer 4
Phi-Strip
  Layer 5
Z-Strip
  Layer 4
Z-Strip
  Layer 5

## Slide 10: ENC Estimation after 7.5 years (Safety factor=5)
Phi-Strip
  Layer 4
Tp(ns) | 250 | 375 | 500 | 750
ENC_FET | 595 | 491 | 437 | 376
ENC_Rs | 483 | 392 | 343 | 288
ENC_RB | 207 | 253 | 288 | 348
ENC_Rf | 600 | 644 | 646 | 640
ENC_Leakage | 1040 | 1265 | 1449 | 1735
ENC_others | 704 | 635 | 588 | 505
ENC_Total | 1639 | 1696 | 1804 | 2005
  Layer 5
Tp(ns) | 375 | 500 | 750 | 1000
ENC_FET | 591 | 525 | 452 | 405
ENC_Rs | 546 | 478 | 401 | 351
ENC_RB | 262 | 301 | 360 | 415
ENC_Rf | 648 | 651 | 653 | 655
ENC_Leakage | 786 | 900 | 1078 | 1242
ENC_others | 647 | 596 | 507 | 472
ENC_Total | 1474 | 1478 | 1530 | 1629
Z-Strip
  Layer 4
  Layer 5
Tp(ns) | 250 | 375 | 500 | 750
ENC_FET | 533 | 463 | 406 | 346
ENC_Rs | 389 | 320 | 280 | 233
ENC_RB | 198 | 249 | 283 | 335
ENC_Rf | 385 | 427 | 425 | 418
ENC_Leakage | 1023 | 1289 | 1465 | 1731
ENC_others | 581 | 427 | 396 | 384
ENC_Total | 1417 | 1551 | 1675 | 1899
Tp(ns) | 375 | 500 | 750 | 1000
ENC_FET | 496 | 441 | 375 | 336
ENC_Rs | 377 | 330 | 273 | 240
ENC_RB | 225 | 256 | 303 | 351
ENC_Rf | 429 | 428 | 420 | 420
ENC_Leakage | 710 | 807 | 955 | 1106
ENC_others | 472 | 429 | 389 | 359
ENC_Total | 1162 | 1178 | 1244 | 1350

## Slide 11: Noise summary
Strip side | Layer | Peaking time (ns) | S/N At startup | S/N after 7.5 years Nomonal background | S/N after 7.5 years 5x Background
Phi | 4 | 250 | 20 | 18 | 15
 |  | 375 | 21 | 19 | 14
 |  | 500 | 22 | 19 | 13
 |  | 750 | 23 | 19 | 12
Z | 4 | 250 | 24 | 22 | 17
 |  | 375 | 28 | 23 | 15
 |  | 500 | 29 | 23 | 14
 |  | 750 | 31 | 22 | 13
Phi | 5 | 375 | 19 | 18 | 16
 |  | 500 | 20 | 19 | 16
 |  | 750 | 22 | 20 | 16
 |  | 1000 | 22 | 20 | 15
Z | 5 | 375 | 26 | 25 | 21
 |  | 500 | 28 | 26 | 20
 |  | 750 | 30 | 26 | 19
 |  | 1000 | 30 | 26 | 18
MIP = 24000 el
1us peaking time not useful.
Probably can be eliminated.

## Slide 12: Table of Contents
FE architecture and Noise evaluation
Timing accuracy
  Jitter due to noise
  Time walk

## Slide 13: Timing Resolution with TOT – Noise jitter
Time jitter depends on the S/N ratio and on the signal amplitude.
Assumed: S/N of 20
Minimum signal of 0.3 MIP
Transient noise simulations
Shaper out
Comparator out
Threshold
(0.25 MIP)

## Slide 14: Timing Resolution with TOT
Max Time window = 87ns
Time Error rms = 25ns
(smallest signal only)
87ns
Peaking Time = 1us
TOT = 6 bits
TOT clock = 17.8 MHz
Time error due to:
Time stamp clock (33MHz)
Time walk, corrected with TOT amplitude
Effect of TOT error (TOT clock)

## Slide 15: Combining the 2 effect
Error from TS clock and time walk
Jitter form noise
Resulted distribution
Approximate the TS and Time walk error as Gaussian and quadratically sum the sigmas.
time
distribution
“TS and Time Walk error”
time
distribution
Jitter from noise
time
distribution
Off line windows
Cumulative distribution function
Normal function
99%

## Slide 16: Timing Resolution with TOT
Peaking time (ns) | TOT bit | TOT clock (Mhz) | TS and Time walk error rms (ns) | Jitter for 0.3 MIP (ns) | Time resolution (ns) | Example Offline window (ns)
375 | 4 | 11.3 | 33 | 35 | 48 | 290
 | 6 | 47.5 | 15 |  | 38 | 230
500 | 4 | 8.5 | 41 | 43 | 59 | 360
 | 6 | 35.7 | 17 |  | 46 | 280
750 | 4 | 5.66 | 56 | 60 | 82 | 500
 | 6 | 23.8 | 21 |  | 64 | 380
1000 | 4 | 4.25 | 72 | 78 | 106 | 640
 | 6 | 17.8 | 25 |  | 82 | 500
Time window calculated as ±3sigma

## Slide 17: Conclusion and next activities
Noise adequate for nominal background up the end of 7.5 years.
x5 safety factor on BK leads to little low S/N due to increase on leakage current of the strips.
Cooling can be improved?
Design of TOT comparator and of shaper BLH completed.
Prototype submission of FE asic is foreseen Nov. 2012.