## Slide 1
EuPRAXIA: Project status summary
Massimo Ferrario (INFN-LNF)
On behalf of the EuPRAXIA@SPARC_LAB Team
This project has received funding from the European Union´s Horizon Europe research and innovation program under grant agreement No. 101079773
LNF Scientific Committee, November 12 , 2025

## Slide 2: Recommendations from previous meeting

## Slide 3: TDR Status and Plans

## Slide 4: TDR Status and Plans

## Slide 5: Civil Infrastructures ready for tender
The expected power consumption for the AQUA operation at 100 Hz repetition rate, delivering up to 1.0 GeV electron beams is 1.1 MW
Electrical loads | kW | %
RF Modulators | 575 | 52
Magnet PSU | 300 | 27
Laser | 15 | 1.3
Experimental users | 10 | 1
Vacuum, electronics and controls | 30 | 2.7
Cooling magnet + RF | 45 | 4.1
HVAC | 120 | 11
Total Expected power consumption | 1095 | 
We are now ready to proceed with the tendering phase for the awarding of the works
Courtesy U. Rotundo, R. Ricci

## Slide 6: Actions to Improve Sustainability
 | Action / Measure | Expected Impact | 
Energy Production | 1.7 MWp photovoltaic systems (including 217 kWp on EuPRAXIA building) | ≈ 2.3 GWh yr⁻¹ of renewable electricity (~15 % of total LNF base load demand) | 
Energy Efficiency – Building | Compliance with EU DNSH and Italian CAM (D.M. 23.06.2022); thermal transmittance optimization; 64 % permeable surface | Reduction of building energy use > 25 %; mitigation of heat-island effect | 
Energy Efficiency – RF Systems | Adoption of > 55 % efficiency X-band klystrons (CERN–CPI VKX83113) and solid-state modulators | 10 % efficiency gain vs. standard systems (~200 MWh yr⁻¹ saved) | 
HVAC Optimization | Sizing based on low-grade heat and specific cooling for sensible heat produced by multipurpose chillers, inverter chillers, free-cooling AHU, heat recovery | ≈ 30 % reduction of HVAC electricity (~300 MWh yr⁻¹ saved) | 
Process Cooling | Closed water loop with adiabatic dry coolers and variable-speed pumps | Energy overhead limited to < 10 %; water saving ~90 % vs. conventional | 
Waste-Heat Recovery | Reuse of recovered heat from data center and HVAC to supply nearby buildings | ≈ 1 GWh yr⁻¹ of thermal energy reused | 
Materials and Construction | Use of recycled aggregates, low-carbon concrete, PVC / PP pipes with ≥ 5 % recycled content | Embodied CO₂ reduction ≈ 5–10 % | 
Excavation Materials Reuse | 97 000 m³ excavated; ~14 000 m³ reused on-site; remainder sent to certified recovery sites | > 70 % reuse rate; reduced landfill waste | 
Greenhouse Gas Reduction | Elimination of SF₆ in MV equipment; recovery for RF circulators; refrigerants GWP < 675 | Near-zero direct GHG emissions | 
Water Management | Rainwater harvesting for toilets and irrigation; green roof SRI ≥ 76 | 30 % reduction in potable water use; stormwater control | 
Smart Control Systems | Building Management System (BMS) + PLC adaptive control for HVAC and cooling | Real-time optimization; predictive maintenance | 
Environmental Monitoring | INFN Environmental Report 2023 baseline; yearly updates and CO₂ footprint tracking | Continuous improvement and compliance reporting | 
Life-Cycle Assessment (LCA) | Comprehensive LCA under preparation with digital twin integration | Quantification of full lifecycle CO₂ and material footprint | 
Courtesy R. Ricci

## Slide 7
EuPRAXIA@SPARC_LAB
S-band Injector
X-band Linac
Plasma module
Undulators
AQUA Beamline
ARIA Beamline
Photon beamlines
17.5 m
33.5 m
9 m
28.5 m
54 m
Plasma chamber: 3.5 m
Plasma capillary: 0.6 m
Courtesy M. Del Franco

## Slide 8: Technological Readiness Level
Sub - systems | TRL | Comments |  |  |  |  |  |  | 
Injector | 9 | S-Band injectors are widely used in many facilities including SPARC_LAB. S-Band technology is fully available in the market. |  |  |  |  |  |  | 
X-Band Linac | 6 | X-Band Linacs are relatively new. Impressive progress has been made and the final testing of the acc. section full prototype will upscale the corresponding TRL level in the upcoming months. |  |  |  |  |  |  | 
Plasma Module | 5 | Extensive R&D has been made to validate the plasma capillary technology and solid results have proved the validity of the technical choice. A full system proven in a real environment is expected to be done in the next year |  |  |  |  |  |  | 
AQUA Undulators | 7 | Technology demonstrated in other facilities (FERMI, SwissFEL, etc.) |  |  |  |  |  |  | 
FEL Beamline | 8 | Most of the components of the photon beamline are implemented at other facilities are commercially available, few systems (needed only for a subset of possible experiments) are still in development |  |  |  |  |  |  | 
RF power system | 8 | X-Band RF power system has been already tested and operated in normal condition in the test-stand. The final operational test will prove the validity and reproducibility of the technical choices in the real setting |  |  |  |  |  |  | 
Laser system | 9 | Photocathode laser is now a proven technology tested in real facilities (including SPARC_LAB). The systems are full available in the market almost as off-the shelf products |  |  |  |  |  |  | 
General elements | 9 | Other elements (Control, mechanics etc) are based on standardized components daily used in other facilities and in other context (e.g. industrial context) |  |  |  |  |  |  | 
TRL LEVEL | TRL Description
TRL 1 | Basic principles observed – Scientific research begins to be translated into applied research and development (R&D).
TRL 2 | Technology concept formulated – The basic principles are explored and practical applications are identified.
TRL 3 | Experimental proof of concept – Active R&D is initiated, including analytical and laboratory studies to validate predictions.
TRL 4 | Technology validated in lab – Basic technological components are integrated to establish that they work together.
TRL 5 | Technology validated in relevant environment – The technology is tested in a simulated or relevant environment
TRL 6 | Technology demonstrated in relevant environment – A prototype system is tested in an environment similar to the operational one.
TRL 7 | System prototype demonstration in operational environment – A working prototype is demonstrated in a real operational setting.
TRL 8 | System complete and qualified – The technology is proven to work in its final form and under expected conditions.
TRL 9 | Actual system proven in operational environment – The technology is fully commercialized and operational in its intended setting.
Risk Mitigation: Two dedicated test facilities, SPARC_LAB and PLASMA_LAB, are actively supporting the development and validation of plasma acceleration concepts, while the TeX facility is dedicated to high power testing of X-band performance. Achieving a Technology Readiness Level (TRL) above 7 for these subsystems will only be possible following the successful operation of the EuPRAXIA@SPARC_LAB facility.

## Slide 9: The Italian Pillar: EuPRAXIA@SPARC_LAB User Facility
The facility aims to operate in two modes: a full-RF mode for initial commissioning, and a hybrid RF+PWFA mode that serves as a demonstrator for plasma-driven FELs user operation. Full-RF mode user operation is also possible.
The facility is expected to begin operations in 2031
•Moderate Energy with High Impact: Operating at around 1 GeV, will deliver Soft X-rays radiation in the “water window”.
•Compact Design: With an accelerating length shorter than 50 meters, it is the most compact facility in the soft X-rays list, at least by a factor 3.
•Technology Demonstrator: it will be also a strategic testbed for integrating advanced acceleration schemes and short period undulators into user-oriented FELs marking a paradigm shift toward compact and cost-effective light sources.

## Slide 10: Scientific Case and Applications
Application Area | Scientific Focus | Techniques | Key Impact
Renewable Energy | • Charge transport in solar cells & catalysts • Photocatalytic H₂ production • PFAS/PClAS analysis | XAS, XES, PI-MS | • Efficient solar materials • Clean hydrogen production • Environmental remediation
Warm Dense Matter (WDM) | • Extreme temperature/density • Astrophysics & fusion | Time-resolved XAS, TR-XES | • Stellar/planetary modeling • Fusion research support
Battery Technology | • Ion migration & interfaces • Solid-state battery study | XAS, non-linear X-ray spectroscopy | • Safer, longer-life batteries • High energy density
Structural Biology | • Live-cell imaging • Cellular processes (stress, DNA damage) | CDI, XAS, CEI | • Real-time biomolecular studies • Disease mechanism insight
Health & Radiobiology | • DNA damage by radiation | X-ray pump–probe, photo-fragmentation | • Radioprotection • Cancer treatment improvement
Atmospheric Chemistry | • VOC/NOx oxidation • Aerosol dynamics | PI-MS, ion spectroscopy | • Pollution models • Climate studies
Astrochemistry | • Radiation chemistry in space • Organic molecule formation | XAS, photochemistry | • Space molecular evolution

## Slide 11: 1st X band full scale prototype ready for high power test
D. Alesini, X-Band LINAC, 9° EUPRAXIA@SPARC_LAB TDR Review meeting, LNF 16-18 June 2025

## Slide 12: Plasma Accelerating Module
Courtesy A. Biagioni

## Slide 13
Plasma Accelerating Module

## Slide 14: The Driver-Witness Separator
The separation of the driver and witness beams is achieved by exploiting their different energies, using a magnetic chicane and a septum dipole.
In the first dipole, the deflection angle differs for the two beams due to their energy difference, resulting in a transverse separation that is preserved through the second dipole. As a result, between the second and third dipoles, the two beams propagate parallel to each other with a transverse offset.
At this point, a septum C dipole is inserted, with the transverse geometry schematically shown in figure below.
The 3D design of the septum dipole
Details of the field in the septum
plasma chamber
Capillary exit
Undulator entrance
Energy distribution of the Comb beam at the plasma exit
The 3D design of the driver-witness separator chicane
Twiss parameters for the witness beam along
the capture/separation transfer line
Courtesy L. Sabbatini

## Slide 15: Radiation Generation: FEL
Courtesy of L. Giannessi, F. Stellato
Notes: ARIA will include a 3m-long Apple 2 modulator, a dispersive section and four 2.2m-long Apple 2 radiators, as in the lower sketch, undulators analogous to those at Fermi.
The Aria beamline will work in seeded configuration adopting an OPA laser in different spectral region (320-400 + 600-800 nm), 200-400 fs duration and 20 uJ Energy.

## Slide 16: Convenzione con Regione Lazio
Protocollo di intesa: MUR – RL – INFN siglato nel dicembre 2024
Convenzione attuativa: RL – INFN firmata il 13.10.2025

## Slide 17: From the Agreement with the Lazio Region
Objective: Construction of the ARIA beamline and the equipment necessary to ensure its operation.
Budget: Total investment of €20M (€10M from regional POR FESR funds, €10M from INFN co-funds).
Project start: 01.10.2025
Project end: 31.12.2028
Organization into 5 macro-areas
  Electron transport (€5.3M)
  Undulator line (€6.0M)
  Photon transport (€2.2M)
  User experimental stations (€4.2M)
  Other project costs (€2.3M)
Courtesy of L. Sabatini

## Slide 18: ARIA: SEEDED FEL line – High-Gain Harmonic generation Full coherence = laser-like statistics
Wavelength range 50 – 180 nm – continuously tunable – 10-100 uJ pulse energy
Total physical length 20 m (not just magnetic) modulator – dispersive section – 4 radiators
Variable polarization (circular left/right, horizontal and vertical)
Design almost readily available. Could be ready for users since the first commissioning phase. Would contribute to establish a user community for the EupraXia at SparcLab user facility
Modulator
Dispersive section
Seed
Radiators
e-beam
Seed
modulated e-beam
nth harmonic radiation
Energy
Phase
initial beam phase space
Phase
Energy
Energy modulated beam
Phase
Energy
Density modulated beam
One of the higher order harmonics is amplified
Courtesy of L. Giannessi

## Slide 19: ARIA: a SEEDED FEL line in the long wavelength range (50-180 nm)
E-bunch shape flexibility: low charge short pulse operation mode – high charge long bunch mode
Synchronization with external lasers
Low e-beam temporal jitter
No other seeded FEL facility covers the range 50-180 nm, except fo the DALIAN light source (specialized in long pulses)
Superposition with HHG sources, but without their limitations on POLARIZATION, phot. energy tuning & intensity
Can be synchronized with HHG sources or external lasers for multicolor multi-pulse pump and probe operation
TWO Modes of operation: Long e-bunch (left) Short e-bunch (right)
Long-e bunch, low current – short seed.
Pulse duration at “long wavelengths”
limited by narrow gain bandwidth
(FERMI like, RF mode only)
e-beam
Seed
FEL
pulse
Short & high current e-bunch, long seed.
Pulse duration limited by e-bunch duration & large gain bandwidth
(EuPRAXIA Beam/Plasma mode)
e-beam
Seed
FEL
pulse
Courtesy of L. Giannessi

## Slide 20: Complementarity with FERMI*
ARIA
FERMI FEL-1*
FERMI
FEL-2*
AQUA
* In the FERMI 2.0 scenario (after FERMI upgrade)
248
4.1
24.8
2.48
49.5
8.2
λ (nm)
5
300
50
500
25
h𝜈 (eV)
150
1000
1500
2000
1.24
0.83
0.63
Higher order
Harmonics at FERMI

## Slide 21: ARIA beamline scientific case
Gas phase & Atmosphere
(Earth & Planets)
Aerosols
(Pollution, nanoparticles)
Molecules & gases
(spectroscopies, time-of-flight)
Proteins
(spectroscopies)
Surfaces
(ablation & deposition)
Photoemission spectroscopy
Photoelectron Circular Dichroism
Raman spectroscopy
Photo-fragmentation of molecules
Time of Flight Spectroscopy
Experimental techniques and typology of samples (& applications)
Courtesy of F. Stellato and F. Villa
50 m
Notes: We have considered to use FEL radiation for photoemission spectroscopy, Raman spectroscopy, time-of-flight spectroscopy, and photo fragmentation of molecules for different samples exploiting the peculiar characteristic of the radiation as the ultra-short length, peak brilliance.

## Slide 22: ARIA: Radiator Undulators two options:
Main features:
variable gap, variable phase for adjustable polarization (EPU) (six motors)
𝛌u = 55.2 mm, Np=42, Lu=2.4 m
working gap: 10 ÷ 32 mm
FERMI FEL-1 Radiator
Courtesy of Bruno Diviacco
APPLE-II Similar to FERMI FEL-1 radiators
built by KYMA in 2009-2010
APPLE X Similar to AQUA radiators
Prototype built by KYMA in 2022-2024 for SABINA
Main features:
variable gap, variable phase for adjustable polarization (EPU) – KRMS independent of polarization
𝛌u = 48 mm, Np=41, Lu=2.0 m
working gap: 10 ÷ 32 mm
(1)
(2)

## Slide 23: Project Cost, Timeline, and Management
The funds allocated by the Ministry have been gradually accumulated over the years and are now sufficient to launch the tender for the construction of the building, which also includes the 2026 allocation. They have been also partially used for R&D activities as support of the TDR preparation.
This situation leaves no financial margin for issuing additional tenders in 2026. Starting from 2027, the cash flow is expected to return positive, allowing the initiation of the procurement phase.
In the meantime, to mitigate the current financial constraints, potential synergies with the ARIA Beamline project will be explored, along with other possible funding sources, at least for the less resource-intensive items.

## Slide 24: Conclusions
EuPRAXIA@SPARC_LAB has reached an advanced design maturity, with most subsystems at TRL ≥ 7 and validated through dedicated test facilities. The TDR delivery is foreseen by February 3rd.
Infrastructure works are ready to enter the tendering phase
AQUA and ARIA beamlines will provide unique FEL capabilities from 4 nm to 180 nm, covering both seeded and SASE regimes with full polarization control.
The ARIA project, co-funded by Regione Lazio and INFN (20 M€), will be a strategic step toward the EuPRAXIA user facility.
The EuAPS project (X-ray betatron radiation source), funded under PNRR, is entering its final installation stage and aims to start operations by April 2026, marking the first step toward the EuPRAXIA plasma-based facility.
First FEL user operations are expected by 2031, establishing EuPRAXIA@SPARC_LAB as Europe’s first plasma-based FEL user facility for photon science.

## Slide 25
Thank for your attention

## Slide 26: AQUA beamline: Undulators
 | Units | PWFA | Full RF
𝜌 (3D) |  | 0.77 | 1.49
Saturation length |  | 20.5 | 20.0
Radiation wavelength |  | 4.0 | 4.0
Photon Pulse Energy |  | 16 | 156
Photon per pulse |  | 3.2 | 31.3
Photon Bandwidth |  | 0.4 | 0.5
Photon pulse length (rms) | fs | 1.0 | 14.1
 | Units | PWFA | Full RF
𝜌 (3D) |  | 0.77 | 1.49
Saturation length |  | 20.5 | 20.0
Radiation wavelength |  | 4.0 | 4.0
Photon Pulse Energy |  | 16 | 156
Photon per pulse |  | 3.2 | 31.3
Photon Bandwidth |  | 0.4 | 0.5
Photon pulse length (rms) | fs | 1.0 | 14.1
10 Apple X undulators for SASE FEL in the water window with variable polarization

## Slide 27: AQUA Beamline: Photon Beamline
GDM
Mirror
Aperture
Spectrometer
Filters
Radial ion. chamber area
Monochromator area
Split & delay line area
Gas absorber
K-B mirrors
Exp. Chamber area
BPM
GDM
BPM
GDM
Filters

## Slide 28: The Concept of User Facility in the EuPRAXIA Project
In the EuPRAXIA project, the user facility is conceived as a cutting-edge, distributed European research infrastructure that provides open access to advanced plasma-based accelerator technologies and associated beamlines. It is designed not only to serve the needs of the scientific community but also to act as a platform for innovation, integrating academia, industry, and technology developers. A distinctive element of the EuPRAXIA user facility is its commitment to open innovation, where collaboration between research institutions, industrial partners, and technology providers is central to the development and application of new accelerator concepts.
Mission | Serve a broad community of users in physics, material science, biology, medicine, and industrial applications through plasma-based electron beams and associated radiation sources.
Access | Open to external users (academic and industrial) through peer-reviewed proposals, ensuring scientific excellence and societal impact. Pilot user access is foreseen from 2031.
Distributed Model | EuPRAXIA is a distributed research infrastructure wich will operate through multiple nodes under a unified governance framework (AISBL) and coordinated access policy.
Beamlines & Instruments | Users will access beamlines including plasma-driven FELs, betatron and ICS X-ray sources, and ultrashort electron and positron beams.
Sustainability | Focus on energy efficiency (e.g., high-efficiency laser systems and RF modules), minimization of physical footprint through compact accelerator designs, and adherence to EU green transition objectives.
Data & Open Science | EuPRAXIA promotes open data policies and integration with the European Open Science Cloud (EOSC), enabling FAIR access to results and infrastructure services.

## Slide 29
Funded by the European Union
EuPRAXIA Scientific Goals
www.eupraxia-facility.org
Flagship Science Goal 2: EuPRAXIA will deliver betatron X rays with about 10^10 photons per pulse, up to 100 Hz repetition rate and an energy of 5-18 keV to users from the medical area. The much reduced longitudinal length of the X ray emission area (point-like emission) leads to an important improvement in image resolution compared to other techniques.
Flagship Science Goal 1: EuPRAXIA will deliver free-electron laser (FEL) X rays with 10^9-10^13 photons per pulse to user areas, covering wavelengths of 0.2 nm to 36 nm. The EuPRAXIA FEL pulses are naturally short (down to 0.4 fs) and will therefore provide users with tools for investigating processes and structures in ultra-fast photon science at a reduced facility foot print.
Flagship Science Goal 3: EuPRAXIA will deliver positron beams at energies from 0.5 MeV to 10 MeV and a repetition rate of 100 Hz for material science studies. Per pulse about 10^6 positrons will be produced in a time duration of 20-90 picoseconds on the sample, allowing time-resolved studies. EuPRAXIA will here advance the capabilities of existing positron sources in flux and time resolution.
Flagship Science Goal 4: EuPRAXIA will deliver electron and positron beams at energies from a few 100 MeV up to 5 GeV for high energy physics related R&D (detectors, linear collider topics). R&D goals include the demonstration of a linear collider stage, a "table top" HEP test beam and studies on positron transport and acceleration towards a linear collider.
Flagship Science Goal 5: EuPRAXIA will deliver photons from an inverse Compton scattering (ICS) source. The photons of up to 600 MeV and with narrow-band spectrum will enable precision nuclear physics and highly penetrative radiography for users.
Flagship Science Goal 6: EuPRAXIA will provide access to a multi-stage, high-repetition rate plasma accelerator in the GeV range to users from accelerator science. This R&D platform will allow the testing of novel ideas and concepts, full optimisation of a plasma collider stage, certain fixed target experiments (also in combination with lasers) and performance studies of conventional versus novel accelerator technology.
Flagship Science Goal 7: EuPRAXIA will provide access to cutting edge laser technology with short pulse length in combination with high energy photon pulses and short electron/positron bunches. Novel schemes of pump probe configurations and ultra-precise timing will be researched, feeding back into laser science.
  Free Electron Laser
  Betatron Radiation Source
  Positron Beams
  e+ / e- beams
  ICS Photon Beams
  High Rep. Rate Laser
  Laser Technology

## Slide 30: Applicazioni Principali di ARIA
Ambito | Applicazioni | Note distintive
Scienza dei materiali & Nanotecnologie | • Fotoionizzazione e spettroscopia fotoelettronica • Studio struttura elettronica • Nanofabbricazione e lavorazione materiali avanzati • Caratterizzazione superfici e semiconduttori | Radiazione VUV ad alta intensità e polarizzazione controllabile
Fotonica & Chimica | • Spettroscopia Raman e fluorescenza • Tecniche pump–probe multidimensionali • Interazioni luce-materia in condizioni estreme | Sincronizzabile con laser esterni e sorgenti HHG
Scienze della vita & Biologia molecolare | • Studi di dinamica molecolare • Reazioni fotoindotte biomolecole • Imaging e spettroscopia in soluzione acquosa | Impulsi ultracorti (<10 fs) ideali per processi femtosecondo
Chimica atmosferica & Ambientale | • Analisi gas rari e diluiti • Studio processi atmosferici e inquinanti (VOC, NOx) • Composizione chimica dell’aria | Esperimenti con campioni gassosi a bassa concentrazione
Industria & Tecnologie abilitanti (KET) | • Ottimizzazione processi produttivi • Sviluppo semiconduttori • Applicazioni in aerospazio e fotonica avanzata | Apertura a PMI e industrie hi-tech; trasferimento tecnologico
Fisica fondamentale & FEL science | • Studio generazione luce da fasci plasma-accelerati • Test nuove configurazioni seeded FEL • Operazioni multi-colore / multi-pulse | Unico FEL seeded 50–180 nm in Europa (complementare a FERMI e HHG)

## Slide 31
EuPRAXIA@SPARC_LAB
365 m
1.7 GeV
Undulator hall
159 m
45 m
Accelerator hall
Experimental hall
Lasers clean rooms
Laser and particle user rooms
Klystron & power supplies hall
Technical rooms
Preparations labs
1 (=>2+) GeV

## Slide 32: X-band linac structures
Describe the X-band accelerating module we want to implement in terms of:
  RF structure design and parameters (electromagnetic design, cooling, etc.)
  Waveguide components (DC, pumping, etc.)
  Expected performance (RF, vacuum, etc.)
  Supports
  Parameters of the power sources (with reference to the dedicated chapter)
Magnetic chicane layout and main parameters.
Quadrupoles and diagnostics
D. Alesini, X-Band LINAC, 9° EUPRAXIA@SPARC_LAB TDR Review meeting, LNF 16-18 June 2025

## Slide 33: ARIA Tuning range parameters
FEL
  Max harmonic = 10
  Undulator K-range from FERMI FEL-1:
  Kmax = 3.4 (CR), 4.35 (LV), 5.45 (LH)
Electron beam parameters:
  Energy 1.0 -> 0.7 GeV
  Energy spread 200 keV @ 0.8 kA -> 400 keV@1.5 kA
  e-beam duration:
    > 100 fs (long bunch mode, 200 pC)
    -> 8 fs (short bunch mode, 30 pC)
  beam emittance 2 mm mrad in long bunch mode/ 0.8 mm mrad in short bunch mode - beta function 10 m
Seed laser:
  We assume a minimum seed energy available in the range, of 20 uJ
  The seed spot size (average) is independent on the wavelength and is 0.5 mm^2
  Seed duration 400 fs (long seed) -> 200 fs (short seed), possibly no frequency chirp – i.e. seed spectral width close to FTL (not essential in short bunch mode)
With APPLE-II undulators

## Slide 34: EUPRAXIA Undulator Mechanical Model for ARIA (Courtesy of Mario Del Franco)
Derived from SABINA Undulator
KYMA (APPLE-X 1.3 m long modules, period 5.5 cm – 10 mm aperture)
Length 2 m, 4.8 cm period,
Polarization circular left, circular right, linear horizontal, linear vertical.
Symmetric field, in circular polarization same focusing strength on the two planes

## Slide 35: ARIA Seed laser option
TOPAS-PRIME tuning curves. Pump: 1 mJ, 100 fs, 800 nm. HE version is commercial and E > 10 uJ for the entire BW.
https://lightcon.com/product/topas-prime-opa/#performance
A
B
Courtesy of M. Galletti