## Slide 1: HV-CMOS Pixel Detector Demonstrator with Serial Powering and Innovative Interconnections Group meeting, Zoom, 23 October 2025
Attilio Andreazza Yanyan Gao
Università di Milano and INFN University of Edinburgh
CCF Project Proposal by
Birmingham, Bristol, Edinburgh, FBK, Heidelberg, Hochschule RheinMain, IHEP, KIT, Lancaster, Milano, Pisa, Torino, Trento

## Slide 2: Project proposal
This proposal aims to develop a large area HV-CMOS pixel detector demonstrator for large-scale production in future Higgs factory experiments, based on multi-chip modules with data aggregation and serial powering.
These multi-chip modules, including low-mass multilayer flexible PCBs, will then be integrated in staves, where modules will be powered in serial mode utilising the on-chip Shunt Low Drop Out (SDLO) regulators. Together with data aggregation, this will substantially reduce the number of stave data and power connections.
Low-mass aluminium flex productions, innovative connection methods (e.g. single-point Tape Automated Bonding), low-mass mechanical support, and efficient cooling technologies will be explored for overall system optimization in power and material budget.
The expertise gained by the participating institutes will be beneficial for the integration of future full-size devices that will be developed by the strategic DRD3 projects in the next few years
Available for comment in DRD3 CDS Repository: CERN-DRD3-PROJECT-2025-014

## Slide 3: Institutes and Contact Persons
Institute | DRD3 | RD50 | Project contact
University of Birmingham | x | x | James Glover
University of Bristol | x |  | Jaap Velthuis
University of Edinburgh | x |  | Yanyan Gao
University of Heidelberg | x |  | Heiko Augustin
Hochschule RheinMain | x |  | Daniel Muenstermann
IHEP | x | x | Yiming Li
INFN and University of Milano | x |  | Attilio Andreazza
KIT | x |  | Ivan Peric
University of Lancaster | x | x | Harald Fox
INFN Pisa | x | x | Fabrizio Palla
FBK Trento | x | x | David Novel
TIFPA and University of Trento | x |  | Roberto Iuppa
INFN Torino | x | x | Stefania Beolé
Participating institutes | 13 | 6 | 
Expression of interest also from Oxford and Syracuse

## Slide 4: Project motivation: Higgs Factories
Barrel Endcap
The IDEA detector concept for FCC-ee
arXiv:2502.21223
Silicon tracking in different regions (IDEA concept shown here, but general considerations are valid for all layouts)
inner vertex detector (R=1.4-3.3 cm)
  3-5 mm resolution, O(200 MHz/cm2), very low material
outer vertex detector (R=13-31 cm)
  ~7 mm resolution, 27 ns timestamp, O(40 kHz/cm2)
  material is a concern
silicon wrapper/TOF (R/z = 200 cm)
  ~7 mm resolution, 27 ns timestamp
  100 m2 (2 layers): ~2.5 105 chips, ~100 kW power

## Slide 5: Project motivation: service integration
Distribution of power and data signals along the local supports
serial powering to reduce dissipation on the distribution lines
minimize the number of connections
Read-out units are:
multi-chip modules (example 2x2 quad modules)
(or large stitched detectors)
Minimal I/O connection on chip requires:
Serial powering chain: all biases generated internally by shunt-LDO regulators
  1 LV and 1 HV line per "stave"
chip-to-chip data transmissions: local data aggregation on module
  1 data-out per "module"
LVDS module configuration with clock data recovery
  1 data-in per module
No current detector providing all these features
Reducing material by developing PCB with Al as conductor
Power IN/OUT
Data IN/OUT
HV

## Slide 6: Low mass mechanical support
Low mass stave prototype
  long barrel layout (1332 mm length)
Light support structures
  water jet truss cutting and structure assemblying
  design checked by FEA
  support constructed and tested in Pisa
Low-mass cooling interface
  carbon cold plate
  2 mm diameter Kapton cooling pipes for water cooling

## Slide 7: Module testing setup
LVDS signals
Detector
GND
Detector
Vin
Power pigtail
Data pigtail
DAQ
GND
DAQ
VDD +3.3V
DAQ
VDD +1.8V
GECCO, flexible readout system developed by KIT
Firmware and sofware adapted to module operation
Adapter card splitting the two power domains
LVDS signals decoupling on the flex PCB

## Slide 8: Project goals
Demonstrate the operation of a CMOS based multi-chip module SP chain in realistic environment
  verifying the chip SLDO performance in multi-chip/module setups, establishing multi-module SP chain DAQ systems
  assessing the feasibility of power bus based on Aluminum conductor
  producing low mass cooling and mechanical supports.
  Many components for this stage are either existing or in advanced R&D stage from previous projects, such as ATLASPix3.1 based quad-chip modules with 150𝜇m thickness being assembled by Edinburgh and Milano, a long mechanical support stave from FCC-ee R&D from Pisa, 50𝜇m thick ATLASPIX3.1 sensors in Heidelberg.
Increase the level of integration above the ATLASPix3.1: Explore high density aluminum flex PCB production and innovative interconnections
  This stage will exploit new sensors to be submitted in LF 150 nm technology around September- December 2025 (led by KIT)
  DAQ systems of the participant institutes will also be upgraded accordingly.

## Slide 9: Stage 1 Completion
Assembly modules with remaining ATLASPIX3.1 chips
  ~6 modules with 150 mm sensors probed by Milano/Edinburgh
  50 mm sensors available from Heidelberg
  Either pick-and-place or dedicated jig
Designed a power bus to test a multi-module serial power chain
  Aluminium conductor to reduce thickness in radiation lengths
  Connecting to modules by pigtails
  4 cm×60 cm size to match CERN Microfabrication Lab capability
  Received quotation from Rui De Oliveira: 14,200 CHF for a panel (5-8 pieces)
  Ready to start production, since module operation issues are solved
Loading of cold plate (half stave with 3 modules + heaters)
  Need tooling for loading and instrumentation for assessing thermal performance
End of stave side
Last module side

## Slide 10: Stage 2 sensors
Need new sensor since ATLASPIX3.1 chip are out of stock
Testing multi-chip integration does not require a chip but a CHIP
  ≥1 cm2 to simplify handling and providing a significant load
Specific features for system level integration, not usually implemented during early sensors R&D
  SLDO for serial powering
  command decoder with clock data recovery
  chip-to-chip data transfer
KIT is planning a submission in LFoundry 150 nm process later this year
  Migration into this technology of KIT TSI/AMS 180 nm designs
  Large die, either half (2 cm2) or full reticle size (4 cm2)
  SLDO from the TSI/AMS design implemented in LF 150
  If contribution from this CCF project, daisy chain of chip data could be implemented
    IP already developed for an ATLASPIX4 prototype run in TSI
  Wish to book some wafers to be dedicated to integrations studies
} already tested on ATLASPIX3.1
} not available on ATLASPIX3.1
} not tested on ATLASPIX3.1

## Slide 11: Stage 2: FBK technology
Fabrication process inspired from the state-of-art LTU-Kharkiv [DOI: 10.15407/fm24.01.143]
Processing inside FBK cleanrooms
Kapton-Al PCBs
  20 mm Al thickness
  25 Kapton thickness
  Wafer level manufacturing (6" wafers)
Feature size
  minimal size is 2×Al thickness = 40 mm
  very high line density (90 mm pitch)
Interconnection
  spTAB 75×75 mm tool tip
  flex-to-chip TAB
  flex-to-flex TAB:
    use TAB as vias to reduce overall material
    connection to additional flexible PCB

## Slide 12: Stage 2 planning
Submission and production of LF generic R&D chips
Thinning of sensors to samples of 150 and 50 mm thickness
Design and production of multi-chip module PCB for LF sensors:
  Requires sequential steps in understanding and verification of chip behaviour:
  Test of chips on single-chip-carriers, to define the operating point, minimal amount of signal, wire bonding and register configuration
  Copper based version, standard wire bonding, to verify the schematics and operation of the multi-chip modules
  Low-mass Aluminum based using FBK technology, implementing tab bonding
Assembly and operation of SP chain with multi-chip modules
  Daisy chaining of modules through adapter cards
  Interface to DAQ system
Realization of an integrated power bus and multi-chip module PCB
  Major step with respect to the separate structure with power bus and module PCB as separate pieces, connected by pigtails
  May test some of the chip-to-flex attach technologies being developed in WG7

## Slide 13: Deliverables and timelines
Deliverable | Timeline
Multi-chip module construction and readout (ATLASPix3.1) | 06/2025
Al-flex production for ATLASPix3.1 power bus | 09/2025
ATLASPix-based SP chain prototype construction and characterisation | 03/2026
Submission and production of new CMOS sensors (LF) | 07/2025-03/2026
Multi-chip readout flex submission for the LF CMOS sensors | 12/2026
Multi-chip LF module construction and readout | 03/2027
Al-flex production for the LF CMOS sensors | 09/2027
LF sensors based SP chain prototype construction | 01/2028
LF sensors based SP chain prototype evaluation | 03/2028

## Slide 14: Cost estimation
Total project cost: 107,000 CHF
  DRD3 CCF contribution (13 institutes × 2650 CHF) 34,450 CHF
  RD50 CCF contribution (6 institutes× 2650 CHF) 15,900 CHF
  Funding from participating institutions 56,650 CHF
Procurements | Cost (CHF)
Al Serial Power Bus for ATLASPIX 3.1 (CERN) | 15,000
Cu Multi Chip Module Flex LF sensors (design verification) | 5,000
Al Multi Chip Module Flex LF sensors (FBK) | 15,000
Al Serial Power Bus for LF sensors (CERN) | 15,000
DAQ Upgrades (FPGA, chip carriers and readout boards) | 15,000
Chip-to-Module assembly jigs | 2,000
Stave loading and test equipment | 10,000
CMOS Wafers production and processing (thinning and dicing) | 20,000
Total project cost: | 107,000

## Slide 15: Institutes' Contribution
Total project cost: 107,000 CHF
  DRD3 CCF contribution (13 institutes × 2650 CHF) 34,450 CHF
  RD50 CCF contribution (6 institutes× 2650 CHF) 15,900 CHF
  Funding from participating institutions 56,650 CHF
Procurements | Institute | Contribution (CHF)
Al Serial Power Bus for ATLASPIX 3.1 (CERN) | Milano (in-kind) | 15,000
Cu Multi Chip Module Flex LF sensors (design verification) | IHEP ? | 5,000
Al Multi Chip Module Flex LF sensors (FBK) |  | 
Al Serial Power Bus for LF sensors (CERN) |  | 
DAQ Upgrades (FPGA, chip carriers and readout boards) | Each institute its own DAQ | 15,000
Chip-to-Module assembly jigs |  | 
Stave loading and test equipment | Pisa (in kind) | 8,000
CMOS Wafers production and processing (thinning and dicing) | Lancaster+Edinburgh | 15,000
Total project cost: |  | 56,000

## Slide 16: Conclusions
Future experiments will need to develop large tracking systems with low-mass services (both electrical and thermal) and efficient power distribution and data handling
In particular there is an increase in interest in the deployment of Aluminum conductor flexible PCB
This Common Project aims to gather groups already addressing this topic in different experiments
  timescale for some experiments is not far away
  prototyping solutions for system issues in parallel to sensor development
  share information about Al flexible PCB vendors
  stimulate the development of IP implementing features for system level integration also in the developing projects within DRD3-WP1
  cost benefit from synergies with already running projects

## Slide 17: backup

## Slide 18: Module assembly
I-V test for HV functionality under probe station before assembly
  failure mode observed during the production of quad modules with direct powering
  a short on one chip may jeopardize the operation of the other chips in the module
Finetech pico die bonder
  used also for the assembly of ATLAS ITk 3D modules
  manual optical alignment between chips and flex-hybrid
Araldite 2011 deposited by stamps method on flex backside
Flex holder
Chip carrier
Diode IV curve

## Slide 19: CMOS modules (1)
Prototyping with ATLASPIX3.1 sensors
  TSI 180 nm CMOS process
  Almost full-reticle size 2 × 2 cm2
  150 mW/cm2
Multi-chip modules
  Single LV and HV bias line
  Common data-in LVDS lines: command, clock, synch, trigger
  Individual modules data-out LVDS lines
  AC coupling to DAQ
Possible to build a serial powering chain
Probing of SLDO operation before assembling

## Slide 20: CMOS modules (2)
The serial powering chain for two modules
  "test modules" with 1 and 2 chips respectively
Each module has an individual regulation process
  1-chip module
    VDDD/A = 1.99/1.97 V
    @ 350 mA
  2-chip module
    VDDD/A = 2.04/2.00 V
    @ 700 mA
1-chip module starts regulating
2-chip module starts regulating

## Slide 21: ATLASPIX3.1 Wafer 6 Probing
Initial probing setup was not testing correctly the VDDD regulator: needle configuration changed in March
The VDDA is regulated at 2.1 V after ~250 mA input current
The VDDD is regulated at 2.1 V after ~150mA input current
Large voltage drop is an issue of the testing setup (long cable and needle contact resistance)
Tested all chips from wafer #6
  11/48 show anomalous behaviour
  Large sensor power consumption
  Does not turn on even at rather high bias currents
  Chip selection critical since module yield is chip yield to the 4th power
Normal sensor
Defective sensor

## Slide 22: Source Scan
Quad module – 3: single wire bonded chip
Fixed wire bonding diagram to have proper setting of configuration pins
Configuration and operation shows the decoupling scheme implemented on the hybrid has good performance
Measurement with 90Sr beta source
Full 132x372 pixel matrix
Pulse height measurement with ToT

## Slide 23: ATLASPIX3
ATLASPIX3 general features
  TSI 180 nm HVCMOS technology
  full-reticle size 20×21 mm2 monolithic pixel sensor
  200 Ωcm substrate (other substrates up to 2 kΩcm also possible)
  132 columns of 372 pixels
  pixel size 50×150 μm2 (25×150 μm2 on recent prototypes)
  breakdown voltage 〜-60 V
  up to 1.28 Gbps downlink
  25 ns timestamping
  analog pixel matrix, digital processing in periphery
Both triggerless and triggered readout modes:
  two End of Column buffers
  372 hit buffers for triggerless readout
  80 trigger buffers for triggered readout

## Slide 24: ATLASPIX3 Serial Powering
shunt

## Slide 25: Risk assessment (What if...?)
LF submission will not provide suitable chips
  hold some ATLASPIX3.1 chips till result of submission is known
  perform stage 2 with P2Pix sensors
  "digital modules" using RD53 pixel chips for HL-LHC (no physical signal, electrical only test – too high power consumption)
Do not get INFN funding for FBK flexible PCB production
  build module flex with standard wire bonding technique
  explore another vendor

## Slide 26: Si tracker: system considerations
Complete system consists of 900'000 cm2 area / 4 cm2 chip = 225k chips (56k quad-modules)
  aggregation of several modules for data and services distribution is essential
  inner tracker will be 5--10% of this
Data rate constrained by the inner tracker
  average rate 10-4 - 10-3 particles cm-2 event-1 at Z peak
  assuming 2 hits/particle, 96 bits/hit for ATLASPIX3
  640 Mbps link/quad-module (assuming local module aggregation) provides ample operational margin
  16 modules can be arranged into 10 Gbps fast links: 3.5k links
    can also assume 100 Gbps links will be available: 350 links
DAQ architecture
  triggerless readout will fit the data transmission budget but requires off-chip re-ordering of data
  triggered readout will be simpler and would also reduce the bandwidth occupancy
Power consumption
  ATLASPIX3 power consumption 150 mW/cm2
  600 mW/chip → 2.4 W/module → total FE power 130 kW
  additional power for on detector aggregation and de-randomizations ~2W/link