## Slide 1: DELPHES Tracking Update
Previous implementation
  Issues
Kalman filter implementation
  Validation
F. Bedeschi,
RD_FCC collaboration meeting
Bologna, December 2025
Outline

## Slide 2: In a nutshell
Calculate track parameters and momentum at origin
Calculate parameter covariance matrix C = Cov(from simplified geometry (cylinders and disks only)
Randomize parameters according to C
Key point is how C is obtained

## Slide 3: Old implementation (1)
The track trajectory is a function of the track parameters
, s) where s is a phase along the trajectory
  Intersection of the trajectory with measurement layers generates a set of N measurements *
  Predicted values are calculated from and the layer geometry
    This relation is non-linear  linearize from approximation of *
Given the error matrix S = Cov(*) minimize the χ2:
Parameter covariance from S and A:

## Slide 4: Old implementation (2)
Measurement covariance S = D + M
  D = diagonal with detector resolutions
  M = contributions from multiple scattering (not diagonal)
M is from parameter variations due to MS at each layer i

## Slide 5: Issues
Inversion of S is expensive (dimension > 100)
  So initialize grid of C(pt, q) at D=0, z0=0
    Get C from bilinear interpolation for tracks inside beam pipe
    Do full calculation only for tracks outside beam pipe
Draw backs:
  C is mostly an approximation (good though!)
  Cannot include mass dependance of MS
    Affects low momentum tracks
  Cannot include single layer efficiencies

## Slide 6: Kalman method (1)
Preamble - Can prove that:
  Ignoring MS:
    The full fit is equivalent to adding one measurement at a time starting from outside and moving in
  Effect of adding the MS contribution of a scattering layer below the last measurement used
  where C0 is the track parameter covariance before including the effect of MS

## Slide 7: Kalman method (2)
Implementation:
  Loop on all layers starting from the last measurement layer outside
    If “measurement” update the covariance matrix accordingly
    Add layer MS contribution for any layer type
Summary:
  Method is fast: involves only inversion of 5x5 matrices
  NO approximations for all tracks
  Easy to implement efficiencies: just decide when using a measurement
  Mass dependance properly included since covariance is recalculated for each track

## Slide 8: Verification: pt scans
Standard Method
Kalman Method

## Slide 9: Verification: angle scans
Standard Method
Kalman Method

## Slide 10: Concluding
Few fixes
  Minor fixes for special cases not used in DELPHES
  Fixed error on second order correction to MS angle
Updated geometry to match full sim
Links to github:
  Official DELPHES: https://github.com/delphes/delphes
  My fork: https://github.com/fbedesch/delphes
  Standalone: https://github.com/fbedesch/Kalman-tracking
Latest version now included in official DELPHES