## Slide 1: Positioning and Orientation System of KM3NeT
Position of the Detector (absolute) Position of seafloor assets (absolute) | <100 m 5 m | n source determination detector construction | Navigation and Absolute Acoustic Positioning System
Absolute orientation of the Detector | 0.2° | n source determination | CR Moon/Sun Shadow
Positioning of DOMs (relative) | <20 cm | detector angular resolution (event direction reconstruction) | Relative Positioning System
Orientation of DOMs (relative) | <9° | detector angular resolution (event direction reconstruction) | Compasses CR Moon/Sun Shadow
Requirements

## Slide 2: Positioning System of KM3NeT: Requirements
Relative lepton track direction | Measure relative positions of DOMs | Relative Acoustic Positioning System
Angular resolution <0.2° | Resolution 20 cm | 

## Slide 3: Relative Acoustic Positioning System (RAPS)
GPS
LBL transceivers
Detection Unit
Hydrophone
White Rabbit Switch Fabric
100 km cable
Synchronise thousands of light sensors, displaced in a km3 volume, 100 km from the coast 1 ns accuracy:
  White Rabbit time precision protocol over Ethernet
Monitor the position of the structure with 10 cm resolution:
  Positioning system synchrnoised to GPS, auto-calibrating LBL. C sound Measures, Electronic latency of each device measured

## Slide 4: Navigation and Absolute Acoustic Positioning System: ORCA
Ramses range meter
RTA61 acoustic releasable transponder
Absolute position of the LBL elements is provided by NAAPS (Navigation and Absolute Acoustic Positioning System):
Provides Geo-referenced positions of DUs
Provides absolute position of LBL elements of RAPS
Nominal Accuracy: ~ 2 meters

## Slide 5: Navigation and Absolute Acoustic Positioning System: ARCA
Commercial USBL (Sonardyne or Kongsberg)
Available on ships used for the deployments
USBL transponder (Applied Acoustics midi, series 1000

## Slide 6: Relative Acoustic Positioning System (RAPS)
Continuous monitoring of the DOMs positions is a mandatory requirement for an accurate direction reconstruction
In KM3NeT the positions of the DOMs are recovered through a relative acoustic positioning system (RAPS) composed of three main sub-systems:
A Long Base-Line (LBL) of acoustic transmitters (beacons) and receivers, located at known positions
An array of digital acoustic receivers (DARs) installed along the detection units (DUs) of the telescope
A farm of PCs for the analysis of acoustic data
Acoustic emitter signals must be detected up to distances of 1 km
20 kHz – 50 kHz
20 kHz – 50 kHz
Suitable frequency range: 20 -50 kHz
Lowest level of PSD: ~40 dB re 1 uPa2/Hz
Attenuation: 1-10 dB/km
Sweep Signal

## Slide 7: Relative Acoustic Positioning System (RAPS)

## Slide 8: RAPS: Acoustic Beacon
Signal Emitted length:
from 0 to 50 ms (typical 5 ms)
Maximum emission amplitude:
180 dB @ 34kHz re 1 μPa at 1 m
Type of acoustic signals:
Monochromatic signals configurable from 1 kHz to 80 kHz
Sine Sweep signals configurable from 20 kHz to 40 kHz (typical 2 kHz range)
Maximum Length Sequence (MLS) signals with lengths from 5.12 ms to 40.96 ms (at 200 ksamples/s)
The commercially available piezo-ceramic Free Flooded Rings (FFR) transducers SX30 from Sensor Tech Ltd have been chosen for LBL beacons. Each beacon can be reconfigured via a dedicated RS232 connection for “in situ” optimization of the signal detection. The signal emission trigger is synchronized with the detector master clock with calibrated time delay of 7±1 µs.
LBL emitters can be also operated as autonomous emitters.
In this case, the Time of Emission (ToEs) is recovered from the Time of Arrival (ToA) of the pulses to the hydrophones at DU bases (fixed positions), knowing the distance between emitter and receivers, and the sound velocity.

## Slide 9: RAPS: Hydrophones in DU Bases
Digital hydrophones are hosted on the base of the DUs. These ‘external’ hydrophones are used to calibrate the LBL by measuring the relative distance among LBL elements. The selected hydrophone is the DG0330 manufactured by Colmar s.r.l.. It consists of a spherical piezo-ceramic element read-out by an analogue board, splitting the signal in two lines with different gains (+46 dB and +26 dB respectively).
Sampling frequency : 195312.5 Hz
Resolution: 24 bits
Dual Gain
All hydrophones calibrated in pressure sensitivity and directionality
Hydrophone data embedded in the Base data packet:
Time stamped by White Rabbit
Time Latency 5 ±1 µs

## Slide 10: RAPS: Hydrophones in DU Bases
Hydrophone location in DU

## Slide 11: RAPS: Long Baseline (LBL)
To provide relative DOM positioning with an accuracy of about 20 cm, the relative position of the LBL elements must be known with an accuracy of the same order.
Auto-calibrating Long Baseline of acoustic emitters and hydrophones
Autocalibration procedure based on range measurements (knowing the sound velocity in situ)
Iterative algorithm → starting point: nominal position provided by NAAPS
Constraint: fixed hydro-emitter distance in Calibration bases
Output: positions of each LBL element, quality factor (sum of squared residuals)
ToE= mean (ToA – range ・csound)
The system is determined if N >= 5
x-corr (library of beacon signals)

## Slide 12: RAPS: Long Baseline (LBL)
ToE: Autonomous Beacons

## Slide 13: RAPS Long Baseline: Status
Current Acoustic Positioning System (APS):
3 autonomous acoustic emitters (tripods)
Emission rate : 10 minutes (12 pulses /cycle – interpulse interval 5 s)
1 piezo sensor for each DOM
ARCA (DU1): no hydro in base. Use DOM 1
ORCA (4 DUs): hydros in 3 bases
ORCA full configuration

## Slide 14
RAPS Long Baseline: Status

## Slide 15: RAPS: Piezo in DOM
The movement of the DUs due to underwater currents is monitored thanks to “internal” piezo-electric Digital Acoustic Receivers (DAR) glued from the inside to the glass sphere of each KM3NeT Digital Optical Module (DOM)
The nominal sensitivity of the sensors is - 160 ± 6 dB re 1V/μPa at 50 kHz with a ± 3 dB variation (long time average) in the range 10 ÷ 70 kHz.
Tests in anechoic acoustically insulated pool at TNO: characterize acoustic behavior of the DOMs in water

## Slide 16: RAPS: DAQ and Control Chain

## Slide 17: RAPS: TOA Output data Format
RUN_number | Detector_ID | DOM_ID | DU_number | floor_number | pos_x | pos_y | pos_z | UTC time | displacement_wrt_nominal_position

## Slide 18: ToA Estimation

## Slide 19: RAPS: Multilateration
System of N equations in 3 variables (N=number of emitters in operations)
Hydro–receivers range = ToF*sound velocity
Variables = [DOM_x, Dom_y, DOM_z]
The algorithm finds the DOM coordinates that minimize the sum of squares of equations
System is over-determined if the number of emitters is >3
DOM positioning algorithm includes the dependency of the sound velocity on the the depth
In first approximation at very deep sea
Effective sound velocity (beacon-receiver) =
a=Δc/Δz ~ constant in deep sea
a・DOMz / [ln(cemitter +a・DOMz )−ln cemitter]

## Slide 20: Relative Acoustic Positioning System (RAPS)

## Slide 21: RAPS: DU Line Fit
In order to recover the position of missing/not working DOMs and improve the RAPS resolution a DU line fit procedure has been developed:
V0(Basic): Filter anomalous RAPS data 3D and Bezier Fit of DU
V1: Filter anomalous RAPS data, include compass data, recover effective current, Fit line using a DU mechanical model

## Slide 22: Multidisciplinary Science with KM3NeT acoustic elements
In the KMNeT APS all data acquired by the acoustic receivers are transmitted to shore at 195 kHz/24 bit for the real-time identification of the acoustic beacon pulses.
Thanks to the KM3NeT data acquisition architecture the acoustic data stream can be also addressed to other software tools for other purposes ( acoustic neutrino detection, bio-acoustics, geophysics,..).

## Slide 23: Towards Acoustic Neutrino Detection
Acoustic Data from the telescope will be immediately duplicated for further analysis:
Acoustic-Optical trigger for neutrino events
Dedicated biological triggers

## Slide 24: Tilt and Compass board
DOM Orientation in KM3NeT is recovered using custom compass boards interfaced with the detector electronics (CLB)
We use the AHRS (Attitude Heading Reference System) to recover DOM
“yaw”, “pitch” and “roll” from 3-D magnetometers and 3-D accelerometers data.
Each board is equipped with 3D accelerometer (tilt: pitch and roll)) and magnetic gauge (compass)
Raw data are sent to shore and analysed taking into account the calibration coefficients of each compass.
Compasses cannot be calibrated in situ (the DU cannot be rotated in water!)
Calibration of the compass before deployment plays a fundamental role
The LNS-AHRS board
The LSM303 board

## Slide 25: Tilt and Compass board: calibration
Each compass mounted in the CLB board and calibrated (hard iron correction)
After DOM integration the compass (inside the DOM) is tested
Acceptance criteria: error less than 3.5° wrt to each cardinal direction
Compass calibration: wobbling
Correct hard iron effects
Compass yaw check after DOM integration.
Rotation of DOM in the horizontal plane
Gyro-gimbal for AHRS calibration
Before integration of CLB in DOM

## Slide 26: Tilt and Compass board: preliminary results
In-plane calibration
DU2 F4, F5
DU3 F3, F11
DU4 F16
No Calibration or old fw
DU2 F9, F12:F18
DU3 F17
DU4 F15

## Slide 27: Calibration Units: Calibration Base
Dedicated assets called Calibration Units will be deployed to:
deploy triggered beacons and hydrophones at the rim of the detector
connect oceanographic instruments to measure sound velocity in situ in real time
ORCA Calibration Base
ARCA Calibration Base

## Slide 28: Calibration Units: Instrumentation Unit
ORCA Instrumentation Unit Anchor
ARCA Instrumentation Unit Anchor
Instrumentation Units are recoverable assets equipped with inductive instruments hosting
CTDs (SBE SIP ODO)
SV meters (Valeport mini SVS)
current meters (Aanderaa DCS or Aquadopp)
absolute pressure gauges (Digiquartz)