## Slide 1
Frontend Electronic Update
For outer Layers of SuperB (L.4 & L.5)
Team: Luca Bombelli, Bayan Nasri, Carlo Fiorini, Paolo Trigilio

## Slide 2: TOT and TS characteristic
Peaking Time = 1us
TOT = 4 bits
TOT clock = 4.25 MHz
Analog TOT
“Analog” TS
Digital TOT
TS

## Slide 3: Phase error of TOT clock when TOT should count “1”
220ns
0
1
2
Max error = 220ns
(including only Phase error of TOT clock)
Peaking Time = 1us
TOT = 4 bits
TOT clock = 4.25 MHz

## Slide 4: Phase error of TOT clock when TOT should count “0”
Peaking Time = 1us
TOT = 4 bits
TOT clock = 4.25 MHz
110ns
0
1
Max error = 110ns
(including only Phase error of TOT clock)

## Slide 5: Timing Resolution with TOT – Time correction with phase error
Peaking Time = 1us
TOT = 4 bits
TOT clock = 4.25 MHz
Max Error = 160ns
Max Time window = 250ns
(including time-walk and TS)
Time Error rms = 72ns
(smallest signal only)
160ns
250ns

## Slide 6: Timing Resolution with TOT – Time correction with phase error
Peaking Time = 1us
TOT = 6 bits
TOT clock = 17.8 MHz
Max Error = 50ns
Max Time window = 87ns
(including time-walk and TS)
Time Error rms = 25ns
(smallest signal only)
87ns

## Slide 7: Timing Resolution with TOT
Peaking time [ns] | TOT bit | TOT clock [Mhz] | Max Time window [ns] | Time Error rms [ns] | Preliminary Jitter for 1 MIP [ns] | Preliminary Jitter for 0.3 MIP [ns]
375 | 4 | 11.3 | 114 | 33 | 10.3 | 34.6
 | 6 | 47.5 | 54 | 15 |  | 
500 | 4 | 8.5 | 141 | 41 | 12.7 | 43.3
 | 6 | 35.7 | 60 | 17 |  | 
750 | 4 | 5.66 | 196 | 56 | 17.6 | 60.3
 | 6 | 23.8 | 74 | 21 |  | 
1000 | 4 | 4.25 | 250 | 72 | 22.9 | 77.9
 | 6 | 17.8 | 87 | 25 |  | 

## Slide 8: Combining the 2 effect
Peaking Time = 1us
TOT = 4 bits
Signal 0.3 MIP
time
distribution
Error from TS clock and time walk
“Max Time window” = 250ns
time
distribution
Jitter form noise
Jitter for 1 MIP; sigma = 77.9ns
time
distribution
Resulted distribution.
Proposal 1: find the “Off line windows” that include 99% of the cases.
Proposal 2: approximate “Max Time window” as Gaussian and quadratically sum the sigma
Off line windows
Cumulative distribution function
Normal function
99%

## Slide 9: Efficiency simulation: results
Layer | Peaking time [ns] | Rate [kHz] | Efficiency | Efficiency (x 5 safety factor)
0 (side 1) | 25 | 186.6 | 99.3% (99.1) | 96.7% (95.5)
1 | 100 | 169.6 | 97.7% (97.9) | 88.6% (88.9)
2 | 100 | 133.6 | 98.0% (98.0) | 89.8% (90.3)
3 | 200 | 116 | 94.7% (94.8) | 76.1% (76.5)
4 | 500 (complex poles) | 25 | 97.8% | 89.1%
5 | 1000 (complex poles) | 16.22 | 97.1% | 86.1%
Phi strips
(From Lodovico)

## Slide 10: Efficiency simulation: results
Layer | Peaking time [ns] | Rate [kHz] | Efficiency | Efficiency (x 5 safety factor)
0 (side 2) | 25 | 187.4 | 99.6% | 98.2%
1 | 100 | 134.2 | 97.4% | 87.4%
2 | 100 | 133.4 | 97.4% | 87.6%
3 | 200 | 79.4 | 97.0% | 85.6%
4 | 500 (complex poles) | 13.42 | 98.5% | 92.6%
5 | 1000 (complex poles) | 8.78 | 98.1% | 90.6%
Z strips

## Slide 11: Efficiency simulation: results
Layer | Peaking time [ns] | Rate [kHz] | Efficiency | Efficiency (x 5 safety factor)
1 | 50 | 169.6 | 98.9% | 94.3%
 | 75 |  | 98.3% | 91.4%
2 | 50 | 133.6 | 99.0% | 95.0%
 | 75 |  | 98.5% | 92.4%
3 | 100 | 116 | 97.3% | 87.3%
 | 150 |  | 96.1% | 81.5%
4 | 375 | 25 | 98.4% | 91.8%
5 | 500 | 16.22 | 98.5% | 92.8%
 | 750 |  | 97.8% | 89.4%
Phi strips – shorter peaking times
Note: Real poles for L1-L3
Complex poles foer L4-L5

## Slide 12: Efficiency simulation: results
Layer | Peaking time [ns] | Rate [kHz] | Efficiency | Efficiency (x 5 safety factor)
1 | 50 | 134.2 | 98.7% | 93.6%
 | 75 |  | 98.1% | 90.5%
2 | 50 | 133.4 | 98.7% | 93.6%
 | 75 |  | 98.1% | 90.6%
3 | 100 | 79.4 | 98.5% | 92.6%
 | 150 |  | 97.8% | 89.0%
4 | 375 | 13.42 | 98.9% | 94.4%
5 | 500 | 8.78 | 99.0% | 95.3%
 | 750 |  | 98.6% | 93.0%
Z strips – shorter peaking times
Note: Real poles for L1-L3
Complex poles foer L4-L5