## Slide 1
Control Systems
Andrea Michelotti
INFN-LNF • Accelerator Division

## Slide 3
telemetria

## Slide 4
A Control System is a system that allows the output variables of a process to be varied (or kept constant) according to predetermined laws.
Open loop
Action is based on initial static information.
Closed loop
Action is based on dynamic information continuously read back from the controlled system.
Notes: Leggi prestabilite > Open Loop, Closed Loop

## Slide 5
Key elements of a Control System:
actuators
sensors
control algorithms

## Slide 6
Controls adopting "CPUs"
Virtual
Machines
uP: microprocessor
t ~ 1 ms
ASIC: Application-Specific Integrated Circuit
FPGA: Field Programmable Gate Array
t ~ ns
Computers t ~ 1-10 ms
PC
Embedded processor
SBC: Single Board Computer

## Slide 7
plant

## Slide 8
plant → sensors/actuators

## Slide 9
plant → sensors/actuators → front-end

## Slide 10
plant → sensors/actuators → front-end → control room

## Slide 11
General characteristics
Open and interoperable with other systems (e.g., experiments, DAQ, machine protection, service plants);
User-friendly, with ergonomic interfaces, data import/export capabilities, and support for custom software integration;
Scalable to match the size of the plant and required performance;
Reliable, avoiding single points of failure and supporting redundancy;
Flexible and adaptable to evolving technologies.

## Slide 12
Obsolescence of standards
time
popularity
The lesson is: a system has to be as independent as possible from hardware standards and specific software products.

## Slide 13
Control Room
UI
UI
UI
UI
Central computer
Devices
Once upon a time
centralized

## Slide 14
UI
UI
UI
UI
CP
CP
CP
Control Room
Devices
Live data request
Distributed CS

## Slide 15
UI
UI
UI
UI
Live data retention/streaming
CP
CP
CP

## Slide 16
UI
UI
UI
UI
CP
CP
CP
SEND COMMAND

## Slide 17
UI
UI
UI
UI
CP
NETWORK
CP
CP

## Slide 18
Abstraction
Saloua Raouda Choucair, Fractional Module

## Slide 19
M
CP
M
M

## Slide 21
Features of a Control System
acquisition/actuation
communication
storage
presentation
analysis / correlation
historization

## Slide 22
acquisition/actuation
communication
storage
presentation
analysis / correlation
historization
DAC
Digital to Analog Converter
0 1 1 1
current
ADC
Analog to Digital Converter
0 1 1 1
tempo
voltage
`
`
`
`
`
acquisition
actuation
UI
UI
CP
CP

## Slide 23
acquisition/actuation
communication
storage
presentation
analysis / correlation
historization
Bus di campo
USB
Serial lines
CAN bus
Profibus
GPIB
...
CP
Embedded devices
Intelligent devices
Digital devices
Analog devices
ADC/DAC
conversion
CP
CP
CP

## Slide 24
acquisition/actuation
communication
storage
presentation
analysis / correlation
historization
CP
CP
NETWORK
CP
Embedded devices
Intelligent devices
Digital devices
Analog devices
ADC/DAC
conversion
CP
Network
interface

## Slide 25
acquisition/actuation
communication
storage
presentation
analysis / correlation
historization
CP
CP
CP
CP
{
float64 temperature_read;
char units;
boolean status;
....
}
{
float64 current_read;
float64 current_set;
char units;
boolean error;
....
}
{
float64 mag_field_read;
float64 mag_field_set;
int polarity;
....
}
{
int aperture;
int time;
int n_pixels_h;
int n_pixels_v;
boolean status;
....
}
average size (@DAFNE)
~ 650 byte

## Slide 26
Nel mezzo del cammin di nostra vita
mi ritrovai per una selva oscura,
ché la diritta via era smarrita.
Ahi quanto a dir qual era è cosa dura
esta selva selvaggia e aspra e forte
che nel pensier rinova la paura!
Tant’è amara che poco è più morte;
ma per trattar del ben ch’i’ vi trovai,
dirò de l’altre cose ch’i’ v’ho scorte.
Io non so ben ridir com’i’ v’intrai,
tant’era pien di sonno a quel punto
che la verace via abbandonai.
Ma poi ch’i’ fui al piè d’un colle giunto,
là dove terminava quella valle
che m’avea di paura il cor compunto
guardai in alto e vidi le sue spalle
vestite già de’ raggi del pianeta
che mena dritto altrui per ogne calle.
650 byte
DAFNE ~1.4 Mbyte
The Divin Comedy
~0.5 Mbyte
Dante Alighieri (1265–1321)

## Slide 27
{
float64 temperature_read;
char units;
boolean status;
....
}
{
float64 current_read;
float64 current_set;
char units;
boolean error;
....
}
{
float64 mag_field_read;
float64 mag_field_set;
int polarity;
....
}
{
int aperture;
int time;
int n_pixels_h;
int n_pixels_v;
boolean status;
....
}
CP
CP
CP
CP
Relational database ➝

## Slide 28
CP
CP
CP
CP
Relational database ➝
{
float64 temperature_read;
char units;
boolean status;
....
}
{
float64 current_read;
float64 current_set;
char units;
boolean error;
....
}
{
float64 mag_field_read;
float64 mag_field_set;
int polarity;
....
}
{
int aperture;
int time;
int n_pixels_h;
int n_pixels_v;
boolean status;
....
}

## Slide 29
{
float64 mag_field_read;
float64 mag_field_set;
int polarity;
....
}
{
float64 mag_field_read;
float64 mag_field_set;
float64 orientation;
int polarity;
....
}
CP
CP
CP
CP
Relational database ➝
{
float64 temperature_read;
char units;
boolean status;
....
}
{
float64 current_read;
float64 current_set;
char units;
boolean error;
....
}
{
int aperture;
int time;
int n_pixels_h;
int n_pixels_v;
boolean status;
....
}

## Slide 30
BEGIN OF DATA
here it is described a rhombus;
each side measures 100 mm;
the orientation of the diagonal is 0 deg; blah blah...;
END OF DATA
Serialization: self-describing data vs formatted data

## Slide 31
<note>
<to>Andrew</to>
<from>Jane</from>
<heading>Reminder</heading>
<body>Don't forget me this weekend!</body>
</note>
{
"note":{
"to":"Andrew",
"from":"Jane",
"heading":"Reminder",
"body":"Don't forget me this weekend!"
}
}
note:
to: Andrew
from: Jane
heading: Reminder
body: "Don't forget me this weekend!"
XML
YAML JSON
Most popular self-describing data formats

## Slide 32
Key
Value
0x16\0x00\0x00\0x00\0x02hello\0x00\0x06\0x00\0x00\0x00world\0x00\0x00
my_data
.... another descriptive sequence .......
my_other_data
Non relational database
e.g. BSON serialization
\0x16\0x00\0x00\0x00 total document size
\0x02 0x02 = field data type is string
hello\0x00 field name
\0x06\0x00\0x00\0x00world\0x00 field value (size of value, value, terminator)
\0x00 type EOO ('end of object')

## Slide 33
User Interface
acquisition/actuation
communication
storage
presentation
analysis / correlation
historization

## Slide 34
User Interface
acquisition/actuation
communication
storage
presentation
analysis / correlation
historization

## Slide 35
CP
CP
CP
acquisition/actuation
communication
storage
presentation
analysis / correlation
historization
z = f(x, y, ...)
y
x
READ
READ
z
WRITE
SEND COMMAND
Correlation and analysis processes

## Slide 36
CP
CP
CP
acquisition / actuation
communication
storage
presentation
analysis / correlation
historization
Long term
storage
z = f(x, y, ...)

## Slide 37
Let’s review the full stack
CP
Low level driver
Low level driver
Live data retention
Command
execution
Monitoring
Feedbacks,
data processing
Live data injection
Command
reception
UI
Live data fetching
Command
issuing
Data correlation
Data retrieval
Data logging
Class driver
Live data return
Live data request

## Slide 38
IT interesting topics
Big data
AI
Virtual machines, Containers/Dockers/Orchestrators (K8S)
Courtesy of Giles Knap (Diamond)​
Bare Metal Virtual Machines Containers

## Slide 39
SERVICE CLUSTER
STORAGE 1/2 PB
PRODUCTION CLUSTER
DEVELOPMENT CLUSTER
SERVICE CLUSTER
PRE-PRODUCTION CLUSTER
376 cores
824 GB RAM
500 TB HD
SPARES
Infrastructure @LNF

## Slide 40
$ practical experience