## Slide 1: The EuPRAXIA@SPARC_LAB project
F. Villa, INFN-LNF
on behalf of the EuPRAXIA@SPARC_LAB collaboration

## Slide 2: Layout
Introduction
EuPRAXIA@SPARC_LAB
FEL beamlines

## Slide 3: Plasma acceleration
Laser Wakefield Accelerator (LWFA):
Drive beam = laser beam
Plasma WakeField Accelerator (PWFA):
Drive beam = high energy electron or proton beam
Courtesy Sci. Am.
Plasma acc: typical >1 GeV/m
RF structures: typical 20-60 MeV/m

## Slide 4
EuPRAXIA: Distributed Research Infrastructure
Beam-driven plasma user facility EuPRAXIA Headquarter
Laser-driven plasma user facility: ELI beamlines
National node
Horizon Europe
National nodes perform technical developments, prototyping and component construction.
Beam-driven site (INFN-LNF, IT) EuPRAXIA Headquarter
Laser-driven site (ELI-Beamlines, CZ)
User Data Center (H)
Theory & simulations (P)
Laser-driven 5 GeV e- R&D (EPAC, UK)
Laser-plasma acc. R&D (F)
Laser-plasma acc. & high rep. rate R&D (D)
Beam diag. (CH)
Laser R&D (E)
Laser R&D (IT)
Beamline applications (GR)

## Slide 5
EuPRAXIA@SPARC_LAB
365 m
1.7 GeV
Undulator hall
159 m
45 m
Accelerator hall
Experimental hall
Lasers clean rooms
Laser and particle user rooms
Klystron & power supplies hall
Technical rooms
Preparations labs
1 (=>2+) GeV

## Slide 6
EuPRAXIA@SPARC_LAB
S-band Injector
X-band Linac
Plasma module
Undulators
AQUA Beamline
ARIA Beamline
Photon beamlines
17.5 m
33.5 m
9 m
28.5 m
54 m
Plasma chamber: 3.5 m
Plasma capillary: 0.6 m

## Slide 7: Expected electron parameters at 1 GeV
Two different configurations:
  500 MeV beam from the X-band linac + 60 cm capillary PWFA acceleration
    Final energy up to 1.25 GeV to reach harder FEL photons
    Smaller accelerated charge
    Shorter pulses
    Final energy greatly upgradable in future with similar building occupancy ()
  1 GeV beam from the X-band linac alone (with additional RF power)
    Larger charge per bunch
    Longer pulses
    At the upper limit of RF technology (not easily upgradable without extending the occupancy)
 | Units | PWFA | Full RF
Electron Energy |  | 1 | 1
Repetition rate |  | 100 | 100
Bunch charge |  | 30 | 200
Peak current at undulator entrance |  | 3.3 | 3.4
RMS bunch length at undulator entrance | 𝜇m | 1.4 | 16.9
RMS normalized emittance (x,y) |  | 0.7, 0.7 | 2.1, 1.0
RMS energy spread |  | 0.5 | 0.2
Slice length |  | 0.5 | 0.5
Slice Normalized emittance (x,y) |  | 0.7, 0.7 | 0.3, 0.3
Slice energy spread | % | 0.04 | 0.02
 | Units | PWFA | Full RF
Electron Energy |  | 1 | 1
Repetition rate |  | 100 | 100
Bunch charge |  | 30 | 200
Peak current at undulator entrance |  | 3.3 | 3.4
RMS bunch length at undulator entrance | 𝜇m | 1.4 | 16.9
RMS normalized emittance (x,y) |  | 0.7, 0.7 | 2.1, 1.0
RMS energy spread |  | 0.5 | 0.2
Slice length |  | 0.5 | 0.5
Slice Normalized emittance (x,y) |  | 0.7, 0.7 | 0.3, 0.3
Slice energy spread | % | 0.04 | 0.02
S2E simulations

## Slide 8: AQUA beamline: Undulators
 | Units | PWFA | Full RF
𝜌 (3D) |  | 0.77 | 1.49
Saturation length |  | 20.5 | 20.0
Radiation wavelength |  | 4.0 | 4.0
Photon Pulse Energy |  | 16 | 156
Photon per pulse |  | 3.2 | 31.3
Photon Bandwidth |  | 0.4 | 0.5
Photon pulse length (rms) | fs | 1.0 | 14.1
 | Units | PWFA | Full RF
𝜌 (3D) |  | 0.77 | 1.49
Saturation length |  | 20.5 | 20.0
Radiation wavelength |  | 4.0 | 4.0
Photon Pulse Energy |  | 16 | 156
Photon per pulse |  | 3.2 | 31.3
Photon Bandwidth |  | 0.4 | 0.5
Photon pulse length (rms) | fs | 1.0 | 14.1
10 Apple X undulators for SASE FEL in the water window with variable polarization

## Slide 9: AQUA Beamline: Photon Beamline
GDM
Mirror
Aperture
Spectrometer
Filters
Radial ion. chamber area
Monochromator area
Split & delay line area
Gas absorber
K-B mirrors
Exp. Chamber area
BPM
GDM
BPM
GDM
Filters

## Slide 10: AQUA beamline: Wavelength tuning
AQUA PWFA
linear
AQUA PWFA
circular
Scale equations
Full start to end simulations (PWFA, linear polarization)
e- extrapolated parameters + Genesis simulations

## Slide 11: AQUA beamline: Scientific case
Coherent Diffraction Imaging
X-ray Spectroscopy
Raman Spectroscopy
Photo-Fragmentation of molecules
(Large) Viruses
Organelles
Bacteria/Cells
Organic molecules
Metals
Semiconductors
Superconductors
Magnetic materials
Experimental techniques and typology of samples
3 nm 2 nm
4 nm

## Slide 12: FEL Photon Beamline
Mainly due to longer wavelengths, respect to AQUA:
Larger grazing angle
Large divergence (recollimation needed)
Polarization (s/p) dependency of the reflectivity
Other aspects are very similar, thus also the equipment will be the same/similar
GMD
FW
BPM
Gas att
BDA
Monochr.
S&DL
Spectr.
GMD
M
YAG
YAG
YAG
YAG
Sh
BPM
YAG
YAG
time
FW
Sh
GMD
YAG
KB
GMD
YAG
Sh
foc
Gas att
BDA
GMD
Spectr.
FW
YAG
YAG
time
FW
Sh
GMD
YAG
KB
S&DL
BPM
YAG
YAG
Spectr.
diag
ARIA (150 – 50 nm, 8 – 25 eV)
Monochr.
e- dumps
Undulators’ end

## Slide 13: ARIA FEL Scheme: HGHG seeding
2 m
80 cm
Modulator (λw=10cm)
Dispersion
chicane
2 m
Radiator (λw=5.5cm)
2.2 m
2 T/m quads
4-dipole chicane
30 cm drifts,
10 cm 0.2-0.3 T dipoles
1 T/m quad
λn=50-160 nm via harmonic amplification (n=3-11)
Laser seed:
λ0=500 nm
λ0=500 nm modulation
Converts electron energy modulation to spatial bunching in harmonics Remove λ0 radiation

## Slide 14: ARIA Beamline
HN | 3 | 3 * | 4 | 4 * | 5 | 5 * | 7 | 9
λ (nm) | 153 | 153 | 115 | 115 | 92 | 92 | 65 | 51
Seed E (μJ) | 1.2 | 2.8 | 8 | 5.6 | 8 | 8 | 30 | 30
Photon E (μJ) | 22 | 13 | 27 | 9.5 | 24.7 | 9 | 9 | 5
FWHM Δt (fs) | 25 | 16 | 23 | 15 | 20 | 15 | 18 | 18
Ph/shot (10^13) | 1.35 | 1.02 | 1.78 | 0.73 | 1.13 | 0.55 | 0.39 | 0.08
BW (%) | 0.85 | 0.95 | 0.71 | 0.7 | 0.63 | 0.67 | 0.43 | 0.4
Pulse size (mm) | 1.2 | 1.15 | 1.11 | 1.2 | 1.17 | 1.08 | 1.07 | 0.8
Pulse div. (mrad) | 0.68 | 0.62 | 0.48 | 0.45 | 0.38 | 0.34 | 0.27 | 0.2
Sim (same e- as AQUA)
Scale eq. (short bunch)
Scale eq. (long bunch)
Simulations with real case parameter are ongoing
Condens. Matter 2022, 7(1),11; https://doi.org/10.3390/condmat7010011

## Slide 15: ARIA Beamline: Scientific case
Photoemission
Spectroscopy
Photoelectron Circular Dichroism
Raman spectroscopy
Photo-fragmentation of molecules
Time of Flight Spectroscopy
Gas phase & Atmosphere
(Earth & Planets)
Aerosols
(Pollution, nanoparticles)
Molecules & gases
(spectroscopies, time-of-flight)
Proteins
(spectroscopies)
Surfaces
(ablation & deposition)
Defining experimental techniques and typology of samples (and applications)

## Slide 16: Timeline
Design
Tender preparation
Tender
Procurement
Test & validation
ARIA Beamline

## Slide 17: Conclusions & Acknowledgements
Plasma accelerators have advanced considerably in beam quality, achieving FEL lasing.
EuPRAXIA is a design and an ESFRI project for a distributed European Research Infrastructure, building two plasma-driven FELs in Europe.
EuPRAXIA@SPARC_LAB is mainly funded by INFN, building tender is ongoing and expected to delivery in 2029, and first FEL light is expected in 2031. In parallel, Regione Lazio is co-funding one beamline (with 10M€) that has to be accounted by end 2028.
EuPRAXIA@SPARC_LAB TDR (AQUA beamline only) is available at https://www.openaccessrepository.it/doi/10.15161/oar.it/aye3c-2cx65
Greatly appreciate slides from and discussions with THE ENTIRE EuPRAXIA@SPARC_LAB TEAM

## Slide 18
Thanks for your attention