## Slide 1
Project Status and Prospects of Super Tau-Charm Facility
Jingyu Tang, USTC
On behalf of the STCF team
INFN-LNF, Rome, April 14, 2026
Notes: 报告时间：25+5

## Slide 2: Topics
General introduction to STCF
Physics goals
Accelerator design and R&D efforts
Detector design and R&D efforts
Project status and planning
Summary

## Slide 3: General Introduction to STCF

## Slide 4
Super Tau-Charm Facility
Multi-Linac
Total 550 m
Positron Damping Ring 150 m
Collider Rings
825 m
Detector
Center-of-Mass energy : 2-7 GeV
Peak Luminosity: > 0.51035 cm-2 s-1 @ 4GeV
Potential to increase lumi. & polarized beam
A factory producing massive tau lepton and hadrons, to unravel the mystery of how quarks form matter and the symmetries of fundamental interactions

## Slide 5: Site: Hefei, Anhui Province
Hefei Comprehensive National Science Center
"Future Big Science City", Hefei, Anhui Province
Funded R&D : 364 Million CNY by Anhui Province
Construction budget : ~5 Billion CNY
Hefei Advanced Light Facility (HALF) - under construction
Super Tau-Charm Facility (STCF)

## Slide 6: Project Promotion
China has a long-established base in tau-charm physics with BEPC (1990~)
STCF was conceived to take the relay for another 30 years

## Slide 7: Physics goals

## Slide 8: Physics at the Tau-Charm Energy Region
Opportunities in 5~7 GeV
Hadron form factors
resonance
Mutltiquark states with s quark
R value / g-2 related
Light hadron spectroscopy
Gluonic and exotic states
Processes of LFV and CPV
Rare and forbidden decays
Physics with  lepton
particles
Physics with D mesons
and
mixing
Charm baryons
Complete family
Hidden-charm pentaquarks
Search for di-charmonium states
More charmed baryons
Hadron fragmentation
Unique Features -c facilities:
Transition region between perturbative and non-perturbative QCD
Threshold effects and quantum correlation of pair production of hadrons and  leptons
Rich resonance structures, large production X-sec for charmonium(-like) states and exotics

## Slide 9: Unique Data Samples
Not only a -charm factory, but also a factory for XYZ, hyperons and light hadrons
Charmed Hadrons
Light Hadrons
-leptons
BelleII: 50 ab-1
STCF: 1 year (1 ab-1)
BESIII 1 year
XYZ
10 years data taken proposal
Notes: STCF: 1 ab-1, one year
BelleII: 50 ab-1 ~10 years
世界独特的超大数据样本 + 高分辨 + 低本底 ➜ 高精度测量 ➜ 重大发现
The energy region of STCF covers the pair production thresholds for τ-leptons, charmed mesons & baryons, and all of the strange hyperons.
Huge samples of XYZ, 𝐽/𝜓, 𝐷^+, 𝐷_𝑠^+, and Λ_𝑐^+ decays could be used to make precision measurements of hadron properties, search for new ones, and study their rare decays
STCF is expected to have higher detection efficiency, low bkg., excellent resolution, and good kinematic constraining.

## Slide 10
Key question 3:
Any new physics? If so, where?
STCF
Key question 2:
New CPV source beyond SM?
Unprecedented large data samples and high-precision measurements
Transition region between perturbative and non-perturbative QCD
Key question 1:
What is the nature of color confinement?
Broad physics are anticipated, several mini-workshops were organized to refine the core scientific goals

## Slide 11: Flagship Measurements at STCF
STCF aims to reveal the mystery of how quarks form matter and the symmetry of fundamental interactions
  Hadron generation: fragmentation and energy correlator
  Exotic hadronic states and more
Scientific question: how quarks form matter
  CP violation in the hyperon decay
Scientific question: symmetry of fundamental interactions

## Slide 12: Accelerator Design and R&D Efforts

## Slide 13: STCF Accelerator Design Goals
Core design goals:
  CoM energy: 2-7 GeV
  Luminosity: >51034 cm-2s-1 @4GeV
  Upgrading potential: polarized beam, higher luminosity
Accelerator structure:
  Double-ring collider: low emittance, high current, large Piwinski angle (crab-waist)
  Injector: full-energy linacs, e+ damping ring, beam transport lines

## Slide 14
Collider Rings
Layout and lattice
  Based on the two-fold lattice scheme
  Key physics issues: Dynamic Aperture/Local Momentum Aperture, Touschek lifetime
  Adjustability (emittance/energy spread) to wide energy range (1.0-3.5 GeV)
  Straight sections for different functions (injection/extraction, damping wigglers, collimation, RF stations, beam crossing, tune matching, etc.)
  Present version: Lattice Ver. 5.0

## Slide 15
Parameters | Units | Value | Value | Value | Value
Mom. compaction factor, αp | 10-4 | 14.07 | 13.36 | 13.9 | 14.3
Energy spread (DW, IBS), σe | 10-4 | 8.12 | 7.16 | 7.52 | 10.02
Beam current, I | A | 2 | 0.8 | 1.5 | 2
Bunch filling ratio |  | 48% |  |  | 
Bunch spacing, τb | ns | 4.0 |  |  | 
Single-bunch charge | nC | 8.34 | 3.34 | 6.25 | 8.34
SR power per beam (Total) | MW | 1.25 | 0.1 | 0.47 | 2.99
Trans. damping time, τx, τy | ms | 18 | 44 | 27 | 13
RF frequency, fRF | MHz | 499.7 |  |  | 
RF voltage, VRF | MV | 2.5 | 0.75 | 1.5 | 6
Bunch length (0.1Ω, IBS), | mm | 9.0 | 9.9 | 9.4 | 8.9
Piwinski angle, Фpiw | rad | 21.53 | 19.09 | 23.12 | 5.12
Ver. beam-beam parameter |  | 0.1 | 0.093 | 0.109 | 0.049
Touschek lifetime (Elegant) | s | 364 | 267 | 371 | 10972
Luminosity, L | cm-2s-1 | 1.0E+35 | 8.0E+33 | 2.6E+34 | 3.3E+34
Parameters | Units | Value | Value | Value |  | Value
Beam energy, E | GeV | 2 | 1 | 1.5 |  | 3.5
Circumference, C | m | 825.524 |  |  |  | 
Crossing angle, 2θ | mrad | 60 |  |  |  | 
L* | m | 0.9 |  |  |  | 
Relative gamma |  | 3913.9 | 1956.9 | 2935.4 |  | 6849.3
Revolution period, T0 | s | 2.75 |  |  |  | 
Revolution frequency, f0 | kHz | 363.15 |  |  |  | 
Ratio, |  | 1% | 1% | 2% |  | 0.5%
Hor. emittance (SR), εx | nm | 8.83 | 2.35 | 4.97 |  | 27.0
Hor. emittance (DW, IBS) | nm | 3.93 | 6.0 | 3.74 |  | 27.0
Ver. Emittance (SR), εy | pm | 88.3 | 23.5 | 99.4 |  | 135
Ver. emittance (DW, IBS) | pm | 39.3 | 60 | 74.7 |  | 135
Hor. beta function at IP, βx | mm | 40 | 40 | 40 |  | 100
Ver. beta function at IP, βy | mm | 0.8 | 2 | 2 |  | 2
Hor. beam size at IP, σx | m | 12.54 | 15.49 | 12.22 |  | 51.96
Ver. beam size at IP, σy | m | 0.18 | 0.346 | 0.39 |  | 0.52
Betatron tunes, νx/νy |  | 28.545/31.58 | 28.55/33.58 | 28.55/32.58 | 28.55/30.58 | 
Parameters | Units | Value | Value | Value |  | Value
Beam energy, E | GeV | 2 | 1 | 1.5 |  | 3.5
Circumference, C | m | 825.524 |  |  |  | 
Crossing angle, 2θ | mrad | 60 |  |  |  | 
L* | m | 0.9 |  |  |  | 
Relative gamma |  | 3913.9 | 1956.9 | 2935.4 |  | 6849.3
Revolution period, T0 | s | 2.75 |  |  |  | 
Revolution frequency, f0 | kHz | 363.15 |  |  |  | 
 |  | 1% | 1% | 2% |  | 0.5%
Hor. emittance (SR), εx | nm | 8.83 | 2.35 | 4.97 |  | 27.0
Hor. emittance (DW, IBS) | nm | 3.93 | 6.0 | 3.74 |  | 27.0
Ver. Emittance (SR), εy | pm | 88.3 | 23.5 | 99.4 |  | 135
Ver. emittance (DW, IBS) | pm | 39.3 | 60 | 74.7 |  | 135
Hor. beta function at IP, βx | mm | 40 | 40 | 40 |  | 100
Ver. beta function at IP, βy | mm | 0.8 | 2 | 2 |  | 2
Hor. beam size at IP, σx | m | 12.54 | 15.49 | 12.22 |  | 51.96
Ver. beam size at IP, σy | m | 0.18 | 0.346 | 0.39 |  | 0.52
Betatron tunes, νx/νy |  | 28.545/31.58 | 28.55/33.58 | 28.55/32.58 | 28.55/30.58 | 
Main Parameters of the Collider Rings (Ver. 5.0)

## Slide 16
Collider Ring Physics Design (1)
IR design:
  ~200 m in length, 60 in bending
  Modular lattice design
  FFT: final focus telescope
  CCY/CCX: local chromaticity correction Y/X
  MCY/YMX/XMC： local matchings
  CS: crab sextupoles
  MS: matching section
IP key parameters
  mm (@2 GeV)
  Crossing angle: 60 mrad
  L*: 0.9 m

## Slide 17
Collider Ring Physics Design (2)
Arc design:
  Four 60 arcs (~57.2 m) and two 30 arcs (33.7 m); another 60 is with IR.
  -I transfer between paired sextupoles
Crossing region
  Length: ~35 m
  Separation between rings: 2.0 m
Straight sections
  Default with FODO cells, functional ones with special designs (e.g. DW with triplets)
60-deg arc lattice
30-deg arc lattice
Crossing region lattice

## Slide 18
Collider Ring Physics Design (3)
Nonlinear dynamics
  Very strong due to strong nonlinear effects and higher-order kinetic effects
  Very limited DA (w/ fringe): >25; and >@10
  Small LMA: ~1.5% （bandwidth）
  Intense optimization with simulations
Touschek scattering
  Simulations (Elegant, SAD)
  Current: ~350 s @ 2 GeV (high bunch charge, very small DA and LMA) (improving)
Error studies
  COD and optics corrections: ok
  Errors at IR lead significant reduction in luminosity: 10-20%
  DA and Touschek lifetime: reduction <10%
Collimation
  Machine protection, MDI background, tunnel radiation dose
  Full ring for collimators: normal at arcs, nonlinear coll. at straights, reducing burden at IR
LMA
With BPM
Errors

## Slide 19
Collider Ring Physics Design (4)
Collective effects, instabilities and longitudinal dynamics
  IBS effects: emittance growth, bunch lengthening
  Impedance control, collective instabilities (feedbacks)
  Requirements to the RF system: HOM-damped TM020 cavities
Beam-beam effects
  Strong concern on X/Z instability
  Simulations (BBWS, BBSS, IBB, Xsuite)
  Tune scans: (0.543, 0.580) for now
Injection and extraction
  Off-axis injection (nominal) and swap-out injection (reserved)
  Dumping extraction (for machine protection, extracting all bunches in one turn) and reserved for swapped bunches
Damping wigglers
  DWs for adjusting damping time, energy spread, emittance
  Influence on focusing, DA and RF frequency

## Slide 20
Collider Ring Physics Design (5)
MDI studies at large
  Joint study group (Accelerator: physics, IR magnet, vacuum, diagnostics, mechanics, alignment; Detector: background sim., inner detectors, luminosity monitor)
  Layout, interfaces and dimensions
  Regular meetings (every two or three months)
Background issues
  Studying beam loss mechanisms and reducing total beam losses (Touschek, beam-gas scattering, injection)
  Effective collimation (controlling most losses outside IR)
  Joint simulations (accelerator and detector) on the background

## Slide 21
Injector Scheme
A compatible injector scheme for both the off-axis and swap-out injections in the collider rings, with off-axis injection first.
Off-axis (baseline scheme):
  Injection: 1.0 nC e+/e- with 30 Hz each
  e+ beam: 1.0GeV/11.6nC/30Hz e- linac, 1 GeV damping ring, 30 Hz
Swap-out (for future):
  Injection: 8.5 nC e+/e- also with 30 Hz each
  e+ beam: 2.5GeV/11.6nC/90Hz e- linac, 1 GeV DR+AR, ext. 30 Hz

## Slide 22
Parameters | Value |  | Unit
Collider ring injection scheme | Off-axis | Swap-out | 
E-gun type | Photo/Therm. | Therm./Therm. | 
E-gun charge | 1.0/11.6 | 8.5/11.6 | nC
Injection e- bunch charge | 1.0 | 8.5 | nC
Injection e+ bunch charge | 1.0 | 8.5 | nC
Injection energy | 1.0-3.5 | 1.0-3.5 | GeV
Optimal energy | 2.0 | 2.0 | GeV
MW frequency | 2998.2 | 2998.2 | MHz
Injection emittance (X/Y, Geo, rms) | 6 | 30 | nm-rad
Injection energy spread (rms) | 0.1 | 0.5 | %
Injection frequency e-/e+ | 30/30 | 30/30 | Hz
e- linac energy for direct injection (EL2) | 1.0 | 1.0 | GeV
e- linac energy for e+ production (EL1) | 1.0 | 2.5 | GeV
e+ linac energy (PS) | 1.0 | 1.0 | GeV
Main linac booster energy for e-/e+ (ML) | 0-2.5 | 0-2.5 | GeV
e+ DR/AR bunch numbers | 6 | 12 | 
e+ DR/AR RF frequency | 499.7 | 499.7 | MHz
e+ DR/AR injection charge | 1.0 | 2.9 | nC
e+ DR/AR injection frequency | 30 | 90 | Hz
e+ DR/AR injection emittance (X/Y) (rms) | 1400 | 1400 | nm-rad
e+ DR/AR extraction emittance (X/Y) (rms) | 11/0.12 | 30/10 | nm-rad
Main Parameters of the Injector

## Slide 23
Injector Physics Design (1)
e- linac design
  With L-band photocathode gun: good emittance and momentum spread for direct injection (1.0 nC for off-axis,
  8.5 nC for swap-out)
  With thermionic gun (11.6 nC) for e+ production (off-axis): modest beam quality (90 Hz for swap-out)
Main linac (e-/e+) design
  Almost the same for off-axis and swap-out injections, only bunch charge different
  Energy boost: 0-2.5 GeV, 30 Hz + 30 Hz
Positron production and capture
  Tungsten target, AMD (pulsed peak field: 6.5 T)
  Relatively mature technique with off-axis injection
  Technically challenging with swap-out injection: high heat deposition, movable target design needed

## Slide 24
Injector Physics Design (2)
e+ linac
  Large aperture acceleration structure:
  capture
Damping ring / accumulator ring
  DR: several examples exist, 1 GeV, 150 m, 6 bunches circulating
  AR: some challenges, multiple off-axis injections, 12 bunches circulating; much larger horizontal acceptance
Beam transport lines
  DR injection line: reducing momentum spread
  DR extraction line: reducing bunch length
  Injection lines to the collider rings: controlling emittance growth, prolonging bunches, 60 horizontal bending

## Slide 25
IR SC quadrupole magnets:
  Based on the CCT technology
  CDR design and prototype design completed
  TDR design evolving along with the physics design
Other IR SC magnets
  Solenoids: screening and compensating the magnetic field from the detector solenoid
  Field cancellation within the two quads (QD1/QF2)
  Field compensation at the IP and at the far ends
  Correction coils/magnets (24 coils each side)
IR Superconducting Magnets (1)

## Slide 26
R&D and prototyping
  Focus on the QD1 (most challenging);
  Electromagnetic field optimization: very good, meeting the design goals
  Studying the fabrication techniques
  Prototype fabrication completed, first test showing good performance (design current/field)
  Next test: field distributions
IR Superconducting Magnets (2)
  QD1 prototype and magnet test/measurement

## Slide 27
Concerning two collider rings and DR
  CRs: Challenging due to very high RF power (>300 kW), deep HOM damping, and low R/Q
  DR: same RF frequency but relaxed requirements
  Room-temperature TM020-mode RF cavity was chosen
R&D and prototyping
  Prototype fabrication almost completed
  Performance test will be soon, using HALF RF
  power source and test platform
Ring RF system
RF parameters | 
Working mode | TM020
Frequency [MHz] | 499.7
R/Q [Ω] | 95
Unloaded quality factor | ~60000
 | 2.48
[mA/V] | 2.88
RF parameters | 
Working mode | TM020
Frequency [MHz] | 499.7
R/Q [Ω] | 95
Unloaded quality factor | ~60000
 | 2.48
 | 2.88
HOM damper
Cavity in fabrication
Schematic
Input coupler ceramic win.

## Slide 28
TDR under way
  CR vacuum very challenging, mature technology for the others
Vacuum requirements for the collider rings
  Very high SR load: up to 17 kW/m (beam current: 2 A; beam energy: 3.5 GeV)
  Very low pressure (dynamic): <510-8 Pa at arcs and straights; ~110-7 Pa at IR
  IR vacuum: very complicated structure (MDI)
  Low impedance
R&D efforts
  Prototype for a standard arc cell vacuum being started
Vacuum System

## Slide 29
RT magnets, Damping Wigglers, and Power Supplies
RT magnets and power supplies
  Conventional design for collider rings, linacs, transport lines
  Permanent magnets considered for Damping Ring dipoles
Damping wigglers
  RT electromagnetic wigglers adopted for baseline design
  SC wigglers under study
  Hybrid structure (with permanent magnet blocks) with special configuration found much helpful (increasing field from 1.6 T to 1.9 T @40mm, flatter field)
  Prototyping of the hybrid DW under way
Chart: 
| -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0.99806 | 0.99844 | 0.9987 | 0.99892 | 0.99911 | 0.99927 | 0.99936 | 0.99946 | 0.99958 | 0.99967 | 0.99974 | 0.99979 | 0.99982 | 0.99985 | 0.99987 | 0.99988 | 0.9999 | 0.99993 | 0.99996 | 0.99999 | 1 | 1 | 0.99997 | 0.99993 | 0.99988 | 0.99983 | 0.9998 | 0.99977 | 0.99972 | 0.99969 | 0.99964 | 0.99958 | 0.99951 | 0.99942 | 0.99932 | 0.99918 | 0.99902 | 0.99886 | 0.99863 | 0.99836 | 0.99802
 | 0.99704 | 0.99745 | 0.99782 | 0.99814 | 0.99843 | 0.99867 | 0.99889 | 0.99908 | 0.99924 | 0.99939 | 0.99951 | 0.99961 | 0.9997 | 0.99978 | 0.99983 | 0.99988 | 0.99992 | 0.99995 | 0.99997 | 0.99999 | 1 | 0.99999 | 0.99997 | 0.99995 | 0.99992 | 0.99988 | 0.99983 | 0.99978 | 0.9997 | 0.99961 | 0.99951 | 0.99939 | 0.99924 | 0.99908 | 0.99889 | 0.99867 | 0.99843 | 0.99814 | 0.99782 | 0.99745 | 0.99704

## Slide 30
Beam Instrumentation
TDR under way
  CR precise bunch meas.: bunch-by-bunch 3D meas., trans. position res. <5 m, long. phase res.<0.2 ps
  CR B-by-B fast feedback: coupled bunch inst. (<0.4 ms)
  IP: orbit feedback
  Injector: bunch length and charge meas.
  Iterations between physics design and BI group are held regularly
R&D efforts in progress, to be tested in light sources and e+/e- beam test platform
  Bunch 3D meas.: probe, signal treat, electronics, S/N, integration
  B-by-B fast feedback: raising bandwidth, avoiding interference to single bunch
  Injector bunch length and charge meas.: cavity-based
  Prototypes: beam tests in different machines (SSRF, HLS, DLS)
Bunch by bunch profile monitor light path diagram
without
with
Offline test for cavity-based meas.

## Slide 31
Technical design iteration with physics design
  Off-axis injection (CR/AR): conventional bump kickers, nonlinear kickers
  Swap-out injection: Ultrafast kickers (stripline type, <6 ns bottom)
  Extraction: swap-out bunch by bunch, MPS extracting all bunches
  Eddy current septum
  Anti-septum
R&D efforts
  Both nonlinear kicker and ultrafast kicker prototypes
  Ultrafast kicker test: <1 ns risetime
Ultrafast kicker
Injection and Extraction System
Eddy current septum
Nonlinear kicker

## Slide 32
High attention on the MDI area
  Intense discussions among different groups
  IP central beam tube: design optimization, prototyping to start
  MDI mechanical model prototype: in fabrication
Technical design on the collimators are on iteration with physics design
IP central beam chamber
RVC (Remote Vacuum Contact)
MDI and Mechanics

## Slide 33
Linac acceleration structures for e-/e+ beams
  Standard: 40 MW klystron driving two 3-m acceleration tubes, with SLED: ~27 MV/m
  A few large-aperture tubes for e+ beam capture and early acceleration: ~20 MV/m
  50 Hz repetition rate 2998-MHz klystron is available in China, but 90 Hz needs more development
Cannon (left) and KMF418B (China, right)
Schematic and structure design
Linac Microwave and Power Source

## Slide 34
With wobbling target, temperature below 400C
Conventional design
Coil1
Coil2
Positron Source
Positron source design
  Mature technique for off-axis injection scheme: heat load, 5.6 J/g
  Technically challenging for swap-out injection scheme: heat load 31.8 J/g; wobbling target design adopted.
  Prototype of the conventional design for the test beam platform under way
 | Parameter | Design | 
 |  | Off-axis | Swap-out
1 | e+ beam for DR/AR | 1 GeV/1.0 nC/30 Hz | 1 GeV/2.5 nC/90 Hz
2 | e- beam on target | 1.0 GeV/11.6 nC/30 Hz | 2.5GeV/11.6nC/90Hz
3 | Beam power | 348 W | 2443 W
4 | Peak power dep. | 5.6 J/g | 32.2 J/g
5 | AMD | 0.5-5 T | 0.5-5 T
6 | e-/e+ conv. Rate | 9.1 % | 25 %
7 | Solenoid field | 0.5 T | 0.5 T
8 | Accel. tube diam. | 30 mm | 30 mm

## Slide 35: e-/e+ Beam Test Platform
Test platform to support several injector R&Ds
  Photocathode e-gun; High-power solid-state modulator; Positron target; Adiabatic matching device (AMD); Large-aperture S-band accel. tube; Beam diagnostics
Design scheme
  100-MeV e- linac + Positron target and AMD +100-MeV e+ linac
Elements fabrication: due 2026.5
Installation and test: 2026.05-09
HALF test hall

## Slide 36
Alignment
  Special attention to the IR (very challenging), the others similar to light sources
Electron sources
  Thermionic e- gun: 10-12 nC technical available
  L-band photocathode e- gun: ~1 nC for off-axis injection (mature), 8.5 nC for e- beam swap-out injection (needing further development)
Control system
  No technical challenges, just following the light sources
Radiation and safety
  Beam loss rate hundreds times higher than light sources, but shielding and safety design method the same
  Need more collimators and local shielding
Other Technical Systems

## Slide 37: Detector design and R&D efforts

## Slide 38: STCF Detector Design
Inner Tracker (4 layers)
  MPGD: cylindrical uRGroove, σx ~100 m
  Silicon: low-mass MAPS, <0.3%X0/layer
Main Drift Chamber (σp/p~0.5% @ 1GeV)
  Small cells with helium-based gas, σx <130 m
PID System (/K ~4σ @ 2GeV, <0.3X0)
  Barrel: DIRC-like TOF - BTOF (σt~30 ps)
  Endcap: RICH (<4mrad), ASHIPH, DTOF
EMC
  pCsI + APD + waveform readout: (σE/E~2.5%, σx~5 mm @ 1GeV & ~1 MHz/crystal )
Solenoid ：1 T
Muon Detector (eff. >95%, mis-rate <3.3% @1GeV)
  inner 5 layers : glass RPC，> 300 Hz/cm2
  outer 10 layers : scintillator strip + SiPM, ~ 2.4 m
Main Performance requirements
Tracking: eff>90%@0.1GeV, σp/p~0.5%@1GeV
Energy meas. : 25MeV-3.5GeV σE/E ~ 2.5% @ 1 GeV
Hadron ID: /K ~4σ @ 2 GeV, ~3σ @ 3 GeV
Muon ID： eff. >95%, mis-rate <3.3% @1 GeV

## Slide 39: ITK : μRGroove and CMOS MAPS
Proposed and developed a novel single-stage MPGD, micro-resistive Groove detector (μRGroove) with larger signals and easier production compared to μRWELL. Developed a low-mass cylindrical μRGroove prototype: material budget ~ 0.23%X0/layer, the best in cylindrical MPGDs.
Ultra-low mass electrode
Cylindrical μRGroove
C-uRGroove Protytpe
Beam test @ CERN SPS
σx < 130μm in 1T
Targeting a low-power MAPS with moderate position resolution and both timing and charge measurement capabilities. Exploring strip-like MAPS designs and a super-pixel design
180nm
Chips received,
testing underway
90nm
Chips received,
to be tested
130nm
Chips received, testing underway
180nm
Supporting quadruple-well with possibility of N-blanket implant and N-gap. Chips received, testing underway
N-blanket implant
N-gap

## Slide 40: MAPS Testing
Characterized the prototype MAPS chips for threshold, noise, charge collection efficiency and capacitance with laser and radioactive sources.
Performed a beam test at CERN PS for detection efficiency, fake hit rate, position resolution, time resolution.

## Slide 41: Main Drift Chamber
Endplate structure optimized to simplify the assembly process. Intensive R&D effort on feedthrough for super-small cells (~5 mm). A full-length super-small cell drift chamber prototype has been constructed.
Waveform digitizing electronics is developed to allow online waveform discriminating algorithms that run on PFGA to identify overlapping signal pulses

## Slide 42: BTOF/DTOF Detectors
A DTOF prototype was built and tested with particle beams at CERN PS to demonstrate the PID capability of the DTOF detector
π/K separation >4σ @ 2GeV/c
A full-length BTOF prototype has been built and tested with particle beams at CERN PS. Data analysis is underway.

## Slide 43: RICH Detector
Cosmic-ray test of a 32×32 cm2 RICH prototype with both THGEM+MM and DMM
Purifying C6F14 with good transmittance achieved
main issue: low photoelectron yield ~2pe/track.
=9.4 mrad
DMM gain 1.2
THGEM MM gain 0
QE of photo cathode needs to be improved !

## Slide 44: Electro-Magnetic Calorimeter : EMC
A crystal calorimeter using pCsI ( short decay time of 30ns ) to tackle the high background rate (~1 MHz/crystal ): crystal unit 5×5×28(15X0) cm3 ; 4 APD(1×1cm2) to enhance light yield, ~8900 crystals in total.
Developed and implemented a dead-time free pileup correction algorithm involving waveform fitting based on pipelined optimal filtering.
Developed a fully-readout ECAL prototype with 5×5 pCsI crystals. Carried out two beam tests of the prototype at CERN PS: σE/E~2.1%, σx~5.5mm, σt~280ps @1GeV
pCsI sprayed with WLS
Light yield : 50 p.e./MeV → 300 p.e./MeV

## Slide 45: Muon Detector
Scintillator strip + WLS + SiPM
  Design and fabrication of the scintillator unit ：reflector, fiber groove, optical coupling, surface processing.
  Fabricated 2.4 long scintillator units (efficiency>95%) and a 50×50 cm2 scintillator strip array
Glass RPC
  Developed glass RPC fabrication techniques and built a 40×40 cm2 glass prototype.
  Focusing on low-resistivity glass RPC for high count rate capabilities. Built some small prototypes.

## Slide 46: Readout Electronics
Ongoing effort on development of readout ASICs and readout systems for all sub-detectors. Prototype ASIC chips and readout systems have been developed and tested (with detectors). Some ASIC designs have undergone three iterations and are maturing.

## Slide 47: Trigger, DAQ, Clock, Data Transmission
Clock jitter ~ 5ps, physics event rate ~400 kHz @Jpsi，data rate ~30 GB/s
Design and development of architectures, algorithms, firmware, software, hardware components, ASICs, prototype systems

## Slide 48: Combined Beam Tests
Two test beam campaigns for combined systems (ITK, RICH, DTOF, EMC, Clock, Trigger, DAQ)
CERN PS T9 beam line (Aug. 2025 & Oct. 2025 )
DTOF Prototype
EMC Prototype
DTOF: σt~25 ps
EMC: σE/E ~2.1%

## Slide 49: Project status and planning

## Slide 50
Project Schedule
 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033-2043
Conceptual design and CDR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Key Technology R&D and TDR |  |  |  |  |  |  |  | ⭐️ |  |  |  |  |  |  |  | 
Construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
14th five-years plan
15th five-years plan
Submit project proposal to central government:
Science, budget, feasibility and contribution to society
14th five-years plan : CDR/TDR and Key technology R&D, 364 M CNY
15th five-years plan : Construction 5 years, ~5 B CNY
Operating for 10-15 years; upgrading; operating again for ~10 years

## Slide 51: Team & Collaboration
Ongoing efforts to strengthen collaboration with BINP, KEK, INFN-LNF, DRD and others, especially on accelerator development
25 universities/Institutes:
170 faculties and 140 graduate students

## Slide 52
Submit project proposal to the central government (National Development and Reform Commission, NDRC) for construction in the 15th Five-Year Plan (2026-2030)
  Several rounds of selection (done, waiting for final decision)
  National competition from all fields
  Lasting about one year from the first half 2025 (first two rounds within CAS)
If approved
  Feasibility study phase will come very soon
  Then the engineering design before the construction start
  Ideal construction plan: 2028-2034 (the 4G light source HALF to complete in 2028)
  Construction budget: ~5.0 billion RMB
Project Proposal to the Government

## Slide 53
Detector and Physics CDR published in 2021 (2024)
Accelerator CDR completed in 2025
  In both Chinese and English editions, Spring 2025
  Internal review (Jan. 2025) and international review (June 2025)
  Published in NST [Nucl. Sci. Tech. 36, 242 (2025)], with 460 authors from around the world
STCF project proposal
  Only in Chinese edition (several versions)
  Submitted to the CAS and the central government
STCF TDR scheduled late 2026
  Chinese edition before October 2026
  English edition by end 2026
Reports Writing

## Slide 54
New R&D efforts
  Two items identified for R&D or prototyping (soon to start):
  Prototype for one standard vacuum cell of the collider ring arcs
  IP chamber prototype
  In late 2026, will identify more items (or the following-up of the current ones) for R&D
More key technology R&D on the accelerator

## Slide 55
IAC meetings
主席 | Guy Wilkinson | U. of Oxford | 英国
副主席 | Frank Zimmermann | CERN | 瑞士
成员 | Marica Biagini | INFN Frascati-National Lab. | 意大利
 | Ikaros Bigi | U. of Notre Dame | 美国
 | Alexander Bondar | BINP | 俄罗斯
 | Tom Browder | U. of Hawaii | 美国
 | 赵光达 | Perking U. | 中国
 | 高原宁 | Perking U. | 中国
 | Wolfgang Gradl | JGUM | 德国
 | David Hitlin | CIT | 美国
 | Tord Johansson | Uppsala U. | 瑞典
 | Marek Karliner | Tel Aviv U. | 以色列
 | Eugeny Levichev | BINP | 俄罗斯
 | 马余刚 | Fudan U. | 中国
 | Mikihiko Nakao | KEK | 日本
 | Stephen Olsen | Chung Ang U. | 韩国
 | Alexey Petrov | South Carolina U. | 美国
 | Antonio Pich | Valencia U. IFIC | 西班牙
 | Makoto Tobiyama | KEK | 日本
 | 赵红卫 | IMP, CAS | 中国
 | 赵振堂 | SARI, CAS | 中国
 | 邹冰松 | Tsinghua U. | 中国
2025. May 3rd IAC meeting
2024 Oct. 2nd IAC meeting
2024 Jan. 1st IAC meeting
International Advisory Committee
Great helps and encouragements!
STCF will be a unique facility with a broad and impressive physics reach. It will allow for results of world-leading precision in many important topics, and has significant discovery potential. It will ideally complement the other facilities that are currently operational or are foreseen for the 2030s and 2040s, and will be of great interest to the international particle physics community……...
The IAC is pleased to note the substantial progress made in physics, detector and accelerator studies …………..
The IAC continues to endorse the very high scientific merit of the project. It congratulates the STCF team on the excellent progress made over the past year. Although substantial challenges remain to be overcome, the IAC considers that STCF will be able to achieve its design goals within the timescale specified,…...

## Slide 56
Support the project application for construction in the 15th Five-Year Plan (2026-2030)
  Under course, national level selection
TDR work
  Until end 2026
  Review in the first half 2027
Strengthen the team and collaboration
  Continuously strengthen the accelerator team by recruiting new staff and inviting more domestic collaborators
  Enhance international collaborations, in particular, BINP, KEK and INFN-LNF
Near-term Planning

## Slide 57: Summary
STCF design and R&D undergone great progresses, many thanks to all the team members and collaborators
Both Detector and Accelerator CDRs completed and reviewed
TDR under way, to be completed by end 2026
Current key technology R&D and prototyping are in schedule, and more items being started
Support the project proposal application for construction in 15th Five-Year Plan
Much welcome international collaboration!
Thanks for your attention!