## Slide 1: GAMMA x 2013

## Slide 2
Dimostratore di AGATA  GSI
  Spostamento e reinstallazione  Meno coinvolti nella gestione
Realizzazione GALILEO
  Realizzazione della struttura di supporto
  Allestimento del punto misura
  Produzione 2 prototipi dei criostati tripli
  Elettronica di processamento per 60 canali Ge + 90 canali AC
  Allestimento DAQ
  Produzione nuovi preamplificatori per rivelatori GASP e i cluster tripli (Milano)
  Realizzazione della camera di reazione (Milano)
  Produzione dell’elettronica di campionamento 60+90 canali (Milano)
Produzione elettronica per 10 rivelatori AGATA (400 canali)
Esperimenti al GSI, GANIL, MSU, Bucarest, Orsay
13 Ricercatori (10.3 FTE) 2 Tecnologi (1.1 FTE) 3 Tecnici (1.9 FTE)
Richieste ~500 kE  Assegnazioni 350 kE
GAMMA-PD 2012

## Slide 3
Dimostratore di AGATA a GSI
  Sperimentazione, supporto
Realizzazione GALILEO
  Produzione 10 criostati tripli
  Produzione 10 schermi anti–Compton
  Produzione collimatore di Pb
  Sviluppo sistema porta target
  Integrazione di rivelatori ancillari (EUCLIDES, TRACE, …)
  Allestimento DAQ
  Meccanica per RFD (Milano)
  Produzione camera di reazione (Milano)
Sviluppo scheda processore del trigger per AGATA
Esperimenti al GSI, GANIL, MSU, RIKEN
13 Ricercatori (10.3 FTE) 2 Tecnologi (1.1 FTE) 3 Tecnici (1.9 FTE)
Richieste ~400 kE
GAMMA-PD 2013

## Slide 4: AGATA

## Slide 5: The AGATA Demonstrator
5 asymmetric triple-clusters (May 2011)
36-fold segmented crystals
555 digital-channels
Eff. 3 – 8 % @ Mg = 1
Eff. 2 – 4 % @ Mg = 30
Full EDAQ with on line PSA and g-ray tracking In beam Commissioning
First installation site: LNL
Main issue is Doppler correction capability
coupling to beam and recoil tracking devices
PRISMA: large acceptance magnetic spectrometer providing event–by–event Z, A identification as well as velocity for the ions entering the device
AGATA Demonstrator @ LNL
Notes: Powerful array in its own right
Still to decide where to site
Still to decide the key test experiments

## Slide 6: Experimental Campaign at LNL
neutrons
protons
Neutron drip-line
Lifetime of the 6.792MeV state in 15O
n-rich nuclei
Lifetimes in n-rich Ni, Cu and Zn isotopes
Lifetimes of the n-rich Cr isotopes
Lifetimes near the island of inversion
Pygmy and GQR states
Neutron-rich nuclei populated by fission
N=51 nuclei
Lifetime of 136Te
Neutron-rich nuclei in the vicinity of 208Pb
Proton drip-line
Molecular structure of 21Ne
Coulex of 42Ca
Isospin Mixing in 80Zr
Octupole-deformed Ra and Th nuclei
Shape transition in 196Os
N=84 isotone 140Ba
n-rich Th and U
g.s. rotation in Dy, Er, Yb
High-lying states in 124Sn and 140Ce
20(+3) exp. 148 days
Order-to-chaos transition in 174W

## Slide 7: Doppler Correction Capability
F
O
N
C
B
Be
a
Li
16O
TKE (MeV)
dE (MeV)
Inelastic scattering 17O @ 20 MeV/u on 208Pb
β≈20%
D.Mengoni, R.Nicolini, F.Crespi
No Dopp Corr
Crystal Centers
Segment Centers
PSA+Tracking
TRACE
FEP
SEP

## Slide 8: Doppler Correction Capability – Simulations
The innovative use of detectors in position-sensitive mode (combining digital DAQ, pulse shape analysis, g-ray tracking) will result in high efficiency (~40%) and excellent energy resolution, making AGATA the ideal device for spectroscopic studies of weak channels.
Conventional array
Segmented detectors
g-ray tracking
Energy (keV)
The effective energy resolution is maintained also at “extreme” v/c values
v/c = 50%

## Slide 9: Femtosecond Lifetime Measurement in 15O
15O 6.79 MeV
τ??
15N 7.3 MeV
τ=0.65 fs
15N 8.3 MeV
τ=2 fs
source(*)
(*)
14N(2H,n)15O and 14N(2H,p)15N reactions @ 32 MeV (XTU LNL Tandem)
Direct lifetime measurement DSAM with 4 ATCs at backward angles
Astrophysical interest – CNO cycle burning rate
C.Michelagnoli – PhD

## Slide 10: Femtosecond Lifetime Measurement in 15O
15O 6.79 MeV
τ??
15N 7.3 MeV
τ=0.65 fs
15N 8.3 MeV
τ=2 fs
source(*)
(*)
14N(2H,n)15O and 14N(2H,p)15N reactions @ 32 MeV (XTU LNL Tandem)
Direct lifetime measurement DSAM with 4 ATCs at backward angles
Astrophysical interest – CNO cycle burning rate
Detected gamma-rays can be sorted in few degrees θ “slices” with a “continuous” distribution
C.Michelagnoli – PhD

## Slide 11: Femtosecond Lifetime Measurement in 15O
Lineshapes defined by the lifetime, reaction kinematics and stopping power
CDCC** calculations of the nucleon transfer process by N. Keeley
**Continuum-Discretized Coupled Channels
transfer to 8.3MeV state in 15N
center of mass x-section
2H
14N
15N
p
2H
14N
16O
15N
p
but also via fusion–evaporation
fusion-evap.
Excited states in 15O and 15N are mainly populated via nucleon transfer reactions
Developed full GEANT4 simulation of the reaction, stopping in target and g–ray detection calculated lineshapes

## Slide 12: Femtosecond Lifetime Measurement in 15O
15O
1.1fs
4.1fs
0 fs
chi-square analysis on all the “theta-slices” ongoing…

## Slide 13: AGATA Demontrator/1p Experimental Program
2010-2011  LNL 5TC
2012  GSI/FRS ≥5DC+5TC
2014  GANIL/SPIRAL2 ~15TC
AGATA D.+PRISMA
AGATA + VAMOS + EXOGAM
AGATA @ FRS
Total Eff. > 10%
Total Eff. > 20%
Total Eff. ~6%
1
2
3
4
5

## Slide 14: AGATA@GSI Commissioning
HECTOR
AGATA
ATC
ADC
ADC
Before Doppler Correction
Thanks to: M.Reese et al. and the AGATA and GSI collaborators
10keV
136Xe (137 MeV/u) + 197Au
v/c ~ 50%
hit pattern of AGATA detectors

## Slide 15: AGATA@GSI–FRS Scientific Program
40th Meeting of the GSI General Advisory Committee
(G – PAC)
Date/Time: November 23 – 24, 2011
Proposal/Title Spokersperson
S424 Scientific and Technical W.Korten
Commissioning Proposal
for the AGATA – PreSpec
campaign
S426 Relativistic M1 – Coulex of N.Pietralla
85Br
S427 Breaking of isospin symmetry E.Sahin
in the mass 70 region: Sudy
of the Tz=-1 nucleus 70Kr S.Pietri
S428 Shape evolution in neutron–
rich Zr isotopes
S429 Quadratic Evolution of Collectivity D.Rudolph
Arround 208Pb (PRESPEC – AGATA)
S430 The Pygmy Dipole Resonance in O.Wieland
64Fe and the properties of neutron
skin
S431 Proton hole states in 132Sn and P.Boutachkov
N=82 shell structure
S433 Coulomb excitation of the band– A.Gadea
terminating 12+ yrast trap in 52Fe C.A.Ur
S434 Isospin Symmetry Breaking F.Recchia
Transition Ratesand Mirror Energy
Difference in Isobaric Multiplets
Light target
Primary Beam Fission
Primary Beam Fragmentation
Light or heavy target

## Slide 16: GALILEO

## Slide 17: The GALILEO Project
GEANT4 by E.Farnea
take advantage of the recent technical developments for AGATA
preamplifiers, digital sampling,
preprocessing, DAQ
→ high count rates (30–50 kHz/det)
use of existing detectors
EB cluster detectors capsules
GASP detectors
→ high photopeak efficiency
use beam facilities at LNL
Tandem, ALPI, PIAVE – stable
SPES – RIB
→ production of new nuclei
30 GASP detectors @ 22.5cm
5 5 5 5 5 5
29o 51o 59o 121o 129o 151o
10 triple cluster (EB clusters) @ 24cm
90o
eph ~ 8% P/T ~ 50%
Start physics campaign in summer 2013

## Slide 18: GALILEO – Mechanics
  Triple cluster cryostat
  end–cap, cold finger, dewar
  use of the EB cluster capsules
  Anti–Compton shield for the TC detector
  recover the crystals from the original EB cluster shields
  Holding structure
  highly flexible, space for ancillary detectors
  Pb collimator
  divided in 4 parts
  Reaction chamber
  accomodate different ancillary detectors
  Beam line
  the structure opens along the beam line
  Ancillary detectors
  integration with the holding structure

## Slide 19: Triple Cluster Detector – First Prototype
dewar
end–cap in
Carbon fiber
Zeolites container
cold finger
capsules
front–end electronics
(warm part)
Design by C.Fanin
Mechanical workshops in Padova and Legnaro
2012 – prototypes
2013 – production 10 cryostats
Testing

## Slide 20: Triple Cluster Detector – AC Shield
2012 – design (possibility of using carbon fiber enclosure)
2013 – production 10 AC shields
construction of the triple cluster AC shield out of the individual crystals of the original EB cluster shield
→ requested the EB AC shields
EB cluster AC shield
Refurbished AC shield for TC detectors

## Slide 21: Triple Cluster Detector – AC Shield
Technical Office of Padova: C.Fanin, M.Turcato, M.Rampazzo, M.Romanato

## Slide 22: Triple Cluster Detector – AC Shield
SCM
Modena

## Slide 23: GALILEO – Location
Experimental Hall II – replacing GASP
PISOLO
8piLP
RMS
July 2012 – beam time allocated for the alignment of
the beam line and start installing the bins
GALILEO

## Slide 24: GALILEO – LN2 Filling System
Under construction in the electronics lab. of INFN Padova
same logic flow as for GASP and EUROBALL
based on NI CompactRio architecture

## Slide 25: GALILEO – Electronics & DAQ
  New electronics is being built in close synergy with AGATA
  * low–noise, fast, low–power consumption *
  new cold part (AGATA FET) – to be done
  use solutions already developed for AGATA
    core type preamplifiers – done
    GTS – done
    AGAVA interface with the VME electronics (collab. with Kracow)
  new developments for AGATA and GALILEO
    low power digitizers – prototype test
    readout and preprocessing on PCI express boards – prototype test
  anti–Compton shields signal readout
    digital (similar to the Ge detectors)
  New DAQ
  based on XDAQ developed at LNL – on going

## Slide 26: GALILEO – Preamplifiers
A.Pullia, G.Pascovici, C.A.Ur
submitted to IEEE Nuclear Science Symposium
a fast low–noise charge sensitive preamplifier based on the core–type AGATA preamplifier
over–threshold fast reset circuitry – to reduce dead–time due to preamp/ADC saturation
ToT signal – recover energy information up to 180 MeV
a fast analog trigger signal can be produced – useful for ancillary detectors
used for both tapered and triple cluster detectors
84 PA already built – tests with det. on-going
INFN Milano&Padova, User Service LNL

## Slide 27: GALILEO – Digital Sampling
Digi-opt12: 12-channel 14/16-bit 100/125-MS/s digitizer with optical output for GALILEO/AGATA
single–ended/differential analog input signals
end termination for both differential– and common–mode components of the input signals
AC or DC coupling to the ADC,
introduction and remotely-controlled adjustment of a differential DC offset, useful for dynamic range maximization
remotely controlled dynamic-range selection,
easily tuned anti-aliasing filter
precise inter-channel time synchronization
optional interleaved mode for equivalent sampling-frequency multiplication
Power consumption < 10 W / board
5 boards built
INFN Milano, Padova, LNL

## Slide 28: GALILEO – Readout&Preprocessing
INFN Padova, LNL
~30 k€
~320 W
~7 k€
~60 W

## Slide 29
Richieste GAMMA 2013 – Stima

## Slide 30
UT 5 MU
  Completamento progetto e disegni tecnici GALILEO
  Progettazione supporto meccanico TRACE
OM 12 MU
  Costruzione criostati GALILEO
  Costruzione schermi AC
  Costruzione supporto meccanico TRACE
LOE 4 MU
  Produzione e test elettronica GALILEO
CALC 1 MU
  Supporto farm di gruppo
Richieste ai Servizi della Sezione