## Slide 1: GravNet
Claudio Gatti
71th LNF Scientific Committee – May 2026

## Slide 2: GravNet A Global Network for the Search of High Frequency Gravitational Waves
Initial sites: Mainz, Bonn, Frascati
GravNet is now a Recognized Experiment at CERN
This MoU aims to extend the network beyond ERC participants.
Radio haloscope
X-band haloscope
Quantum Sensing

## Slide 3: GravNet CDR - available on arXiv
GravNet-CAPP Collaboration:
Y. Kim et al. “Search for high-frequency gravitational waves via reanalysis of cavity axion data,” PHYSICAL REVIEW D 113, 072015 (2026).
C-band
Radio

## Slide 5: FLASH Founding Meeting
The FLASH founding meeting will be held in July to formalize the collaboration.

## Slide 6: WP1 Physics Reach (L. Visinelli and F. Mescia)
“Cross correlation”
What do we gain if we correlate “axion” signals measured at the same frequency with NMR and cavity experiments within one De Broglie wavelength (10Km)? (Sreemanti Chakraborti)
NMR axion experiment: Deniz Aybas (Bilkent University); R&D in Uni Camerino cryostat at 1.5K in a 12T magnet (J. Rezvani).

## Slide 7: Physics Reach for FLASH TDR
Axion, Dark Photons, HFGW
HFGW
HFGW
TM010
Axion, Dark Photons
Credit Younggeun Kim (Mainz)
Credit Adrián Muñoz Urán (UPCT Cartagena)
HFGW
Chameleons,
HFGW, Scalars
Scalars
TE011
For the TDR writing, we are simulating the cavity modes with the new geometry and recalculating the couplings.

## Slide 8: WP2 Cryogenic Design (C. Ligi)
Definition of the RF cavity cryostat general layout details
Cryostat cryo/mechanical design of
  RF cavity
  vacuum shield
  70 K radiation shield
Cryogenic turret cryo/mechanical design
Cryogenic transfer lines design
4K cryostat for the prototype
Credit C. Capoccia

## Slide 9: P&ID for the FLASH Plant
Update of the
existing cryoplant and
Integration of the
proposed FLASH
cryo-turret in a digital
P&ID
Credit C. Ligi, R. Nikam
DAFNE Cryo plant
Valve Box
FLASH
FINUDA Magnet

## Slide 10: PFD for the FLASH Turret
Initial scheme for the FLASH cryoturret – validation and review in progress with CERN experts
70K
5K
4.2K
2K
FLASH Cryostat
Turret

## Slide 11: New Magnet Cryogenics Control System
The new FINUDA Magnet cryogenics control system (NI compact RIO – 9045) was delivered last month
Technicians are working in these weeks to
  Move the wiring (some hundreds of wires) from the old control system to the new one – A new flange needed with several connectors (purchase order in progress).
  Update the old Labview software to the new 2025 version on the new PLC
Credit L. Capuano, L. Petrucciani, G. Di Pirro

## Slide 12: FLASH Cryogenic Plant - Infrastructure Status and Open Items
PED (pressure equipment directive) Certification
  Cold box opening scheduled for May for inspections and non-destructive tests.
  Includes recertification of more than 20 safety valves from the cryogenic plant and FINUDA magnet turret — offer requested. (In progress — pending budget approval for valves)
Plant Maintenance (Vorbuchner Company - Germany) Quote received — maintenance feasible by end of 2026 or early 2027. (Order to be placed upon budget confirmation)
Water Cooling Infrastructure The cryogenic compressor (200 kW) and ancillary systems require dedicated water cooling. Three open items:
  Compressor cooling tower: damaged — evaluating replacement. Study ongoing.
  FINUDA magnet power supply: former DAΦNE cooling circuit no longer available — dedicated solution required. Study ongoing.
  Turbomolecular pumps: new chiller to be procured.
Plant Control System (Siemens Simatic S7-400 PLC) Full replacement exceeds current budget. Existing system maintained with available spare boards.

## Slide 13: 4K Cryostat for the Cavity Prototype
The design of the cryostat for the prototype is almost completed
300K Stainless Steel Flange
50K Copper Flange (+ Al Shield)
4K Copper Flange
Cavity prototype
Pulse Tube refrigerator
Feedthroughs for cavity tuning
300K SS flange design is complete – it will be machined by an external company (waiting for budget to be available)
The rest will be machined at LNF’s mechanical workshop
Rotary/linear Feedthroughs to be purchased from Pfeiffer (same as above for budget)
Wiring:
  4 RF lines
  54 DC wires
Credit C. Ligi and G. Chiaraluce

## Slide 14: WP3: RF Cavity (S. Tocci and A. Diaz)
Tuner
Cooling manifold is not needed for prototype
Cooling/connection rods for prototype only
Loop Antenna (TE mode)
Monopole Antenna (TM mode)
Rotating disk
S. Tomassini
S. Tocci
Cavity Prototype

## Slide 15: Status of Cavity Prototype
Mode | Theory (GHz) | Simulation (GHz) | 
TM010 | 0.65 | 0.71 | 1.43
TM011 | 0.85 | 0.89 | 1.16
TM110 | 1.04 | 1.12 | 1.90
TM111 | 1.17 | 1.24 | 1.50
TM012 | 1.28 | 1.29 | 1.47
TM210 | 1.40 | 1.41 | 2.06
TM211 | 1.50 | 1.51 | 1.59
TM112 | 1.51 | 1.55 | 2.46
TM020 | 1.51 | 1.58 | 2.07
TM212 | 1.77 | 1.78 | 1.68
Mode |  |  | 
TM010 | 0.65 | 0.71 | 1.43
TM011 | 0.85 | 0.89 | 1.16
TM110 | 1.04 | 1.12 | 1.90
TM111 | 1.17 | 1.24 | 1.50
TM012 | 1.28 | 1.29 | 1.47
TM210 | 1.40 | 1.41 | 2.06
TM211 | 1.50 | 1.51 | 1.59
TM112 | 1.51 | 1.55 | 2.46
TM020 | 1.51 | 1.58 | 2.07
TM212 | 1.77 | 1.78 | 1.68
Credit Adrián Muñoz Urán
RF Simulations completed
Mechanical design completed
Copper purchased
Copper roughness measured (Ra <0.6 micron)
Chemical solution for surface treatment tested on a Cu sample at LNL (target Ra<0.4 micron)
Cu packed and ready to be shipped (with many delays!) to Bonn for fabrication. Then to LNL for surface treatment and back to LNF for measurements.
Credit F. Quattrociocchi

## Slide 16: Measurement of Friction in the FLASH Tuning System
Tuner
Rotating disk
Vacuum Hole
RF sliding contact
Springs
Metal contact
Credit S. Tomassini

## Slide 17: Measurement of Friction in the FLASH Tuning System
Credit R. Doglia, A. Santoni, S. Tomassini
R
N
T

## Slide 18: Measurement of Friction in the FLASH Tuning System
Temperature (K)
Preliminary results in liquid nitrogen compatible with expectations.
Tests will be repeated in vacuum.

## Slide 19: Impact of Friction on Torsional Deformations
Ongoing simulations to understand the impact of the measured torque on the tuning system and the impact on the cavity tunability.

## Slide 20: WP4: Signal Amplification and Acquisition (P. Falferi and G. Lamanna)
Setup in Camerino University
Cryostat temperature T=1.6 K
Similar results obtained in Trento by P. Falferi
We now expect 2.2 K total noise in FLASH at 120 MHz.
No need to cool SQUID to lower T (e.g. 300 mK)!
Credit J. Rezvani, N. Pinto (Camerino) and T. Jameson, P. Beltrame (Liverpool)

## Slide 21: RF Interference Survey of the DAFNE/FLASH Hall
Credit L. Calligaris (Uni Pisa)

## Slide 22: Readout Electronics Scheme
Credit L. Calligaris
RF signal from cavity antennas are multiplexed to proper SQUID and amplified
Several options for room temperature electronics are considered to take into account requirements on: number of channels; tunability; bandwidth.
Plan to test it on the prototype.

## Slide 23
Credit A. Rettaroli, G. Mazzitelli and G. Dho
WP5: Data Analysis and Computing (K. Schmieden and G. Mazzitelli )
Spectrum digitizer successfully integrated into the FLASH/QUAX DAQ, together with all required auxiliary equipment (thermometers, cryogenic switch, etc.).
DAQ pipeline optimised strongly reducing the latency.
Storage and tape for the experiment are now available and ready to be used (handled by RUCIO)
Slow control of auxiliary variables are being integrated
Online monitor and GPS have been introduced
Ready for next QUAX run

## Slide 24: WP6: FINUDA Decommissioning and FLASH Commissioning (S. Gazzana)
Credit C. Capoccia and F. Rosatelli
This monday

## Slide 25: Refurbishment of Extraction Tools
Original FINUDA assembly tools retrieved from outdoor storage near the DAFNE area
Tools had to to be checked for corrosion and structural integrity

## Slide 26: Refurbishment of Extraction Tools
Work entrusted to an external company
Tools refurbishing 80% completed
Survey to establish reference geometry for tools alignment done!

## Slide 27: Work is underway to complete the “Clessidra” extraction by summer.

## Slide 28: Safety Analysis
Credit S. Gazzana
Consultancy contract currently underway for the preparation of a Risk Analysis (RA) relating to the FLASH experiment
What we are doing:
Mapping all risks of the FLASH+FINUDA integrated system
Ranking them by severity: direct safety risks, equipment protection, operational issues
Using the well-established FINUDA safety architecture as our starting point
How we are doing it:
Preliminary Hazard Analysis (done) — first screening of all potential hazards, filtering out non-credible scenarios
HAZOP — systematic review of how the system can deviate from normal operation and what the consequences are
Fault Tree Analysis — detailed logic analysis of the most critical scenarios to understand root causes and verify that barriers are adequate

## Slide 30: QUAX@LNF
Successful test of new tuning system (T=4K)
Heat switch repaired and installed
Improved calibration of HEMT and TWPA amplifiers with cryogenic noise-source
Successful test of TWPA with B=8.5T
Test of multi-mode acquisition for HFGW
Anti-vibration jaw (G. Pileggi)
If no further problems arise, we plan to begin data taking by the end of May!

## Slide 31: Successful test of TWPA with B=8.5T
Credit A. Rettaroli, V. Spasiano, T. Jameson, P. Beltrame

## Slide 33: COLD Lab Expansion Completed
4K cryostat for FLASH prototype
BF DR for qubit tests
HFGW and Axion experiment
Office
Storage Room
NbSe2 qubit Lab
LHe 8T cryostat
SC cavities

## Slide 34: New BlueFors Dilution Refrigerator in Operation
Testing now new qubit production from CNR IFN
Purchasing qubits from ConScience (Chalmers)

## Slide 35: In summary
Next steps in 2026:
Start QUAX Run as soon as possible (50 MHz scan)
Extraction of FINUDA “Clessidra” before summer
FLASH Prototype fabrication within summer
Quantum sensing experiments within fall
FLASH TDR by the end of the year
Pros:
New Staff positions (Tocci, Dho(50% FLASH))
New PostDoc positions (Rettaroli, D’Elia, Nikam)
PhD Student (Santoni )
New Undergrad. students (Spasiano, Doglia)
Cons:
Too much bureaucracy
Too much “bad” digitalization
 Too many delays (lost 4 months of COLD activity) and higher costs
RELIC
A new lab class on light dark matter
With M. Vignati and A. Cruciani