## Slide 1: Status of the I-Tracker Hardware
F. Grancagnolo
June 26, 2012

## Slide 2: Separation of functions
Gas containment
Wire support
Gas vessel can freely deform without affecting
the internal wire position and tension.
Wire support structure not subject to differential
pressure can be light and feed-through-less.
Gas vessel
Wire cage

## Slide 3: Gas Vessel
Solve buckling instabilities
Inner cylinder sandwich:
2 C-fiber skins, 2-ply each,
HM M30S 53 ET443 51%
+ C-foam core, 5 mm total
Grafoam® FPA-10
(0.100 g/cm2 total)
End plates: 4-ply
orthotropic (0-90-90-0)
HM M30S 53 ET443 51%
60 μm/ply - 0.0053 g/cm2
(0.021 g/cm2 total)
load multiplier = 2.4

## Slide 4: Gas Vessel
inner joint
outer joint

## Slide 5: Gas Vessel
Coupling of end plates with inner cylinder
conceptual drawing
inner cylinder section
machined insert ring
machined insert ring
end-plate
membrane
carbon fiber screw
M4
gasket
5 mm
Inner cylinder
C-foam sandwich
27 MPa
1 screw/cm2
(240 screws)
2700 N/screw
breaking load
> 9000 N
(class 10.9)

## Slide 6: Gas Vessel
Coupling of end plates with outer cylinder
conceptual drawing
spoke
stays
gasket
10 mm
C-foam
outer cylinder C-insert
end-plate
membrane
36 6x12 cm2 front end cards
s. steel
insert
C-fiber/C-foam
sandwich
gasket
s. steel
insert
gasket
s. steel
insert

## Slide 7: Gas Vessel
Material budget
 | type | # of ply - thick | [g/cm2] | X0 [10-3] | [Kg]
Inner Cylinder | HM M30S 53 ET443 Grafoam® FPA-10 HM M30S 53 ET443 | 2 ply – 120 μm 4.76 mm 2 ply – 120 μm | 0.011 0.079 0.011 | 1.95 | 4.50
Inner ring | C-fiber inserts (2.3%) | 10 mm 232.5 cm2 60 cm3 | 1.700 0.040 | 39.81 0.92 | 0.10
End plates | HM M30S 53 ET443 | 4 ply – 240 μm | 0.021 | 0.41 | 0.26
Outer ring | C-fiber inserts |  |  |  | 
Outer Cylinder | … Grafoam® FPA-20 … | 32 ply – 2.5 mm 10 mm 32 ply – 2.5 mm | 0.325 0.324 0.325 |  | 

## Slide 8: Gas Vessel
Possible improvements
  Running the drift chamber gas mixture at low pressure:
    i.e. He / iC4H10 = 80/20 at 500 mbar (see ref. ………)
    besides reducing the gas contribution to multiple
    scattering, allows for using lighter C-fiber and C-foam:
    Areal mass and X0 may then become, respectively,
    0.051 g/cm2 (0.100) and 1.0×10-3 X0 (1.95×10-3)
    for the inner cylinder and
    0.012 g/cm2 (0.021) and 2.3×10-4 X0 (4.1×10-4)
    for the end plates.

## Slide 9: Gas Vessel
M. Cascella et al.
contribution to the
Elba Conference, May 2012

## Slide 10: Gas Vessel
Graphene loaded C-fiber
(avoids the need of a metal sheet)
gas containment
electrostatic shielding
electromagnetic shielding
Formation of a ‘tortuous path’ of platelets inhibiting diffusion of gases through a polymer
composite (Nielsen Model)

## Slide 11: Wire Layout
36 co-axial layers of para-axial wires in 24 azimuthal sectors;
stereo angles from ±100 mrad to ±180 mrad;
384 square drift cells per layer (16 per sector);
cell size ranging from 6.27 mm at the innermost layer, to 11.12 mm at the outermost one;
ratio of field wires to sense wires = 5 : 1;
13824 sense wires – 69120 field wires – 3072 guard wires;
sense wires 20 μm diameter gold plated W (30 g /100 μm);
field wires 40 μm diameter gold plated Al (25 g /100 μm);
total wire tension 2220 Kg.

## Slide 12: Drift Cell Layout
+ stereo angle
- stereo angle
guard layer
field and guard wires: 40 μm diameter Au-plated Al
sense wires: 20 μm diameter Au-plated W

## Slide 13: Inner layers layout
inner cylinder
inner cylinder
guard wires
layer
@ z = ±L/2
@ z = 0
r =

## Slide 14: Outer layers layout
outer cylinder
guard wires
layer
@ z = ±L/2
@ z = 0
r =
outer cylinder

## Slide 15: Chamber layout
Radii (at z = 0) |  | 
Inner Cylinder | 370.0 | mm
Guard wires layer | 375.0 | mm
First active layer | 380.0 | mm
Last (36th) active layer | 685.0 | mm
Guard wires layer | 690.0 | mm
Outer Cylinder | 720.0 | mm
Radii (at end plate) |  | 
Inner Cylinder | 370.0 | mm
Guard wires layer | 388.2 | mm
First active layer | 393.5 | mm
Last (36th) active layer | 709.1 | mm
Guard wires layer | 714.3 | mm
Outer Cylinder | 720.0 | mm
Active length | 2000 | mm
Number of layers / of stereo sectors | 36 / 24 | 
Number of cells per layer / per sector | 384 / 16 | 
Cell size (at z=0) | 6.27 ÷ 11.12 | mm
2α angle | 30° | 
Stereo angle | 100 ÷ 180 | mrad
Stereo drop | 13.5 ÷ 24.1 | mm
sense wires | 13824
field wires | 69120
guard wires | 3072

## Slide 16: The Wire Cage Assembly
Assembly strategy
Constrain the end rings at the
  outer radius to a rotating jig
  able to withstand the wire
  tension.
Remove the struts.
Buildup the layers by rotating
  the jig.
Recover the wire tension by
  pulling on the stays for each
  sector.
Mount the struts
Insert inner cylinder
Close with the outer panels

## Slide 17
Layers buildup

## Slide 18
Layers buildup

## Slide 19
Layers buildup

## Slide 20
Layers buildup

## Slide 21
Layers buildup

## Slide 22
Layers buildup

## Slide 23
Layers buildup

## Slide 24
Layers buildup

## Slide 25
Layers buildup

## Slide 26
Layers buildup

## Slide 27
Layers buildup

## Slide 28
Layers buildup

## Slide 29
Layers buildup

## Slide 30
Layers buildup

## Slide 31
Layers buildup

## Slide 32
Layers buildup

## Slide 33
Layers buildup

## Slide 34: The Prototype
Half way through
Scheduled to be completed
by end of summer

## Slide 35: Wire Cage Materials

## Slide 36: Wire Cage
inner cylinder
outer cylinder
end-plate
membrane
spoke
stays
active
area
2220 Kg
24+24
= 50 Kg/spoke
or 1.7 Kg/cm
load on stays:
load on spokes:
50 Kg/8 =
6.25 Kg/stay
cos(64°)
or 14.3 Kg/stay

## Slide 37
Spokes
3x5 mm2 unidirectional C-fiber
max displacement < 6 mm under 500 N

## Slide 38: Spacers
polycarbonate

## Slide 39: Field wire boards

## Slide 40: Sense/Field wires board (signal side)
signal connector or
soldered signal cable
16
channels

## Slide 41: Sense/Field wires board (HV side)
HV connector or
soldered HV cable
16
channels

## Slide 42: Wire cage
Material budget
 | [g/cm2] | X0 [10-3] | Hit probability | [g/cm2] | X0 [10-3]
Spokes | 0.397 | 9.30 | 0.0225 | 0.009 | 0.2
Stays | 0.009 | 0.19 | 0.00775 |  | 
Spokes connecting ring | 0.850 | 19.9 | 0.023 | 0.019 | 0.5
Spacers | 0.074 | 1.80 | 0.878 | 0.065 | 1.6
field wires board | 0.720 | 2.64 | 0.05 | 0.036 | 1.3
sense wire board | 1.800 | 6.59 | 0.024 | 0.045 | 1.6
R/O board components |  |  |  | 0.027 | 1.2
HV board components |  |  |  | 0.047 | 2.0
R/O cables |  |  |  | 0.001 | 0.0
HV cables |  |  |  | 0.019 | 1.2

## Slide 43: Total Material Budget
 |  | Wire Cage |  | Gas Vessel |  | TOTAL | 
 |  | [g/cm2] | X0 [10-3] | [g/cm2] | X0 [10-3] | [g/cm2] | X0 [10-3]
Upstream End-Plate | Spokes + Stays | 0.009 | 0.2 | 0.021 | 0.4 | 0.203 | 6.3
 | Spacers | 0.065 | 1.6 |  |  |  | 
 | Wires board | 0.081 | 2.9 |  |  |  | 
 | R/O components | 0.027 | 1.2 |  |  |  | 
Downstream End-Plate | Total above | 0.182 | 5.9 | 0.021 | 0.4 | 0.297 | 10.7
 | R/O + HV comp. | 0.074 | 3.2 |  |  |  | 
 | R/O + HV cables | 0.020 | 1.2 |  |  |  | 
Inner Cylinder | Connecting rings |  |  | 0.107 | 2.5 | 0.208 | 4.4
 | Sandwich |  |  | 0.101 | 1.9 |  | 

## Slide 44: Front-end Electronics
F. Grancagnolo - The I-Tracker
44

## Slide 45
The actual geometry implementation reproduce in a detailed way the description of the new configuration (see F. Grancagnolo talk).

## Slide 46
Electronics boards: 12 cm x 6 cm x 3mm G10 (FR4);
signal cables (only downstream): 2.032 cm x 25 µm Kapton + 40 µm 16 pairs of Copper wires;
HV cables (only downstream): 500 µm Copper wire + 500 µm Teflon insulation;
Wire anchoring (see next slide);
Carbon fiber wire support.
Connecting ring is described as a circular layer: 1.0 cm x 1.5 cm Carbon fiber

## Slide 47
The wire anchoring system:
Field wire board: 4 mm x 200 µm G10(FR4);
Spacer: (see F. Grancagnolo talk for details) made of polycarbonate, instead of holes it is drawn with spokes but with the same area ratio.
Sense wire board: 1 cm x 200 µm G10(FR4) plus components: 1) termination resistance: 1.6 mm x 800 µm x 450 µm Aluminum; 2) HV Capacitance: 3.17 mm x 1.57 mm x 1.7 mm Aluminum; 3) HV resistance (only downstream): 5 mm x 2.5 mm x 550 µm Aluminum.
FWboard
FWboard
Spacer
Spacer
SWboard

## Slide 48: Backgrounds from stopping target
Average single cell occupancy integrated over 120 ns vs time within a mircobunch
All contributions together

## Slide 49: Performance (momentum resolution)
σ ~ 155 keV/C
Shift ~ 60 keV/C
eff ~ 90%
cutacc~ 43%

## Slide 50: Performance (momentum resolution)
σ ~ 110 keV/C
Shift ~ 40 keV/C
eff ~ 90%
cutacc~ 43%
In case of gas at lower pressure an a inner wall made of two 80µm C-fiber skins and 3mm C-foam @ 80 mg/cm3

## Slide 51
At the current stage we have a basic pattern recognition that we used to test and train the chain of Pattern Recognition an Kalman filter.
The basic ideas of this pattern recognition are:
Identify cluster of contiguous cells per layer;

## Slide 52
Start by the larger cluster at the outermost radius;
Define a point in space as the crossing points between the extreme hit of the selected cluster with the extreme hits of the clusters at the lower layer;
continue to go down (in layer) until there are potential crossing point;
With the all potential 3D points, use robust helix fit of the TT.