## Slide 1: An overview of FLUKA
Daniele Calzolari (CERN SY-STI-BMI) with material from previous lectures by G. Lerner, A. Lechner, F. Salvat Pujol, F. Cerutti
An overview of FLUKA https://agenda.infn.it/event/51984/
Roma 4/5/2026

## Slide 2: Where we come from
FLUKA was born in the 60s at CERN with Johannes Ranft
It was further developed in the 70s and 80s in a collaboration between Leipzig University, CERN and Helsinki University of Technology for applications, e.g. at CERN’s high energy accelerators, and in the 90s with INFN, among others for the design of SSC and LHC
From 2003 until August 2019 maintained and developed under a CERN & INFN agreement
From December 2019, new CERN distribution aiming to ensure FLUKA's long-term sustainability and capability to meet the evolving requirements of its user community, welcoming contributions by both established FLUKA contributors as well as new partners within an international collaboration.
Presently a joint development & management team based in the CERN Accelerators and Technology Sector and Radiation Protection Group and at ELI-Beamlines (Prague) and FNAL, with contributors from the CERN Research and Computing Sector, JRC-Geel, ANL, BNL, and STFC, is in place.

## Slide 3: FLUKA.CERN distribution
https://fluka.cern

## Slide 4: Licensing scheme
Licenses are free except for commercial use
They are granted for non-military use only
For central FLUKA installations on computing clusters of universities/institutes it is not necessary to obtain an Institutional FLUKA Licence. However, it is mandatory that all FLUKA users register on the fluka.cern website and accept the Single User Licence Agreement.
Registration options | access to
FLUKA Single User License Agreement | binary code
Affiliates of institutes with a FLUKA Institutional License Agreement | source code too
CERN Staff members and Fellows | 
Affiliates of institutes which signed the FLUKA Memorandum of Understanding | development version (binary and source code)
Companies which purchased a FLUKA Commercial License Agreement | binary code

## Slide 5: User support
FLUKA user forum
https://cern.ch/fluka-forum
Note: an independent one-time registration is required to be able to participate
FLUKA training
https://indico.cern.ch/category/9178
Beginner and advanced courses are held on a regular basis across the world
The first topical course (on Radiation Protection) was held in November 2024

## Slide 6: Flair
https://flair.cern

## Slide 7: 1. The transport problem

## Slide 8: Monte Carlo methods: history
First experiments by Fermi (~1930) to study neutron diffusion, no publications
Extensive use for neutronics in nuclear weapons applications. First proposal by Stanislaw Ulam, with contribution by Metropolis and Neumann
Radiation source
Propagation in matter
Scoring
Neutrons: best example (no continous Coulomb scattering)
… but also other particles (p, e+/-, photons, pions, muons etc.)
Radioactive elements decay
Interaction described as cross sections: likelihood of interaction per unit quantity of interest (solid angle, energy, ...)
Any quantity related to the particle fluences, energy deposition or interaction events
Non trivial problem!
The transport problem

## Slide 9: Particle interactions: cross section and mean free path
Particle-matter interactions are stochastic processes, governed by the laws of quantum physics and relativity (i.e., Quantum Field Theory)
The fundamental quantity of each particle-matter interaction process is the cross section (σ), measured in barn (1b = 10-24 cm2)
For each particle travelling through matter, we can use it to compute the mean free path (λ, in units of length), measuring the average distance between two interactions:
The cross section is a property of the physics process, and it depends exclusively on the characteristics of the initial and final states (i.e., identity and energy of the particles/atoms). Everything else in the above formula is simply there to “count” the target atoms in the volume of interest.
Atomic density (1/volume)
Material density (mass/volume)
Molar mass (mass/mol)
Avogadro’s number (6.022∙1023 mol-1)

## Slide 10: Application: transport problem
Given a particle density n0(r,E,Ω,t=0), determine the radiation field of any given particle species, with different energies E, and directions Ω
Source particle
Sample step until next interaction
Sample nature of interaction
Sample final state of generated particles

## Slide 11: …and charged particles?
Coulomb scattering & ionization losses: charged particles lose energy and interact almost continuously
Typical Monte Carlo solution → condensed history:
  Moliere theory of multiple Coulomb scattering: the cumulated effect of several scattering events is condensed in a distribution
  Ionization losses (below the δ-ray threshold) distributed on the track length
Source particle
Sample step until next interaction
Sample nature of interaction
Sample final state of generated particles

## Slide 12: How to solve the transport problem?
Several solution strategies for the transport problem:
  Analytical: only restricted geometries and interaction models
  Spectral: with symmetries, expand in appropriate basis functions. Restricted cases
  Numerical quadrature integration: inefficient in high-dimensional integrals
  Monte Carlo: general, efficient for arbitrary geometries and radiation fields
Generic Monte Carlo problem: P is a probability measure, g is a function of the random variable
Sample Xi from the correct distribution (not trivial!) given a pseudo random number
Calculate the g(Xi) quantity of interest
Obtain the integral as the mean

## Slide 13: Application: scoring & estimation
The typical applications require the scoring of fluence/star related quantities (energy deposition, number of interactions, etc)
Any physical observable is the average of the contribution of all particles in the field. The estimator chosen is the sample mean, under the assumption that the CLT can be applied
In FLUKA, the choice made is to adopt a batch analysis (instead of history by history). Assuming N batches, with ni primary particles and average scoring xi in the i-th batch, the estimator and uncertainty are:

## Slide 14: Uncertainty and statistics
How many primaries? The more, the better*. In general, as rule of thumb:
This does not include systematic errors, such as:
  Physics
  Algorithm artifacts
  Missing (or uncertain) data
  Material & geometry composition
  Uncertainty on the source terms (beam losses estimation)
Relative error | Estimator quality
>50 % | Garbage
20 – 50 % | Order of magnitude
10 – 20 % | Questionable
<10 % | Reliable (generally)
*biasing is an effective alternative solution

## Slide 15: 2. Geometries in Monte Carlo

## Slide 16: Geometries in Monte Carlo
When following the particles, the code continuously ask:
  Where am I?
  Where am I going?
  How far can I travel before an interface?
The geometry implementation in the codes (FLUKA, GEANT, …) needs to be fast and versatile.
Most recent codes allow to use CAD imported assemblies with tesserated solids
Simple and extremely fast
Employs lattice and replica capabilities
Each volume has a “mother”
More complicated to implement ex-novo
Lot of geometry shapes available
FLUKA: Constructive solid geometry
GEANT: Hierarchical

## Slide 17: Geometries in FLUKA
Four fundamental concepts:
  Body: basic geometry object (finite or infinite: planes, spheres, …).
  Zone: sub-region composed by intersection and subtraction of bodies.
  Region: union of zones
  Lattices: duplication of existing regions confined in a container volume

## Slide 18: CAD / unstructured meshes
Geometries can be described also using unstructured meshes:
  More precise geometry descriptions (including gaps, penetrations, details)
  ...but more complicated to perform parametric scans (varying a single element in the geometry)
30 MeV
protons
CAD
MESH
FLUKA
ICRP P145 phantom
(initialization < 10 s)

## Slide 19: Linebuilder: a specific accelerator solution
Together with FEDB (FLUKA Element DataBase), organize all the necessary information for creating complex, modular and detailed geometry
Build beamlines in 3D
Automatically handles the scorings (USRBIN)
Elementary models + instruction set
Betatron halo collimation
pp collision debris
Muon collider MDI geometry
A. Lechner et al., Phys. Rev. Accel. Beam (22), 071003, 2019.
Now public here!

## Slide 20: 3. Main interaction models

## Slide 21: Photon interactions basics
Photons can be produced by many different mechanisms:
  Bremsstrahlung emission
  Gamma de-excitation after nuclear reactions
  Radiative neutron capture
  Electron-positron annihilation
  Particle decay (e.g., π0)
Their interaction mechanisms vary depending on the photon energy and on the target material:

## Slide 22: Photon interactions cross sections
Extra: photonuclear reactions (lower cross sections)

## Slide 23: Charged particle interactions with electrons and nuclei
Coulomb interactions with atomic electrons
Leads to the ionization (or excitation) of the atoms, with the production of knock-off electrons (δ-rays if high-E)
Most relevant energy loss mechanism up to:
  Tens of MeV for e+/-
  Hundreds of GeV or more for μ+/- and charged hadrons*
Causes energy deposition in the material → heating
Coulomb interactions with atomic nuclei
Dominant source of angular deflections for charged particles
The associated energy loss is referred to as Non-Ionizing Energy Loss (NIEL)
In general, NIEL is less relevant than atomic electron losses, except for low-energy heavy ions
Radiative processes
Lead to the emission of photons from the interaction between the particle and the field of the atomic nuclei
Dominant energy loss mechanism for high-energy projectiles*
*for high-energy hadrons, nuclear interactions play a major role in the energy loss mechanisms

## Slide 24: Coulomb interactions with atomic electrons: Bethe formula
Key equation describing the energy losses via ionization for all charged particles heavier than e+/-
High stopping power at low energies due to high photoelectric cross sections
Minimum Ionizing Particles (MIP) at βγ ≈ 3-3.5, releasing 1-2 MeV cm2/g
Radiative losses dominate at high energy
At the critical energy , ionization and radiative stopping power are equal:
For e+/-, is substantially lower

## Slide 25: Nuclear interactions: introduction
In nuclear interactions, the strong force plays a major role (but electroweak processes also take place)
ELASTIC INTERACTIONS
Do not modify the internal structure of the particles involved in the interaction, i.e., the initial and final states are the same
They “only” yield energy transfer (including the recoil of target nuclei in projectile-nucleus reactions) and angular deflections
There are no energy thresholds
They are highly relevant for neutral projectiles (e.g., neutrons) at low energy. For charged projectiles, they compete with Coulomb scattering.
INELASTIC INTERACTIONS
The internal structure of the particles is modified in the interaction, and/or new particles are produced
Energy thresholds are usually present, because typically one needs a minimum amount of energy to “break” the incoming particles/nuclei, produce new particles (e.g., pions), and/or excited nuclear states.
Exception: neutron capture (inelastic interaction with no threshold)

## Slide 26: Nuclear interactions: nucleon-nucleon cross sections
Nucleon-nucleon cross sections are the basis to understand more complex cross sections with nuclei.
At low energies, elastic interactions are dominant. At intermediate energies, the reactions proceed through intermediate resonant states (e.g., Δ(1232))
At high energies, the cross section is driven by inelastic processes involving single partons (quarks/gluons), and it reaches a constant value for both pn and pp reactions.

## Slide 27: Inelastic hadron-nucleus reactions
FAST STAGE (10-22 s)
The projectile interacts with nucleons, producing secondaries (mainly π, but also, other hadrons, γ…) with high multiplicity (≈log[E])
The more energetic secondaries leave the nucleus and develop a forward-directed hadronic cascade (see next slides)
The less energetic secondaries can deposit energy within the nucleus, leaving it into an excited state
SLOW STAGE (10-16 s)
MeV-scale light fragments from evaporation and photons from γ-deexcitation
Heavier fragments from fission (when possible)
In summary, one gets:
An energetic hadronic shower from the fast stage*
MeV-scale fragments and photons
Optionally, fission products (that may be radioactive, as the residual nuclei)
*if the projectile has enough energy

## Slide 28: Focus on neutron interactions
Neutrons are hadrons with unique features:
  Long half-life (>10 minutes) → effectively stable
  No charge → no Coulomb force
They travel long distances through matter, and they undergo a moderation process, i.e., they progressively lose their energy via a sequence of elastic nuclear interactions
Eventually they can thermalize, i.e., their kinetic energy can drop to the thermal scale (≈25 meV at room temperature)
TYPICAL NEUTRON CROSS SECTION PATTERN:
Low-E (≲ eV)*
eV-MeV range*
High-E (>MeV)*
σ decreases with E (σ≈1/v), n capture reactions take place
Resonances are present, varying with the target nucleus (difficult to model)
The behaviour becomes similar to the one of the other hadrons
*highly variable with A
>MeV region not shown

## Slide 29: High-energy e+/-, γ: electromagnetic (EM) showers
When the projectiles are above the previously introduced critical energy , the dominant interaction mechanisms in matter are:
An electromagnetic shower (or cascade) develops, where the above processes are repeated until the produced particles fall below
The key parameter is the radiation length X0:
  Mean distance over which the energy of e+/- is reduced to 1/e
  7/9 of the photon Bremsstrahlung mean free path
X0 represents the characteristic length of the EM shower steps
Note: neutrons can also appear (with relatively low abundance) from photonuclear reactions

## Slide 30: EM showers: key features and energy deposition
EM shower evolution vs depth, in units of X0 (t = z/X0):
X0 by material, where
Maximum number of particles at depth tmax:
The peak energy deposition in the target material (important to assess the impact of the shower!) is typically right before tmax
(typically a few X0 depending on projectile energy and material)

## Slide 31: Hadronic showers
We have seen that the interaction cross section of high energy hadrons tends to stabilize → we can define a nuclear interaction length λI, i.e., the mean distance travelled between two inelastic interactions
High energy hadrons generate showers similarly to the electromagnetic ones, but they involve sequences of hadronic interactions
λI is the key parameter of hadronic showers and it’s typically longer than X0
The particle content of hadronic showers is richer compared to EM ones
Neutral pions decay into two photons, leading to the generation of secondary EM showers within the hadronic shower itself!
The fraction of energy that goes into EM particles varies stochastically between showers

## Slide 32: 4. FLUKA main capabilities

## Slide 33: Physical processes: continuous and discrete
Main assumption: particle scattering occurs on a single target
Typical inter-atomic distances are ~1Å. MC simulation of electron transport << 100 eV is generally questionable
De Broglie wavelength
Discrete processes: simple!
Coulomb scattering & ionization: continuous

## Slide 34: Physical processes: continuous and discrete
hadron-hadron and hadron-nucleus interactions
nucleus-nucleus interactions (including deuterons)
photon interactions (>100 eV)
electron interactions (> 1 keV; including electronuclear)
muon interactions (including photonuclear)
neutrino interactions
low-energy (<20 MeV) neutron point-wise interactions
particle decay
synchrotron radiation emission
Simple algorithm: the particles are unaffected between interactions
Main discrete interaction mechanisms
Source particle
Sample step until next interaction
Sample nature of interaction
Sample final state of generated particles

## Slide 35: Physical processes: continuous
Elastic scattering of charged particles on screened electrostatic potential of target atoms (Coulomb scattering)
Collisions of charged particles with target electrons: continuous energy loss along the particle step
Typical solutions: condensed history for ionization losses, and Molière theory for multiple Coulomb scattering
Warning: in residual gas or thin geometries (few elastic collisions) single Coulomb scattering shall be adopted
EMFP: mean free path between Coulomb interactions
IMFP: mean free path between ionization losses
e- in Al
1 MeV e- ≈ 104 interactions

## Slide 36: Scoring & estimators
The result of the Monte Carlo experiment is called estimator. The main types used in the MDI are:
  Star like quantities: energy deposition, ionizing dose, displacement damage
  Fluence like quantities: e+/- fluence, 1 MeV n eq. in Si
  Double differential distribution (angle/energy) of particles crossing a boundary
  Particle spectra in volumes
When the full phase-space is required to transmit information, the data are stored in particle lists

## Slide 37: Biasing
Biasing is a variance reduction technique which distort distribution to minimize the variance.
Among the various techniques, the most important ones are:
  Region importance biasing: applied when a particle crosses a boundary between two region with different importance
  Mean free path: the cross sections are scaled by a factor to enhance the rare interactions
Figure of merit: σ2t

## Slide 38: 5. Radiation Quantities

## Slide 39: What happens in case of LHC beam losses?
Air
Rock/soil
Magnet
Tunnel walls
Water supply lines
Considering again a single 450 GeV proton that interacts with an LHC magnet
FLUKA geometry: section (x-y) of the LHC tunnel showing a dipole magnet

## Slide 40: What happens in case of LHC beam losses?
Air
Rock/soil
Magnet
Tunnel walls
Water supply lines
Large radiation shower developing both within the magnet and in the surrounding tunnel!
FLUKA geometry: section (x-y) of the LHC tunnel showing a dipole magnet

## Slide 41: Accidental loss: historical example from SPS (2004)
In the pre-LHC phase, an incident occurred at the SPS during the extraction of an LHC-like beam (450 GeV protons, 3.4∙1013 p, 2.5 MJ)
Major damage to the vacuum chamber, requiring a magnet replacement (weeks of downtime)
CERN-AB-Note-2005-014

## Slide 42: Energy deposition in SC magnets: quenches
Maximum temperature increase that LHC dipole coils can sustain without losing their superconducting (SC) state:
There are regions where the margin is a mere increase of 2 K
An instantaneous energy deposition of O(mJ/cm3) can lead to a quench
After a quench, it can take ~1/2 day to recover (cryogenics)
Systems are in place to protect SC magnets from quenching
Figure of merit: Heat deposition

## Slide 43: Material degradation from TID
A key observable linked to energy deposition is the Total Ionizing Dose (TID), i.e., the energy deposition per unit material mass:
, in units of Gy = J/kg
TID can alter the mechanical, electrical, and optical material properties of organic materials, compromising the integrity and the functioning of the accelerator equipment
Damage to magnets coils and insulation is particularly critical, but TID affects also cables, lubricants, etc.
LEP damage to cables and magnet insulation (NIM B)
Grease, lubricants (M. Ferrari)
Magnet insulation (P. Fessia)
Figure of merit: Dose

## Slide 44: Displacement Damage (DD) and DPA
Non-Ionizing Energy Loss (NIEL) can cause material damage by displacing atoms from their reference position in the lattice
Quantified by the Displacement Per Atom (DPA):
Number of atomic displacements from the reference position in the lattice (e.g., DPA=0.1 means that ~10% of the atoms have been displaced)
 | SC type | Radiation source | Shielding inserts (Δr) | Scenario | DPA-NRT | Ionizing dose
HL-LHC final focus quadrupoles | Nb3Sn | Proton-proton collision debris | 1.6 cm W-alloy | 3000 fb-1 (10 years) | 1.5x10-4 | 20-30 MGy
FCC-hh final focus quadrupoles | Nb3Sn / REBCO | Proton-proton collision debris | 4 cm W-alloy | 30 ab-1 (20 years) | 4-5x10-3 | 60-80 MGy
Muon Collider (10 TeV) arc magnets | Nb3Sn / REBCO | Muon decay | 3 cm W-alloy | 10 ab-1 (5 years) | 5x10-5 | 20 MGy
Muon Collider target solenoid | REBCO | Proton beam on target | 35 cm W-alloy +H20+BC layer | 10 ab-1 (5 years) | 5x10-3 | 50 MGy
Relevant for radiation damage studies to superconductors, with interesting cross-disciplinary links (e.g., fusion magnets)
A. Lechner

## Slide 45: Displacement Damage (DD) and DPA
Non-Ionizing Energy Loss (NIEL) can cause material damage by displacing atoms from their reference position in the lattice
Quantified by the Displacement Per Atom (DPA):
Number of atomic displacements from the reference position in the lattice (e.g., DPA=0.1 means that ~10% of the atoms have been displaced)
Relevant for radiation damage studies to superconductors, with interesting cross-disciplinary links (e.g., fusion magnets)
10-3 DPA → Loss of superconductivity
0.1 DPA → Loss of thermal conductivity
~1 DPA → Embrittlement and hardening
~10 DPA → Swelling
Not only colliders!
Structural materials for fission & fusion energy.
Steven J. Zinkle, Jeremy T. Busby

## Slide 46: How (and why) FLUKA?

## Slide 47: The “naked” inputfile
WHAT(1)
Card name
WHAT(2)
WHAT(3)
WHAT(4)
WHAT(5)
WHAT(6)
SDUM
FLUKA’s story began a long time ago (1970s)…
…no graphical interfaces, input and output via text file
Input files:
  can be very long > 50k lines
  based on “cards”: .inp file
  Each card has 1 name, 6 values (called WHATs), 1 string (called SDUM)
BEAMPOS 4750.5 130.0 4866.5 NEGATIVE
BEAM -0.4 0.2 5.0 1.E-4 1.E-4 ELECTRON

## Slide 48: Flair: the GUI
In 2006, Flair was born! It is a layer between the user and FLUKA
Flair ≠ FLUKA
How are the cards grouped?
Alphabetical listing
also available
Input file tree
Cards grouped according to
their “field of action”

## Slide 49: Flair: the GUI
In 2006, Flair was born! It is a layer between the user and FLUKA
Flair ≠ FLUKA
Online geometry view and editing!
Many other advantages such as:
Parametric scan capability
Automatic postprocessing
Plotting

## Slide 50: (Some) possible sources of radiation
The basic sources FLUKA considers are:
  Beam-like: one or multiple beams starting from fixes positions
  Volumetric: uniformly distributed in volumes
Special sources available in FLUKA
  Colliding beams
  Cosmic rays
  USRBIN source
… or program your own custom sources (Source routine)!

## Slide 51: Geometry and materials
FLUKA employs a combinatorial geometry (described few slides ago…)
Materials are assumed homogeneous (except for crystals!) → only the stoichiometry and the density matter
A set of base elements and compounds is provided by standard. It includes:
  VACUUM → obvious definition (electric field is allowed only here!)
  BLCKHOLE → particles are stopped. This must surround your whole geometry
Element definition
Compound definition

## Slide 52: Physics & transport
FLUKA is not a toolkit
Users can select the lower energy thresholds for production and transports
Some interaction are not on by default (e.g. photonuclear). If needed, they need to be requested
The production (and tracking) of low energy electrons and photons is one of the most CPU expensive tasks. Users should set the lowest value compatible with their simulation
  Basic idea: put transport threshold at energy such that the range is smaller than the bin length

## Slide 53: FLUKA scoring
Where?
In regions, across boundaries, on region-independent grids
When?
At the end of each cycle or at each event
What?
Energy deposition and derivatives (dose), fluence or current versus energy, angle or other kinematic variables, time, DPA, residual activity…
Output?
Saved in [inputname]nnn_fort.## files, where nnn is the cycle number & ## is the logical unit number chosen by the user
Results?
Post-processing utilities merge cycles, calculate average and rms, provide data files for plotting. Available via Flair
User code needed for processing of custom scoring!
Results normalised per primary

## Slide 54: FLUKA scoring
Energy deposition
USRBIN
EVENTBIN
On a grid or in selected regions
Fluence
vs. position
vs. energy
vs. energy or other
USRBIN
USRTRACK USRCOLL
USRBDX
USRYIELD
On a grid
In a region
On a surface
On a surface
At interaction
Energy-integrated
Single-differential
Double-differential E,surf
Double-differential, single interval on 2nd variable.
If angle, wrt beam
Activation
RESNUCLEi
USRBIN
vs. position
vs. nuclide
In a region
On a grid or in selected regions

## Slide 55: Some case studies

## Slide 56: Muon collider: target
Radiation damage in superconducting solenoid
p impacting on a target, producing π+-
Muon yields
Tentative extraction
(spent proton beam)
…decaying in μ+ and μ-

## Slide 57: Muon collider: detectors
Table: radiation load for each magnet in the final focus

## Slide 58: Inner triplet W shielding for HL-LHC
Dose < 30 MGy
Beam loss / radiation source
MC simulation
Mitigation strategy

## Slide 59: Beam-gas collisions in LHC
beam
scattered particles
gas
Despite the vacuum system, the beam can interact with residual gases, causing radiation showers
There are also beam instruments that exploit local injections of gas to perform specific measurements (e.g., Beam Gas Curtain monitor) causing local showers with higher intensity
D. Prelipcean

## Slide 60: FCC-ee dipole shielding
SR photons are intercepted by photon stoppers all around the FCC-ee arcs
For the high-energy beam modes (with higher SR Ec) massive shielding is required to mitigate the resulting radiation levels in the tunnel → shielding is an important (and expensive) design element for the FCC-ee!
Baseline material: Pb94Sb6 (10.88 g/cm3)
W-alloys (17-19 g/cm3) discarded for cost reasons
B. Humann

## Slide 61: Other applications (selection)
High-energy physics & accelerators: beam-induced background (BIB), energy deposition in magnets and detectors, machine protection, system design (collimation, beam dump, etc.)
Radiation protection: dose calculations, shielding optimization for accelerators and facilities, residual activation and environmental impact studies
Medical physics: proton and heavy-ion therapy simulations, patient dose distributions, treatment planning verification, radiobiology studies
Space & aerospace: cosmic ray interactions, astronaut dose assessment, spacecraft shielding design, single-event effects in electronics
Nuclear engineering & activation: radionuclide production, material activation, decay heat, waste and transmutation studies
Detector design & experiments: background estimation, radiation damage to the detectors
Industrial & applied physics: radiation effects on electronics (SEE, TID), irradiation facilities, sterilization, non-destructive testing and material analysis

## Slide 62
Thank you for your attention!