## Slide 1: Status of FTK & requests 2013
Paola Giannetti, INFN Pisa, for the FTK Group
ATLAS Italia, May 17, 2012
Old Milestones: we have even more relaxed our schedule
Status of FTK work
Money requests for 2013
NEWS & Future steps
TDR with tested prototypes June 2013
University of Geneva joined FTK for the LAMB project
LPNHE and University of Tessaloniki show interest
Heidelberg got few funds (25 keuros x 4 years)
However we miss manpower !

## Slide 2: VS: 45degree phi towers (0.3<h<1.15)
4 pix links (L1, L2) + 4 SCT links
RODs per tower (0.3<h<1.15)
Total 16 ROLs for 2 towers
1 EDRO + 1AMB
=1 tower

## Slide 3: VS idea born for m~5-10 (CDF chip, 6 layers only) – now m~30 !
80% bank e, m~20
→ no more than ~10 kHz event – a lot of fakes because 6 layers only
NO VS study for m~30 but certainly worse!
Take only muon triggers (use L1 ID in the header)
We will also prescale events inside FTK_IM
We will use banks with low efficiency to reduce # found roads
We will cut the Amboard output at 1000 roads.
  Events will start to be complete only when m < ~20 (later in the store).
  NO TRACK FITTING – ONLY ROAD FINDING!
Verify integration of FTK prototypes with ATLAS TDAQ
Verify that real-time FTK output with collision data
corresponds to FTK simulation

## Slide 4
NEW crate @CERN this week for LAB 4
Extra PC + Quest needed

## Slide 5: AMBoard generations & tests
Old – CDF like
64 AMchips
New – 128 AMchips
6 A @ 48 Volts
270 Watts@1,8 V
5V / 345A,
3,3V /115A,
48V /81A,
Final crate – Wiener - soon @CERN
AMBslim5 for
standard test stands
AMBslim5++ for cooling tests
NEW:AMBFTK
for 2015 (PI-MI)
Just ordered the PCB
LAMBFTK just routed
(PG-PI-PV)
PI-PV

## Slide 6: Next tests: AMBFTK and Proto-AUX
P3: 12 (1.5 GHz)+ 8 (3GHz)
= 20 serial links
TEST OF: - Serial links
VME on Proto AUX
Compatibility with new AMchip
A lot of high frequency
Serial links
Proto
AMBoard
Proto
AUX
ISOLA per buon contatto P3
Milano - Pavia:
Mechanics studies
Tested OK
Backplane
VME

## Slide 7: AMCHIP04 big Jump in technology! (LNF, Pisa, Milano + ideas from USA)
65
nm
2011-12
3.80 mm
3.31 mm
64 patterns= 2 full custum cells
14 mm^2 = 8192 Patterns + 228 pads
Variable Resolution: high fake rejection with smaller banks
(Talk G. Volpi Animma 2011)
NEW AMCHIP
Annovi, Beretta, Crescioli, Liberali, Sacco, Stabile, Hoff – Ongoing tests
Consumption & perfomances Measured soon!

## Slide 8: What for 2015? Small production
If we have to use the small chip (14 mm^2):
2 barrel wedges like VS or more:: 8 AMBFTKsA32 LAMBs, 1 k chips
How much costs 1kchips? 500 chips → 4 wafers, 7,765 k€/wafer
12 wafer=1500 chips 93 keuro for a 66% yield??
This is not too expensive for a demonstrator (small & modern)
After this (2015) we can do the pilot run
8 AMBoards → 20 keuro
32 LAMBs → 20 keuro
1,5 kchips → ~90 keuro
~ 130 keuro
in 2014
+ production FTK_IM

## Slide 9
Richieste 2013 – linee guida
Produzione rimandata ancora
2012 si costruiscono e testano pre-prototipi
2013 prototipi finali e loro tests (Test stand=CDF Crates to be adjusted)
20 k€ a Pavia per LAMB finali – Test Stand (TS) VME
10 k€ a Pisa per AMBFTK finali
5 k€ a Milano per Test Stand (sviluppo di firmware)
20 k€ a LNF per FTK_IM finale piccola produzione.
chip AM 2013: IMPORTANTE prepararsi allo step finale costoso
  Crescita dell’area per ridurre il rischio step finale (x10)
  Input/output Serializzati per liberare pads per VCC/GND
  Multi-packaging of dies per aumentare la densita’
  → 100 k€ a Milano per 1+ 20 k€ a LNF per 2 + 20 k€ per 3
Integration test still based on EDRO in 2013:
  5 k€ a Bologna per ‘rewarking’ of EDROs e miglioramento
  test stand
  SUPER TOT 200 k€

## Slide 10: Summary 2013
Milano: 5 k€ schedina chip + AMchip05, 100 k€
Pisa: 10 k€ new AMBFTK +10 k€ SJ for possible problems
Pavia: 20 k€: LAMBFTK (small prod) + Test stands
LNF: 20 k€ FTK_IM e 40 k€ Amchip
Bologna: 5 k€ (spese di laboratorio)
Tot: 200 keuro + 10 SJ
Summary schedule
Produzione rimandata ancora:
2012 si costruiscono e testano pre-prototipi
2013 prototipi finali e loro tests
2014 costruzione dimostratore (possibilmente coprire Barrel)
2015 prima presa dati

## Slide 11
Backup

## Slide 12: Responsabilita’ e ME
Paola G. L2 4 mesi
Marco P. L2 4 mesi
Agostino L. L2 1 mese
Andrea N. L2 1,5 mesi
Annovi A. L2 4 mesi
Volpi G. L3 2 mesi
Mauro V. L3 3 mesi
A. Stabile L3 1 mese
Valentino L. L3 1 mese
Responsabilita’ descritte a questa pagina: https://twiki.cern.ch/twiki/bin/viewauth/Atlas/FastTracKer
Integrazione di FTK con prototipi americani @CERN:
Pisa 1 mesi
Milano 1 mesi
Frascati 1 mesi
Pavia 1 mesi
Bologna 1 mesi

## Slide 13: Missioni interne
4 K€ Frascati integrazione prototipi e AMchip I e II
5 K€ Pisa integrazione prototipi
4 K€ Milano AMchip I e II
4 K€ Pavia integrazione prototipi
Bologna integrazione prototipi

## Slide 14: Conclusions
We are working hard for both the Final FTK
& the intermediate versions (vertical slice and demonstrator)
First prototypes (chip and boards) will be under tests in June.
the AMchip just arrived, as planned.
the vertical slice plan has been reduced (LHC schedule).
the TDR in 2013 should start final approvals
A demonstrator expected in 2015, big production will start after.

## Slide 15: ANALYSIS of VS data
This task is independent of the hardware task:
If hardware produces the same roads as FTKsim →
can do everything else with FTKsim –
F. Crescioli since February: try to reconstruct top events in VS:
  apply track isolation to leptons
  measure rejection for muons from b-jets
  measure efficiency for muons from Ws
In 3 months: (a) choosing the right strategy to have FTK tracks available to trigger algorithms, (b) learning to run muComb – muIso on them.
V. Cavaliere and A. McCarn are joining Francesco’s effort now. Additional help would be welcomed from HLT experts.
Fakes will be a problem – but let’s prepare the algos

## Slide 16
2013
A minimum of Two 45 degree wedges in the barrel
If the run is extended to 2013, enlarge the vertical slice
in 2012 for real triggering → “small demonstrator”
  primary vertex identification, beam spot calculation …….
  Track-isolated muons, highly ionizing particles …..
DONE
NO run EXTENSION

## Slide 18
FTK: Projects to Institutions
4 DF crates:
cluster finding
split by layer
8 “core” crates:
AMboard
Data Organizer
GigaFitter
S-links
Raw data
ROBs
Track data
ROB
Pisa & Frascati & Fermilab
the AMChip could be 3D
Frascati-Waseda:
Clustering in
Pixels-SCT
mezznines
Pixels
& SCT
RODs
Chicago GigaFitter + Data Organizer + HW
Pisa:
AMBoard
Illinois:
Final board
in core crate
USA-Italy
“2-outHola”
Fermilab:
DF motherboards
USA+Italy: crates + links + backplanes…
1 Readout Crate
Argonne

## Slide 19
LAMB
Standard cell chip
40 MHz clock
FPGA
for
Roads
AMBoard
P3
serial
LVDS
Control
FPGA
FPGA
for
SS
Input
AM0+TSP+DO+TF+HW
CPU vme
AM1+TSP+DO+TF+HW
AM2+TSP+DO+TF+HW
AM3+TSP+DO+TF+HW
AM4+TSP+DO+TF+HW
AM5+TSP+DO+TF+HW
AM6+TSP+DO+TF+HW
AM7+TSP+DO+TF+HW
11LayFit+HW
AM10+…..
AM11+…..
AM12+…..
AM13+……
AM14+…..
AM8+…..
AM9+…...
11LayFit+ HW final
AM15+…..
11LayFit+ HW final
11LayFit+HW
OPTION A
AUX card
Connectors for
Hits LVDS Cables
DO+TF+HW
HW
TF
DO
DO
INPUT
FIFOs
HW
TF
DO
HW
TF
DO
HW
TF
DO
Connectors for
tracks output
Interface
SSMAP
Processing Unit
Pisa +Chicago
ITALIAN DUTIES for
3x10**34
PISA
DATA FORMATTER
FRASCATI
FERMILAB