## Slide 1
L. Ratti
Università degli Studi di Pavia
INFN Pavia
Hit time resolution study
SVT-TDR phone meeting, 13/07/2012

## Slide 2
Hit time estimation
with tth the threshold crossing time and twalk the time needed by the signal to reach the threshold (depending on the signal amplitude and, in turn, on the input charge). Actually
tth can be measured with the sensitivity provided by the time stamp clock
twalk can be estimated based on the amplitude measurement, whose accuracy depends on the TOT clock and on the shaping function
both measurements are affected by noise sources in the system
Consider a readout channel with threshold discrimination
The time of arrival of a particle, t0 (corresponding to the signal start time, drift time of the charge in the detector is considered negligible), can be estimated if tth and twalk are known

## Slide 3
Time resolution simulations
Simulations performed with Wolfram Mathematica by means of purely statistical methods (no time transients involved)
Simulation input:
delta response of the channel + peaking time
discriminator threshold
time stamp clock period (TCK,TS)
TOT clock period (TCK,TOT)
event energy distribution (MPV and sigma for a Landau distribution)
noise

## Slide 4
Time resolution simulations – time stamp
A random charge signal with Landau distribution is generated
The TS clock is assumed to start at t=0
t0 is a uniformly distributed random time
If tre (rising edge time of the discriminator) falls between the i-th and the (i+1)-th TS clock pulse, then TS=i=IntegerPart[tre/TCK,TS] and the best estimate of the time stamp is (i+0.5)xTCK,TS

## Slide 5
Time resolution simulations – TOT counts
A sort of acceptance-rejection method is applied to account for the effect of the random phase on TOTD:
  a random number 0<r<1 is generated
  if FractionalPart[TOTA/TCK,TOT]<r TOTD=IntegerPart[TOTA/TCK,TOT], else TOTD=IntegerPart[TOTA/TCK,TOT+1]
The same TOT interval (TOTA) may result in the count TOTD of j or j+1 TOT clock pulses, depending on the relative position of the signal with respect to the TOT clock (TOTA=3.1TCK,TOT is more likely to result in 3 counts than in 4, TOTA=3.9TCk,TOT is more likely to result in 4 counts than in 3)

## Slide 6
Distribution of TOTA contributing to TOTD=j
Only (j-1)Ttot<TOTA<(j+1)Ttot can contribute to TOTD=j
TOTA close to (j-1)TCK,TOT and (j+1) TCK,TOT are much less likely to contribute to TOTD=j
TOTA close to jTCK,TOT have probability close to 1 to result in j TOT counts
This was not accounted for correctly in previous studies, leading to an overestimation of the time walk contribution to hit time resolution

## Slide 7
Time resolution definition
For the k-th of the N total simulated events, given the time stamp TSk and the TOT count TOTD,k, the error Dterr,k in t0 reconstruction is defined as
where
t0,est,k is the estimated hit time for the k-th event
twalk(TOTD,k) is the estimated time walk as a function of the TOT count for the k-th event
The hit time resolution is defined as the standard deviation of the distribution of the errors Dterr,k, k=1,…,N

## Slide 8
TS contribution to time resolution
Not surprisingly, the TS contribution to hit time resolution is TCK,TS/sqrt(12)
Case of a TS frequency of 25 MHz; the event time reconstruction error is uniformly distributed between -20 ns and 20 ns
st0=11.5 ns

## Slide 9
Time walk contribution to hit time resolution
If represented as a function of the peaking time, the time walk contribution to time resolution depends on the tp/TCK,TOT ratio
Distribution of the event time reconstruction error in the case of tp=100 ns and tp/TCK,TOT=4
st0=2.1 ns

## Slide 10
Time walk contribution to hit time resolution
If represented as a function of the TOT clock period (TCk,TOT), the time walk contribution to time resolution does not depend on the tp/TCK,TOT ratio

## Slide 11
Hit time resolution (TS and time walk)
The following equation
is found to be consistent with results from simulations including contributions from both time stamp and time walk
Distribution of the event time reconstruction error in the case of tp=400 ns, tp/TCK,TOT =4 and TS=40 ns
st0=21 ns

## Slide 12
Noise contribution to hit time resolution
Simulations have also been performed including noise effects
for each event, two random charge samples with Gaussian distribution and sigma=ENC are generated (fully uncorrelated noise); one sample is subtracted from the threshold when calculating tre, the other when calculating tfe
Distribution of the event time reconstruction error in the case of tp=400 ns, tp/TCK,TOT =3 and TS=66 ns

## Slide 13
Hit time resolution including noise effects
Layer | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC (no rad effects) [e- rms] | σt0 (w/o noise) [ns] | σt0 [ns]
0 u | 25 | 4 | 30 | 892 | 9.6 | 9.8
0 v | 25 | 4 | 30 | 893 | 9.6 | 9.8
1 z | 75 | 4 | 30 | 1106 | 9.8 | 10.6
1 phi | 75 | 4 | 30 | 697 | 9.8 | 10
2 z | 100 | 4 | 30 | 1070 | 9.9 | 11.1
2 phi | 100 | 4 | 30 | 660 | 9.9 | 10.3
3 z | 150 | 4 | 30 | 864 | 10.1 | 11.9
3 phi | 150 | 4 | 30 | 669 | 10.1 | 11.2

## Slide 14
BaBar data (phi layers)

## Slide 15
Comparison with BaBar results
To reproduce time resolution measurements in BaBar (holds also for SuperB SVT)
event energy distribution (MPV and sigma in the case of a Landau distribution)
actual threshold during detector operation
some numbers for the noise in the different layers (found several, slightly different figures), possibly from measurements; noise may depend from the absorbed dose, so numbers may change significantly depending on the time spent in the experiment
real TOT vs Q relationship, accounting for output range limitations in the shaper and non linearities in the transconductors (look up table, or empirical interpolating function)
Layer | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC (no rad effects) [e- rms] | σt0 (w/o noise) [ns] | simulated σt0 [ns] | measured σt0 [ns]
3 phi | 200 | 3 | 15 | 1700 | 20.1 | 24.5 | ~35
5 phi | 400 | 3 | 15 | 1200 | 22.3 | 30.8 | ~50