## Slide 1
L. Ratti
Università degli Studi di Pavia
INFN Pavia
Hit time resolution study
SVT-TDR phone meeting, 27/07/2012

## Slide 2
Hit time estimation
with tth the threshold crossing time and twalk the time needed by the signal to reach the threshold (depending on the signal amplitude and, in turn, on the input charge). Actually
tth can be measured with the sensitivity provided by the time stamp clock
twalk can be estimated based on the amplitude measurement, whose accuracy depends on the TOT clock and on the shaping function
both measurements are affected by noise sources in the system
Consider a readout channel with threshold discrimination
The time of arrival of a particle, t0 (corresponding to the signal start time, drift time of the charge in the detector is considered negligible), can be estimated if tth and twalk are known

## Slide 3
Time resolution simulations
Simulations performed with Wolfram Mathematica by means of purely statistical methods (no time transients involved)
Simulation input:
delta response of the channel + peaking time
discriminator threshold
time stamp clock period (TCK,TS)
TOT clock period (TCK,TOT)
event energy distribution (MPV and sigma for a Landau distribution)
noise

## Slide 4
Time resolution simulations – time stamp
A random charge signal with Landau distribution is generated
The TS clock is assumed to start at t=0
t0 is a uniformly distributed random time
If tre (rising edge time of the discriminator) falls between the i-th and the (i+1)-th TS clock pulse, then TS=i=IntegerPart[tre/TCK,TS] and the best estimate of the time stamp is (i+0.5)xTCK,TS

## Slide 5
Time resolution simulations – TOT counts
A sort of acceptance-rejection method is applied to account for the effect of the random phase on TOTD:
  a random number 0<r<1 is generated
  if FractionalPart[TOTA/TCK,TOT]<r TOTD=IntegerPart[TOTA/TCK,TOT], else TOTD=IntegerPart[TOTA/TCK,TOT+1]
The same TOT interval (TOTA) may result in the count TOTD of j or j+1 TOT clock pulses, depending on the relative position of the signal with respect to the TOT clock (TOTA=3.1TCK,TOT is more likely to result in 3 counts than in 4, TOTA=3.9TCk,TOT is more likely to result in 4 counts than in 3)

## Slide 6
Distribution of TOTA contributing to TOTD=j
Only (j-1)Ttot<TOTA<(j+1)Ttot can contribute to TOTD=j
TOTA close to (j-1)TCK,TOT and (j+1) TCK,TOT are much less likely to contribute to TOTD=j
TOTA close to jTCK,TOT have probability close to 1 to result in j TOT counts
This was not accounted for correctly in previous studies, leading to an overestimation of the time walk contribution to hit time resolution

## Slide 7
Time resolution definition
For the k-th of the N total simulated events, given the time stamp TSk and the TOT count TOTD,k, the error Dterr,k in t0 reconstruction is defined as
where
t0,est,k is the estimated hit time for the k-th event
twalk(TOTD,k) is the estimated time walk as a function of the TOT count for the k-th event
The hit time resolution is defined as the standard deviation of the distribution of the errors Dterr,k, k=1,…,N

## Slide 8
TS contribution to time resolution
Not surprisingly, the TS contribution to hit time resolution is TCK,TS/sqrt(12)
Case of a TS frequency of 25 MHz; the event time reconstruction error is uniformly distributed between -20 ns and 20 ns
st0=11.5 ns

## Slide 9
Time walk contribution to hit time resolution
If represented as a function of the peaking time, the time walk contribution to time resolution depends on the tp/TCK,TOT ratio
Distribution of the event time reconstruction error in the case of tp=100 ns and tp/TCK,TOT=4
st0=2.1 ns

## Slide 10
Time walk contribution to hit time resolution
If represented as a function of the TOT clock period (TCk,TOT), the time walk contribution to time resolution does not depend on the tp/TCK,TOT ratio

## Slide 11
Hit time resolution (TS and time walk)
The following equation
is found to be consistent with results from simulations including contributions from both time stamp and time walk
Distribution of the event time reconstruction error in the case of tp=400 ns, tp/TCK,TOT =4 and TS=40 ns
st0=21 ns

## Slide 12
Noise contribution to hit time resolution
Simulations have also been performed including noise effects
for each event, two random charge samples with Gaussian distribution and sigma=ENC are generated (fully uncorrelated noise); one sample is subtracted from the threshold when calculating tre, the other when calculating tfe
Distribution of the event time reconstruction error in the case of tp=400 ns, tp/TCK,TOT =3 and TS=66 ns

## Slide 13
Comparison with BaBar time resolution data (including noise)
Background hit effects have been taken into account in SVT time resolution measurements at some point in time during BaBar operation
Layer | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC (no rad effects) [e- rms] | σt0 (w/o noise) [ns] | simulated σt0 [ns] | measured σt0 [ns]
3 phi | 200 | 3 | 15 | 1700 | 20.1 | 24.5 | ~35
5 phi | 400 | 3 | 15 | 1200 | 22.3 | 30.8 | ~50
Apparently overestimated due to spurious background hits
In the following two slides, simulation results are compared to data from 2008 BaBar OPR runs; agreement is fairly good, especially if radiation induced noise degradation is considered (20% noise increase after ~8 year operation is assumed for the AToM chip in the second slide)

## Slide 14
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | simulated σt0 [ns] | measured σt0 [ns] | 
1 | phi | 200 | 3 | 15 | 1200 | 0.44 | 0.19 | 20.3 | 23.8 | 23.7 | +0.4%
 | z | 200 | 3 | 15 | 880 | 0.32 | 0.18 | 20.4 | 22.3 | 25.4 | -12.2%
2 | phi | 200 | 3 | 15 | 1240 | 0.46 | 0.19 | 20.2 | 23.8 | 23.5 | +1.3%
 | z | 200 | 3 | 15 | 970 | 0.32 | 0.17 | 20.4 | 23.5 | 25.9 | -9.3%
3 | phi | 200 | 3 | 15 | 1440 | 0.48 | 0.19 | 20.2 | 24.6 | 25.3 | -2.8%
 | z | 200 | 3 | 15 | 1180 | 0.31 | 0.17 | 20.4 | 24.5 | 27.0 | -9.2%
4 | phi | 400 | 3 | 15 | 1350 | 0.61 | 0.25 | 22.0 | 32.2 | 35.6 | -9.5%
 | z | 400 | 3 | 15 | 1210 | 0.58 | 0.23 | 22.2 | 31.2 | 34.4 | -9.3%
5 | phi | 400 | 3 | 15 | 1600 | 0.62 | 0.24 | 22.0 | 35.2 | 37.0 | -4.9%
 | z | 400 | 3 | 15 | 1200 | 0.56 | 0.21 | 22.2 | 31.9 | 36.0 | -11.4%
BaBar SVT: fresh detector

## Slide 15
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | simulated σt0 [ns] | measured σt0 [ns] | 
1 | phi | 200 | 3 | 15 | 1440 | 0.44 | 0.19 | 20.3 | 25.1 | 23.7 | +5.9%
 | z | 200 | 3 | 15 | 1056 | 0.32 | 0.18 | 20.4 | 23.8 | 25.4 | -6.2%
2 | phi | 200 | 3 | 15 | 1488 | 0.46 | 0.19 | 20.2 | 25.1 | 23.5 | +6.8%
 | z | 200 | 3 | 15 | 1164 | 0.32 | 0.17 | 20.4 | 24.4 | 25.9 | -5.6%
3 | phi | 200 | 3 | 15 | 1728 | 0.48 | 0.19 | 20.2 | 26.3 | 25.3 | +3.9%
 | z | 200 | 3 | 15 | 1416 | 0.31 | 0.17 | 20.4 | 25.9 | 27.0 | -4.1%
4 | phi | 400 | 3 | 15 | 1620 | 0.61 | 0.25 | 22.0 | 34.8 | 35.6 | -2.2%
 | z | 400 | 3 | 15 | 1452 | 0.58 | 0.23 | 22.2 | 33.4 | 34.4 | -2.9%
5 | phi | 400 | 3 | 15 | 1920 | 0.62 | 0.24 | 22.0 | 37.7 | 37.0 | +1.9%
 | z | 400 | 3 | 15 | 1440 | 0.56 | 0.21 | 22.2 | 34.8 | 36.0 | -3.3%
BaBar SVT: older detector (+20% noise increase)

## Slide 16
SuperB SVT: time resolution simulations (noise included)
Simulations performed
for Layer 0 to 5
in the case of Layers 4 and 5, for 2 different values of the tp/TTOT,CK ratio, 4 and 6
including noise from circuit simulations in different conditions:
  fresh detector
  after 7.5 year operation ( main effect from detector leakage current increase)
  after 7.5 year operation including x5 safety factor (equivalent to 37.5 year SVT operation)

## Slide 17
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
0 | u | 25 | 4 | 30 | 892 | 0.45 | 0.2 | 9.6 | 9.7
 | v | 25 | 4 | 30 | 893 | 0.45 | 0.2 | 9.6 | 9.7
1 | phi | 75 | 4 | 30 | 1106 | 0.45 | 0.2 | 9.8 | 10.7
 | z | 75 | 4 | 30 | 697 | 0.45 | 0.2 | 9.8 | 10.2
2 | phi | 100 | 4 | 30 | 1070 | 0.45 | 0.2 | 9.9 | 11.4
 | z | 100 | 4 | 30 | 660 | 0.45 | 0.2 | 9.9 | 10.5
3 | phi | 150 | 4 | 30 | 864 | 0.45 | 0.2 | 10.3 | 12.4
 | z | 150 | 4 | 30 | 669 | 0.45 | 0.2 | 10.3 | 11.7
SuperB SVT: fresh detector (L0-3)

## Slide 18
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
0 | u | 25 | 4 | 30 | 905 | 0.45 | 0.2 | 9.6 | 9.7
 | v | 25 | 4 | 30 | 907 | 0.45 | 0.2 | 9.6 | 9.8
1 | phi | 75 | 4 | 30 | 1160 | 0.45 | 0.2 | 9.8 | 10.8
 | z | 75 | 4 | 30 | 812 | 0.45 | 0.2 | 9.8 | 10.3
2 | phi | 100 | 4 | 30 | 1127 | 0.45 | 0.2 | 9.9 | 11.5
 | z | 100 | 4 | 30 | 778 | 0.45 | 0.2 | 9.9 | 10.8
3 | phi | 150 | 4 | 30 | 1040 | 0.45 | 0.2 | 10.3 | 13.1
 | z | 150 | 4 | 30 | 836 | 0.45 | 0.2 | 10.3 | 12.3
SuperB SVT: 7.5 year old detector (L0-3)

## Slide 19
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
0 | u | 25 | 4 | 30 | 958 | 0.45 | 0.2 | 9.6 | 9.7
 | v | 25 | 4 | 30 | 959 | 0.45 | 0.2 | 9.6 | 9.7
1 | phi | 75 | 4 | 30 | 1352 | 0.45 | 0.2 | 9.8 | 11.0
 | z | 75 | 4 | 30 | 1165 | 0.45 | 0.2 | 9.8 | 10.8
2 | phi | 100 | 4 | 30 | 1332 | 0.45 | 0.2 | 9.9 | 12.0
 | z | 100 | 4 | 30 | 1132 | 0.45 | 0.2 | 9.9 | 11.5
3 | phi | 150 | 4 | 30 | 1470 | 0.45 | 0.2 | 10.3 | 15.1
 | z | 150 | 4 | 30 | 1254 | 0.45 | 0.2 | 10.3 | 14.1
SuperB SVT: 7.5 year old detector x5 (L0-3)

## Slide 20
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
4 | phi | 250 | 4 | 30 | 1220 | 0.55 | 0.25 | 11.0 | 17.8
 |  | 375 | 4 | 30 | 1140 | 0.55 | 0.25 | 12.5 | 23.2
 |  | 500 | 4 | 30 | 1086 | 0.55 | 0.25 | 14.3 | 28.8
 | z | 250 | 4 | 30 | 982 | 0.55 | 0.25 | 11.0 | 15.9
 |  | 375 | 4 | 30 | 886 | 0.55 | 0.25 | 12.5 | 20.1
 |  | 500 | 4 | 30 | 819 | 0.55 | 0.25 | 14.3 | 24.2
5 | phi | 375 | 4 | 30 | 1257 | 0.55 | 0.25 | 12.5 | 24.9
 |  | 500 | 4 | 30 | 1187 | 0.55 | 0.25 | 14.3 | 30.8
 |  | 750 | 4 | 30 | 1106 | 0.55 | 0.25 | 18.6 | 42.6
 | z | 375 | 4 | 30 | 925 | 0.55 | 0.25 | 12.5 | 20.5
 |  | 500 | 4 | 30 | 866 | 0.55 | 0.25 | 14.3 | 25.2
 |  | 750 | 4 | 30 | 808 | 0.55 | 0.25 | 18.6 | 34.3
SuperB SVT: fresh detector (L4-5)

## Slide 21
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
4 | phi | 250 | 4 | 30 | 1353 | 0.55 | 0.25 | 11.0 | 18.7
 |  | 375 | 4 | 30 | 1271 | 0.55 | 0.25 | 12.5 | 24.9
 |  | 500 | 4 | 30 | 1263 | 0.55 | 0.25 | 14.3 | 32.2
 | z | 250 | 4 | 30 | 1074 | 0.55 | 0.25 | 11.0 | 16.6
 |  | 375 | 4 | 30 | 1041 | 0.55 | 0.25 | 12.5 | 22.2
 |  | 500 | 4 | 30 | 1049 | 0.55 | 0.25 | 14.3 | 28.5
5 | phi | 375 | 4 | 30 | 1304 | 0.55 | 0.25 | 12.5 | 25.5
 |  | 500 | 4 | 30 | 1251 | 0.55 | 0.25 | 14.3 | 32.0
 |  | 750 | 4 | 30 | 1204 | 0.55 | 0.25 | 18.6 | 45.2
 | z | 375 | 4 | 30 | 977 | 0.55 | 0.25 | 12.5 | 21.2
 |  | 500 | 4 | 30 | 937 | 0.55 | 0.25 | 14.3 | 26.4
 |  | 750 | 4 | 30 | 913 | 0.55 | 0.25 | 18.6 | 37.1
SuperB SVT: 7.5 year old detector (L4-5)

## Slide 22
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
4 | phi | 250 | 4 | 30 | 1639 | 0.55 | 0.25 | 11.0 | 21.1
 |  | 375 | 4 | 30 | 1696 | 0.55 | 0.25 | 12.5 | 30.7
 |  | 500 | 4 | 30 | 1804 | 0.55 | 0.25 | 14.3 | 41.6
 | z | 250 | 4 | 30 | 1417 | 0.55 | 0.25 | 11.0 | 19.3
 |  | 375 | 4 | 30 | 1551 | 0.55 | 0.25 | 12.5 | 28.8
 |  | 500 | 4 | 30 | 1675 | 0.55 | 0.25 | 14.3 | 49.4
5 | phi | 375 | 4 | 30 | 1474 | 0.55 | 0.25 | 12.5 | 27.6
 |  | 500 | 4 | 30 | 1478 | 0.55 | 0.25 | 14.3 | 36.0
 |  | 750 | 4 | 30 | 1530 | 0.55 | 0.25 | 18.6 | 54.6
 | z | 375 | 4 | 30 | 1162 | 0.55 | 0.25 | 12.5 | 23.8
 |  | 500 | 4 | 30 | 1178 | 0.55 | 0.25 | 14.3 | 30.4
 |  | 750 | 4 | 30 | 1244 | 0.55 | 0.25 | 18.6 | 46.7
SuperB SVT: 7.5 year old detector x5 (L4-5)

## Slide 23
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
4 | phi | 250 | 6 | 30 | 1220 | 0.55 | 0.25 | 10.3 | 17.4
 |  | 375 | 6 | 30 | 1140 | 0.55 | 0.25 | 11.0 | 22.8
 |  | 500 | 6 | 30 | 1086 | 0.55 | 0.25 | 12.0 | 27.7
 | z | 250 | 6 | 30 | 982 | 0.55 | 0.25 | 10.3 | 15.6
 |  | 375 | 6 | 30 | 886 | 0.55 | 0.25 | 11.0 | 19.3
 |  | 500 | 6 | 30 | 819 | 0.55 | 0.25 | 12.0 | 23.1
5 | phi | 375 | 6 | 30 | 1257 | 0.55 | 0.25 | 11.0 | 24.5
 |  | 500 | 6 | 30 | 1187 | 0.55 | 0.25 | 12.0 | 30.0
 |  | 750 | 6 | 30 | 1106 | 0.55 | 0.25 | 14.4 | 41.0
 | z | 375 | 6 | 30 | 925 | 0.55 | 0.25 | 11.0 | 19.9
 |  | 500 | 6 | 30 | 866 | 0.55 | 0.25 | 12.0 | 24.0
 |  | 750 | 6 | 30 | 808 | 0.55 | 0.25 | 14.4 | 33.1
SuperB SVT: fresh detector (L4-5)

## Slide 24
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
4 | phi | 250 | 6 | 30 | 1353 | 0.55 | 0.25 | 10.3 | 18.5
 |  | 375 | 6 | 30 | 1271 | 0.55 | 0.25 | 11.0 | 24.6
 |  | 500 | 6 | 30 | 1263 | 0.55 | 0.25 | 12.0 | 31.4
 | z | 250 | 6 | 30 | 1074 | 0.55 | 0.25 | 10.3 | 16.3
 |  | 375 | 6 | 30 | 1041 | 0.55 | 0.25 | 11.0 | 21.3
 |  | 500 | 6 | 30 | 1049 | 0.55 | 0.25 | 12.0 | 27.2
5 | phi | 375 | 6 | 30 | 1304 | 0.55 | 0.25 | 11.0 | 24.9
 |  | 500 | 6 | 30 | 1251 | 0.55 | 0.25 | 12.0 | 31.4
 |  | 750 | 6 | 30 | 1204 | 0.55 | 0.25 | 14.4 | 44.1
 | z | 375 | 6 | 30 | 977 | 0.55 | 0.25 | 11.0 | 20.6
 |  | 500 | 6 | 30 | 937 | 0.55 | 0.25 | 12.0 | 25.0
 |  | 750 | 6 | 30 | 913 | 0.55 | 0.25 | 14.4 | 35.8
SuperB SVT: 7.5 year old detector (L4-5)

## Slide 25
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
4 | phi | 250 | 6 | 30 | 1639 | 0.55 | 0.25 | 10.3 | 20.8
 |  | 375 | 6 | 30 | 1696 | 0.55 | 0.25 | 11.0 | 30.4
 |  | 500 | 6 | 30 | 1804 | 0.55 | 0.25 | 12.0 | 41.9
 | z | 250 | 6 | 30 | 1417 | 0.55 | 0.25 | 10.3 | 19.0
 |  | 375 | 6 | 30 | 1551 | 0.55 | 0.25 | 11.0 | 28.3
 |  | 500 | 6 | 30 | 1675 | 0.55 | 0.25 | 12.0 | 39.1
5 | phi | 375 | 6 | 30 | 1474 | 0.55 | 0.25 | 11.0 | 27.0
 |  | 500 | 6 | 30 | 1478 | 0.55 | 0.25 | 12.0 | 35.3
 |  | 750 | 6 | 30 | 1530 | 0.55 | 0.25 | 14.4 | 52.9
 | z | 375 | 6 | 30 | 1162 | 0.55 | 0.25 | 11.0 | 23.0
 |  | 500 | 6 | 30 | 1178 | 0.55 | 0.25 | 12.0 | 29.8
 |  | 750 | 6 | 30 | 1244 | 0.55 | 0.25 | 14.4 | 45.4
SuperB SVT: 7.5 year old detector x5 (L4-5)

## Slide 26
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
4 | phi | 250 | 18 | 30 | 1220 | 0.55 | 0.25 | 9.7 | 17.1
 |  | 375 | 18 | 30 | 1140 | 0.55 | 0.25 | 9.8 | 22.3
 |  | 500 | 18 | 30 | 1086 | 0.55 | 0.25 | 9.9 | 27.4
 | z | 250 | 18 | 30 | 982 | 0.55 | 0.25 | 9.7 | 15.2
 |  | 375 | 18 | 30 | 886 | 0.55 | 0.25 | 9.8 | 18.7
 |  | 500 | 18 | 30 | 819 | 0.55 | 0.25 | 9.9 | 22.3
5 | phi | 375 | 18 | 30 | 1257 | 0.55 | 0.25 | 9.8 | 23.9
 |  | 500 | 18 | 30 | 1187 | 0.55 | 0.25 | 9.9 | 29.4
 |  | 750 | 18 | 30 | 1106 | 0.55 | 0.25 | 10.3 | 40.3
 | z | 375 | 18 | 30 | 925 | 0.55 | 0.25 | 9.8 | 19.3
 |  | 500 | 18 | 30 | 866 | 0.55 | 0.25 | 9.9 | 23.2
 |  | 750 | 18 | 30 | 808 | 0.55 | 0.25 | 10.3 | 31.3
SuperB SVT: fresh detector (L4-5)

## Slide 27
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
4 | phi | 250 | 18 | 30 | 1353 | 0.55 | 0.25 | 9.7 | 18.3
 |  | 375 | 18 | 30 | 1271 | 0.55 | 0.25 | 9.8 | 24.0
 |  | 500 | 18 | 30 | 1263 | 0.55 | 0.25 | 9.9 | 30.8
 | z | 250 | 18 | 30 | 1074 | 0.55 | 0.25 | 9.7 | 15.9
 |  | 375 | 18 | 30 | 1041 | 0.55 | 0.25 | 9.8 | 20.9
 |  | 500 | 18 | 30 | 1049 | 0.55 | 0.25 | 9.9 | 26.6
5 | phi | 375 | 18 | 30 | 1304 | 0.55 | 0.25 | 9.8 | 24.5
 |  | 500 | 18 | 30 | 1251 | 0.55 | 0.25 | 9.9 | 30.6
 |  | 750 | 18 | 30 | 1204 | 0.55 | 0.25 | 10.3 | 43.0
 | z | 375 | 18 | 30 | 977 | 0.55 | 0.25 | 9.8 | 20.0
 |  | 500 | 18 | 30 | 937 | 0.55 | 0.25 | 9.9 | 24.5
 |  | 750 | 18 | 30 | 913 | 0.55 | 0.25 | 10.3 | 34.5
SuperB SVT: 7.5 year old detector (L4-5)

## Slide 28
Layer |  | tp [ns] | tp/TCK,TOT | fCK,TS [MHz] | ENC [e- rms] | MPV [MIP] | sigma [MIP] | σt0 (w/o noise) [ns] | σt0 [ns]
4 | phi | 250 | 18 | 30 | 1639 | 0.55 | 0.25 | 9.7 | 20.7
 |  | 375 | 18 | 30 | 1696 | 0.55 | 0.25 | 9.8 | 29.8
 |  | 500 | 18 | 30 | 1804 | 0.55 | 0.25 | 9.9 | 40.9
 | z | 250 | 18 | 30 | 1417 | 0.55 | 0.25 | 9.7 | 18.8
 |  | 375 | 18 | 30 | 1551 | 0.55 | 0.25 | 9.8 | 28.1
 |  | 500 | 18 | 30 | 1675 | 0.55 | 0.25 | 9.9 | 38.5
5 | phi | 375 | 18 | 30 | 1474 | 0.55 | 0.25 | 9.8 | 26.8
 |  | 500 | 18 | 30 | 1478 | 0.55 | 0.25 | 9.9 | 35.0
 |  | 750 | 18 | 30 | 1530 | 0.55 | 0.25 | 10.3 | 52.7
 | z | 375 | 18 | 30 | 1162 | 0.55 | 0.25 | 9.8 | 22.6
 |  | 500 | 18 | 30 | 1178 | 0.55 | 0.25 | 9.9 | 29.2
 |  | 750 | 18 | 30 | 1244 | 0.55 | 0.25 | 10.3 | 44.3
SuperB SVT: 7.5 year old detector x5 (L4-5)