## Slide 1: Upgrade of the ESRF Light Source: Achievements and Perspectives
P. Raimondi
On behalf of the Accelerator & Source Division

## Slide 2
ESRF Upgrade 2009-2018
@ Funding for Phase1(from 2009 to 2015) secured to deliver:
Eight new beamlines, with an extension of the experimental hall
Refurbishment of many existing beamlines
Developments in synchrotron radiation instrumentation
Upgrade of the X ray source for availability, stability and brilliance
While maintaining an operational facility
The Upgrade Programme
@ Phase 2 under study

## Slide 3
Storage ring
6GeV, 844 m
Booster synchrotron
200 MeV  6 GeV
300m, 10 Hz
E- Linac
200 MeV
32 straight sections
DBA lattice
42 Beamlines
12 on dipoles
30 on insertion devices
72 insertion devices: 55 in-air undulators, 6 wigglers, 11 in-vacuum undulators, including 2 cryogenic
Energy | GeV | 6.04
Multibunch Current | mA | 200
Horizontal emittance | nm | 4
Vertical emittance | pm | 3.5
The ESRF today

## Slide 4: Accelerator Upgrade Phase 1
Upgrade of BPM electronics
  Improvement of the beam position stability
  Coupling reduction
6 m long straight sections
  No change in magnet lattice
  Canted undulators
7 m straight sections
  Lattice symmetry breaking
  New magnets necessary
Cryogenic in-vacuum undulators (see Chavanne talk)
Diagnostics developments
New RF Transmitters
New RF Cavities

## Slide 5: Upgrade of BPM Electronics
Sum signal of the 4 buttons:
  Lifetime monitor
  Instant Fractional-Beamloss monitor
224 Libera
Brillance
Slow Acquisition
(10 Hz, orbit correction)
Fast Acquisition (10 kHz)
For fast global orbit correction
Turn by Turn
(355 kHz, for lattice studies)
First Turn mode
(For injection tuning)
Post-Mortem
(Data loging on trigger)

## Slide 6: Coupling reduction
Achieving lower coupling
  Better resolution of the response matrices  improved model
  New correction method: minimization of Resonance Driving Terms
  Increased number of skew quad correctors: 32  64
  Down to 3.5 pm
Maintaining small coupling
  ID gap variations with magnetic field errors induce varying contributions to coupling
  Local correction of ID magnetic field errors
    2 skew quad correctors, lookup table
  Automatic periodic retuning of the correction
  εz < 5 pm on medium term (1 week)

## Slide 7: Coupling reduction
Maintaining low emittance during USM: 1 week delivery
@ Vertical Diffraction Limit reached routinely
Current
Vertical emittance
Lifetime
3.5 pm
50 hours
200 mA

## Slide 8: New orbit feedback
Previous
  Slow feedback: 224 BPMs, 96 steerers, every 30 s
  Fast feedback: 32 dedicated BPMs, 32 dedicated steerers
  Combination of the 2 systems is delicate
From this run
  Single system from DC to 200 Hz
    224 Libera BPMs
    96 standard steerers up to 200 Hz (integrated in the sextupoles)
    New power supplies
    10 kHz operation
  Much better correction of the orbit distortion induced by IDs

## Slide 9: New orbit feedback
8 mn
ID11
ID17
ID27
Feedback OFF
Horizontal OFF
Horizontal ON
Vertical OFF
Vertical ON
2.5 mm
0.9 mm
@ sub mm stability routinely achieved in V
@ mm stability routinely achieved in H
rms
Cell1
Cell32
224 BPM

## Slide 10: 6 m sections
6 m section no canting
    ID18, ID20 , ID14, ID1, ID31, ID15
    ID 24 full 6m operational with 4 carriages
6 m Large Angle canting
    ID30 (±2.2 mrad )
    ID16 (±2.7 mrad )
No change in optics
New vacuum chambers
Cabling & piping modification
Front End modification for canting

## Slide 11
5 metres
Qd6
S22
S24
QF7
Qd8
Qd6
S24
QF7
Qd8
S22
7 metres
bpm
bpm
7 metre
3 single cell cavities
C
C
C
QF7_HG
QD6_HG
S22_IR
S24_200
Infra Red beam port
bpm
bpm
QF7_HG
QD6_HG
S24_200
S22
bpm
bpm
C
ID 1.6 m
C
ID 1.6 m
C
C
Mini beta test
QD_low
7 m ID straight Sections
New girders
New quadrupoles
Individual power supplies
New vacuum chambers
1st symmetry breaking
Goal:
Redistribute RF cavities to install undulators in the present dedicated RFstraight sections
Create 2 lower vertical beta points to reduce the in-vacuum undulator gap from 6 to 4 mm

## Slide 12: 6&7 m straight sections
First 7 m straight section next winter shutdown
Test of mini beta optics during first half 2013
Installation of the RF cavities during second half 2013
5 metre standard Section
6 metre Section (6173 mm)
7 straight sections already converted to 6 metres First large canting installation this summer
7 metre Section

## Slide 13: Solid State RF transmitters
SY: Booster Synchrotron
75 kW tower of 128 RF modules
4 Waveguide switches to
4 water loads
2 five-cell cavities
x 2 couplers
Replacing one 352.2 MHz 1.3 MW klystron booster transmitter
SYRF now ready for TopUp operation, (Electrical power reduced from 1200 to 400 kW).
Goal: Prevent klystron obsolescence
Prepare future upgrades
Klystrons at l’ESRF
1.3 MW -352MHz
Booster RF : Four 150 kW amplifiers in operation

## Slide 14: Single cell NC HOM damped cavity
9 MV with 12 to 18 cavities (4.7 ± 0.4 M)
Planned operation at 300 mA
Power capability to sustain up to 500 mA
No HOM up to 1 A
HOM absorbers:
Ferrite loaded tapered ridges
HOM dampers = ridge waveguides
Based on 500 MHz BESSY, MLS, ALBA design [E. Weihreter et al.]
ESRF 352.2 MHz design: several improvements
352 MHz
3 power prototypes
under test at ESRF
Goal: RF distribution to create a new experimental station
Prepare future upgrades

## Slide 15: But while preparing the upgrade…
The priority is still machine operation:

## Slide 16
Availability (%)
Mean time between failures (hrs)
Mean duration of a failure (hrs)
99.04 98.78 98.91 98.34
75.80 67.50 107.8 46
0.73 0.82 1.18 0.76
2009 2010 2011 2012
Machine Statistics for 2009-2012
ESRF: the most stable and bright SR source
  Operation: Accelerator and Source
Accelerator and Source Division
ESRF Record
( 4 weeks only !)
Notes: 16

## Slide 17
Energy | GeV | 6.04
Multibunch Current in 7/8+1 | mA | 200 4 (single)
Horizontal emittance | nm | 4
Vertical emittance | pm | 3.5
91 % of Beamtime available for Timing Experiments
Filling modes in 2011
Mode 7/8+1: 200 mA

## Slide 18
Lifetime maintained in excess of 45 hours in multibunch (7/8+1)
Reduction of the lifetime in multibunch limited to less than 10 hours despite a reduction of the coupling by an order of magnitude ==> Still no topping-up envisaged
The other modes do not benefit from the coupling reduction because the emittance is vertically blown up to get a reasonable lifetime
    ==> Topping up would be valuable
Lifetime evolution
4 pm
45 hours
1 week of delivery to users

## Slide 19
Top Up Project
Pro: Reduced heat load variation on the beamline optics.
 Improves stability
Con: Increased number of injections.
 Disturbs stability
@ Survey of Top Up operation at
ESRF/ APS/ SPRing8/ PETRA/ SOLEIL/ DIAMOND/ BESSY/ ELETTRA/ ALBA /SLS
Top Up is multi parameter with discrepancies between institutes!
@ ESRF has developed a lot of expertise in the design of the optics and in the layout of beamlines to manage heat load variation, especially for the UPBLs, which should be less sensitive to refills.
    Could we still gain (a lot) by reducing the current variation ?
    What would be the (maximum) current variation which would make a refill transparent?
@ Most facilities operate in Top Up mode, except ESRF

## Slide 20
Top Up Project
20
Mode 7/8 200 mA, 45h, 5pm vertical emittance:
Dt= 30 mn  DI<≈ 2 mA instead of 40 mA today with an injection every 12hours
Mode 16 bunch 90 mA, 6h, 6pm vertical emittance:
Dt= 30 mn  DI<≈ 10 mA instead of 30 mA today with an injection every 6 hours and vertical emittance *10
@ 15-30mn Top-Up cycle seems reasonable
@ We are doing tests and studies during MDTs
(including feedback from Users)
@ We are upgrading our injector to improve reliability and operation
Standard decay 2mA
30mn
Possible Top-UP scheme

## Slide 21: The Quest for 4th Generation SR The last few years have been characterize by a World-Wide R&D carried on by Accelerator Engineers to find solutions to improve the SR beam parameters. The Science in general benefits by any of this improvements: - Horizontal Emittance - Vertical Emittance => Diffraction Limit reached routinely everywhere - Bunch Length => Very costly solutions (e.g. SC Crab Cavities) - Energy Spread => No solutions exists for a significant decrease (< 0.05-0.1%) in SR - Beam Current => Close to the limits imposed by the BL

## Slide 22
Brillance
(photons/s/mm2/mrad2/0.1%BW)
1900 1920 1940 1960 1980 2000
Synchrotron radiation
Diffraction limit
Free electron laser
Troisième
génération
Deuxième génération
Première génération
Tubes à
rayons X
ESRF (2008)
ESRF (1994)
Brilliance =
photons /s / mm2 /mrad2 /0.1% bandwidth
Number of photons per second
Size horizontal*vertical
Divergence horizontal *vertical
In a bandwith of 0.1 % around the considered energy.
Progress of the ESRF Brilliance
Progress of X ray light sources are summarized in the evolution of the brilliance

## Slide 23: Low Horizontal Emittance SR The most immediate advantages of such machines are: - Brigthness Increase while maintaining the same flux - Spacial Resolution Increase - Transverse Coherence The first two points improve almost linearly for an emittance decrease from 2-4nm down to 50-100pm. For lower emittance the gain become less than linear due to: - the diffraction limit - mismatch of the electron beam with the X-Ray beam The coherence starts to be of significance for emittances below 5-10pm. For example: @10KeV 80% coherence needs about 1pm emittance.

## Slide 24: Brilliance at lower horizontal emittance
Electron beam:
6.039 GeV
I=0.2 A
Hor. Emittance [nm] | 4 | 0.15 | 0.01
Vert. Emittance [pm] | 3 | 2 | 2
Energy spread [%] | 0.1 | 0.09 | 0.09
Betax[m]/Betaz [m] | 37/3 | 6/2 | 6/2
~ x 25
~ x 5

## Slide 25
USRs – Coherent Fraction

## Slide 26: ESRF toward a 4th Generation SR The world wide effort in lattice design and technology developments has paved the road the possibility of studying options to upgrade the ESRF storage ring lattice in order to significantly lower (by a factor 20-40) the equilibrium horizontal, within the constraints underlined in the ESRF “purple book” (par. 3.1.8), in particular: - Maintain as much as possible unchanged the existing Straight Sections and BeamLines - Maintain the present Injection Scheme and Injection Complex - Reuse as much as possible the existing ARCs hardware (Power Supplies, Vacuum System, Diagnostic etc…) - Reduce Operation Costs, specifically Wall-Plug Power. These constraints pose limits to the ultimate ring performances and raise technical and logistic challenges. On the other end they are consistent with the following crucial points: - Cost comparable with a “Phase II” budget expenditure - Upgrade to be completed by beginning of next decade (2020) - Less than 1 year ShutDown for installation and commissioning

## Slide 27
Cell packed with magnets
Stronger focusing: tunes 36.44/13.39 → 75.66/27.60
  Chromaticity: -130/-58 → -102/-75
Smaller 𝛽 functions Chromaticity correction needs
Smaller dispersion stronger sextupoles
Less radiated power (x2 less)
} ⇒ {
DBA
7-bend achromat
The present Double Bend Achromat (left) should be replaced by a New lattice (example on the right)

## Slide 28: New Lattice Engineering The complexity of the problem is relatively contained, since it is limited only to the design of a 25m long Arc (*32). However the technical aspects are very challenging: - High gradients magnets (4 times more) - Tight tolerances (2 times more) - Small vacuum chamber (2 times less) - Very compact design It should be stressed that the 4th Generation SRs take advantage of all the R&D and Know-How accumulated in the last 20 years at ESRF and the rest of the world: - Lattice design - Vacuum technologies (e.g. NEG coating that allows the use of smaller vacuum chambers) - Magnet technologies (better modeling and manufacturing) - Diagnostic (e.g. Libera BPMs) - Controls - Operations - …

## Slide 29: Quadrupole Magnet Design G> 100T/m
EM quadrupole
PM quadrupole
Solutions Compatible with a
“Soleil-type Vacuum Chamber”

## Slide 30
Upgrade performances have been benchmarked by SLAC w.r.t. the Pep-X 10pm storage ring proposal

## Slide 32
Phase II Upgrade could be an excellent opportunity to:
- Improve and Expand the Science Reach of the SR-based Light Sources
- Enabling New Technologies
- Realize a World-Class SR, we might expect an overall 100 fold increase in brightness of a SR-Based Light Source
- Provide Invaluable Know-How to:
Continue the push for higher perfomances SR-based Light Sources

## Slide 33
The budget evaluation is divided in 2 parts. The first part contains all what is need in term of R&D and prototyping and all what can used be anyhow on the present machine (Top-Up, RF, Upgrade of the injector, IDs,..) (mostly be paid with the money of phase 1). The second part is the fresh capital money needed to implement the new lattice (No other improvements included!).
This budget evaluation will be use to evaluate the cost but also mostly to get all the tasks to perform. It should contains all items even if the cost is low.  Please add the missing items.
The price evaluation is mostly based on the cost evaluation of the 6 metre and 7 metre projects.The prices are in 2012 euros. The estimation of the inflation willbe done by finance.
The preliminary budget profile covering 2013-2018 for each item is based on the planning.
We should not inflate too much the individual the price, but be realistic. We have anticipated a contingency of 10 % that could be re-distributed.
The cost of the building corresponds to the construction of the Vercors building (4400 square metre total) (taken out of the EX2 project phase 1).
External manpower should be evaluated in the cost (Drafting, engineering, and installation).
The evaluation suppose that we re-use the existing Ids and mostly the FE
The evaluation of the resources profile could be done as soon as the tasks and planning are evaluated.
The cost of the cabling, diagnostics & control could be underestimate. It depends on what is re-used.
New lattice project schedule and budget evaluation

## Slide 34
New lattice project schedule and budget evaluation
"DRAFT Very Preliminary"

## Slide 35
New lattice project schedule and budget evaluation
"DRAFT Very Preliminary"

## Slide 36
New lattice project schedule and budget evaluation
"DRAFT Very Preliminary"

## Slide 37
New lattice project schedule and budget evaluation
Warning:
The budget exercise is based on estimation and is still be not exhaustive (few items not included).
There is no large over cost.
It does not include other activities or development required for the existing machine.
Should we add additional margin ?
"DRAFT Very Preliminary"

## Slide 38
New lattice project schedule and budget evaluation
"DRAFT Very Preliminary"

## Slide 39
New lattice project schedule and budget evaluation
ECAPS Planning
"DRAFT Very Preliminary"

## Slide 40: Short and Mid Term path The ASD has been working very hard in all the machine subsystems in order to improve the performances and reliability of the source. There are a lot of tasks planned for the next few years that, together with what already done will virtually complete most of the envised “Phase-I” upgrades. In order to define a mid term strategy we must consider that a big extend of what has been done so far for Phase-I and the remaining activities are synergic and/or essential for a more radical upgrade of the SR. In particular, the much more demanding SR parameters do require: - High level of control/diagnostic/stabilization (e.g.: Libera-BPMs, FOC etc) - HOM-damped RF-Cavities (to allow operation with shorter bunches: 5-10ps) - TOP-UP (even with the same Dynamic-Aperture of the present ring Tau<2-5hrs) - Improved reliability - Smaller Gap/shorter period Undulators (to take full advantage of the increased vertical stay-clear - ...

## Slide 41: Short and Mid Term path In the next 2-4 years we will continue all the already foreseen activities. In particular: - TopUp - HOM-Damped Cavities - 7m/Low-Beta Section are an essential part of the ESRF upgrade path and of any possible SR Lattice Upgrade. The amount of effort/FTEs/Budget to be dedicated to a New Lattice Design and related R&D, remains to be defined. Anyway the ESRF-Divisions/Groups have enough resources to progress on the studies, without impacting the present activities, at least up to a white-paper stage (by end of 2012).

## Slide 42
MANY thanks for your attention
Experimental hall extension May 2012