## Slide 1: KLOE: present status and upgrades
Danilo Domenici – LNF
On behalf of the KLOE-2 Collaboration

## Slide 2: Report Overview
KLOE present Status:
  Detector
  Data Taking
  Data Analysis
KLOE Upgrades Status:
  Crystal Calorimeter - CCAL
  Quadrupole Calorimeter - QCAL
  Inner Tracker - IT

## Slide 3: KLOE Apparatus Today
Detector Status
EMC is fully functional
  Calibration with cosmics completed
  Calibration with Bhabha and γγ in progress
DC is fully functional
  Two TDC boards under repair (3% of total channels)
  Calibration with cosmics completed
Trigger is fully functional
  Two dish boards to be repaired
Data Taking / Monitoring / Offline
Online monitoring and DAQ are performing well
  Few 10’ stops given by daq busy related to beam losses
L3 processes working
  Online Bhabha selection has a reduced rate due to machine background. New code fixing this problem under test
Night & week-end data taking dedicated to collect data for Amadeus collaboration up to the end of this run
  Motivation: make some physics out of this data-taking, test data storage to CNAF, training shifts, DAQ and Offline analysis

## Slide 4: Example of Data Quality
T1 – T5 (ns) crossing time of innermost – outermost ECAL layers for cosmic muons
Reconstruction of CM Energy for Bhabha events with the DC

## Slide 5: EMC/DC vs Background
DC hard enough to survive 600 kHz bkg as counted by the EMC
400 kHz of EMC background corresponds to a 30% accidental counts in 100 ns window  1% fakes in a prompt time window

## Slide 6: Data Analysis Progress since last SC
Γ(η→π+π-γ) / Γ(η→π+π-π0) | arXiv:1209.4611 Accepted for publication (PLB) DOI 10.1016/j.physletb.2012.11.032
UL(φ→ηU, η→π0π0π0) | arXiv:1210.3927 Submitted to PLB
γγ→η and Γ (η→γγ) | arXiv:1211.1845 Submitted to JHEP
aµ had,ππ with σ(π+π-γ)/σ (μ+μ-γ) | Final result Draft under review of the collaboration
UL( KS→π0π0π0) | Final result Draft in progress
φ→KSKL→π+π-π+π-: CPT and Lorentz invariance | Preliminary (almost final) result
UL(e+e-→Uγ) | Preliminary result
UL(e+e-→Uh) | Preliminary result

## Slide 7: Search for Dark Forces
Hypothesis: existence of a hidden gauge sector, able to
explain several unexpected astrophysical observations,
weakly coupled with SM through a mixing mechanism of
a new gauge boson U with the photon
D2
2
MU (MeV)
MU (MeV)
f→hU
e+e-→Ug
e+e-→Uh
KLOE
preliminary
U
e+
ε2
ε2αD

## Slide 8: CPT & Lorentz Invariance Test
KLOE-2 preliminary
Δa0 = (-6.2 ± 8.2stat ± 3.3sys ) 10-18 GeV
ΔaX = ( 3.3 ± 1.6stat ± 1.5sys ) 10-18 GeV
ΔaY = (-0.7 ± 1.3stat ± 1.5sys ) 10-18 GeV
ΔaZ = (-0.7 ± 1.0stat ± 0.3sys ) 10-18 GeV
Neutral kaon interferometry based analysis with π+π-π+π- final state
Search for asymmetry in distribution of decay time difference between the two kaons in the kaon flight direction andevent sidereal time (SME framework)

## Slide 9: Detector Upgrades Overview
Inner Tracker
QCAL
CCAL

## Slide 10
forward plate
8 aluminum shells
LYSO crystals produced by SICCAS
PCB housing SiPM and calibration LED
shell and PCB
holder
QD0
coupling plate
CCALT Layout
1 calorimeter/side, 4 shells/calo,
3 modules/shell, 4 crystals/module

## Slide 11: CCALT Components and Tests
Tests in progress
Energy resolution = 10-15 % at 511 keV measured for all crystals with 22Na source and 1Gs/s digitizer
Crystal wrapping: adhesive mylar is chosen
Testbeam @BTF of single crystal σt ~ 450 ps @150 MeV
Performance at high rates to be tested with a pulsed UV-LED
with Mylar
<Q> = 15 pC
22Na Spectra
Q (pC)
w/o Mylar
<Q> = 12 pC
SiPM Signal

## Slide 12: CCALT Schedule
November
Production of forward plates
Production of photodetectors holder plates (3D print in ABS)
Finalization of the design of the QD0 coupling plate
Production of PCB and mounting and test of SiPM
December
Production of QD0 coupling plates
Anodization of aluminum parts
Completion of crystals characterization with 22Na
Wrapping of all crystals
Assembly of all modules
Test of the final FEE chain with cosmics

## Slide 13: QCALT: detector
QCALT calorimeter consists of 2 dodecagonal structures, covering the region close to IP
Each calorimeter is build in 2 halves to be coupled during insertion to the beam pipe.
Each module (1/12), consists of a sampling calorimeter with 16 towers, each composed by 5 layers of scintillator tiles and 5 layers of W/Cu absorbers
Light from tiles is routed outside using multicladding WLS fibers readout using circular 1.2 mm Ø SiPM
The total number of TDC channels is about 2000

## Slide 14: QCALT: detector
First QCALT already assembled
Each tile tested using 90Sr source to check fiber-tile coupling
LY of towers measured with cosmic rays
Plastic fiber holder already polished and ready to be coupled to SiPM
All materials (tiles, fibers, tungsten) for second QCALT ready
Mechanical preparation of steel structure and painting done
Tiles grooved, installation in progress
Half QCALT with W/Cu shielding
Fiber holder
Tiles/WLS stack
Before polishing
After polishing

## Slide 15: QCALT: SiPM
Final PCB produced and sent to FBK for SiPM bonding
Final SiPM production (round 1.2 mm diameter) completed
Bonding and resining in progress
Test on preliminary PCB satisfying (optical properties, HV working point, gain)
Test of final PCB with cosmics and final FEE chain in progress

## Slide 16: QCALT: FEE
Full FEE chain electrically tested
Readout based on TDC
No charge measurement needed 
SiPM calibration done by measuring dark rate
Cooling by flushing air in each PCB box  tested
Test board for single SiPM
Preamp and HV regulator board
Assembled FEE module

## Slide 17: QCALT Schedule
November-End: final test of FEE chain
December-Mid: assembly of PCB SiPM on the existing modules
December-End: gain calibration of all SiPM
January-Mid: completion of mechanical assembly
January-End: cosmic rays test

## Slide 18: Cylindrical-GEM Inner Tracker
4 layers at 13/15.5/18/20.5 cm from IP and 700 mm active length
rφ  250 µm and z  400 µm
XV strips-pads readout (20o÷30o stereo angle)
2% X0 total radiation length in the active region
3 mm
2 mm
2 mm
2 mm
Cathode
GEM 1
GEM 2
GEM 3
Anode
Read-out
Conversion & Drift
Transfer 1
Transfer 2
Induction
Cylindrical Triple GEM
FEE boards

## Slide 19: IT Status
We have already shown in previous meetings the construction procedure of the Cylindrical-GEM detectors
At the last SC we reported on the successful creation of the first 2 Layers of the IT
Since then the third detector Layer has been completed
Tests with β source and cosmic rays have been accomplished
Layer 1
Layer 2
Layer 3

## Slide 20: 90Sr Source Scan
FEE
FEE
X-view Hits distribution
V strips
not illuminated
V-view Hits distribution
FEE
FEE

## Slide 21: Cosmic rays Test
tracking provided by external 10x10 cm2 Triple-GEM
Test with final HV cables and distributors, final FEE and DAQ system
top/bottom scintillators for trigger

## Slide 22: Cosmic rays Test
3D view
Z vs X
(Lego View)
noise
cosmic tracks

## Slide 23: IT Operation at High Temperature
DAFNE has recorded beam pipe temperatures higher than those foreseen (up to 50 °C)
Temperature tests on Layer2 showed some operation instability for T > 35-40 °C due to the mechanical “relaxation” of the GEM foils
To cope with this problem:
The DAFNE Interaction Point will be cooled: mock-up tests indicate that the operation temperature can be kept under 30 °C
We introduced a 300 µm thick spacing grid between GEM electrodes for L3 and L4
PEEK grid assembled
grid placed around the GEM

## Slide 24: Blocking Capacitor
During the β source tests we have observed «splash events» with large hit multiplicity
The effect can be explained as X-talk due to capacitive coupling between GEM3Bottom and the Readout plane
Splash events are strongly suppressed by the insertion of a Blocking Capacitor circuit (BC): the current induced on G3Bottom flows to ground rather than into the detector
without BC
C = 2.2 nF
R = 10 Ω
BC-PCB

## Slide 25: IT Time Schedule
Layer 4
  Cathode already done
  This week: GEM and readout delivery
  Up to December-End: GEM test and cylindrical gluings
  November-End: Readout connector soldering
  December-Mid: Readout cylindrical gluing
  December-End: Readout CF lamination
  January-End: Assembling and sealing
February-Mid: General assembling of 4 IT Layers and test

## Slide 26: Conclusions
KLOE is operating properly with a smooth data taking
Analysis of old KLOE data still provides interesting results
All detector upgrades are proceding steadily
Expected completion foreseen for middle of February 2013

## Slide 27: Spares

## Slide 28: DC Trips

## Slide 29: Layout of a GEM
Bottom side of the active area is divided in 4 Macro-Sectors (MS), each with its own HV connection tail
Top side of MS is furthermore divided in 10 Sectors, all independentely supplied
HV tails have 11 connections (1 bottom MS + 10 top S) ending on 0.8 mm fiberglass stiffener
Sectorization is for minimizing damage in case of discharge
Sector HV independance is for minimizing loss in case of damage: just a single Sector can be turned off
3 mm overlap reagion
pinholes
HV tails
fiberglass stiffener

## Slide 30: Manufacturing a C-GEM
Epoxy glue (Araldite 2011) is distributed by hand on a 2 mm wide line
3 GEM foils are spliced together with a 3 mm overlap and closed in a vacuum bag (0.9 bar)
Alignement pinholes
Vacuum holes

## Slide 31: Manufacturing a C-GEM
Vacuum bag envelope
GEM is protected with a Mylar sheet and wrapped on the cylindrical mold
Transpirant tissue (PeelPly from RiBa) is placed around to distribute vacuum
Final cylindrical GEM with internal and external rings

## Slide 32: Readout Plane
Readout plane is realized at CERN TE-MPE-EM
It is a kapton/copper multilayer flexible circuit
Provides 2-dimensional readout with XV strips on the same plane
X are realized as longitudinal strips
V are realized by connection of pad through conductive holes and a common backplane
Pitch is 650 µm for both
X strip
V strip
X pitch 650µm  X res 190µm
V pitch 650µm  Y res 350µm

## Slide 33: Readout CF Lamination
The readout is shielded with a very ligth Carbon fiber composite structure realized by RiBa Composites, Faenza, IT
The shield is composed by a sandwich of two 90 µm thick carbon foils prepreg with epoxy (Carbon-Epoxy 90g/m2 58% Fibra T300) spaced by a 5 mm thick Nomex honeycomb (ECA-I 4.8-48 3/16-3.0)
first 90µm CF skin
5mm HC
second 90µm CF skin
curing 24h in autoclave
final readout electrode

## Slide 34: Assembling a triple-GEM
The second electrode (GEM3) is placed on the machine with its mold and
Fixed to the bottom plate
The top flange with Readout is moved down around the GEM

## Slide 35: Blocking Capacitor

## Slide 36: Material Budget
Material | Radiation Length (cm)
Copper | 1,43
Polyimide - Kapton | 28,6
Carbon fiber | 28
Argon | 14000
Isobuthane | 17000
Epoxy - Araldite 2011 | 33,5
Honeycomb - Nomex | 1250
Fiberglass - FR4 | 16
Air | 30500
Aluminum | 8
Gold | 0,33
 | Thickness (µm) | Radiation Length (%)
Copper | 3 | 1,68E-04
Polyimide | 50 | 1,40E-04
Copper | 3 | 1,68E-04
GEM foil | 56 | 4,76E-04
Copper | 3 | 2,10E-04
Polyimide | 50 | 1,75E-04
Honeycomb | 3000 | 2,40E-04
Polyimide | 50 | 1,75E-04
Copper | 3 | 2,10E-04
Cathode foil | 3106 | 1,01E-03
Gold | 0,1 | 3,03E-05
Copper | 5 | 2,45E-04
Polyimide | 50 | 1,75E-04
Copper | 5 | 1,05E-04
Epoxy | 12,5 | 3,73E-05
Polyimide | 125 | 4,37E-04
Epoxy | 12,5 | 3,73E-05
Polyimide | 50 | 1,75E-04
Copper | 3 | 2,10E-04
Gold | 0,1 | 3,03E-05
Anode Foil | 263 | 1,48E-03
Carbon fiber | 90 | 3,21E-04
Honeycomb | 5000 | 2,40E-04
Carbon fiber | 90 | 3,21E-04
CF Shield | 3200 | 9,54E-04
Total 1 Layer |  | 4,87E-03
Total 4 Layers |  | 1,95E-02
The KLOE-2 requirement of X0 < 2% is fulfilled