## Slide 1: Generation of high brightness electron beams from plasma-based accelerators
FIRB: Project of research funded by the Italian Government (2013-2015)
Enrica Chiadroni
Laboratori Nazionali di Frascati
2nd PAC Meeting
November 19th, 2012

## Slide 2: Motivations
Plasma Acceleration has been already demonstrated
  I. Blumenfeld et al., Nature 445, p. 741 (2007)
  W. P. Leemans, Nature Physics vol. 2, p.696-699 (2006)
  P. Muggli et al, in Proc. of 2011 Particle Acc. Conf., New York, NY, USA, TUOBN3
  …
The main issue is now on the beam quality
  High peak current, low emittance, small energy spread, stability, repeatability
Future applications
  FELs
  Multi-staging compact colliders
  Advanced radiation sources

## Slide 3: Method
External injection of electrons to be accelerated in the plasma
Laser Wakefield Acceleration
  Laser Pulse Energy: 3 J
  Laser Pulse Length: 35 fs (FWHM)
  Bunch length: < 100 fs
  Dg/g : 0.1%
  en = 1 mm mrad
  Initial Beam energy: 160 MeV
Plasma Wakefield Acceleration
  Single bunch or comb beam
    Bunch length < 100 fs
    200 pC
    en = 1 mm mrad
  …
Hollow Dielectric Waveguide Capillaries, with LPGP Orsay, B. Cros et al.

## Slide 4: Plasma Acceleration Beamline
laser input line
300 TW, < 25 fs
Ti:Sa laser
Plasma capillary

## Slide 5: Milestones
Start-to-end simulations
Generation and transport of HBEBs down to the plasma capillary
Plasma interaction chamber
Diagnostics
  HBEBs
  Plasma

## Slide 6: Resources
Electron source
(Photo-cathode)
RF photo-injector
FLAME laser
LWFA
--------------
PWFA
Diagnostics: electrons and plasma
Univ. of Lecce (A. Lorusso)
LNF
LNF
Univ. La Sapienza (A. Mostacci)
Univ. of Milan
(C. A. Potenza)
2 Post-Docs and 2 Fix-term researchers
LNF
Univ. La Sapienza
(A. Mostacci)
Univ. of Milan
(C. A. Potenza)
LNF
Univ. La Sapienza
(A. Mostacci)
Univ. of Milan
(C. A. Potenza)
Collaborations
ENEA (C. Ronsivalle)
Univ. of Tor Vergata
(A. Cianchi)
RAS (A.E. Nikolay)
IST (L.O. Silva)
CNRS (B. Cros)
CNR (L. Gizzi)
CNRS
(J. Fuchs, K. Ta Phuoch, J.R. Marques)

## Slide 7: Tasks
Electron source
(Photo-cathode)
RF photo-injector
FLAME laser
LWFA
--------------
PWFA
Univ. of La Sapienza
- Electron beam transport and measurement
- Study of beam dynamics in the plasma
Study and development of plasma diagnostics
Data analysis
LNF
- S2E simulations
beamlines installations
Study and design of the plasma chamber
Generation, acceleration and transport of HBEBs up to the IC
Laser transport up to the IC
Synchronization
Electron diagnostics (EOS, DR, etc..)
Univ. of Lecce
- Study and development of novel metallic photocathodes based on thin layers of Mg, Yt and Pb
Univ. of Milan
- Simulations of laser/beam plasma interaction (Qfluid and Aladyn)
- Characterization of betatron radiation for transverse electron beam diagnostics
Diagnostics: electrons and plasma

## Slide 8: Tasks
Electron source
(Photo-cathode)
RF photo-injector
FLAME laser
LWFA
--------------
PWFA
Diagnostics: electrons and plasma
LNF | Univ. of La Sapienza | Univ. of Lecce | Univ. of Milan
S2E simulations | Electron beam transport and measurement | Study and development of novel metallic photo-cathodes based on thin layers of Mg, Yt and Pb | Simulations of laser/beam plasma interaction (Qfluid and Aladyn)
Beam lines installation |  |  | 
Study and design of the plasma chamber | Study of beam dynamics in the plasma |  | 
Generation, acceleration and transport of HBEBs up to the IC |  |  | 
 |  |  | Characterization of betatron radiation for transverse electron beam diagnostics
Laser transport up to the IC | Study and development of plasma diagnostics |  | 
Electron and laser synchronization |  |  | 
Electron diagnostics (EOS, DR, etc..) | Data analysis |  | 

## Slide 9: Time Schedule
Start-to-end simulations |  | 
Laser/electron beams transport to IC |  | 
Electron beam diagnostics |  | 
Study and design of IC | IC machining and installation | 
 | Plasma diagnostics | 
Study and design of new cathodes | Cathodes test at LNF | 
 | LWFA EXPERIMENT PWFA | 
t
1 y
2 y
3 y

## Slide 10: Impact on SPARC_LAB Activities
Our project has not destructive interferences with other activities at SPARC_LAB
  Plasma acceleration beamline already exists => External Injection Beamline
  FLAME already exists and works: our project will benefit of
    laser transport experience for Thomson back-scattering
    Laser and electron beams synchronization studies
  Commissioning of the beamline is in common with Thomson experiment
  Beam time request only the second and third year

## Slide 11: Thanks!

## Slide 12: The SPARC_LAB Activities
Laser/Plasma physics (High gradient acceleration)
  Particle Beam driven Plasma Acceleration => COMB
  External injection (EXIN)
  Self-Injection (=> γ-RESIST)
FEL physics
  4-pulses comb beam
  Three stages superradiant cascade
  Seed sources: Kagome’ fibers (N. Joly, M. E. Couprie)
Advanced radiation sources and applications
  X-ray Thomson backscattering (ELI-NP, THOMSON)
  Broad band and narrow band THz radiation (TERASPARC)
Advanced beam physics and accelerator technology
  ELI-NP
  COMB
Laser/Plasma based ion sources (LILIA)
Positron source (POSSO)
1st PAC Meeting, June 6th, 2012

## Slide 13: Plasma Acceleration Beamline: EXternal INjection
44th LNF SC Meeting, June 4th, 2012
Complete Simulations for injection and acceleration in capillary (SEP. 2012)
Start Acquisition Procedure for magnets of diagnostic transport line (OCT. 2012)
Complete Design of Interaction Chamber (DEC. 2012)
Gas capillary

## Slide 14: Plasma Acceleration Beamline: EXternal INjection
44th LNF SC Meeting, June 4th, 2012
Hollow Dielectric Waveguide Capillaries, with LPGP Orsay, B. Cros et al.

## Slide 15: Plasma Acceleration Beamline: COMB
44th LNF SC Meeting, June 4th, 2012
Resonant plasma Oscillations by Multiple electron Bunches
Weak blowout regime with resonant amplification of plasma wave by a train of high brightness electron bunches produced by Laser Comb technique  5 GV/m with a train of 3 bunches, 100 pC/bunch, 50 m long, 20 m spot size, in a plasma of density 1022 e-/m3 at p=300 m ?
Ramped bunch train configuration to enhance transformer ratio?
High quality bunch preservation during acceleration and transport?
Strong blowout regime with pC/fs bunches  TV/m regime ?

## Slide 16: Simulation parameters (by A.R. Rossi)
Laser parameters
Energy: 3 J (both realistic and conservative);
Length: 35 fs (FWHM);
w0: 64.5 um;
Rayleigh range: ~ 16.6 cm;
Gaussian profiles;
Guided by transverse plasma density tapering;
Acceleration length: ~ 22 cm.
In - Beam parameters
Charge: 5 pC
σtr: ~ 10 um;
σz: 3.5 um;
εn: 1.2 mm – mrad;
δγ/γ: 10-3;
Energy: 160 MeV
In the code, the laser is guided by a transverse density tapering since the presence of a capillary tube needs to be implemented (work in progress). However the transverse mode in the capillary, if the laser is well matched (w0=0.645 Rcap), should not be too different from the TEM00 of free space [1]. Moreover, the leakage of energy from the capillary boundary has been implemented by multiplying the laser intensity by [1]:
Exp[-s/Ld] with Ld~ 7.4 m for Rcap= 100 um
which allows for a long accelerating plasma channel, since the laser parameter is less than 1 and the plasma wave is linear and slippage is not critical. The main yet unanswered question is what happens to the plasma wave when 2Rcap λp (work in progress), which however is not our case for now. Moreover, the capillary radius has been take quite large in order to simulate an easier experimental setting (as regards laser pointing).
In the following the plasma channel is composed of a 2 cm long matching ramp, with linearly increasing density from an initial value n0=5x1015 cm-3, and an accelerating stage with n0=1017 cm-3. The subsequent matching from plasma to vacuum is still missing due to numerical instabilities. The two simulations differ in the injection phase dz0, measured as the distance from the laser and witness.
[1] B. Cross et al., Phys. Rev. E, 65 026405 (2002).

## Slide 17: Setting 1: dz0=110 fs (by A.R. Rossi)
Out - Beam parameters
σtr: ~ 3.6 um;
σz: 3.5 um;
Εn: 3.1 mm – mrad;
δγ/γ: 0.24 (!!) but mostly linear;
Energy: 351 MeV
<Ez>=0.87 GV/m

## Slide 18
Out - Beam parameters
(not including 68 “out of bucket” lost particles)
σtr: ~ 3.6 um;
σz: 3.5 um;
εn: 2.5 mm – mrad;
δγ/γ: 5 x 10-2 (no significant beam loading);
Energy: 565 MeV
<Ez>= 1.84 GV/m
Setting 2: dz0=156 fs (by A.R. Rossi)
These particles have a significant portion of their total energy in transverse momenta. Eventually, they are doomed to leave the bucket.

## Slide 19
Setting 2: dz0=156 fs (by A.R. Rossi)
Further optimization needed!
These particles have a significant portion of their total energy in transverse momenta. Eventually, they are doomed to leave the bucket.
Out - Beam parameters
σtr: ~ 3.6 um;
σz: 3.5 um;
Εn: 3.1 mm – mrad;
δγ/γ: 0.24 (!!) but mostly linear;
Energy: 351 MeV
<Ez>=0.87 GV/m

## Slide 20
A train of 3 electron drive bunches,
each of them 25 μm long, with 200 pC at 150 MeV, 1 μm rms normalized emittance, could accelerate up to 250 MeV a 20 pC, 10 μm long witness bunch, injected at the same initial energy in a 10 cm long plasma of wavelength 383 μm.
The drive bunches will loose energy to excite the plasma accelerating field up to 1 GV/m in favour of the witness bunch.
Simulations show also that the witness bunch can preserve a high quality with a final energy spread less than 1 % and 1.6 μm rms normalized emittance.
Preliminary QFLUID simulations