## Slide 1: Nuclear Physics for Hadron Therapy
G. Battistoni, INFN Milano

## Slide 2: Outline
Introduction: the basics of hadron therapy
The role of Monte Carlo in particle therapy
The Bragg peak and related physics
The fragmentation of nuclear projectiles
The control of treatment:
  production of b+ emitters
  emission of prompt gamma rays
  emission of charged particles

## Slide 3: Credits
U. Amaldi, Tera Foundation
V. Patera, Univ Roma 1 and INFN
A. Ferrari, CERN
T. Böhlen, CERN
P. Sala, INFN
A. Mairani, CNAO
M. Durante. GSI

## Slide 4: Oncological Radiotherapy
Purposes
Deliver a high dose to tumoral tissue
”Conformal” dose distribution on the target volume
Spare as much as possible healthy tissues and “Organs at Risk”
“Conventional”: photons (from accelerated electrons)
Hadron Therapy (“Particle Therapy”): protons or Light Ions (Z<18)‏

## Slide 5: Basic strategy of radiotherapy
(fonte: Prof. U.Amaldi)

## Slide 6: Use of multiple beams (different directions)
Also:
Modulation of intensities

## Slide 7: Examples of different solutions
(fonte: Prof. U.Amaldi)

## Slide 8: Motivation of Particle Therapy (hadrontherapy)

## Slide 9
(fonte: Prof. U.Amaldi)
“Charged Particle Therapy” to better preserve healthy tissues ans organs at risk

## Slide 10: Release of dose modulated in depth
Beams at edifferent energies delever dose at different depths

## Slide 11: Longitudinal conformation: the concept of Spread Out Bragg Peak (SOBP)

## Slide 12: Different ion beam delivery strategies
Active conformation via energy
variation and lateral magnetic deflection of pencil-like beams
Pencil beam
http://p-therapie.web.psi.ch/
Passive conformation of scattered broad beam with compensator (distal edge) and collimator (lateral shaping)
Broad
beam
Chu et al, Rev Sci Instrum 1993
Notes: 12

## Slide 13
Rasterscan Method @ GSI / HIT/ CNAO
scanning of
focussed
ion beams
in fast
dipole magnets
active variation
of the energy,
focus and
intensity in the
accelerator and
beam lines
Haberer et al., NIM A , 1993
Notes: 13

## Slide 14
The Fundamental Formula
The equation relating dose to fluence and stopping power is the starting point of most beam line design problems. From the figure :
dose = fluence × mass stopping power
N protons
area A
Δx

## Slide 15: Basic physics ingredients
Knowledge of Stopping power: S ≡ – dE/dx (MeV/cm) mass stopping power:

## Slide 16: Charged particle dE/dx: Bethe-Bloch and corrections
16
16
Spin 0
(spin1 is similar):
ln 44 relativistic rise
I : mean excitation energy , material-dependent;
δ : density correction;
C : is the shell correction, important at low energies
Tmax : maximum energy transfer to an electron (from kinematics);
L1 : Barkas correction (z3) responsible for the difference in stopping power for particles-antiparticles;
L2 : Bloch (z4) correction
G : Mott corrections
Valid for m>>me, However, the formulation for electron/positrons is similar, except for the “energetic” collisions with atomic electrons.

## Slide 17
17
17
Mott corrections
[data from A.A. Golubev et al, NIMB 263 (2007) 339]
238U range in copper
500MeV/n
950MeV/n
Example of effect of Mott corrections implementation in the stopping power, in its fluctuations and in the delta-ray spectrum in the FLUKA MC code.
Mott parametrization adapted from by T. Lijian, H. Qing and L. Zhengming, Radiat. Phys. Chem. 45 (1995) 235
Remarkable effects are found for high Z ion beams,
effect non negliglible for C beams at therapy energies
Notes: M.C.Morone, IEEE 2012M.C.Morone, IEEE 2012
M.C.Morone, IEEE 2012
17

## Slide 18: Different behavior at very low energy
p on Carbon (FLUKA Monte Carlo)
Bethe-Bloch behaviour

## Slide 19: Coulomb collisions: “nuclear” stopping power
The “nuclear” stopping power is the energy loss due to Coulomb collisions with atomic nuclei, rather than with atomic electrons
The nuclear stopping power is usually negligible with respect to the electronic stopping power, apart at low energies/heavy ions

## Slide 20: “Nuclear” (Sn) vs “Electronic” (Se) stopping power
The total (S), nuclear (Sn) and electronic (Se) stopping power for Oxygen ions in Silicon (left), and Silver ions in Gold (right). The abscissa is the ion total kinetic energy. The partition function Sn/(Sn+Se) is also plotted

## Slide 21
Mean Excitation Energy: I
This graph from ICRU 49 [2] shows the dependence of I on atomic number Z. Irregularities in I/Z vs. Z are caused by atomic shell structure. It’s obvious that interpolating I accurately between measured values (from range or stopping power measurements) is not easy.
Mixtures obey the Bragg additivity rule, which is easily derived by assuming the absorber to be composed of several discrete sheets:
Compounds and molecules are more complicated because I is affected by chemical bonding. Water turns out to be a particularly difficult case, which is unfortunate.

## Slide 22: The Physics of Bragg Peak
The shape of the Bragg peak depends on:
variation of stopping power with energy
the transverse size of the beam,
range straggling: the peak of the depth-dose distribution increases in absolute width as beam energy increases.
beam energy spread,
nuclear interactions,
low energy contamination,
effective source distance,
Experimentally: on the dosimeter used in the measurement.

## Slide 23
nuclear buildup or low energy contamination
nuclear reactions take away from the peak and add to this region
depth from beam energy
width from range straggling and beam energy spread
1/r2 and transverse size set peak to entrance ratio
Prom PTCOG lectures: Anatomy of the Bragg Peak
overall shape from increase of dE/dx as proton slows

## Slide 24
The ‘local energy deposition’ approximation fails at the entrance to a water tank where longitudinal equilibrium has not yet been reached. You can see this if you measure a Bragg peak vertically so that the proton beam enters from air. This scan, courtesy of IBA, is from the Burr Center.
Nuclear Buildup

## Slide 25
The fluence on the central axis of a pencil beam decreases with depth because of out-scattering of the protons. The dose on axis (fluence × stopping power) therefore goes down; the Bragg peak vanishes. A scan along the axis with a small ion chamber would show this; a scan with a large one would not.
In a broad beam the axial fluence is restored by in-scattering from neighboring pencils (transverse equilibrium). A scan along the axis with a small ion chamber will therefore measure the ‘true’ Bragg peak.
Transverse Equilibrium

## Slide 26: Measurements are fundamental but a calculation tool is necessary: the role of Monte Carlo
Realistic description of particle interactions, especially in complex geometries and inhomogeneous media where analytical approaches are at their limits of validity
Possibility to investigate separate contributions to quantities of interest which may be impossible to be experimentally assessed and/or discriminated
Startup and Commissioning of new facilities: e.g., shielding calculations; beamline modeling, generation of input data for Treatment Planning ( meas. time)
Validation of dose calculations: in water-equivalent system and in patient anatomy (CT)
Dedicated applications: imaging of secondary emerging radiation for treatment verification (PET, prompt gamma…)
KEY ISSUES: reliability of physics models

## Slide 27: The case of FLUKA code. Short description:
FLUKA is a general purpose tool for calculations of particle transport and interactions with matter
All Hadrons (p, n, , K, pbar, nbar, (anti)hyperons…)
Electromagnetic (, e+/-) and μ and n
Nucleus-nucleus
Low energy neutrons (0-20 MeV, multigroup, ENDF… )
Full mixed field capability
Transport in magnetic field
Combinatorial (boolean) and Voxel geometries
Double capability to run either fully analogue and/or biased calculations
On-line evolution of induced radioactivity and dose
Radiation damage predictions (NIEL, DPA)
User-friendly GUI interface thanks to the Flair interface
http://www.fluka.org
More than 5000 users all over the world
1 keV-1000 TeV

## Slide 28: Charged Particle Therapy with Light Ions heavier than protons
Light ions advantages in radiation treatments of tumor wrt IMRT:
Better Spatial selectivity in dose deposition: (p,12C)
Reduced lateral and longitudinal diffusion (12C)
High Biological effectiveness (12C)
Treatment of highly radiation resistent tumours, sparing surrounding OAR
Additional involved nuclear physics:
nuclear reactions of projectile  fragmentation,…

## Slide 29: 12C Bragg peaks vs exp. data
Experiment: circles (270 AMeV) and triangles (330 AMeV)
FLUKA: lines
Sommerer et al: Phys. Med. Biol. 51 2006

## Slide 30: Accurate MC calculations: playing with a proton beam
Dose vs depth
energy deposition
in water for a 200 MeV p beam with various approximations for the physical processes taken into account

## Slide 31: The relevant aspects of Nuclear Physics
Proton therapy (p, E: 10-250 MeV):
  Reaction cross sections (beam attenuation) +++
  Elastic cross sections +
  Particle (p,n,α..) emission + (mostly for background, ++ radiobiology)
  Positron emitter production + (“+” only because data available)
  gamma de-excitation
Therapy with light ions (ions, E: 10-400 MeV/n):
  Reaction cross sections (beam attenuation) +++
  Fragment (α included) production +++
  Particle emission, p +++, others +
  Positron emitter production +++
  gamma de-excitation
Conventional therapy (γ, E: 3-30 MeV)
  (γ,x) (particularly (γ,n)) + (mostly for background)

## Slide 32: Playing with a proton beam II part
Dose vs depth
energy deposition
in water for a 214 MeV real p beam under various conditions.
Exp. Data from PSI

## Slide 33: Bragg peaks vs exp. data: 12C @ 270 MeV/n
Exp. Data Jpn.J.Med.Phys. 18, 1,1998
Close-up of the dose vs depth distribution for 270 MeV/n 12C ions on a water phantom.
The green line is the FLUKA prediction with the nominal 0.15% energy spread
The dotted light blue line is the prediction for no spread, and the dashed blue one the prediction for I increased by 1 eV

## Slide 34: The case of nuclei: Bragg peaks vs exp. data: 12C @ 270 & 330 MeV/n
Exp. Data Jpn.J.Med.Phys. 18, 1,1998
Dose vs depth distribution for 270 and 330 MeV/n 12C ions on a water phantom.
The full green and dashed blue lines are the FLUKA predictions
The symbols are exp data from GSI

## Slide 35: FRAGMENTATION OF 12C in biological tissue
Mitigation and attenuation of the primary beam
Different biological effectiveness of the fragments wrt 12C
Production of fragments with higher range vs primary ions
Production of fragment with different direction vs primary ions
Dose release in healthy tissues with possible long term side effects, in particular in treatment of young patients must be carefully taken into account in the Treatment Planning System
Exp. Data (points) from Haettner et al, Rad. Prot. Dos. 2006
Simulation: A. Mairani PhD Thesis, 2007, Nuovo Cimento C, 31, 2008
12C (400 MeV/u) on water
Bragg-Peak
Dose over the Bragg Peak :
p ~ 1-2 %
C ~ 15 %
Ne ~ 30 %
Courtesy of Andrea Mairani

## Slide 36: Bragg peaks vs exp. data: 20Ne @ 670 MeV/n
Dose vs depth distribution for 670 MeV/n 20Ne ions on a water phantom.
The green line is the FLUKA prediction
The symbols are exp data from LBL and GSI
Exp. Data Jpn.J.Med.Phys. 18, 1,1998
Fragmentation products
mostly α’s and p’s

## Slide 37: What should we know about 12C fragmentation?
Production yelds of Z=0,1,2,3,4,5 fragments
d2/ddE wrt angle and energy, with large angular acceptance
For any 12C energy of interest (100-300 MeV/nucl)
Measurements on thin target of all materials crossed by C beam
Detect the correlation between emitted fragments
12C , E
12C , E'
,A,Z
',A',Z'
X,Ex,x,x
Y,Ey,y,y
Not possible a complete DB of measurements
We need to train a nuclear interaction model with the measurements!!

## Slide 38: What we already know: thick target measurement
Projectile Energy[MeV/N] Target
4He 100, 180 C, Al, Cu, Pb
12C 100, 180,400 C, Al, Cu, Pb
20Ne 100, 180,400 C, Al, Cu, Pb
28Si 800 C, Al, Cu, Pb HIMAC by Kurosawa et al.
40Ar 400 C, Al, Cu, Pb
56Fe 400 C, Al, Cu, Pb
126Xe 400 C, Al, Cu, Pb
20Ne 337 C, A, Cu and U BEVALAC by Schimmerling et al.
93Nb 272 Al, Nb BEVALAC by Heilbronn et al.
93Nb 435 Nb
4He 155 Al NSRL by Heilbronn et al.
12C 155 Nb
4He 160 Pb SREL by Cecil
4He 180 C, H2O, steel, Pb
12C 200 H2O GSI by Günzert-Marx et al.
12C 400 H2O GSI by Haettner et al.
Courtesy of M. Durante
Tentative & incomplete list
A lot of integral measurements measurements are already around.. But very few for the correct triplet of projectile,target and energy
Notes: 38
Thank you, Mr. Chairman. It’s my great pleasure to give a talk to you. I’ll be speaking about some of the overview of the fragmentation of heavy charged particles in relation to radiotherapy.

## Slide 39: What we already know: thin target measurement
Projectile Energy[MeV/N] Target
4He 135 C, Poly, Al, Cu, Pb
12C 135 C, Poly, Al, Cu, Pb Sato et al.
20Ne 135 C, Poly, Al, Cu, Pb
40Ar 95 C, Poly, Al, Cu, Pb
12C 290, 400 C, Cu, Pb
20Ne 400, 600 C, Cu, Pb Iwata et al.
40Ar 400, 560 C, Cu, Pb
4He 230 Li, C, CH2, Al, Cu, Pb
14N 400 Li, C, CH2, Al, Cu, Pb
28Si 60 Li, C, CH2, Al, Cu, Pb Heilbronn et al.
56Fe 500 Li, C, CH2, Al, Cu, Pb
12C 400 C, Poly Toshito et al.
only with
detectors
at ~ 0°
Tentative & incomplete list
A lot of measurements on thin target are already around.. but not wrt production angle and energy
Emulsion Chamber: angle ok
E ~OK, low stat, no corr

## Slide 40: The IDEAL detector
On an event by event basis, the ideal detector should:
Identify all the fragment produced, i.e. detect charge , with 0 < Z < 6 and detect mass, on all the solid angle
Detect the energy of the fragments ( from 0 to 700 MeV p)
Measure the emission angle of the fragments (0-90 deg)
Detect all the correlations, with systematic below few % (rescattering in TG, out of TG fragmentation, etc..)
Starting from scratch, such a detector would be VERY, VERY expensive , would take LONG, LONG time and a VERY LARGE group to be designed and built.

## Slide 41: The FIRST collaboration
FIRST stands for: Fragmentation of Ions Relevants for Space and Therapy  S371 is the GSI label
INFN: Cagliari,LNF,LNS,Milano,Roma3,Torino: C.Agodi, G.Battistoni, M.Carpinelli, G.A.P.Cirrone, G.Cuttone , M.De Napoli, B.Golosio, Y.Hannan, E.Iarocci, F.Iazzi, R.Introzzi, A.Mairani, V.Monaco, M.C.Morone,P.Oliva, A.Paoloni, V.Patera, L.Piersanti, N.Randazzo, F.Romano, R.Sacchi, P.Sala, A.Sarti, A.Sciubba, C.Sfienti, V.Sipala, E.Spiriti
DSM/IRFU/SPhN CEA Saclay, IN2P3 Caen, Strasbourg, Lyon: S.Leray, M.D.Salsac, A.Boudard, J.E. Ducret, M. Labalme, F. Haas, C.Ray
GSI: M.Durante, D.Schardt, R.Pleskac, T.Aumann, C.Scheidenberger, A.Kelic, M.V.Ricciardi, K.Boretzky, M.Heil, H.Simon, M.Winkler
ESA: P.Nieminem, G.Santin
CERN: T.Bohlen

## Slide 42: The ALADIN setup @GSI
TPC MUSIC IV
TOF
WALL
Neutron detector
Interaction
region
ALADIN
MAGNET
Beam
Beam
First data taken in 2011
under analysis
Target
Vertex
Bmon
Start
New IT
Ptagger

## Slide 43: From an example of MC model comparison

## Slide 44
Charge changing cross sections on Water and Polycarbonate

## Slide 46: “Typical” modeling of nuclear interactions:
Target nucleus description (density, Fermi motion, etc)
Preequilibrium stage with current exciton configuration and excitation energy
(all non-nucleons emitted/decayed + all nucleons below 30-100 MeV)
Glauber-Gribov cascade with formation zone
(Generalized) IntraNuclear cascade
Evaporation/Fragmentation/Fission model
γ deexcitation
t (s)
10-23
10-22
10-20
10-16
Cross sections: absorption/quasi-elastic
Transition from single to multiple chains/collisions
Transition (hN) from resonance production to quark string models
Onset of formation zone
Fast light fragments
(Pion interactions below 1 GeV)
(In medium cross-sections)
Spin and parity…
Statistical multi-fragmentation or binary emission?

## Slide 47
DPMJET-III
  DPMJET (R. Engel, J. Ranft , S. Roesler1): Nucleus-Nucleus interaction model. Used in many Cosmic Ray shower codes. Based on the Dual Parton Model and formation zone Glauber cascade, like the high-energy FLUKA h-A event generator
Modified and extended version of rQMD-2.4
  rQMD-2.4 (H. Sorge et al.2) Cascade-Relativistic QMD model
  Successfully applied to relativistic A-A particle production
BME (BoltzmannMasterEquation)
  FLUKA implementation of BME from E.Gadioli et al (Milan)
1010
5
0.1
E (GeV/A)
Electromagnetic dissociation
FLUKA
Evaporation- fission- fragmentation module
handles fragment deexcitation
Tested and benchmarked in h-A reactions
(Projectile-like evaporation is responsible for the most energetic fragments)
Example: Heavy ion interaction models in FLUKA
1proc. MC2000 , p 1033 (2001)
2NPA 498, 567c (1989), Ann.Phys. 192,266 (1989), PRC 52, 3291 (1995)

## Slide 48
THE BME* (Boltzmann Master Equation) – FLUKA interface for nucleus – nucleus interactions below 150 MeV/n
A version of the BME-FLUKA event generator considering two different reaction mechanisms is implemented in FLUKA
1. COMPLETE FUSION
Preequilibrium according to the BME theory
In order to get the multiplicities of the pre-equilibrium particles and their double differential spectra, the BME theory is applied to a few representative systems at different bombarding energies and the results are parameterized
2. PERIPHERAL COLLISION
three body mechanism
or
“inelastic scattering” (for high b)
The complete fusion cross section decreases with increasing bombarding energy. We integrate the nuclear densities of the projectile and the target over their overlapping region,, and obtain an excited “middle source” and two fragments (projectile and target-like). The kinematics is suggested by break-up studies.
*M. Cavinato et al., Nucl. Phys. A 643, 15 (1998); 679, 753 (2001)

## Slide 49: BME event generator benchmarks
12C + 12C @ 16.5 MeV/n
exp. data
S.V. Förtsch (iThemba LABS, SA)
et al.
silicon detector telescope
(low energy threshold of ~ 5 MeV/n)
Fragment energy distribution at different emission angles
Histo: BME in FLUKA
Dots : Data

## Slide 50
Courtesy of K.Parodi
How can we monitor a treatment?

## Slide 51: Spec’s of hadrontherapy monitor
Measure shape and absolute value of dose to check the agreement between the planned target volume and the actually irradiated volume
The measurement should be done during the treatment (in-beam)
Must rely on a given secondaries generated by the beam that comes out from the patient, to spot the position of the dose release
Must be able to deal with the other secondaries that come out that acts like background

## Slide 52: baseline dose monitoring in HT : PET
Baseline for monitor in HT is PET : autoactivation by p & 12C beam that creates b+ emitters.
Isotopes of short lifetime 11C (20 min), 15O (2 min), 10C (20 s) with respect to conventional PET (hours)
Low activity in comparison to conventional PET need quite long acquisition time (few minutes)
Metabolic wash-out, the b+ emitters are blurred by the patient metabolism
No direct space correlation between b+ activity and dose release ( but can be reliable computed by MC)

## Slide 56: Correlation between b+ activity and dose
Projectiles & target fragmentation
Target fragmentation

## Slide 57: Applications of FLUKA to p therapy @ MGH
mGy
mGy
Clival Chordoma, 0.96 GyE / field
Planned dose

## Slide 58: Post-radiation PET/CT @ MGH
Clival Chordoma, 0.96 GyE / field, DT1 ~ 26 min, DT2 ~ 16 min
Bq / ml
Bq / ml
Average Activity
1 Field
2 Field
K. Parodi et al, IJROBP 2007
… and FLUKA-voxel functionalities being also used at HIT …

## Slide 59: 12C(p,x)11C and 16O(p,x)15O cross sections.

## Slide 60: Recent Model Development: Spin/parity: isomers… etc
Spin/parity dependent evaporation (Hauser-Feshbach) is still too complex to be implemented in MC codes
As a consequence isomer production wrt ground state production cannot be reliably computed
Individual level population  gamma emission are hard to predict
Furthermore, it is difficult to keep track of the total angular momentum and parity evolution of the system during the cascade and pre-equilibrium stages, particularly at medium/high energies
Some work going on at least for the Fermi break-up part (light systems) when conditions are well defined

## Slide 61: Spin-parity in Fermi Break-up in FLUKA code:
… however it implicitly assumes that the emission takes place in L=0. Now in FLUKA when the compound nucleus spin and parity, Jπ, are known*:
The minimum orbital momentum, Lmin, required to match Jπ is computed
Sn is restricted to the subset of spin combinations compatible with Lmin
If Lmin > 0, then ECoul  ECoul + Bcentrifugal
* At present only the cases where no emission has taken place before Fermi break-up are considered
The probability of splitting into n fragments of given masses, mi, spins, si, … is given by:

## Slide 62: Spin-parity in Fermi-Break-up in FLUKA code
In most MC’s, for A<16, evaporation is substituted by Fermi break-up
In cases where spin and parity of the residual nucleus are known, conservation laws, constraints on available configurations and centrifugal barrier (if L=0 is forbidden), are enforced in the fragment production
Straightforward example : photonuclear reaction in the GDR region
Effect : residual nuclei production
Application: background from induced activity in underground experiments
12C + in GDR
J = 1-
3 and  + 8Be impossible in L=0
Factor 3 on 11C production

## Slide 63: (p,d), (n,d) reactions:
Excitation functions for the production of 11C (left), 15O (right): now deuteron formation at low energies is treated directly and no longer through coalescence (Data: CSISRS, NNDC, blue Fluka2011.2, red Fluka2012.2)

## Slide 64: Background or Signal?
The p, 12C beams generate a huge amount of secondaries.. expecially prompt single gs. and neutrons in the 1-10 MeV range. Can be used to track the beam inside the patient
The nuclear models inside MC (FLUKA&G4) are becoming able to fully describe this physics  huge development effort ongoing
G4

## Slide 65: The prompt gamma saga…
The gamma are quite copiously produced by proton and 12C beam.
The emission region stretches along all the beam path but has been shown to ends near the Bragg peak for both beams.
There is a huge background due to neutrons & uncorrelated gamma produced by neutrons. This background is beam, energy and site specific
It’s not simple backpointing the g direction: take profit by the SPECT technique… but the energy of these g is in the 1-10 MeV range-> much more difficult to stop and collimate!!

## Slide 66: Prompt gs @GANIL
73 AMeV carbon beam
g peak correlated with BP
MC one order of magnitude off but it’s improving fast)
Neutrons background (TOF rejection ?)
BP position

## Slide 67: Possible prompt g monitoring: Gamma camera
Large flux, maybe enough stats for in-beam
Collimation like Anger camera in SPECT (? 1<Eg<10 MeV )
Well known technique, robust, compact
Wide g energy spectrum  careful design
Neutron background rejection? TOF not so easy to exploit.
Collimation reduces stats

## Slide 68: Lyon group: GANIL/GSI data
[figures and exp. data taken from F. Le Foulher et al IEEE TNS 57 (2009),
E. Testa et al, NIMB 267 (2009) 993]

## Slide 69: Gamma De-excitation in Fluka
At the end of evaporation: cascade of  transitions
At high excitation: assume continuous level density and statistical emission:
At low excitation: through discrete levels
  Tabulated experimental levels (RIPL-3) and branchings
  Rotational approximation outside tabulations
  Account for discrete levels in evaporation and the fast (cascade and/or pre-equilibrium) stages (to be extended to rQMD and DPMJET))
  Photon angular distribution according to multipolarity and spin ( effort to estimate residual spin value and direction)
See A. Ferrari et al., Z. Phys C 71, 75 (1996)
L= multipole order
=level density at
excitation energy U
f = strength from single
particle estimate (c)+ hindrance (F)

## Slide 70: Examples: photon spectra, pre-2011 status
Histograms: FLUKA results with stat errors. Dots: expt data from Dickens et al. report ORNL-4847 (1973) and G.L.Morgan, report ORNL-5563 (1979)
Ti(n,x) at 19 MeV
W((n.x) at 18-20 MeV

## Slide 71: Improved model: example
Overall shape
Unchanged
More details are evident

## Slide 72: GANIL: 90 deg photon yields by 95 MeV/n 12C in PMMA
Ganil after correction of the data
Blue: fluka
Red: data
Exercise: subtract from data only the amount of background needed to get to the same level as simulation in the first two points
Preliminary

## Slide 73: GSI: 90 deg photon yield by 310 MeV/n 12C in Water
Here the simulation plots changed, because of a technical mistake in
the normalization
(factor 9/12 )
And a correction in the detector distance from target (small)
Preliminary

## Slide 74
Photon yields by 80 MeV/n C in PMMA
Energy spectrum of “photons” for 160 MeV p on PMMA. FLUKA red line, data black dots (C.Agodi et al., JINST 2012 in press)
Absolute comparison
Preliminary
PMMA
12C
LYSO crystals


## Slide 75
NaI detector
PMMA
target
Pb
Collimator
Schematic layout
(dimensions mm)
from J.Smeets et al., IBA
Photon yields by 160 MeV p in PMMA
Energy spectrum of “photons” after background subtraction (collimator open – collimator closed) for 160 MeV p on PMMA. FLUKA red line, data black line (J.Smeets et al., IBA, ENVISION WP3)
Absolute comparison
Preliminary

## Slide 76: What about charged particles??
Charged particles have several nice features as
The detection efficiency is almost one
Can be easily back-tracked to the emission point-> can be correlated to the beam profile & BP
proton
beam
BUT…
They are not so many
Energy threshold to escape ~ 100 MeV
They suffer multiple scattering inside the patient -> worsen the back-pointing resolution

## Slide 77: MC is essential to investigate long term effects to healthy tissues…
Important Issue  Secondary Neutrons…

## Slide 78
Again example from FLUKA: Thick target examples: neutrons
natC(p,xn) @ 113 MeV, stopping target
Data: NSE110, 299 (1992)
natC(p,xn) @ 68 MeV, stopping target
Data: JAERI-C-96-008, 217 (1996)

## Slide 79: Neutron interaction: typical cross section
tot
thermal  1/v
unresolved resonance region
resolved
resonance
region
Ekin incident neutron
1eV
1keV
1MeV
Resonances  energy levels in compound nucleus A+1Z*
resonance
spacing
few eV
Resonance spacing too dense  overlapping resonances
Evaluated nuclear data files (ENDF, JEFF, JENDL...)
  typically provide neutron  (cross sections) for E<20MeV for all channels
   are stored as continuum + resonance parameters

## Slide 80: Neutronics (below 20 MeV)
All codes make use of Evaluated Nuclear Data Files for neutron propagation below 20 MeV  inclusive and uncorrelated.
New requirements @ LANL:
Correlated n and  emission from fission  advances in endf and/or event generators
Modeling delayed n,  emission in simulations, from photon and particle interrogation
Crititicality: well reproduced in many fast, intermediate, and thermal assemblies. However well known compensating errors in fission, inelastic scattering and capture data….  new precision measurements/theory for fission (cross sections, n spectra, products) and capture

## Slide 81: Photonuclear interaction: example
Reaction:
208Pb(γ,x n)
20Eγ 140 MeV
Cross section for multiple neutron emission as a function of photon energy, Different colors refer to neutron multiplicity  n , with 2n8
Symbols: exp data (NPA367, 237 (1981) ; NPA390, 221 (1982) )
Lines: FLUKA

## Slide 82: Just published

## Slide 83
Depth dose curves in PMMA obtained using GATE/Geant4 and FLUKA for monoenergetic (up) protons (134 MeV) and (right) carbon ions (260 AMeV). Point-to-point relative dose discrepancies between the two codes are superimposed.

## Slide 84
Outgoing gamma energy distributions per primary particle obtained with GATE/Geant4 and FLUKA for monoenergetic (up) protons (134 MeV) and (right) carbon ions (260 AMeV) irradiating a PMMA target. Neither energy nor time selection were used

## Slide 85
Comparison of the location of production of the prompt gammas exiting from the target obtained using GATE/Geant4 and FLUKA for (a) the proton beam (134 MeV) (b) the carbon ion (260 AMeV) beam.

## Slide 86
Depths of production of the β+ emitters (11C, 15O) obtained combining the fluence of the protons in the PMMA target (GATE/Geant4 and FLUKA) to experimental cross-sections compared to the depths of production of the annihilation photons and depths of production of the β+ emitters (11C, 15O) obtained using the internal models of GATE/Geant4 and FLUKA.

## Slide 87
Outgoing proton energy distributions per primary particle obtained with GATE/Geant4 and FLUKA for monoenergetic (up) protons (134 MeV) and (right) carbon ions (260 AMeV) irradiating a PMMA target.

## Slide 88
Energy spectra of secondary protons corresponding to 0°, 10°, 20° and 30° angles obtained using GATE (left) and FLUKA (right) for the carbon ion beam (260 AMeV) configuration.

## Slide 89
Lethargy plots corresponding to outgoing neutrons obtained using GATE/Geant4 and FLUKA for monoenergetic (up) protons (134 MeV) and (right) carbon ions (260 AMeV) irradiating a PMMA target.

## Slide 90: Thank you for the attention

## Slide 91
Thick/Thin target examples: neutrons
9Be(p,xn) @ 256 MeV, stopping target
Data: NSE110, 299 (1992)
Pb(p,xn) @ 3 GeV, thin target
Data: NST32, 827 (1995)

## Slide 92: FLUKA (BME+preeq): (,xn) examples
Excitation functions for the production of radioisotopes from  interactions on Au (left) and Bi ( right) (Data: CSISRS, NNDC)

## Slide 93: Cascade/preequilibrium transition:
Angle-integrated 90Zr(p,xn) at 80.5 MeV (INC+preeq left, preeq only right). The lines show the total, INC, preequilibrium, and evaporation contributions. Exp. data: M. Trabandt et al., Phys. Rev. C39, 452 (1989).

## Slide 94: Equilibrium particle emission (evaporation, fission, and nuclear break-up)
Probability per unit time of emitting a particle j with energy E
Probability per unit time of fissioning
From statistical considerations and the detailed balance principle, the probabilities for emitting a particle of mass mj, spin Sj,ħ and energy E, or of fissioning are given by:
(i, f for initial/final state, Fiss for fission saddle point)
ρ’s: nuclear level densities
U’s: excitation energies
Vj’s: possible Coulomb barrier for emitting a particle type j
BFiss: fission barrier
Qj’s: reaction Q for emitting a particle type j
σinv: cross section for the inverse process
Δ’s: pairing energies
Neutron emission is strongly favoured because of the lack of any barrier
Heavy nuclei generally reach higher excitations because of more intense cascading

## Slide 95: Isotope production for 209Bi(n,xn)*:
FLUKA (lines with dashing) vs exp. data (symbols).
Data: CSISRS database, NNDC (BNL)
The reliability of (p,xn) reactions should be comparable given the similarities

## Slide 96
96
AA reaction cross sections
[L. Sihver et al, Adv Space Res 49 812 (2012)]
Improvements in the AA reaction cross sections (finalized beginning 2011) and inter-comparison with other codes
M.C.Morone, IEEE 2012
Notes: 96