## Slide 1: A circular e+e- collider to study H(125) properties - accelerator
Frank Zimmermann
Frascati, 14 February 2013
work supported by the European Commission under the FP7 Research Infrastructures project EuCARD, grant agreement no. 227579
many thanks to Roy Aleksan, Alain Blondel, John Ellis, Patrick Janot, Mike Koratzinos, Katsunobu Oide, Valery Telnov, Rogelio Tomas, Marco Zanetti

## Slide 2: outline
motivation
machine proposals
parameters, lifetime, key concepts
various features
a long-term strategy
HF quality indicators
the path forward

## Slide 3
FNAL site filler, 16 km
& FNAL VLLC 233 km ring
circular HFs – a few examples
T. Sen, E. Gianfelice-Wendt, Y. Alexahin, FNAL
IHEP Chinese HF
+ Super pp Collider
50 or 70 km
Q. Qin, IHEP
SuperTRISTAN in Tsukuba: 40 km
K. Oide, KEK
LEP3: 27 km
TLEP (LEP4): 80 km
near Geneva
A. Blondel, J. Osborne, F. Zimmermann
SLAC/LBNL
design:
27 km
Y. Cai, SLAC

## Slide 4: LEP3, TLEP (LEP4) (e+e- -> ZH, e+e- → W+W-, e+e- → Z,[e+e-→ t )
key parameters
 | LEP3 | TLEP (LEP4)
circumference | 26.7 km | 80 km
max beam energy | 120 GeV | 175 GeV
max no. of IPs | 4 | 4
luminosity at 350 GeV c.m. | - | 0.7x1034 cm-2s-1
luminosity at 240 GeV c.m. | 1034 cm-2s-1 | 5x1034 cm-2s-1
luminosity at 160 GeV c.m. | 5x1034 cm-2s-1 | 2.5x1035 cm-2s-1
luminosity at 90 GeV c.m. | 2x1035 cm-2s-1 | 1036 cm-2s-1
at the Z pole repeating LEP physics programme in a few minutes…

## Slide 5: S. Henderson’s Livingston Chart: Luminosity
TLEP-Z
TLEP-W
TLEP-H
TLEP-t
adding TLEP to the chart!

## Slide 6
circular HFs – beam lifetime
LEP2:
beam lifetime ~ 6 h
dominated by radiative Bhahba scattering with cross section s~0.215 barn
LEP3:
with L~1034 cm−2s−1 at each of several IPs:
tbeam,LEP3~18 minutes from rad. Bhabha scattering
    → solution: top-up injection
additional beam lifetime limit due to beamstrahlung:
(1) large momentum acceptance (h ≥ 3%), and/or
(2) flat(ter) beams and/or
(3) fast replenishing
(V. Telnov, K. Yokoya, M. Zanetti)
(H. Burkhardt)
(A. Blondel)

## Slide 7
circular HFs – beamstrahlung
t>0.5 s at h=1.0% (4 IPs)
t>5 s at h=1.5%
t>50 s at h=2.0%
t> 8 min at h=2.5%
simulation w 360M macroparticles
t varies exponentially w energy acceptance h
post-collision E tail → lifetime t
TLEP at 240 GeV:
M. Zanetti (MIT)
t>2 s at h=2.0% (4 IPs)
t>12 s at h=2.5%
t>50 s at h=3.0%
t> 4 min at h=3.5%
TLEP at 350 GeV:

## Slide 8
circular HFs – beamstrahlung
simulation w 360M macroparticles
t varies exponentially w energy acceptance h
post-collision E tail → lifetime t
beam lifetime versus acceptance h for 1 IP:

## Slide 9
beamstrahlung luminosity spectrum
LEP3 beamstrahlung more benign than for linear collider
M. Zanetti (MIT)
LEP3 & ILC:

## Slide 10: luminosity formulae & constraints
SR radiation
power limit
beam-beam limit
>30 min beamstrahlung lifetime (Telnov) → Nb,bx
→minimize ke=ey/ex, by~bx(ey/ex) and respect by≥sz

## Slide 11
 | LEP2 | LHeC | LEP3 | TLEP-Z | TLEP-H | TLEP-t
beam energy Eb [GeV] circumference [km] beam current [mA] #bunches/beam #e−/beam [1012] horizontal emittance [nm] vertical emittance [nm] bending radius [km] partition number Jε momentum comp. αc [10−5] SR power/beam [MW] β∗x [m] β∗y [cm] σ∗x [μm] σ∗y [μm] hourglass Fhg ΔESRloss/turn [GeV] | 104.5 26.7 4 4 2.3 48 0.25 3.1 1.1 18.5 11 1.5 5 270 3.5 0.98 3.41 | 60 26.7 100 2808 56 5 2.5 2.6 1.5 8.1 44 0.18 10 30 16 0.99 0.44 | 120 26.7 7.2 4 4.0 25 0.10 2.6 1.5 8.1 50 0.2 0.1 71 0.32 0.59 6.99 | 45.5 80 1180 2625 2000 30.8 0.15 9.0 1.0 9.0 50 0.2 0.1 78 0.39 0.71 0.04 | 120 80 24.3 80 40.5 9.4 0.05 9.0 1.0 1.0 50 0.2 0.1 43 0.22 0.75 2.1 | 175 80 5.4 12 9.0 20 0.1 9.0 1.0 1.0 50 0.2 0.1 63 0.32 0.65 9.3
LEP3/TLEP parameters -1
soon at SuperKEKB:
bx*=0.03 m, bY*=0.03 cm
SuperKEKB:ey/ex=0.25%

## Slide 12
 | LEP2 | LHeC | LEP3 | TLEP-Z | TLEP-H | TLEP-t
VRF,tot [GV] dmax,RF [%] ξx/IP ξy/IP fs [kHz] Eacc [MV/m] eff. RF length [m] fRF [MHz] δSRrms [%] σSRz,rms [cm] L/IP[1032cm−2s−1] number of IPs Rad.Bhabha b.lifetime [min] ϒBS [10−4] nγ/collision DEBS/collision [MeV] DEBSrms/collision [MeV] critical SR energy [MeV] | 3.64 0.77 0.025 0.065 1.6 7.5 485 352 0.22 1.61 1.25 4 360 0.2 0.08 0.1 0.3 0.81 | 0.5 0.66 N/A N/A 0.65 11.9 42 721 0.12 0.69 N/A 1 N/A 0.05 0.16 0.02 0.07 0.18 | 12.0 5.7 0.09 0.08 2.19 20 600 700 0.23 0.31 94 2 18 9 0.60 31 44 1.47 | 2.0 4.0 0.12 0.12 1.29 20 100 700 0.06 0.19 10335 2 74 4 0.41 3.6 6.2 0.02 | 6.0 9.4 0.10 0.10 0.44 20 300 700 0.15 0.17 490 2 32 15 0.50 42 65 0.43 | 12.0 4.9 0.05 0.05 0.43 20 600 700 0.22 0.25 65 2 54 15 0.51 61 95 1.32
LEP3/TLEP parameters -2
LEP2 was not beam-beam limited
LEP data for 94.5 - 101 GeV consistently suggest a beam-beam limit of ~0.115 (R.Assmann, K. C.)

## Slide 13
FNAL site filler
SLAC/LBNL design
circular HFs – arc lattice
IHEP design
T. Sen, E. Gianfelice-Wendt, Y. Alexahin
Q. Qin
K. Oide
Y. Cai
KEK design

## Slide 14
βx*=20cm,
βy*=0.5cm
FNAL site filler
SLAC/LBNL design
circular HFs – final-focus design
IHEP design
T. Sen, E. Gianfelice-Wendt, Y. Alexahin
Q. Qin
Y. Cai
K. Oide
KEK design

## Slide 15
FNAL site filler
±1.6%
circular HFs - momentum acceptance
±2.0%
SLAC/LBNL design
K. Oide
KEK design
after optics
correction
±1.3%
with synchrotron motion &
radiation
(sawtooth)
KEK design
before optics
correction
±1.1%
T. Sen, E. Gianfelice-Wendt, Y. Alexahin
Y. Cai

## Slide 16
circular HFs – top-up injection
double ring with top-up injection supports short lifetime & high luminosity
top-up experience: PEP-II, KEKB, light sources
A. Blondel

## Slide 17: top-up injection
SPS as LEP injector accelerated e± from 3.5 to 20 GeV (later 22 GeV) on a very short cycle:
acceleration time = 265 ms or about 62.26 GeV/s
Ref. K. Cornelis, W. Herr, R. Schmidt, “Multicycling of the CERN SPS: Supercycle Generation & First Experience with this mode of Operation,” Proc. EPAC 1988
assuming injection from the SPS into the top-up accelerator at the same energy of 20 GeV and final energy of 120 GeV: acceleration time = 1.6 seconds
total cycle time = 10 s looks conservative (→ refilling ~1% of the LEP3 beam, for tbeam~16 min)
Ghislain Roy & Paul Collier

## Slide 18: top-up injection: schematic cycle
10 s
energy of accelerator ring
120 GeV
20 GeV
injection into collider
injection into
accelerator
beam current in collider (15 min. beam lifetime)
100%
99%
almost constant current

## Slide 19: top-up injection at PEP-II/BaBar
Before Top-Up Injection
After Top-Up Injection
average ≈ peak
luminosity (H≈1)!
J. Seeman

## Slide 20
Top-up injection will work for a Circular Higgs Factory.
A full energy injector is needed.
A synchrotron injector will work the best, but is more than is needed (60 Hz!).
A rapidly ramped storage ring is likely adequate (4 sec).
The detectors will need to mask out the buckets with damping injected bunches during data taking as had been done for PEP-II/BaBar:
HF 2012 conclusions (John Seeman, SLAC):
top-up injection: feasibility
BaBar trigger masking:
Mask all of ring a few tens of turns.
Mask injected bunch area for 1250
turns or about 0.9 msec.

## Slide 21
for one day (July 3, 2006): H≈0.95
for one month (August 2007): H≈0.63
J. Seeman,
7 Dec. 2012
PEP-II Hübner factor

## Slide 22
Circular Collider & SR Experience
1992 ESRF, France (EU) 6 GeV
ALS, US 1.5-1.9 GeV
1993 TLS, Taiwan 1.5 GeV
1994 ELETTRA, Italy 2.4 GeV
PLS, Korea 2 GeV
MAX II, Sweden 1.5 GeV
1996 APS, US 7 GeV
LNLS, Brazil 1.35 GeV
1997 Spring-8, Japan 8 GeV
1998 BESSY II, Germany 1.9 GeV
2000 ANKA, Germany 2.5 GeV
SLS, Switzerland 2.4 GeV
2004 SPEAR3, US 3 GeV
CLS, Canada 2.9 GeV
2006: SOLEIL, France 2.8 GeV
DIAMOND, UK 3 GeV
ASP, Australia 3 GeV
MAX III, Sweden 700 MeV
Indus-II, India 2.5 GeV
2008 SSRF, China 3.4 GeV
2009 PETRA-III, Germany 6 GeV
2011 ALBA, Spain 3 GeV
3rd generation light sources
…
CESR
BEPC
LEP
Tevatron
LEP2
HERA
DAFNE
PEP-II
KEKB
BEPC-II
LHC
SuperKEKB (soon)
well understood technology &
typically exceeding design performance
within a few years

## Slide 23
Emittances in Circular Colliders &
Modern Light Sources
Y. Funakoshi, KEK
R. Bartolini,
DIAMOND
TLEP (240)
LEP3
Top up injection essential for achieving small vertical emittance
Lenny Rivkin, 2nd LEP3 Day

## Slide 24
circular HFs: synchroton-radiation heat load
LEP3 and TLEP have 3-10 times less SR heat load per meter than PEP-II or SPEAR! (though higher photon energy)
N. Kurita, U. Wienands, SLAC

## Slide 25: TLEP polarization
LHeC equilibrium polarisation vs ring energy, full 3-D spin tracking results (D. Barber, U. Wienands, in LHeC CDR, J. Phys. G: Nucl. Part. Phys. 39 075001)
“… by adopting the levels of alignment that are now standard for synchrotron-radiation sources and by applying harmonic closed-orbit spin matching, there is reason to hope that high polarisation in a flat ring can … be obtained”
80% at the Z pole

## Slide 26
TLEP3 key components
tunnel
SRF system
cryoplants
magnets
injector ring
detectors
tunnel is main cost:
3x LEP tunnel = 2.1 BCHF
9x LHeC tunnel cost estimate = 2.25 BCHF
inofficial/official TLEP tunnel cost ~2.5 BCHF

## Slide 27
TLEP3 key issues
SR handling and radiation shielding
optics effect energy sawtooth
[separate arcs?! (K. Oide)]
beam-beam interaction for large Qs
and significant hourglass effect (K. Ohmi)
IR design with even larger momentum
  acceptance
integration in LHC tunnel (LEP3)
Pretzel scheme for TERA-Z operation?
impedance effects for high-current running
  at Z pole

## Slide 28
A. Fasso
3rd TLEP3 Day
shielding & activation for Ec>1 MeV
LEP design study extended up to 130 GeV

## Slide 29: transverse impedance & TMCI
LEP bunch intensity was limited by TMCI: Nb,thr~5x1011 at 22 GeV
LEP3 with 700 MHz: at 120 GeV we gain a factor 5.5 in the threshold, which almost cancels a factor (0.7/0.35)3 ~ 8 arising from the change
in wake-field strength due to the different RF frequency
LEP3 Qs~0.2, LEP Qs~0.15: further 25% increase in TMCI threshold?
only ½ of LEP transverse kick factor came from SC RF cavities ,
LEP3 beta functions at RF cavities might be smaller than in LEP ,
LEP3 bunch length (2-3 mm) is shorter than at LEP injection (5-9 mm)
M. Lamont, SL-Note-98-026 (OP)
instability threshold, feedback etc for Tera-Z operation w 1 A current? question by K. Yokoya, Feb. 2013

## Slide 30
Circular & Linear HF:
peak luminosity vs energy
K. Yokoya, KEK
LEP3/TLEP would be THE choice for e+e- collision energies up to ~370 GeV
LEP3 , TLEP
x 4 IPs

## Slide 31: vertical rms IP spot sizes in nm
LEP2 | 3500
KEKB | 940
SLC | 500
LEP3 | 320
TLEP-H | 220
ATF2, FFTB | 72 (35), 65
SuperKEKB | 50
SAPPHiRE | 18
ILC | 5 – 8
CLIC | 1 – 2
in regular
font:
achieved
in italics:
design
values
LEP3/TLEP
will learn
from ATF2 &
SuperKEKB
by*:
5 cm→
1 mm

## Slide 32: extrapolation from past experience
 | LEP2→TLEP-H | SLC→ILC 250
peak luminosity | x400 | x2500
energy | x1.15 | x2.5
vertical geom. emittance | x1/5 | x1/400
vert. IP beam size | x1/15 | x1/150
e+ production rate | x1/2 ! | x65
commissioning time | <1 year → ? | >10 years →?
recent comment by eminent German particle physicist:
“TLEP is much riskier and its performance highly uncertain;
while the ILC performance numbers are very conservative” [?]

## Slide 33: a glance at LHC & LHC upgrades
E. Todesco, L. Rossi, P.. McIntyre
HE-LHC: in LHC tunnel (2035-)
ECoM=33 TeV,x1034cm-2s-1
VHE-LHC: new 80 km tunnel
ECoM=84-104 TeV,x1034cm-2s-1
J. Osborne, C. Waaijer, S. Myers
LHC is the 1st Higgs factory!
ECoM=8-14 TeV,1034cm-2s-1
total cross section at 8 TeV: 22 pb
1 M Higgs produced so far – more to come
15 H bosons / min – and more to come
20-T dipole magnet
80 km tunnel
8  14 TeV: ggH x1.5
14  33 TeV:
ggH HH x6
HL-LHC (~2022-2030)
will deliver ~9x more H bosons!
ECoM=14 TeV,5x1034cm-2s-1
with luminosity leveling
F. Cerutti, P. Janot
16 T magnets over 80 km (Ex6)
likely “easier” than 20 T
magnets over 27 km (Ex2.5)!?

## Slide 34
PSB
PS (0.6 km)
SPS (6.9 km)
LHC (26.7 km)
TLEP (80 km,
e+e-, up to
~350 GeV c.m.)
VHE-LHC
(pp, up to
100 TeV c.m.)
same detectors!
also: e± (120 GeV) – p (7 & 50 TeV) collisions
LEP3
(e+e-, 240 GeV c.m.)
possible long-term strategy
≥50 years of e+e-, pp, ep/A physics at highest energies
(E. Meschi)

## Slide 35
parameters
for LHC
HL-LHC,
HE-LHC
and
VHE-LHC
(examples)
O. Dominguez
& F. Zimmermann

## Slide 36
collider parameters | TLHeC |  | VHE-TLHeC | 
species | e± | p | e± | p
beam energy [GeV] | 120 | 7000 | 120 | 50000
bunch spacing [ms] | 3 | 3 | 3 | 3
bunch intensity [1011] | 5 | 3.5 | 5 | 3.5
beam current [mA] | 24.3 | 51.0 | 24.3 | 51.0
rms bunch length [cm] | 0.17 | 4 | 0.17 | 2
rms emittance [nm] | 10,2 | 0.40 | 10,2 | 0.06
bx,y*[cm] | 2,1 | 60,5 | 0.5,0.25 | 60,5
sx,y* [mm] | 15, 4 |  | 6, 2 | 
beam-beam parameter x | 0.05, 0.09 | 0.03,0.01 | 0.07,0.10 | 0.03,0.007
hourglass reduction | 0.63 |  | 0.42 | 
CM energy [TeV] | 1.8 |  | 4.9 | 
luminosity [1034cm-2s-1] | 0.5 |  | 1.6 | 
parameters for TLHeC & VHE-TLHeC (examples)

## Slide 37: arrangement in VHE-LHC tunnel
H. Piekarz, Proc. HE-LHC’10, p. 101
30 mm V gap
50 mm H gap
Bin = 0.5 T
Bextr = 1.5 T
20-T magnet
VHE-LHC injector ring “LER”
(using transmission line magnet)
Lucio Rossi
CLIC workshop
28 Jan. 2013

## Slide 38: VHE-LHC’s LER magnets compatible with TLEP and VLHeC – 100 MW SR
advantages:
cheap, like resistive magnets
central gap could be shortcircuited
magnets separated: provides electrons at 120 GeV and protons at 5 TeV/beam
limited cryopower (HTS) in shadow of SCRF cavities
SC cables developed already for SC links (HiLumi) and power applications
SR taken at 300 K
Lucio Rossi
CLIC workshop
28 Jan. 2013

## Slide 39: Lucio Rossi’s «plan for all»
according to Physics needs, the 80 km tunnel can:
  be alternative to HE-LHC
  or be complementary to HE-LHC
  accomodate at negligible extra-cost TLEP and VLHeC
  modular detector design allows evolution from TLEP-H/TLHeC to VHE-LHC
Lucio Rossi
CLIC workshop
28 Jan. 2013
2017-2020 is critical time!

## Slide 40
If what you have done yesterday
still looks big to you,
you haven’t done much today.
Mikhail S. Gorbachev

## Slide 41: maximum TLEP luminosity
maximum theoretical luminosity is
Max. of 0.1
For LEP3 this is =6cm-1 (0.6/0.1cm-1). For TLEP =0.75/0.1cm-1. Difficult to go beyond this without nanobeam /crab-waist scheme
total power limit (100 MW SR)
Beam-beam limit
at 120 GeV
Mike Koratzinos

## Slide 42: even higher TLEP luminosity?
charge compensation (CC) – counteracting the electric field of the incoming beam by a second beam of opposite charge
4-beam collisions at DCI, Orsay, 1971
- not a spectacular success
new idea (V. Telnov, M. Koratzinos): use charge compensation to suppress beamstrahlung and push luminosity in crab-waist scheme

## Slide 43: artist’s impression of CC-TLEP
Accelerator ring magnets
main ring magnets
Thermal power management
Vacuum management
Clockwise e+ anticlockwise e-
Clockwise e- anticlockwise e+
Vacuum chamber
Mike Koratzinos

## Slide 44
V. Telnov, 3 TLEP3 Day
Valery Telnov’s estimate for CC TLEP

## Slide 45: HF quality indicators
readiness / maturity
cost , electrical power
peak luminosity , #IPs
integrated luminosity
  Hübner (H) factor = integrated lumi/(peak lumi x calendar time for physics)
  HLEP ≈0.2, HLHC ≈0.2, HKEKB≈0.7, HPEP-II≈0.7
  commissioning time
  expandability

## Slide 46: HF Accelerator Quality (My Opinion)
 | Linear C. | Circular C. | LHeC | Muon C. | g-g C.
maturity |  |   |   |  | 
size |  |  |  |  | 
cost |  |  -  |  |  | 
power |  |  |  |  | 
#IPs | 1 | 4 | 1 | 1 | 1
com. time | 10 yr | 2 yr | 2 yr | 10 yr | 5 yr
H factor | 0.2 (SLC) | 0.5 (1/2 PEP-II) | 0.2? | 0.1? | 0.1?
Higgs/IP/yr | 7 k [10 k] | 20-100 k | 5 k | 5 k | 10 k
expanda-bility | 1-3TeV e+e-, gg C. | 100 TeV pp | gg C. | 10 TeV mm | LC later
inspired by S. Henderson, FNAL

## Slide 47
the path forward

## Slide 48: the path forward
set up international collaboration(s) & work structure
  ERC proposal on large-acceptance IR
  design by Rogelio Tomas
  TLEP Design Study Proposal for ECFA
  INFN-LNF could play a key role!
goal: publish TLEP Conceptual Design Study Report by end of 2014!

## Slide 49
ERC Consolidation Grant
Proposal “LEAF” – Draft
PI: Rogelio Tomas
includes international
network for feeding new
ideas, guidance, local
support for experimental
tests, review & collaboration

## Slide 50: draft work topics: TLEP accelerator
parameter optimization with regard to lifetime and luminosity, at different energies, & different tunnels
RF system design, prototyping & integration for collider and accelerator ring
optics design for collider ring including low-beta IRs, off-momentum dynamic aperture, different energies
beamstrahlung: lifetime, steady state beam distribution, dependence on tune etc.
beam-beam interaction with large hourglass effect
emittance tuning studies, errors, tolerances, etc.
optics design and beam dynamics for the accelerator ring, ramping speed etc
impedance budget, CSR, instabilities
cryogenics system design
magnets design: collider ring dipole, accelerator ring dipole, low-beta quadrupole
radiation, shielding, cooling for 100 MW SR power
vacuum system design
engineering study of 80-km tunnel
design of injector complex including e+ source, and polarized e- source
machine detector interface, integration of accelerator ring at detector (s), low-beta quadrupoles, shielding (e.g. against beamstrahlung)?
injection scheme
polarization, Siberian snakes, spin matching, acceleration & storage, polarized sources
(19 September 2012)

## Slide 51
TLEP Design Study
Proposal
to be submitted to
ECFA

## Slide 53: summary
TLEP is a great opportunity for HEP!
  unparalleled “ZH” luminosity in 4 IPs, allowing for highest-precision Higgs studies
  also Tera-Z and Mega-W factory, + t-tbar studies
  future conversion into 100 TeV pp collider with lots of synergies (tunnel, cryo, detectors), & ep option
LEP3 as backup
TLEP3 accelerator R&D to address key issues
  radiation shielding
  IR optics, beam-beam effects, and injector ring
  tunnel, RF system, arc magnets,…
plans for international collaboration & CDSR

## Slide 54: TLEP events & references
A. Blondel, F. Zimmermann, “A High Luminosity e+e- Collider in the LHC Tunnel to study the Higgs Boson,” arXiv:1112.2518v1, 24.12.’11
K. Oide, “SuperTRISTAN - A possibility of ring collider for Higgs factory,”
KEK Seminar, 13 February 2012
1st EuCARD LEP3 workshop, CERN, 18 June 2012
A. Blondel et al, “LEP3: A High Luminosity e+e- Collider to study the Higgs Boson,” arXiv:1208.0504, submitted to ESPG Krakow
P. Azzi et al, “Prospective Studies for LEP3 with the CMS Detector,”
arXiv:1208.1662 (2012), submitted to ESPG Krakow
2nd EuCARD LEP3 workshop, CERN, 23 October 2012
P. Janot, “A circular e+e- collider to study H(125),” PH Seminar, CERN, 30 October 2012
ICFA Higgs Factory Workshop: Linear vs Circular, FNAL, 14-16 Nov. ’12
A. Blondel, F. Zimmermann, “Future possibilities for precise studies of the X(125) Higgs candidate,” CERN Colloquium, 22 Nov. 2012
3rd TLEP3 Day, CERN, 10 January 2013
4th TLEP mini-workshop, CERN, 4-5 April 2013
https://espace.cern.ch/LEP3
https://cern.ch/accnet

## Slide 55
“A circle is a round straight line with a hole in the middle.”
  Mark Twain,
  in "English as She Is Taught",
  Century Magazine, May 1887

## Slide 56
back-up slides

## Slide 57
HTS prototype dipole at FNAL
Test: B max = 0.5 T, Imax = 27 kA, dB/dt max = 10 T/s , T max ~ 25 K
SC magnets require typically 10 x less space than NC magnet of the same field and gap; the magnet weight is very significantly reduced.
transmission-line
HTS/LTS magnets
schematic HTS/LTS LEP3 magnet
H. Piekarz,
1st EuCARD LEP3 Day
acceleration time ~0.1 s,
total cycle ~1 s; fast SC
magnets might support
1 minute lifetime
in collider ring!
Circular HF HiTech option

## Slide 58
circular Higgs factories become
popular around the world
LEP3 2011
SuperTristan 2012
LEP3 on LI, 2012
LEP3 in Texas, 2012
FNAL site filler, 2012
West Coast
design, 2012
Chinese Higgs
Factory, 2012
UNK Higgs
Factory, 2012