## Slide 1: Simulation and Debug The Vertical Slice experience Federico Lasagni Manghi

## Slide 2: Why a simulation?
To provide feedback:
During the development of boards
During the development of firmware
Assembling the boards
To determine the characteristics of the system:
  Efficiency
  Purity

## Slide 3: Structure (now) for the VS
C++ program, ROOT analysis tools.
Evolved together with the Vertical Slice:
Data reading class
FTK_IM mezzanine simulation: clustering
EDRO simulation
AM simulation
Compare results at all steps
AM
EDRO

## Slide 4: Validation of VS online simulation
Debugged “VS online simulation” versus FTKSim
Difference traced to different format
Imported “bystream decoder” for SCT into FTK online simulation
Differences found and corrected in VS online simulation
  Inversion of strip number for SCT side = 1
  Renumbering of link number

## Slide 5: What we obtain
The HW and the simulation are compared for:
Hits after mezzanine data clusterization
Roads from the AMBoard
We can read Simulated values (event per event) of:
Hits after EDRO data conversion
Roads from AM Simulation
  These are useful if we have saved the spy-buffers with the
  corresponding info in the hardware

## Slide 6: When has it been used?
To test the EDRO-AMB system
  Firmware
  Communication
To test the communication with the FTK_IM
To test the FTK_IM firmware
To test the whole VS system
To better understand the necessary setup

## Slide 7
Tests
Offline Tests of components
Offline tests of full VS
Online Tests without data
Tests with real data:
  Period January – February 2013
  P-Pb collisions at 8 TeV and p-p collisions at 2.76 TeV
  focusing on run 219171 p-p collisions at 2.76 TeV
  Level 1 Rate ≈ 30 kHz

## Slide 8: The EDRO-AMB System
We have tested the system from the arrival of the hits in the EDRO board to the road firing.
DEFINITIONS
Efficiency = Correct fired roads / expected roads
Purity = Correct fired roads / total fired roads
Expected and correct means “predicted by simulation”

## Slide 9: Analyzing data from this part Sim vs real VS
0 Errors / 276 roads
Efficiency > 88%, at 95% CL

## Slide 10: Issues Discovered in FTK_IM
Wrong interpretation of the hit values in different layers
Mezzanine Firmware production of wrong Module ID
Hit duplicated in mezzanine
We should have solved these issues, however we had no time to do it before shutdown

## Slide 11: What we observed: many roads are lost by the VS
Patterns fired in simulation
Patterns fired by VS

## Slide 12
Efficiency and Purity
Both should go to 1 when correcting for known errors

## Slide 13: Dataflow problems also…
Rare data-flow problems for roads
  Wrong end-words
  Missing end-words
  Very rare missing FTK fragments
Data-flow stops (unclear origin)
  At warm start
  After long periods of data-taking

## Slide 14: Data-flow error rate (much lower)
Errors/event in the sample

## Slide 15: Conclusions
Validated VS Simulation using FTKSim
Used it to test the VS and its components from development to integration in ATLAS
Found several issues and the sources of some
Provided efficiency and purity of the components and the whole VS system
TODO: fix data-manipulation issues, investigate data-flow issues