## Slide 1: IAPP - FTK workshop – Pisa 11-15 march, 2013
Marco Piendibene – University of Pisa & INFN
AMboard HW & FW

## Slide 2: Outline
Associative Memory Board for FTK (AMBFTK)
Hardware description AMBFTK
Firmware implementation of AMBFTK
Evolution of the board: serial link processor (AMBSLP)

## Slide 3: AMBftk
INPUT FPGAs
OUTPUT FPGAs
CONTROL FPGA
ERNI high speed connector (data I/O)
CLOCK DISTRIBUTION NETWORK
100 MHz, lvds, ttl
Direct connection to AUX card
(no backplane)
EUROCARD 9U
(400mm x 360mm)
Custom shape for placing the dc-dc converters

## Slide 4
VME connectors
(power, configuration, debug)
VME slave
VME data fan out
LAMB connectors
LAMB connectors
JTAG connectors
AMBftk
Bottom side: cpld for parallel buses (refresh)

## Slide 5
48V, 3.3V
(from vme connector)
4 dc-dc converter 48 to 1,2V (25 A each)
Lamb power connectors
AMBftk

## Slide 6
8
4
White lines: parallel distribution
Red lines: serial distribution, 2Ghz
12
12 input serial links @2GHz
4 Layers (SCT) on 4 serial links
4 Layers (PIXEL) on 8 serial links
=> 12 input serial links
AMBftk

## Slide 7
blu lines: serial connection, 2GHz
16
16 output serial links @2GHz
AMBftk
4 serial link per LAMB, total 16 output links

## Slide 8
Power distribution : each Lambs needs a lot of power: 25A @ 1.2V
Input FPGAs: Xilinx Spartan6 with Low Power Gigabit Transceiver (GTP) xc6slx45T / xc6slx75T
High speed on PCB => signal integrity issue
Control FPGA: Xilinx Spartan6 (xc6slx16)
VME slave FPGA: Xilinx Spartan6 (xc6slx16)
VME data fan out: XILINX CPLD
GTP: Ultra-fast data transmission between chips, over backplanes, or over longer distances
Output FPGAs: Xilinx Spartan6 with Low Power Gigabit Transceiver (GTP) xc6slx75T
FPGA on the board: XILINX

## Slide 9
Simple logic
GTP implementation to receive data from AUX card
GTP implementation to send data (for half of the buses) to LAMBS
Temporary buffers to store data (FIFO)
Diagnostic/debug tools (spybuffers)
GTP
GTP
fifo
spy
From AUX card
To Lambs
AMBFTK: firmware (Input FPGA)
xc6slx45T / xc6slx75T
Parallel distribution
Serial distribution

## Slide 10
Simple logic
GTP implementation to receive data from Lambs
GTP implementation to send data to AUX card
Temporary buffers to store data (FIFO)
Diagnostic/debug tools (spybuffers)
GTP
GTP
fifo
spy
to AUX card (all serial links)
from Lambs
(all serial)
AMBFTK: firmware (Output FPGA)
xc6slx75T
4 serial links
(LAMB0)
4 serial links
(LAMB1)
8 serial links

## Slide 11
Very simple State Machine (FSM)
AMBFTK: firmware (CONTROL FPGA)
RESET
Wait ee
Send_init_ev
Receive and distribute hits.
Collect roads and send them out to AUX card.
Wait end event from input and output fpgas (the previous event has been processed)
Send init event to fpga and Lambs
Generate INIT_event when: (a) EE is received by SCT, PIX and ROAD chips (4 signals)
Receive error (code & stream info) and generate an action (freeze or stopless-removal) comparing with Severity error
For Freeze: check that the event involved in the error is totally processed and than generate the freeze to all AMBFTK FPGAs. Send Freeze upstream.
Generate Operation Code to the LAMBs

## Slide 12
The VME fpga implements the slave VME functions
Decode the incoming addresses
Send read/write instruction to correct fpga
  Write configuration registers
  Read status register
  Configuration of the pattern banks (Amchips)
AMBFTK: firmware (vme FPGA and fanout cpld)
VM
E
B
A
C
K
P
L
A
N
E
VME INTERFACE
FPGA
SCT
PIXEL
CONTROL
VMEDATA
REPEATER
FPGA
ROAD EVEN
ROAD ODD
AUX
CARD
VMEDATA
VMEDATA
VMEDATAINP
VMEDATAAUX
VMEDATAOUT
LAMBS
CPLD
xc6slx16

## Slide 13
AMBFTK: actual PCB
9U eurocard (400mm x 360mm)
14 layers (6 routing, 8 power)
Minimum track widh/clearance: 3 mils (75 um)
Fineline BGA: 0,8 mm pitch
Smallest package: 0402
400mm

## Slide 14
- Bus distrubuted all serially
Power:
1,0V AMchip & FPGA cores
1.2V AMchip IP core
2.5V I/O
New Lambs dimension
AMSYSTEM:AMBSLP, the new amboard for amchip05

## Slide 15
Power:
From 48V? How many pin?
40 A per Lamb @1.0 V – dc-dc converter
1.2 V for AMchip IP.
  Where? From 2.5V? On the Lamb?
2.5 V
connector LAMB/AMboard
AMSYSTEM:AMBSLP
Samtec connector