## Slide 1: LPNHE (IN2P3 CNRS)

## Slide 2: Laboratoire de Physique Nucléaire et de Hautes Energies
Mixed research unit (UMR) of Institut National de Physique Nucléaire et de Physique de Particules (IN2P3 CNRS) and Pierre et Marie Curie university (UPMC) and Paris Diderot university.
~ 100 researchers + 50 technical staff

## Slide 5: People with implications in Si sensors and FTK
in IAPP
in IAPP
Giovanni Calderini – Director of research
  Former BaBar tracker project leader
  Planar pixels for ATLAS upgrade
Giovanni Marchiori – Researcher
  Experience in Silicon detectors
Marco Bomben – Post-doc
  Experience in Silicon detectors
  ATLAS pixel test beam coordinator
Jacques Chauveau – Professor UPMC
  Experience in Silicon detectors
Francesco Crescioli – Research Engineer
  FTK experience
Jean-Francois Genat – Research Engineer
  Experience in chip design
Olivier Le Dortz – Research Engineer
  FPGA and perif. electronics experience

## Slide 6
Edgeless planar sensors (FBK-LPNHE)
  Aim to phase-II ID (mid-outer layers)
  Reduced dead area at periphery (~100 μm)
  Sensors designed & simulated via TCAD
  Tests started in our clean room
  Next: CCE at periphery w/ laser, sources, beams
Contribution to ATLAS IBL
  Simulations (Silvaco)
  pixel-over-guard rings design
  several n-in-n and n-in-p productions
Sensors
Cut line

## Slide 7
FTK simulation &
data preparation software
FTKSim
Pattern generator
from data & constants
FTKSim in ATHENA
JobOptions for trigger
studies
AMchip
dev
Hardware
Software
FTK Vertical Slice
FTK VS integration with ATLAS online software
FTK experience

## Slide 8: Associative Memory ~ AMchip
The associative memory is the core component of the pattern recognition stage of FTK
Performs the higly demanding task of coarse tracks finding in the full event.
The associative memory hardware is based on a custom made ASIC: AMchip
ASIC
design
AMchip04
AMchip-based associative memory device first used
in CDF (Amchip03).
AMchip03
6-layers patterns @ 18-bit
~5kpatt/chip
40 MHz
FTK needs more advanced technology:
AMchip04
8-layers @ 15-bit (configurable3-7 bit w/ ternary logic)
~8kpatt/chip
100 MHz
AMchip05
High speed serial I/O
~32kpatt/chip
Stream merge function
Design phase
Used by
FTK VS

## Slide 9: LPNHE activities in FTK/IAPP
Development of a low-noise alimentation framework for radiation damaged ATLAS sensors
(collaboration with CAEN)
Test-stand development for FTK board validation
and commissioning
    AMchip tests
    Boards tests
    Integration HW/SW