## Slide 1
R.Rescigno
Simulation toolkit with CMOS detector in the framework of hadrontherapy
INPC13

## Slide 2
Hadrontherapy
  Use of charged particles to treat the cancer
  Particles properties:
    Finite Range
    Bragg peak –BP- curve (energy loss)
    BP position depends on electron density material
Steep dose gradient
Mispositioning of this gradient can lead to:
  Under-dosage in target volume
  Over-dosage of an organ at risk
Tissue thickness(mm)

## Slide 3
On-line range monitoring
  QAPIVI: Quality Assurance by Proton Vertex Imaging
  Method: Using protons from 12C fragmentation
Correlation between two physics processes
  Ionization
  Nuclear interactions
Deposited Energy
12C @ 370 MeV/u
BP @ 210 mm
Target thickness(mm)
Bragg Peak - BP
Longitudinal position of proton production point - Vertex
detector
target
12C
target
12C
proton
target
target
In given condition, it was demonstrated that , in theory (without detector information), millimetric precision on Bragg peak position could be achieved*
* P. Henriquet 2012

## Slide 4
The simulation toolkit
  Simulation toolkit based on GEANT4
Epitaxial layer
Bulk
Particle
4
  Detector
  CMOS type
  MIMOSA26
 50 μm
Pixel Array: 1152 × 576 pixels
Dimension: 11× 21 mm
Pitch: 18.4 m
  Vertex reconstruction steps
Clustering: find out the hits generated by a particle.
Tracking: looks for aligned clusters to built a track.
Vertexing: search for most probable tracks intersection point
y
x
z
  Detector:
  8 CMOS planes
  Target:
  PMMA - C5 H8 O2
  Beam Monitoring:
  2 CMOS plane
250 mm
100 mm
100 mm
Experimental setup
Binary output

## Slide 5
Results
  Detector response simulation
Longitudinal vertex position
Residuals: True – Reconstructed
Thin target
8 mm
  Algorithm validation
Performed with a thin (8 mm) target
Efficiency tracking & vertexing ~ 99%
Phenomenological model based on experimental data
Proton 80 MeV
Mean: 4.4
RMS: 1.7
Carbon: 80 MeV/u
Mean: 21.1
RMS: 4.7
Experimental data
Simulation
Proton 80 MeV
Mean: 4.5
RMS: 2
Carbon: 80 MeV/u
Mean: 22.5
RMS: 2.6

## Slide 6
Results thick target
Longitudinal vertex position
Comparison: True vs. Rec
Longitudinal vertex position
Residuals: True - Rec
Thick target
250 mm
Conclusion & outlook
  Detector response and reconstruction chain integrated in simulation
  Vertex resolution limited by diffusion process and not by detector/algorithms
  Algorithm taking into account diffusion process is under study
Thank you
target