## Slide 1: Nuclear fragmentation measurements for hadrontherapy
Vincenzo Patera
Universita’ di Roma “Sapienza” & INFN-LNF

## Slide 2
Hadrontherapy Motivation
Light ions advantages in radiation treatments of tumor wrt IMRT:
Better Spatial selectivity in dose deposition: (p,12C)
Reduced lateral and longitudinal diffusion (12C)
High Biological effectiveness (12C)
Treatment of highly radiation resistent tumours, sparing surrounding OAR
INFN has a long standing activity in this field, not only in beam facility realization (CNAO) but also in Treatment Planning System development (TPS INFN-IBA joint project)

## Slide 3: FRAGMENTATION OF 12C in bio tissue
Mitigation and attenuation of the primary beam
Different biological effectiveness of the fragments wrt 12C
Production of fragments with higher range vs primary ions
Production of fragment with different direction vs primary ions
Dose release in healthy tissues with possible long term side effects, in particular in treatment of young patients must be carefully taken into account in the Treatment Planning System
Exp. Data (points) from Haettner et al, Rad. Prot. Dos. 2006
Simulation: A. Mairani PhD Thesis, 2007, Nuovo Cimento C, 31, 2008
12C (400 MeV/u) on water
Bragg-Peak
Dose over the Bragg Peak :
p ~ 1-2 %
C ~ 15 %
Ne ~ 30 %
Courtesy of Andrea Mairani

## Slide 4: Fragmentation and dose monitoring
MC unreliable for large emission angle, probing the very tail of angular distribution of frag’s
Fragment emission also from region near BP? And with enough energy to exit from the patient body and be detected?
Low energy protons are surely emitted by the Carbon beam.
The detection efficiency is almost one
Can be easily back-tracked to the emission point  can be correlated to the beam profile & BP
Envision WP2 Report
proton
beam
K Gwosch et al Phys. Med. Biol. 58 3755
C Agodi et al Phys. Med. Biol. 57 5667

## Slide 5: Data - MC comparison: 12C ions
Integral quantities (fragment yields, charge changing cross sections) are generally within 10-30%
Build-up of charged fragments for 12C beam @400MeV/n in water
Bolhen et al, Phys. Med. Biol. 55 (2010) 5833–5847

## Slide 6: Data - MC comparison: 12C ions
NB: the accuracy on delivered dose MUST be below 3%
Some MC benchmarks:
Sommerer et al. 2006, PMB Garzelli et al. 2006, ArXiv Pshenichnov et al. 2005, 2009 Mairani et al. 2010, PMB Böhlen et al. 2010, PMB Hansen et al. 2012, PMB
Differential/double- differential quantities (vs angle and/or energy)  larger discrepancies found!
Bolhen et al, Phys. Med. Biol. 55 (2010) 5833–5847

## Slide 7: What we yet miss to know about 12C fragmentation?
Lot of data exists at 00 or on thick target. We need to know, on thin target:
Production yelds of Z=0,1,2,3,4,5 fragments
d2/ddE wrt angle and energy, with large angular acceptance
For any 12C energy of interest (100-300 MeV/nucl)
Measurements on thin target of all materials crossed by C beam
12C , E
12C , E'
,A,Z
',A',Z'
X,Ex,x,x
Y,Ey,y,y
Not possible a complete DB of measurements
We need to train a nuclear interaction model with the measurements!!

## Slide 8: Recent thin target, Double Diff Cross Section C-C measurements
LNS 62AMev C beam
See M. De Napoli talk in this session (2009)
GANIL 95AMev C beam - E600 collaboration (2011)
GSI 400Mev C beam
FIRST experiment
This talk (2011)
Proposal:
GSI 200AMeV C beam
FIRST experiment 2014
The community is exploring the interesting region for therapeutical application.
?

## Slide 9: Measurement @95AMeV : 12C beam
Array of 5 SI + CsI telescopes
Courtesy of M. Labalme

## Slide 10: Measurement @95AMeV : 12C beam
Obtained results for Single and Double Diff. X Section.
  one interesting conclusion: Composite targets can be deduced from the cross sections of elemental targets (-> organic tissues)
Courtesy of M. Labalme

## Slide 11: The FIRST experiment at GSI
FIRST stands for: Fragmentation of Ions Relevants for Space and Therapy  S371 is the GSI label
FIRST has the aim to measure the C-C fragmentation double differential cross section at GSI 12C beam in the 200-400 AMeV range
INFN: Cagliari,LNF,LNS,Milano,Roma3,Torino: C.Agodi, G.Battistoni, A.Brunetti M.Carpinelli, G.A.P.Cirrone, G.Cuttone , M.De Napoli, B.Golosio, Y.Hannan, E.Iarocci, F.Iazzi, R.Introzzi, A.Mairani, F.Marchetto, V.Monaco, M.C.Morone,P.Oliva, A.Paoloni, V.Patera, L.Piersanti, G.Raciti, N.Randazzo, F.Romano, R.Sacchi, P.Sala, A.Sarti, A.Sciubba, C.Sfienti, V.Sipala, E.Spiriti, S.Tropea, H.Younis
DSM/IRFU/SPhN CEA Saclay, IN2P3 Caen, Strasbourg, Lyon: A. Boudard, J.E. Ducret, C. Fink, F. Haas, D.Juliani, J.Krimmer, M. Labalme, C.Ray, S.Leray, M.Rousseau, M.D.Salsac, L.Stuttge
GSI: T.Aumann, K.Boretzky, M.Durante, M.Heil, G.Ickert, A.Kelic, N.Kurz, Y.Leifels, A. LeFevre, R.Pleskac, M.V.Ricciardi, D.Rossi, D.Schardt, C.Scheidenberger, C.Schuy, H.Simon, M.Winkler
University Sevilla & CNA: J.M. Quesada, A.Bocci, J.P.Fernandez-Garcia, M. I. Gallardo, M.A. Cortes-Giraldo, M.A.G. Alvarez
ESA: P.Nieminem, G.Santin
CERN: T.T. Böhlen
R.Pleskac et al. NIM A 678 (2012) 130–138

## Slide 12: What do we expect from MC (12C case) ?
The Z>2 produced fragments approximately have the same velocity of the 12C beam and are collimated in the forward direction
The protons are the most abundant fragments with a wide b spectrum 0<<0.6 and with a wide angular distribution with long tail
The Z=2 fragment are all emitted within 200 of angular aperture
The DE/DX released by the fragment spans from ~2 to ~100 m.i.p.
400 MeV/nucl 12C on 12C
Kinetic energy (MeV/nucl)
Emission angle (Deg)
400 MeV/nucl 12C on 12C
FLUKA
FLUKA
Do not trust MC too much!

## Slide 13: The ALADIN setup @GSI
The choice of GSI has 2 main motivations:
“Terapeutical” beam of 12C @ 200-400 MeV/u available
Existing setup designed for higher E and Z fragments: Dipole magnet, Large Volume TPC, TOF Wall, low angle Neutron detector.
New detectors added to optimize the Interaction Region:
silicon Vertex Tracker, Start Counter scintillator counter, Beam Monitor drift chamber, scintillator Proton Tagger/Calorimeter
TPC MUSIC IV
TOF
WALL
Neutron detector
Interaction
region
ALADIN
MAGNET
Beam
Beam

## Slide 14: Who measures what...?
Target
Magnet
TPC MUSIC IV
TOF WALL
Vertex
Bmon
Start
Vertex Frags emissiondirection  
Start  start TOF and trigger
TOF WALL  frags position & TOF, trigger
Beam mon Beam direction & impact point
Tagger  Large  frags: position, TOF, dE/dX
TPC MUSIC  , dE/dx after bending
LAND2  low angle neutron
Land2
Setup redundancy  allows calibration and systematic checks of the reconstructed fragment features: Z, A, , E.
Interaction Region
P Tagger
Beam Veto
Beam Veto  Veto of the non interactiong beam

## Slide 15: The FIRST simulation
We coded a detailed simulation based on FLUKA 2011 of our setup. During the design phase MC has been used to optimize Space and time resolution, Particle ID, Trigger design, Background and out of target interactions evaluation
Before data taking reconstruction software has been developed using the MC “data”, produced in the same format of the ROOT based actual data
After the data taking the embedding of the actual detector performances in to the simulation give us the direct comparison with the data for acceptance and efficiency evaluation

## Slide 16: August 2011 Data taking
Data taking with 12C 400 AMeV beam.
7 x106 calibration events (no magnetic field or no target)
28 x106 production with 8 mm graphite target.
3 x106 production events with 0.5 mm gold target.
!! TPC MUSIC IV not in operation. !!
Detector calibration done & finalizing analysis.
Period | Run range | 1 SC | 2 SC & .not.VETO | 4 SC & KENTROS | 6 SC & TOFOR | 7 VETO | 9 LAND-Cosmics | 10 KENTROS-Cosmics | TOT EVENTS
6 | 188-248 | 6835378 | 4949973 | 406379 | 6394124 | 1891499 | 2327865 | NO | 9169110
7 | 249-386 | 11431948 | NO | NO | NO | NO | 1468429 | NO | 12900349
8 | 387-471 | 9043428 | NO | NO | NO | 56924 | 682593 | 301229 | 9963032
10 | 474-525 | 4532646 | NO | NO | NO | 58842 | 710797 | 157656 | 5384078
TOT |  | 31843400 | 4949973 | 406379 | 6394124 | 2007265 | 5189684 | 458885 | 37416569

## Slide 18: Start Counter
Trigger & TOF measurement. 150 micron thick fast scintillator, with radial fibers read-out. HAMAMTSU H10721-210 40% q.e. 250ps/"(p.e.)
TARGET
BEAM
SC
BM
Ptag
VD
scint
ε>99% for ALL the RUNS
Very Stable performance vs run number!
Max variation ~ 5 ps
Efficiency
Time resolution : st (ns)

## Slide 19: Beam Monitor
Drift chamber: measures the direction and the impact point of the beam on the target
3 rectangular cell/plane (8x5 mm2)
6 planes for each U-V views
Ar-CO2 80/20 gas mixture @ 2.2 kV©√
TARGET
BEAM
SC
BM
Ptag
VD
Correct matching of the correct carbon track among possible pile-up beam track in the “slow” vertex detector
Input position and direction of the 12C projectile (beam spot ~ 6mm FWHM)

## Slide 20: The vertex detector
Tracks all the charged fragments downstream the target (<40deg).
4 planes of 2x2 cm2 active area, each made of two MIMOSA 26 silicon pixel detectors (MAPS), 3mm spaced, 18.4 mm pitch
TARGET
BEAM
SC
BM
Ptag
VD

## Slide 21: Vertex Detector
TARGET
BEAM
SC
BM
Ptag
VD
Tracking resolution ~ 10 µm (x,y) and 60 µm (z) is fundamental to correctly extrapolate the fragment track along ~ 6m to the TOFWALL
Tracking efficiency for fragments ~ 99%
The vertex provides also information on the fragment charge looking at the number of fired pixels
x Residuals (mm)
s ~ 10 mm
s ~ 60 mm
z Residuals (mm)
Fragment charge

## Slide 22: Large angle proton Tagger
TARGET
BEAM
SC
BM
Ptag
VD
Detects large angle (100-600) slow protons (He). Measures TOF (expected st=250ps), DE (expected sE/E = 10%
EJ-200 fast scintillator ( decay time 2.1 ns, 10000 photons/MeV) read by AvanSiD (IRST/FBK) 4x4 mm2 active area SiPM
= 300 ps
No vertex info used
TDC time (ns)
BARRELl
Big Endcapl
Small Endcapl
Precise impact position given by vertex detector for q<600. At larger q (barrel) coarse position given by ring of scintillating fiber that run along f

## Slide 23: Proton tagger: first P/He id
TARGET
BEAM
SC
BM
Ptag
VD
ADC counts
Helium
Proton
ADC counts
Time (ns)
Helium
Proton
p/He PID on Small Endcap: no impact position used yet
Matching hits with vertex tracks improve both TOF & dE/dx measurements  particle Energy.
Vertex
Beam
monitor
An energy calibration of the tagger is scheduled at 80 MeV proton beam of INFN LNS in Catania. Tagger is travelling now…

## Slide 24: Fragments in TOF WALL
Gives arrival time, dE/dx and impinging position of the fragments.
Two walls made of 96 2x1x110 cm3 scintillators read by two PMTs, grouped in 8 slats unit.
With no TPC working only the impact position on the TOFWALL gives the bending of the fragments
Magnet
TPC
TOF WALL
Land2
IR
Q1,t1
Q2,t2
Calibration run at high statistic with no B field to align with vertex tracking.
Calibration run with B field sweep with no target at high statistic to calibrate the vertical position

## Slide 25: TofWALL resolutions
Comparison between the front/rear slats allows for direct evaluation of the energy and time resolution
The resolution on up-down time difference gives the resolution on the vertical inpinging position Y of the fragment
TW Energy (MeV)
TW Energy (MeV)
Y resolution (cm)
sE(Efront-Erear)/Emean
Efront-Erear (MeV)
Yfront-Yrear (cm)
-100 -50 0 50 100
-30 -20 -10 0 10 20 30

## Slide 26: Frags in TOF WALL: data vs MC
The exp data are in fair agreement with MC -> different Z efficiency
TOF-Ttrig (ns)
TOF (ns)
Sqrt(DETW/cosq)/DEBB*Z2)
12C 400MeV/u on C
DATA
12C 400MeV/u on C
MC (FLUKA)
C
B
Be
Li
He
p
C
B
Be
Li
He
p
Sqrt(DETW/cosq)/DEBB*Z2)
Fragment
definition?

## Slide 27: The global reconstruction
The global reconstruction runs in a “transparent” way on data and MC: same algorithms on same data structure
Matches the information of the different region/detector of the setup
Systematic study/comparison of the difference between data/MC is underway: momentum scale, material effect
Care is needed for the difficult estrapolation from IR to the far away detector after the bending magnet
Fragmented events
Data
PRELIMIARY

## Slide 28: Z_ID performances
  2D algorithm based on ToF vs detected dE/dx in the ToFWall to identify Z regions
  Vertex Z ID capabilities not yet exploited

## Slide 29: Preliminary frag. yelds at small angles
First look at small angle -> Correspond to the region that induce the dose beyond the distal part of the treatment region.
Reconstructed yelds are heavily distorted by the efficiencies ( tracking/selection/etc..) and by acceptance… to be applied
The data distribution seems to be wider in angle than MC
MC
Data PRELIMINARY
FLUKA MC

## Slide 30: efficiencies., acceptances and all that
Efficiencies are computed using MC and checked on the data
Very CPU intensive process for double differential X section
The selection efficiency accounts for all the PID/selection cuts applied on the already reconstructed tracks

## Slide 31: A “side product”: Emulsion Chambers
2 cloud emulsion chambers by OPERA experiment have been exposed to fragments ( 2 hours) by G. De Lellis and coworkers from Napoli University .
Detect fragments at large angle, mainly He and protons, 300<q<750.
Comparison on going with the proton tagger distributions.
Density grain is proportional to energy loss . High spatial resolution (~m). High angular resolution (~mrad). Multiparticle separation
Only low occupancy possible low statistic. Possible calibration with the proton tagger energy and Z distributions
Target + vertex
emulsion chambers

## Slide 32: Outlook
There is an interest in light ions use in hadrontherapy different form 12C
The FIRST detector can measure the fragmentation cross sections d2/ddE by ions like Helium, Litium or Oxigen
FINUDA Drift Chamber in the setup instead of TPC after the bending magnet
7Li on 12C @250MeV/nucl
The experimental setup is also designed to be able to measure fragmentation cross section also with heavier ions like Fe @ 1Gev/nucl  would be interesting for radioprotection in space. ESA and NASA are also interested in this measures.
The collaboration back up all these options  future largely depends on the GSI interest/possibility to pursue these measurements
FLUKA MC

## Slide 33: Summary & Conclusions
An international collaboration (France, Germany, Italy, Spain) has been created to measure at GSI the d2/ddE fragmentation cross section of interest for hadrontherapy and space radioprotection
The detector is an evolution of a pre-existing setup, optimized for the detection of fragments with large angular acceptance and with an accuracy at the few % level
Fragmentation data with 12C already taken in August 2011. Finalizing analysis, first look at small angle results.
In next future the setup could be a facility to measure the fragmentation of light ions (He, Li, O projectiles) and/or of projectiles (Fe) of interest for space radioprotection if GSI will give us a window of opportunity

## Slide 34
Spare slides

## Slide 35: Summer 2011 dataset: activities on-going
Evaluation on data of detector efficiencies and acceptances.
Alignment of detailed simulation with the detector performance
Refinement of the reconstruction software: geometry survey, global reconstruction development and debugging
Calibration of the Proton Tagger on the 80 MeV proton beam at LNS (Catania)
New tracking system testing with cosmics ( drift chambers from FINUDA, an HyperNuclei experiment at Dafne, the Frascati e+e- collider)
Software
Hardware

## Slide 36: Mixed Radiation Field in 12C Ion Therapy
FLUKA benchmark against thick target data
Courtesy of Andrea Mairani
12C on water
@400 MeV/u
Angular distribution
H He Li Be B C
@ 15.9 cm
2°
Energy distribution
@ 31.2 cm
Exp. Data (points) from Haettner et al, Rad. Prot. Dos. 2006
Simulation: A. Mairani PhD Thesis, 2007, PMB to be published
The secondary fragments broad the lateral dose proﬁle and go beyond the tumor region.
Notes: 36

## Slide 37: What we already know: thick target measurement
Projectile Energy[MeV/N] Target
4He 100, 180 C, Al, Cu, Pb
12C 100, 180,400 C, Al, Cu, Pb
20Ne 100, 180,400 C, Al, Cu, Pb
28Si 800 C, Al, Cu, Pb HIMAC by Kurosawa et al.
40Ar 400 C, Al, Cu, Pb
56Fe 400 C, Al, Cu, Pb
126Xe 400 C, Al, Cu, Pb
20Ne 337 C, A, Cu and U BEVALAC by Schimmerling et al.
93Nb 272 Al, Nb BEVALAC by Heilbronn et al.
93Nb 435 Nb
4He 155 Al NSRL by Heilbronn et al.
12C 155 Nb
4He 160 Pb SREL by Cecil
4He 180 C, H2O, steel, Pb
12C 200 H2O GSI by Günzert-Marx et al.
12C 400 H2O GSI by Haettner et al.
Courtesy of M. Durante
Tentative & incomplete list
A lot of integral measurements measurements are already around.. But very few for the correct triplet of projectile,target and energy
Notes: 37
Thank you, Mr. Chairman. It’s my great pleasure to give a talk to you. I’ll be speaking about some of the overview of the fragmentation of heavy charged particles in relation to radiotherapy.

## Slide 38: What we already know: thin target measurement
Projectile Energy[MeV/N] Target
4He 135 C, Poly, Al, Cu, Pb
12C 135 C, Poly, Al, Cu, Pb Sato et al.
20Ne 135 C, Poly, Al, Cu, Pb
40Ar 95 C, Poly, Al, Cu, Pb
12C 290, 400 C, Cu, Pb
20Ne 400, 600 C, Cu, Pb Iwata et al.
40Ar 400, 560 C, Cu, Pb
4He 230 Li, C, CH2, Al, Cu, Pb
14N 400 Li, C, CH2, Al, Cu, Pb
28Si 60 Li, C, CH2, Al, Cu, Pb Heilbronn et al.
56Fe 500 Li, C, CH2, Al, Cu, Pb
12C 400 C, Poly Toshito et al.
only with
detectors
at ~ 0°
Courtesy of M. Durante
Tentative & incomplete list
A lot of measurements on thin target are already around.. but not wrt production angle and energy
Emulsion Chamber: angle ok
E ~OK, low stat, no corr