## Slide 1
99Mo production via 100Mo(n,2n)99Mo using accelerator neutrons
Yasuki Nagai
Japan Atomic Energy Agency
INPC2013 Firenze
99mTc
99mTc-labeled radiopharmaceuticals
medical diagnostics
>25 million/year
Constant supply of 99Mo
key issue to ensure
the routine application
of 99mTc.
Shortage of 99Mo
99Mo: fission product of highly enriched 235U (HEU) at five research reactors
 45 – 54 years since their first operation: unexpected accidents

## Slide 2
Alternative production method
Points to be considered:
1) Production yield: meet a significant part of the domestic demand of 99Mo
2) Safety & efficacy of 99mTc radiopharmaceutical preparation: ensured
 Radionuclide purity of 99mTc: {United States Pharmacopeia (USP)}
 99Mo & concentration of other - & -emitters in 99mTc < 0.015 & < 0.01%
 labeling efficiency of 99mTc radiopharmaceutical complex > 90%
3) Without HEU (public concern due to the proliferation of nuclear weapons)
4) Cost of produced 99Mo: (facility & operation cost)
Reactors:  235U(n,f)99Mo using low enriched 235U  Mo(n,)99Mo
2. Accelerators:
 100Mo(p,2n)99mTc direct 99mTc production Canada
 100Mo(,n)99Mo, 238U(,f)99Mo USA, Canada
 98Mo(n,)99Mo parent 99Mo production
 100Mo(n,2n)99Mo (our proposal)

## Slide 3
Y.Nagai, Y.Hatsukawa: J.Phys.Soc.Japan (2009)
Production yield of 99Mo by 100Mo(n,2n)99Mo
 (b)
100Mo(n,x) reaction X-section
Characteristic points:
(n,2n): large at En  14 MeV, 10-times larger than that of 98Mo(n,)99Mo.
(n,X): radioactive waste production are quite small.
100Mo sample of over 200 g: used. (reused)
intense (n): obtained using an accelerator SPIRAL-2 project, Avilov et al. NIM (2010)
Neutron energy (MeV)
0 10 20 30 40
14MeV
Neutron yield
Neutrons from 40 MeV d + C
Lhersonneau et al. NIM (2009)

## Slide 4
 40 MeV 5 mA d-beam
Minato & Nagai: J. Phys. Soc. Japan, (2010)
99Mo requirement in Japan: 84TBq/week (domestic production)
40 MeV 5 mA d ＋C  20% of the demand in Japan (100Mo : d=2 cm)
99Mo production yield using neutrons from C(d,n)
Latest neutron data: Lhersonneau et al. NIM (2009)
Evaluated cross section in the Japanese Evaluated Nuclear Data Library (JENDL-4.0)
100Mo 2days irradiation
d = 1 cm 2 cm 4 cm
250g 100Mo 2days irradiation

## Slide 5
Safety & efficacy of 99mTc radiopharmaceutical preparation
235U Fission Accelerator
Specific activity of 99Mo 370 TBq/(g 99Mo) 37 GBq/(g Mo)
Separation of 99mTc: Alumina cow (Al2O3) ?
Milking of 99mTc

## Slide 6
310C
795 C
Tc2O7
MoO3
0 200 400 600 800 1000 (C)
points: in 99mTc
99Mo (other RIs) < 0.015 (0.01) %
99mTc produced in 100Mo O3 volatilizes
at a temperature lower than that of
the sublimation of MoO3.
No chemical processing
Separation process : within one hour
Mo 凝縮域
Thermochromatographic Separation of 99mTc from 99Mo
Electric Furnace
Tc condense
照射Mo+Tc
(白金ボート)
(Platinum boat)
Vapor pressure (atom)
Perrier & Segre J.Chem.Phys. (1937)
Notes: 1

## Slide 7
14 MeV : 3H + d  n + 4He {Ed  0.35 MeV}
Fusion Neutronics Source, JAEA
3  1012 n/s in operation !!
Akkus et al.: Ann. Nucl. Energy (2001)
Energy spectrum from 3H(d,n)4He
Quasi monoenergy
Insulated
Transformer
High Voltage
Power Supply
Ion Source
Accelerating
Tube
R&D work of 99Mo production using 14 MeV neutrons

## Slide 8
Quality of 99mTc
 before separation
99Mo
97Zr (T1/2=17 h)
97Nb (T1/2=1.2 h)
separation easy
Waste very small
 after separation
impurity < 0.01%
 Labeling efficiency >99% using a thin layer chromatography plate

## Slide 9
Potential to produce a wide variety of RI production
diagnosis: 99mTc therapy: 90Y therapy & diagnosis: 64Cu,67Cu
62 h
reactor (research) reactor (power plant) accelerator (proton)
100Mo(n,2n)99Mo 90Zr(n,p)90Y 64Zn(n,p)64Cu, 68Zn(n,np)67Cu
Y. Nagai et al. JPSJ 78 (2009) T. Kin et al. JPSJ 82 (2013)
USA requirement 440 TBq/y
0.45 MeV

## Slide 10
Summary
Y. Nagai et al, JPSJ 82 (2013)
accelerator
Neutron
converter
Thermochromatographic separation of 99mTc
from MoO3
MoO3
Labeling
Since we proposed a new route to produce 99Mo via 100Mo(n,2n)99Mo,
we carried out all important steps necessary to obtain 99mTc with high quality.
We proposed a new system for
Generation of Radioisotopes with Accelerator Neutrons by Deuterons (GRAND)
 Prototype facility of GRAND