## Slide 1
Nuclear microprobes in biomedicine and environment: technical developments and applications
Ph. Moretto, Interface Physique-Chimie pour le Vivant Centre d'Etudes Nucléaires de Bordeaux-Gradignan Chemin du Solarium, 33175 Gradignan cedex, FRANCE INTERNATIONAL NUCLEAR PHYSICS CONFERENCE
INPC2013, 2-7 June 2013, Firenze, Italy
Notes: Thank the organisers.

## Slide 2
INPC2013, 2-7 June 2013, Firenze, Italy
0
Outline
Microbeam lines @ AIFIRA
Analysis techniques and elemental mapping
Nanotoxicology
STIM-PIXE Tomography
Neurobiology
Conclusions
2
Notes: The aim of this talk is to give you some example of achievements in the biomedical field using nuclear microprobes. Mainly nanotoxicology which is a fast growing field.
I’ll start by a brief technical description of the neamlines.
I’ll limit the Scope of this talk to analytical appplications of nuclear micrprobes.

## Slide 3
The AIFIRA facility : experience room and HVEE 3.5 MV In Line Singletron Accelerator
1
INPC2013, 2-7 June 2013, Firenze, Italy
3
Notes: 1st microbeam developed in Bx in the early ninetees
AIFIRA facility (small scale commissonned in 2006)
View of the experience room
Singletron dedicated to such applications (high brigthness/ high enegu stability)

## Slide 4
Electrostatic deflexion plates
Object Collimator
Aperture diaphragm
Sample
Magnetic quadrupoles
Microbeam line for micron lateral resolution
The first microbeam line at CENBG
Demagnification factors (1/10)
INPC2013, 2-7 June 2013, Firenze, Italy
4
1
Notes: Typical microbeam line based on a focusing system composed of magnetic quadrupoles.
The layout on this scheme (very similar to a centred optical system) object, lens, image and magnification factor.. Aberration..

## Slide 5
object
image
beam axis
-A
B
C
-D
-C
The high resolution CENBG microbeam line
1
5
INPC2013, 2-7 June 2013, Firenze, Italy
Notes: Two stages system
Raytracing showing the enveloppe of the beam the horizontal and vertical planes
Demagnification 100 and 69 at the price of higher aberartion coefficients

## Slide 6
Object aperture
Doublet
Intermediate image
Triplet
Switching magnet
Magnetic shielding
Massive granit block
9.12 m long beam line
Doublet-Triplet configuration
Ref : F. Andersson et al., Nucl. Instr. Meth. B266(8) (2008)1653
S. Incerti et al., Nucl. Instr. and Meth. B260 (2007) 20
1
INPC2013, 2-7 June 2013, Firenze, Italy
6
Notes: Doublet-Triplet – crossover and diagnostic box
Mounted on a standalone granit stone to avoid any vibration

## Slide 7
Microbeam lines @ AIFIRA
1
INPC2013, 2-7 June 2013, Firenze, Italy
7

## Slide 8
INPC2013, 2-7 June 2013, Firenze, Italy
Beam
The chamber can be equipped with up to 4 Si(Li) detectors.
Line fully remote controlled using a network loop (other beamlines as well) for safe operation of micron D+ beam…
Ref : Barberet P. et al., Technical description of the CENBG nanobeam line, Nucl. Instr. Meth. B2009; 267: 2003-2007
1
8
Microbeam lines @ AIFIRA
Notes: The endstation equiped with precision stage to position samples and different kind of detection (X-ray, particle).

## Slide 9
Triplet configuration : High current mode (1.5 MeV protons)
Beam FWHM = 0.938 µm
Beam FWHM = 1.099 µm
Object size = 20 µm
Beam current on target ~ 500 pA
Method : linear scanning over the edge of a Si wafer
Using the triplet only :
~ 1 µm beam size in typical PIXE configuration
X
Y
Performances
1
INPC2013, 2-7 June 2013, Firenze, Italy
9
Notes: Performances : two modes of operation triplet (high intensity) or quintuplet (low intensity mode)
How to measure the lateral resolution : scan the beam over the sharp edge of a wafer. Deconvolution of the signal using a gaussian shape for the beam FWHM…

## Slide 10
Quintuplet configuration : Low current mode (1.5 MeV protons)
Beam FWHM = 256 nm
Beam FWHM = 187 nm
Object size = 5 µm
Beam current on target ~ 10000 ions / second
Method : linear scanning over the edge of a Si wafer
Using the quintuplet:
~ 200x250 nm beam size in typical STIM configuration
X
Y
1
INPC2013, 2-7 June 2013, Firenze, Italy
10
Performances

## Slide 11
Analysis and imaging techniques in Biology, Medicine and Environment
Emerging techniques : MeV-SIMS, Ion Induced fluorescence, Confocal PIXE…
2
INPC2013, 2-7 June 2013, Firenze, Italy
11
Notes: Basically There are three main techniques available for working in the biomedical field… and their extension in 3D mode…
To study cellular or tissue mechanisms (toxicity, uptake, translocation, accumulation, efflux)
Combination of spatial distribution and sensitivity (metal in organic matrix, animal or vegetal), easy to use, few spectral interferences, possibility to quantify in absolute mode, concentrations expressed in terms of overall organic mass of samples… Cryotechniques, cryosection, no contamination of specimens during sample preparation…

## Slide 12
3
Nanotoxicology
Mechanisms of translocation in cells and tissues
Mechanisms of translocation in plants
Bioaccumulation of nanoparticles in the environment
Imaging techniques and nano-vectors
Nanoparticles as sensitisers for radio-therapy
12
INPC2013, 2-7 June 2013, Firenze, Italy
12
Notes: Potential toxicity of nanoparticles massively employed nowadays in household products, cosmetics, industry, …
The impact on the environment is questioned and on long term effect on human beeings.
Those particles are employed as vector for drug delivery in situ.

## Slide 13
Stratum
Granulosum
Stratum
Spinosum
Stratum
Corneum
Human epidermis and STIM imaging
20µm
STIM
3
13
INPC2013, 2-7 June 2013, Firenze, Italy
13
Notes: We started in european programme FP5 (Nanoderm) 15 years ago.
Penetration studies for solar formulation (TiO2 had been perfered to some chemical UV filters)
Percutaneous penetration ?
Left : histological section stained with hematoxilin on the right, the STIM image (frozen virgin section - no staining)

## Slide 14
Stratum
Granulosum
Stratum
Spinosum
Stratum
corneum
10µm
STIM
Ref : Skin morphology and layer identification using different STIM geometries, P. Aguer et al. NIM B 231 (2005) 292-299
Human epidermis and STIM imaging
3
14
INPC2013, 2-7 June 2013, Firenze, Italy
14
Notes: Zoom with higher resolution. Single corneocytes are visible in stratum corneum. (the highest organic density in srat. Corneum)

## Slide 15
STIM
Calcium
The barrier function controlled by ionic concentrations
The barrier effect is a physiological function that involves also other epidermal strata where complex homeostasic mechanisms regulate mineral ions.
Any change in the barrier efficiency modify the calcium gradient and is the trigger for barrier repair process
Phosphorus
PIXE
PIXE
Ref : Simon M. et al., The skin barrier function: a micro-PIXE study, X-Ray Spectrometry, 2009; 38: 132-137 3
3
15
INPC2013, 2-7 June 2013, Firenze, Italy
15
Notes: The barrier function is one of the most important physiological function. It preserves the body homeostasis by controlling the water loss.
The technique allows the measurement of the Ca gradient through he epidermis

## Slide 16
INPC2013, 2-7 June 2013, Firenze, Italy
Trans-epidermal penetration of TiO2
100 µm
Anthelios XL 60 F / 24H
16
3
Notes: Model of animal native skin after exposure to a solar formulation cpntaininf TiO2 nanoparticles. Three scans performed on the epidermis…

## Slide 17
INPC2013, 2-7 June 2013, Firenze, Italy
Ti
100 µm
Ref : Gontier E. et al., Is there penetration of titania nanoparticles in sunscreens through skin? A comparative electron and ion microscopy study. Nanotoxicology. 2008; 2(4): 218-31.
Anthelios XL 60 F / 24H
17
Trans-epidermal penetration of TiO2
3
Notes: TiO2 are detected via their chemical fingerprint (Titatnium) using PIXE.
No penetration in depth (at least in the living stratum) in healthy skin. The conclusion of the study was to evaluate skin with imparied barrier function

## Slide 18
HaCat Cells exposed to TiO2 Nanoparticles in vitro
IPCV/Seznec H., AIFIRA/TITANIUMS
Phosphorus
STIM
Potassium
Titanium
Multi-detectors analysis
HaCat Cells / P25 NPs
18
3
INPC2013, 2-7 June 2013, Firenze, Italy
Notes: In vitro studies on cell lines to evaluate the penetration in cells.
The HaCat human keratinocyte model and Ti determination after exposure in vitro to TiO2 P25 nanoparticles.
Monolayer.

## Slide 19
IPCV/Seznec H., AIFIRA/TITANIUMS
min
max
Density
N
C
C
C
C
N
N
N
max
HaCat Cells exposed to TiO2 Nanoparticles in vitro
3
STIM: 2 Mev He+
HaCaT
50 µm
Titanium map
Scan size: : 70 x 70 µm
STIM
Scan size: 58 x 58 µm
19
INPC2013, 2-7 June 2013, Firenze, Italy
Notes: Quantitative technique (See micro-domains…) :
The TiO2 NPs agregates may be observed both in STIM and PIXE mode…

## Slide 20
Increase of Ca in cells exposed to uncoated nano-TiO2
Phosphorus
Potassium
Titanium
ROI
0
20
40
60
80
100
120
Na
Mg
P
S
Cl
K
Ca
Ti
Control
TiO2-P25
FITC-TiO2-P25
0
1
2
3
Ca
mg/g Dry Mass
mg/g D.M
Region of Interest
Ref: TiO2 nanoparticles induced intracellular calcium homeostasis modification in primary human keratinocytes. Towards an in vitro explanation of TiO2 nanoparticles toxicity, Marina Simon et al., Nanotoxicology, 5,2 (2011) 125-139.
3
20
INPC2013, 2-7 June 2013, Firenze, Italy
Notes: There are optical fluorescence techniques avalaible via the functionalisation of NPs using fluorescent probes like fluorescin.
FITC-NPs could induce different cell response !! Main drwback for this technique!!!

## Slide 21
Anatomy of an adult hermaphrodite
1.5 MeV H+ MICROBEAM
256 x 256 pixels
Scale bar 10 µm
B.
C.Elegans : STIM-PIXE microanalysis
3
21
INPC2013, 2-7 June 2013, Firenze, Italy
STIM
Phosphorus
Calcium
Sulfur
Notes: Future : multicellular organisms because of the possibilty to use it as a marker of the environment.
We use the C. elegans nematode.
To study the translocation in organs at the full body scale.

## Slide 22
C.Elegans exposed to TiO2 nanoparticles: head/pharynx
22
3
Experimental Conditions: 1.5 MeV H+ - STIM : 15 min, PIXE : 1h00
INPC2013, 2-7 June 2013, Firenze, Italy
PIXE-3D
Calcium
PIXE-3D
Phosphorus
PIXE-3D
Sulfur
PIXE-3D
Titanium
PIXE-3D
Potassium
STIM-3D
pharynx
intestin
Notes: The heads of two worms collapsed. You can the two pharynx structures...

## Slide 23
H+, He+ beam
SAMPLE
Energy of transmitted
protons
X-ray
detector

X rays
z
x
On axis STIM detector
y
x
Horizontal line scan
 Horizontal tomographic slice
across the specimen
Principle of STIM- and PIXE-Tomography
4
To reconstruct an horizontal slice, scan the beam along the transverse horizontal axis
 Linear projection : to determine the local sample thicknesss (areal density in g/cm2)
Repeat the same measurements at different angles  set of linear projections
Reconstruct the distribution of the mass density (g/cm3) using analytical or algebraic
reconstruction algorithm (filtered backprojection , ART, ...).
Reconstruction performed slice by slice. Slices are numerically stacked for 3D map
Notes: To obtain the full 3D structure, we have developed a tomography techniques

## Slide 24
Micrometric screws
Rotation axis
Sample
Sample holder
Y
Z
X
Experimental conditions
4
EXP. CONDITIONS (STIM): Very low beam intensity (< 1 fA)
Spatial resolution < 1 mm
Non destructive (no section, no radiation damage)
24
INPC2013, 2-7 June 2013, Firenze, Italy
Notes: The experimental device with the gonometer (4 degrees of freedom) and the sample mmounted on the tip of a capilary/needle

## Slide 25
25
3D STIM
1.5 Mev H+
Scan: 200 x 100 μm
3D projections
4
INPC2013, 2-7 June 2013, Firenze, Italy
DIC optical microscopy
C.Elegans nematode : Tomography of adult worms
Notes: On the right a few slices…

## Slide 26
26
3D STIM
1.5 Mev H+
Scan: 200 x 100 μm
3D projections
4
INPC2013, 2-7 June 2013, Firenze, Italy
DIC optical microscopy
C.Elegans nematode : Tomography of adult worms
Notes: Differential optical interferometry (left)
STIM

## Slide 27
27
3D STIM
1.5 Mev H+
Scan: 200 x 100 μm
3D projections
4
INPC2013, 2-7 June 2013, Firenze, Italy
DIC optical microscopy
C.Elegans nematode : Tomography of adult worms
Notes: On the right a few slices…

## Slide 28
Scale bar: 10 µm
P
S
K
Ca
Ti
Slice 3
Slice 2
Slice 1
C.Elegans nematode : PIXE-Tomography of adult worms
P
S
K
Ca
Ti
P
S
K
Ca
Ti
28
4
INPC2013, 2-7 June 2013, Firenze, Italy
Notes: Three slices shown on the previous slide…

## Slide 29
5
Neurobiology
Role of metals in neurodegenerative diseases
Altered brain functions and cerebral biochemistry
Anatomy of the brain and trace elements…
29
INPC2013, 2-7 June 2013, Firenze, Italy

## Slide 30
Parkinson’s disease and dopaminergic Cell
Background - In Parkinson’s disease (PD):
- selective loss of dopaminergic neurons from Substantia Nigra pars compacta (SNpc)
Loss of the enzyme Tyrosine Hydroxylase (TH) activity (involved in dopamine biosynthesis)
Fe is increased in dopaminergic neurons of the SNpc
Is iron involved in the aetiology of PD ?
Hydroxydopamine (6-OHDA) is a neurotoxin known to selectively kill dopaminergic neurons.
Experimental models : - Rats treated with 6-hydroxydopamine (6-OHDA)
            - PC12 dopaminergic cultured cells treated with 6-OHDA
Main objectives:
to establish whether the experimental models of PD (known to present a decreased TH activity) would also show an increased Fe content ?
to determine the subcellular distribution of iron, iron proteins (transferrin,…) and dopamine related proteins (TH, …) and if these distributions are modified in experimental models of PD ?
5
30
INPC2013, 2-7 June 2013, Firenze, Italy
30
Notes: SNpc : substencia Nigra (pc ?)

## Slide 31
Combined use of hard X-ray phase contrast imaging and X-ray fluorescence microscopy for sub-cellular metal quantification, E.Kosior, S.Bohic, H.Suhonen, R.Ortega et al., Journal of Structural Biology 2012;177(2):239-47
- X-ray fluorescence (a) – ID22/ESRF
- X-ray Phase contrast (b) – ID22/ESRF
- STIM (c) map of the cell C – AIFIRA
The cell nucleus is highlighted in red.
On the phase map there are 2 areas selected for thickness calculation
On the STIM map there are 3 selected areas X, Y, Z, which were chosen to calculate the areal mass.
31
Chemical Imaging of the Dopaminergic Cell
5
b
C
INPC2013, 2-7 June 2013, Firenze, Italy
31
Notes: Multimodality using SXRF (X-ray fluorescence er Phase Contrats ESRF ID22 and STIM (AIFIRA) for imaging and mass determination

## Slide 32
5
32
STIM and PIXE analysis of a single PC12 cell exposed 100 μM FeSO4.
Quantification of iron in dopaminergic cells
C: cytoplasm
N: nucleus
Nu: nucleoli
Pr: perinuclear region
17,5 µm
STIM PIXE
INPC2013, 2-7 June 2013, Firenze, Italy
32
Notes: Voir report AIFIRA (2011-2)

## Slide 33
Trace element concentration in PC12 dopaminergic cells (preliminary results)
The number of analyses for each condition were respectively N= 6, 8, 5 and 4. Each analysis corresponds to a cell monolayer of about 200 cells.
In order to evaluate whether differences are statistically significant, 15 analyses for each condition are required
33
Quantification of iron in dopaminergic cells
5
INPC2013, 2-7 June 2013, Firenze, Italy
33

## Slide 34
34
7
Conclusions
Nowadays, most relevant experiments are conducted using a multimodal approach, combining tabletop techniques usually employed in cellular or molecular biology, advanced optical microscopy (fluorescence, confocal,…) and bulk analytical techniques (ICP-MS,…).
When trace element distribution is concerned on a microscopic scale in biological matrix, Nuclear Microscopy is a versatile technique that easily takes place in the panel of the high resolution methods such as SIMS or SXRF.
The number of papers in dedicated Bio-Journals is increasing . The use of our techniques by the « bio » community is slowly progressing together with the expertise of the IBA groups.
European networks and programmes : NANODERM (FP5), CELLION (FP6), SPIRIT (FP7), SPRITE(FP7),… Possibility of TNA
INPC2013, 2-7 June 2013, Firenze, Italy

## Slide 35
7
Thank you for your attention …
35
INPC2013, 2-7 June 2013, Firenze, Italy

## Slide 36: Geant4 Intern. Conference at the Physics- Medicine-Biology frontier (7-11 Octobre, Bordeaux)
36
http://geant4.in2p3.fr/2013/
INPC2013, 2-7 June 2013, Firenze, Italy
8

## Slide 37: Microbeam Workshop 2013 October 3-4, 2013 Bordeaux
8
37
www.cenbg.in2p3.fr/microbeam2013/
INPC2013, 2-7 June 2013, Firenze, Italy