## Slide 1: Nuclear-related techniques at LABEC for the analysis of atmospheric aerosols
S.Nava, G. Calzolai, M. Chiari, F.Lucarelli, M. Giannoni,
M. Fedi, L. Giuntini, L. Carraresi, F. Taccetti
INFN - Florence, Italy
and Physics Dept. - University of Florence, Italy
http://labec.fi.infn.it

## Slide 2: Atmospheric aerosol
Impact on human health
Modificatication of atmosphere properties (effects on climate, visibility, etc.)
Particles size and composition
Complex system of solid and liquid particles (diameter from a few nm to 100 m)
origin: primary or secondary
Aerosol sources
Need to measure the concentration, composition and particle size as a function of time, with a good spatial resolution: a lot of (small) samples to be analysed by fast, sensitive, quantitative, multielemental techniques

## Slide 3: Ion Beam Analysis (IBA)
Particle Induced X-ray Emission (PIXE): Z>10
Particle Induced Gamma-ray Emission (PIGE): B, Li, Na, Mg, Al
Elastic Scattering (EBS and PESA): H, C, N, O
Multielemental
Not destructive

## Slide 4: Aerosol measurements @ LABEC
http://labec.fi.infn.it
ion sources
+HV (3MV)
Multi-angle scattering chamber
Pulsed beam facility
External microbeam
External beam for culturale heritage applications
external beam for PIXE-PIGE on aerosol samples:
elements Z>10
in vacuum elastic scattering:
H, C, N, O
AMS spectrometer:
14C on the carbonaceous component
tandetron scheme

## Slide 5: Aerosol PIXE-PIGE set-up
SDD “BIG” Detector (X > 4 keV)
25 mm Be + 450 mm Mylar 80 mm2, 450 mm, 165 eV
SDD “SMALL” Detector (X < 6 keV)
8 mm Be window
10 mm2, 300 mm, 145 eV
HPGe Detector(g)
60 x 23 mm, 28%
1 keV @1.33 MeV
He
Both Si(Li) sobstituted by Silicon Drift Detectors (SDD)
Very good energy resolution at moderate Peltier cooling (-10°C)
High counting rates (up to ~50-100 kHz)
EXTERNAL SET-UP
two X-ray detectors
Proton deflector
(Lucarelli et al., XRS 2013)

## Slide 6: PMx daily samples
Daily samples collected in 1 year 1-2 days
47 mm
PM1 PM2.5 PM10
“daily samples”
Multi-target holder
Sample scanning
i ~ 30-200 nA, ~ 0.5-3 minutes per sample
PM10 on Teflon (CF2) filters
50 nA - 2 min.
Small SDD
Big SDD
keV
keV
Sequential samplers
Na
Mg
Al
Si
S
K
Ca
Ti
V
Cr
Mn
Fe
Ni
Cu
Zn
Br
Pb
Rb
Sr
Zr

## Slide 7: Aerosol hourly samples
Fine fraction PM2.5
Coarse fraction PM2.510
Beam size corresponding to 1 hour of sampling
i ~ 100 - 300 nA
~ 1-3 min./spot
1 week of hourly 3-9h samples (168 h) meas.
Example: artistic glass production at Montelupo Fiorentino (FI)
Very useful as most particulate matter emissions and their atmospheric dilution processes change within a few hours
g/m3
Kapton
Nuclepore
Streaker continuous sampler

## Slide 8
Scattering chamber for EBS-PESA-PIXE measurements @ LABEC
Proton elastic scattering techniques
Example of IBA mass closure
Montelupo Fiorentino (2002-2003)
(Chiari et al., XRS 2005)
PM10
C, N, O and H measured by EBS (Elastic Backscattering Spectroscopy) and PESA (Particle Elastic Scattering Analysis)
All the aerosol mass is reconstructed by IBA!

## Slide 9
IC
 inorganic ions
HR-ICPMS
 soluble
component of metals
PIXE (PIGE, EBS, PESA)
 elemental concentrations
TEFLON FILTER
Integrated approach with complementary chemical techniques
QUARTZ FILTER
  GC & GC-MS
   PAHs and n-alkanes
  Thermo-optical analysis  TC, EC, OC

## Slide 10: PATOS
First extensive field campaign for the study of PM in Tuscany (Italy) two 1-year sampling campaigns: - PM10 (2005-2006) - PM2.5 (2008-2009)
  Grosseto
  Arezzo
  Livorno
  Firenze
  Capannori
  Prato
Average chemical composition

## Slide 11: Saharan intrusions
High sensitivity for mineral dust elements (Na, Mg, Al, Si, K, Ca, Ti, Mn, Fe, Sr) ~ half minute/sample is sufficient
SDD detector
30 sec.
Important contribution to PM in southern Europe
European legislation specifies that PM10 limit values are not to be applied to events defined as natural, which include “long-range transport from arid zones”
Field campaigns followed by IBA analysis, together with atmospheric/meteorological data, may provide an effective method to trace the contribution of desert dust to PM10 quality standards
Al concentration (ng/m3)
ng/m3

## Slide 12: Contribution to PM10 and limit overcomings
From measured concentrations of crustal elements it is possible to calculate the contribution of Saharan dust to PM10 and to determine which limit exceedances are due to this component
soil =1.35 Na + 1.7 Mg + 1.9 Al + 2.1 Si + 1.4 Ca + 1.4 Fe + 1.7 Ti + 1.2 K
(Nava et al, ATM.ENV. 2012)
PM10 concentration (mg/m3)
mineral dust (soil)
other components (PM10 – soil)
Firenze (2005-2006)

## Slide 13: Source Apportionment by receptor models
The PM composition is a combination of the compositions of the aerosols emitted by the different sources
By multivariate statistical analysis, like Principal Component Factor Analysis and Positive Matrix Factorization, it is possible to identify aerosol sources and quantify their impact.
Several important source markers can be detected by IBA

## Slide 14
Source apportionment results
Important contribution of biomass burning in the most polluted sampling site of PATOS
Confirmed by hourly data
K and Cl highly correlated (r = 0.95)
Periodic pattern with peaks starting at about 18:00 and lasting during the night
ng/m3

## Slide 15: Source Apportionment by 14C-AMS
Elemental Carbon
Organic Carbon
fossil
modern
EC/OC
fossil
modern
(Calzolai et al. NIMB 2012)

## Slide 16: European projects
EMEP European Monitoring and Evaluation Programme Convention on Long-range Transboundary Air Pollution
two 1 month intensive campaings in 2012-2013 in 15 sites to measure PM10 chemical composition with special emphasis on mineral dust, to assess the contribution of natural episodes
~ 1000 daily samples analysed by PIXE
1-year long field campaigns in 4 urban areas in 2013: Barcelona (Spain), Athens (Greece), Porto (Portugal), Florence (Italy), chemical characterization of PM10 and PM2.5 and source apportionment
~ 1000 daily samples and ~ 32 streaker samples (~5000 points) by PIXE
Testing and Development of air quality mitigation measures in Southern Europe
Notes: 16

## Slide 17: Particulate matter in polar areas
PIXE-PIGE analysis of very small samples:
  present-day PM (Artic and Antarctic)
  mineral dust particles archived in ice core samples (DomeC, Antarctica)
(Marino et al., NIMB 2008, Marino et al., GRL 2009)
Dust particles are deposited over Antarctica after long-range transport from continental areas.
PIXE-PIGE results show that ice dust composition during cold stages is similar to the composition of southern South-American sediments, while it relevantly differs from Australian and the South-African ones.
(Lucarelli et al., XRS 2011)
ICE DUST (COLD STAGES)
SEDIMENTS

## Slide 18
Thank you for the attention!!!