## Slide 1: Studies of neutron-rich isotopes at the CARIBU facility
Guy Savard
Argonne National Laboratory
&
University of Chicago
INPC 2013
June 2-7 2013, Firenze, Italy

## Slide 2: Why study heavy neutron-rich isotopes?
We have the tools and techniques
to study them:
Mass known
Half-life known
nothing known
neutrons
protons
We know little about them
Nature uses them to produce half of the heavy isotopes
We just don’t have available the right beams with the right purity and properties
They are critical to many societal applications

## Slide 3: CARIBU – Californium Rare Ion Breeder Upgrade
ATLAS
Access to n-rich region obtained at ATLAS via fission of the most neutron-rich “available” very heavy nuclei (e.g. 252Cf)
Project goal: Provide neutron-rich radioactive beams to user community
  Low-energy
    Masses, decay spectroscopy, laser spectroscopy, …
  Reaccelerated through ATLAS at up to 15 MeV/u
    Single particle structure, gamma-ray spectroscopy, …
Project Description
  Gas catcher/RFQ cooler
  Source and radiological issues
  Isobar separator
  ECR Charge-breeder
  Diagnostics
  Experimental equipment
X-array
CPT mass spectrometer
HELIOS spectrometer
Gammasphere

## Slide 4: Neutron-rich beam source: CARIBU “front end” layout
Main components of CARIBU
  PRODUCTION: “ion source” is 252Cf source inside gas catcher
    Thermalizes fission fragments
    Extracts all species quickly
    Forms low emittance beam
  SELECTION: Isobar separator
    Purifies beam
  DELIVERY: beamlines and preparation
    Switchyard
    Low-energy buncher and beamlines
    Charge breeder to Increase charge state for post-acceleration
    Post-accelerator ATLAS and weak-beam diagnostics
tape station
X-array

## Slide 5: CARIBU gas catcher: transforms fission recoils into a beam with good optical properties
Based on smaller devices developed at ANL
  Radioactive recoils stop in sub-ppb level impurity Helium gas
  Radioactive ion transport by RF field + DC field + gas flow
  Stainless steel and ceramics construction (1.2 m length, 50 cm inner diameter)
  Fast and essentially universally applicable
  Extraction in 2 RFQ sections with μRFQs for differential pumping
He gas
DC gradient
To acceleration and mass separator
RF (cone)
RF (body)
252Cf

## Slide 6: Californium source and transport cask
Cf source is made at the HIFR high-flux reactor in Oak Ridge (~50 rem/hr unshielded)
  Progression of 3 sources … 2 mCi, 80 mCi, “1 Ci”
Transported in a steel/cement cask to Argonne
Installed in the CARIBU transport cask using manipulators in hot cells at Argonne
Move in the cask on site at Argonne
For installation in the gas catcher, the source and shielding plug are pushed from the storage location into position at the end of the gas catcher.
The assembly is sealed to the gas catcher, the source being inside the gas catcher.

## Slide 7
1 Ci 252Cf source
about 20% of total activity extracted as ions
works for all species
complementary to uranium fission
Extracted isotope yield at low energy (50 keV)
> than 500 neutron-rich species extracted at > 1/s
> 150 whose masses have never been measured

## Slide 8: Fragment selection: Isobar separator
R = 20000
132Sn
CARIBU Beams
Compact design (fits on HV platform):
  two 60º bends
  50 cm radius
  first-order mass resolving power: 20,000
Far from stability, mass separation is larger …
but so is needed rejection ratio
Electrostatic multipoles (up to 5th order corrections)
Dipoles
R = 5000
R = 20000
R = 40000
Rh,Ru
Tc
Mo
Nb

## Slide 9
Selection by compact CARIBU isobar separator
M/DM = 9000-14000 @ >80% transmission … still being improved

## Slide 10: Beam Delivery
After isobar separation, two options for beam use
Low energy experiments after beam bunching
  Mass measurement
  Laser Spectroscopy
  Beta decay studies
Reaccelerated Beams
  Use ECR-1 as charge breeder
  Inject ions into ATLAS in high charge state (q/m > 0.15) and energy (~100-200 keV)
Source / Gas Catcher
Isobar Separator

## Slide 11: CARIBU ECR Charge-Breeder System
Fission Source
Einzel Lens
Steering Correction
Mass Analysis
Charge Analysis
Faraday Cup/MCP Diagnostics
 V
Source Z-axis
Shielding
Gas catcher
RFQ cooler
ECR Source
MCP Diagnostics
50 kV
HV

## Slide 12
ECR Charge Breeder Results
In order to accelerate beams in ATLAS the charge-to-mass ration (q/m) must be raised to >1/8 (depending on the desired energy).
Best breeding efficiencies: 11-16% for all gases, solid, & RIBs.
Rate and Efficiency for Mass 142/25+, 129Xe25+ and 133Cs26+ as function of Voltage difference between ECRCB & 1+ source

## Slide 13: CARIBU beams reaccelerated to Gammasphere (… and HELIOS)

## Slide 14: Decay of 142Cs in Gammasphere: Expanded b-decay level scheme of 142Ba

## Slide 15: The power of Gammasphere: Spin-Parity Assignments via Angular Correlations

## Slide 16
144Ba: 2+
144Ba: 4+
144Nd: 2+
Counts
144Ba: 6+
144Nd: 4+
180Hf: 4+
Eg (keV)
16
72Ge
DT12
180Hf
144Ba/Nd
208Pb

600-MeV 141Cs + 208Pb (50 mg/cm2)
650-MeV 144Ba + 208Pb (1mg/cm2) first Digital GS + CHICO2 expt.  Rochester – LLNL – ANL collab.
First Coulomb excitation measurements with CARIBU beams
First Coulex with 141Cs – two goals:
  1. Demonstrate feasibility & study backgrounds from stable beam contamination
  2. Measure B(E2) of the 11/2+ state in 141Cs
Improved system to study 144Ba
  Use CHICO to detect recoil and provide kinematic selection and better Doppler correction
  Measure B(E2) and B(E3) to study onset of octupole deformation

## Slide 17: Beam Delivery
After isobar separation, two options for beam use
Low energy experiments after beam bunching
  Mass measurement
  Laser Spectroscopy
  Beta decay studies
Reaccelerated Beams
  Use ECR-1 as charge breeder
  Inject ions into ATLAS in high charge state (q/m > 0.15) and energy (~100-200 keV)
Source / Gas Catcher
Isobar Separator

## Slide 18: The CARIBU low-energy experimental area
Delivers 1.5 kV to 10 kV beam to experimental stations
TAPE STATION
(installed)
CPT
(installed)
X-ARRAY
(installed)
BPT
(late 2013)
Pulsed beams with rates from ~ 50 ms to seconds
LASER SPECTROSCOPY: After CPT move (2013/2014)
Low emittance
Experimental stations:
Limited amount of space … removal of Tandem will provide new experimental area

## Slide 19: Mass measurements of neutron-rich nuclides
Canadian Penning Trap (CPT) has measured more than 100 neutron-rich nuclides, including more than 70 from CARIBU (including 6 isomers)
~ 20 had never been previously measured by any technique
Currently reaching isotopes produced at the 10-6 fission branch level
For some nuclei, no prior information on the nuclide existed!
Can measure the mass with a production rate of ~ 1 ion / s
Mass precision ~ 10-7 to 10-8 (10 -100 keV/c2) for masses approaching the r process
Masses determined via a measurement of the ions’ cyclotron frequency
Original
Original
Area II 2012
Original
Area II 2012
CARIBU 2013
J. Van Schelt et al., Phys. Rev. C 85, 045805 (2012)
J. Van Schelt et al., Phys. Rev. Lett., submitted (2013)

## Slide 20: Comparison with the 2003 atomic mass evaluation
In Sn Sb Te I Xe Cs Pr Nd Pm Sm Eu
Gd
Higher N
Trends indicate nuclei are less bound with neutron excess (affects the location of the r-process path)
Good agreement with other Penning trap results and reaction Q value measurements
Large disagreement with results obtained with β-decay measurements
J. Van Schelt et al., Phys. Rev. C 85, 045805 (2012)
J. Van Schelt et al., Phys. Rev. Lett., submitted (2013)
Less binding
Notes: mention these trends are consistent with JYFLTRAP seen in other elements

## Slide 21: Effect on the r process: comparisons with the FRDM mass model
r-process path
Ran simulations to compare our new measurements with mass models for the r process
Result: FRDM (and other mass models) have insufficient mass precision for r process models
Comparative Review, Nuclear Structure and Nuclear Astrophysics, May 20, 2013
21
Effect of masses on r-process simulations (with T = 1.5 GK)

## Slide 22: CPT Measurement campaigns

## Slide 23: CPT Measurement campaigns
1437 - Being completed from previous PAC
1481 -measurements for r-process studies
1480 - measurements for new isotope discovery
Ongoing heavy-peak measurements

## Slide 24: Further development of CARIBU beams
EBIS to replace ECR:
New low-energy experimental area
Expect x 2-3 gain
Higher beam purity
RFQ to replace PII
Expect x 2 gain
New cryomodule
Fall 2012:
Summer 2013:
2014 – 2015:
Fall 2013:
New stronger, thinner source:
Expect x 5-10 gain
Isotope | Half-life (s) | Low-Energy Beam Yield (s-1) | Accelerated Beam Yield (s-1)
104Zr | 1.2 | 6.0x105 | 2.1x104
143Ba | 14.3 | 1.2x107 | 4.3x105
145Ba | 4.0 | 5.5x106 | 2.0x105
130Sn | 222. | 9.8x105 | 3.6x104
132Sn | 40. | 3.7x105 | 1.4x104
110Mo | 2.8 | 6.2x104 | 2.3x103
111Mo | 0.5 | 3.3x103 | 1.2x102
EBIS

## Slide 25: ATLAS layout with ongoing and planned upgrades
CARIBU
New in-flight separator (AIRIS)
EBIS
MHB RFQ new cryomodule
cryomodule and rebuncher rearranged
New low-energy experimental hall
Improved instrumentation

## Slide 26: Further development of CARIBU beams
EBIS to replace ECR:
New low-energy experimental area
Expect x 2-3 gain
Higher beam purity
RFQ to replace PII
Expect x 2 gain
New cryomodule
Fall 2012:
Summer 2013:
2014 – 2015:
Fall 2013:
New stronger, thinner source:
Expect x 5-10 gain
Isotope | Half-life (s) | Low-Energy Beam Yield (s-1) | Accelerated Beam Yield (s-1)
104Zr | 1.2 | 6.0x105 | 2.1x104
143Ba | 14.3 | 1.2x107 | 4.3x105
145Ba | 4.0 | 5.5x106 | 2.0x105
130Sn | 222. | 9.8x105 | 3.6x104
132Sn | 40. | 3.7x105 | 1.4x104
110Mo | 2.8 | 6.2x104 | 2.3x103
111Mo | 0.5 | 3.3x103 | 1.2x102
EBIS

## Slide 27: Status
CARIBU facility is operational
  First RIB facility based on a gas catcher … it works. Over 500 neutron-rich isotopes available at low energy
  Over 70 different neutron-rich radioactive isotope species have been used for experiments in the last year
  Low-energy program in full swing with experiments approved by last two PACs
  Reaccelerated beam program initiated with decay experiments and first Coulomb excitation at Gammasphere, reaccelerated beam experiments approved in Dec 2012 PAC being run
Current source ( ~ 150 mCi) will be replaced by a 1 Ci source in the fall. Combined with completion of ATLAS intensity upgrade (and fire damage repair), will yield gains of ~6-12 in intensity for low-energy and reaccelerated beams.
Next ATLAS/CARIBU PAC will be held at the end of summer 2013 (call for proposals expected soon). Will accept proposals for all ATLAS/CARIBU beams and the first GRETINA campaign.