## Slide 1
Notes: ----- Meeting Notes (14/03/13 11:54) -----

## Slide 2
March –> June – Working Groups Meeting with int. experts
June 2 - One day international meeting during EAAC
July 31 - Conceptual Design Report ready
By the end of 2013 IRIDE approval?
IRIDE road map

## Slide 4
I R I D E
Interdisciplinary Research Infrastructure with Dual Electron linacs&laser
Massimo.Ferrario@lnf.infn.it
on behalf of
D. Alesini1, M. P. Anania1, M. Angelone, D. Babusci1, A. Bacci3, A. Balerna1, M. Bellaveglia1, M. Benfatto1, R. Boni1, R. Bonifacio7, M. Boscolo1, F. Bossi1, B. Buonomo1, M. Castellano1, L. Catani4, M. Cestelli-Guidi1, V. Chiarella1, A. Clozza1, A. Cianchi4, R. Cimino1, F. Ciocci14, E. Chiadroni1, C. Curceanu1, S. Dabagov1, G. Dattoli14, P. De Felice5, G. Delle Monache1, D. Di Gioacchino1, D. Di Giovenale1, E. Di Palma14, G. Di Pirro1, A. Doria14, U. Dosselli1, A. Drago1, A. Esposito1, R. Faccini2, M. Ferrario1, G. P. Gallerano14, A. Gallo1, M. Gambaccini11, C. Gatti1, G. Gatti1, A. Ghigo1, L. Giannessi14, F. Giorgianni2, E. Giovenale14, C. Guaraldo1, R. Gunnella8, S. Ivashyn12, S. Loreti5, S. Lupi2, A. Marcelli1, C. Mariani16, M. Mattioli2, G. Mazzitelli1, P. Michelato3, M. Migliorati2, C. Milardi1, E. Milotti13, S. Morante4, D. Moricciani2, A. Mostacci2, V. Muccifora1, P. Musumeci10, E. Pace1, C. Pagani3, V. Palmieri, L. Palumbo2, M. Pedio, A. Perrone9, A. Petralia14, V. Petrillo3, P. Pierini3, A. Pietropaolo, M. Pillon, R. Pompili4, C. Quaresima15, L. Quintieri5, J. V. Rau, C. Ronsivalle14, J. B. Rosenzweig10, A. A. Rossi, A. R. Rossi3, E. Sabia14, L. Serafini3, D. Sertore3, O. Shekhovtsova12, I. Spassovsky14, T. Spadaro1, B. Spataro1, V. Surrenti14, A. Tenore1, A. Torre14, C. Vaccarezza1, A. Vacchi13, P. Valente2, G. Venanzoni1, S. Vescovi1, F. Villa1, N. Zema15, M. Zobov1.

## Slide 5
I R I D E
Interdisciplinary Research Infrastructure with Dual Electron linac&laser
Massimo.Ferrario@lnf.infn.it
on behalf of
(1) INFN-LNF
(2) INFN and Universita’ di Roma”La Sapienza”
(3) INFN and Universita’ di Milano
(4) INFN and Universita’ di Roma”Tor Vergata”
(5) Istituto Nazionale di Metrologia delle Radiazioni Ionizzanti, ENEA C R Casaccia.
(7) INFN and Universidade Federal da Paraiba, Brazil
(8) Universita’ di Camerino
(9) INFN and Universita’ del Salento
(10) UCLA, Los Angeles, USA
(11) INFN and Universita’ di Ferrara
(12) ITP NSC KIPT, Kharkov, Ukraine
(13) INFN and Universita’ di Trieste
(14) ENEA – Frascati
(15) CNR
(16) CNISM and Universita’ di Roma”La Sapienza”

## Slide 6
IRIDE short history
December 6 – Whatever else deadline
December 14 – First IRIDE preparatory meeting
December 17 – First IRIDE presentation at LNF
December 19 – Whatever else endorsement
January 29 – First draft of IRIDE proposal
January 30 – IRIDE presentation in Direttivo
February 11 – Second IRIDE preparatory meeting
March 14 – Giornate di Studio IRIDE

## Slide 7
2K-CRYO
2K-CRYO
GeV
GeV
GeV
I R I D E is a large infrastructure for fundamental and applied physics research. Conceived as an innovative and evolutionary tool for multi-disciplinary investigations in a wide field of scientific, technological and industrial applications, it will be a high intensity “particle beams factory”.
Based on a combination of a high duty cycle radio-frequency superconducting electron linac (SC RF LINAC) and of high energy lasers it will be able to produce a high flux of electrons, photons (from infrared to g-rays), neutrons, protons and eventually positrons, that will be available for a wide national and international scientific community interested to take profit of the most advanced particle and radiation sources.
PWA
1032
1030
n,po
1014
e+
109
g

## Slide 8
We can foresee a large number of possible activities, among them:
Science with Free Electron Lasers (FEL) from infrared to X-rays,
Nuclear photonicswith Compton back-scattering g-rays sources,
Fundamental physics with low energy linear colliders
Advanced Neutron sources by photo-production,
Science with THz radiation sources,
Physics with high power/intensity lasers,
R&D on advanced accelerator concepts including plasma accelerators and polarized positron sources
ILC technology implementation
Detector development for X-ray FEL and Linear Colliders
R&D in accelerator technology and industrial spin – off

## Slide 9
The main feature of a SC linac relevant for IRIDE is the possibility to operate the machine in continuous (CW) or quasi-continuous wave (qCW) mode with high average beam power (>1 MW) and high average current (>300 mA).
The CW or qCW choice, combined with a proper bunch distribution scheme, offers the most versatile solution to provide bunches to a number of different experiments, as could be envisaged in a multi-purpose facility.

## Slide 10
INFN is in a leading position in the SC RF technology, with knowledge and strong capabilities in the design, engineering and industrial realization of all the main component of a superconducting radiofrequency accelerator.
INFN strongly participated to TESLA since the early design stages through the final engineering and shares the know-how and has the recognized intellectual property of several main components one of which is the cryo-module concept and its evolution.

## Slide 11
The laser system complex is deputed to deliver optical photon beams able to fulfill the several requirements of the IRIDE facility:
drivers of photo-cathodes for electron beam generation
colliding laser pulses to drive the back-scattering Compton
(Yb:YAG, 100 W, 1 J, 0.1% bw)
drivers for high advanced acceleration experiments
(Ti:Sa, 1 PW, 1022 W/cm2)

## Slide 12
Free electron Lasers
CRYO
CRYO
1.5
GeV
1.5
GeV
3
GeV
The IRIDE project will provide a new concept of FEL facility by merging the two technologies of FEL oscillators and fourth generation radiation sources by developing a facility providing radiation from IR to EUV to the nm region down to Å level using a mechanism of emission already successfully tested at SPARC.

## Slide 13: A Free Electron Laser is a device that converts a fraction of the electron kinetic energy into coherent radiation via a collective instability in a long undulator
Radiation properties:
GW power - Monocromaticity - Tunability from IR to X– Short pulses

## Slide 14
SASE FEL
Self Amplified
Spontaneous Emission
≥ 0.1 nm
Limited by electron beam quality
FEL Oscillator
≥ 100 nm
Limited by mirrors reflectivity
FEL Amplifier
Laser-Seeded
≥ 10 nm
Limited by seeding sources

## Slide 16
Science with Photons

## Slide 17: Protein imaging
Using extremely short and intense X-ray pulses to capture images of objects such as proteins before the X-rays destroy the sample.
Single-molecule diffractive imaging with an X-ray free-electron laser.
Individual biological molecules will be made to fall through the X-ray beam, one at a time, and their structural information recorded in the form of a diffraction pattern.
The pulse will ultimately destroy each molecule, but not before the pulse has diffracted from the undamaged structure.
The patterns are combined to form an atomic-resolution image of the molecule.
The speed record of 25 femtoseconds for flash imaging was achieved.
Models indicate that atomic-resolution imaging can be achieved with pulses shorter than 20 femtoseconds.
Lawrence Livermore National Laboratory (LLNL)

## Slide 18: make a movie of chemical reactions
Chemical reactions often take place incredibly quickly: orders of magnitude of femtosecond are not rare. The atomic changes that occur when molecules react with one another take place in moments that brief.
The XFEL X-ray laser flashes make it possible to film these rapid processes with an unprecedented level of quality.
Since the flash duration is less than 100 femtoseconds, images can be made in which the movements of detail are not blurred.
And thanks to the short wavelength, atomic details become visible in the films.
To film a chemical reaction, one needs a series of pairs of X-ray laser flashes.
The first flash in each pair triggers the chemical reaction. With the second flash, a snapshot is then made.
The delay between the two flashes can be precisely modified to within femtosecond and a series of snapshots can be made at various times following the start of the reaction.
In each case, the images are of different molecules, but these images can be combined into a film.
xfel.desy.de

## Slide 19
THz radiation source
The interest for having high-power, sub-ps pulsed radiation covering the spectral range from THz to MIR is rapidly growing, both as it is a powerful tool for investigating the behavior of matter at low energy, and as it allows for a number of possible applications spanning from medical science to security.

## Slide 20
THz radiation source
Superconductivity Energy gap Symmetry of the order parameter Direct determination of the superfluid density Dynamics of Cooper pairs
Low-dimensional materials
Dimensionality crossover Non-Fermi liquid normal states Broken symmetry ground states
Coherent Phase Transitions Polarons Structural Phase Transitions
Magnetic sub-ps Dynamics
Condensed Matter Physics
Life Sciences
Macromolecules conformation
Secondary and tertiary structure
Coherent dynamic development
Imaging
3D tomography of dry tissues
Near-field sub-wavelenght spatial resolution
Polar liquids
Hydrogen bond
Van der Waals interactions
Acoustic-Optic phonon mixing in water
Solutions
Static and dynamic interactions between solvated
ions and solvent
Physical and Analytical Chemistry
New Technologies
THz technologies
Array THz detectors
Metamaterials
Medical diagnostic
Skin cancer detection
Industrial production
Material inspection
Production line monitoring
Defense industry/Homeland security
Detection of explosives and biohazards

## Slide 21
THz radiation source

## Slide 22
Neutron Source
A Neutron Source can be realized by photo-production sending high energy electrons on a suitable high Z target. This kind of source allows to obtain neutrons with an energy spectrum that spans over more than 9 decades of energy from few meV up to hundred of MeV, even if most of them have energy around the nuclear equilibrium temperature of the target material (for W, it is around 1 MeV)
CRYO
CRYO
1.5
GeV
1.5
GeV
3
GeV
n,po

## Slide 23
Neutron Source
This source may be suitable for multiple applications, ranging from material analysis for industrial and cultural heritages purposes to chip irradiation and metrology. These applications envisage the development of properly designed beam lines with neutron moderation and possibly cold/thermal neutron transport systems. The proposed new facility will represent a great opportunity for research and development of neutron instrumentation (e.g. detectors) as well as training of young scientist in the use and development of neutron techniques.

## Slide 24
Neutron Source
Neutron Resonance Capture Analysis (NRCA): Each resonance is the fingerprint of a nuclear specie (isotopical recognition) thus allowing for the elemental material analysis (qualitative and quantitative) especially on metallic samples (e.g. cultural heritages).
Bragg Edge Transmission (BET): By means of this technique, stresses and strain in bulky samples can be analysed. This analysis is very important for both industrial as well as cultural heritages applications.
Chip irradiation : In order to test the robustness of electronic devices to neutron field in a few minutes, neutron beams produced at facilities are desirable as the may provide an almost atmospheric-like neutron spectrum but several order of magnitude more intense.
Radiography and Tomography (NR, NT): By means of radiography it is possible to obtain an image of a object that evidences the internal structure, by rotating the sample with respect to the incident beam and collecting images for each angular position a 3D image of the object is obtained (tomography).
Neutron metrology: In this context, The Italian National Institute of Ionization radiation Metrology (INMRI) is interested in having in Italy (and especially in Roma area) a high energy neutron source in order to develop primary standards for neutron emission rate and energy spectrum calibration

## Slide 25
The special feature of Neutrograph is it's intensity together with a moderate collimation.
These properties allow the investigation of dynamic processes with an excellent time resolution and the transmittance through strongly absorbing and bulky materials.
A totally new spectrum of scientific
and engineering applications could be developed.
Among the experiments are investigations of heat exchangers and combustion engines, parts from aircrafts, fossils and historical heritage.
Institut Laue-Langevin (ILL) in Grenoble

## Slide 26
Advanced g-ray Compton Source
The state of the art in producing high brilliance/spectral density mono-chromatic g-ray beams will be soon enhanced, stepping up from the present performances (g-ray beams with bandwidth nearly 3% and spectral density of about 100 photons/s.eV) up to what is considered the threshold for Nuclear Photonics, i.e. a bandwidth of the g-ray beam lower than 0.3% and a spectral density larger than 104 photons/s.eV.
CRYO
CRYO
1.5
GeV
1.5
GeV
3
GeV
e+

## Slide 27
Advanced g-ray Compton Source

## Slide 28
Advanced g-ray Compton Source
studies of the nucleus structure at the Pigmy and Giant Dipole Resonance with unprecedented resolution in reconstructing the nuclear states: this is crucial also to understand some unknown processes in the stellar nucleo-sinthesys
studies of two level barionc states in the high energy resonance of the nuclei, above 20 MeV and up to 60 MeV, crucial to reconstruct the equation of state of the nuclear matter
detection and imaging of fissile and strategic material with isotopic reconstruction of the components with large impact on the national security scenario
remote sensing and diagnosys of nuclear wastes in containers, with reconstruciotn of the isoptope and nuclear composition of the waste material, with large impact on the atomic energy scenario
medical imaging and therapy

## Slide 29
g-e Linear Collider
The precise measurement of the p0 width through the process e g p0 e (Primakoff effect), and the search for light dark bosons in the energy region of few to hundreds MeV. These measurements, which provide important tests of the Standard Model, are not possible at present electron-photon colliders due to the low photon intensities of the machines.
po width measurement: the axial anomaly of Adler, Bell and Jackiw (non-conservation of the axial vector current) is responsible for the decay of the neutral pion into two photons. It bridges in QCD the strong dynamics of infrared physics at low energies (pions) with the perturbative description in terms of quarks and gluons at high energies. The anomaly allows to gain insights into the strong interaction dynamics of QCD and has received great attention from theorists over many years.

## Slide 30
g-e Linear Collider
Search for dark forces: several puzzling astrophysical observations (PAMELA abundance of positrons, ATIC excess, WMAP haze, INTEGRAL signal) could be explained on a common ground by existence of a new, beyond-standard-model (BSM), weakly interacting boson “U”. The mass of the U boson is expected to be at MeV or GeV scale. Such a particle would be a slim dark matter candidate and, technically, a gauge boson of a "hidden sector" abelian symmetry group U(1).
At IRIDE we can search for U boson via the lepton triplet production process in the electron-photon collision. The main QED process of the lepton triplet production is through u channel exchange (“BH diagram”) and the t channel exchange (“VCS diagram”).
The U-boson contribution is included as the t-channel part with the photon line modified by the mixing with the U.

## Slide 31
g-g Linear Collider
The vacuum of QED poses some still unsolved challenges which are central not only in the context of field theory, but also of super-symmetry and string theory as well. The elastic photon-photon scattering offers unique opportunities to probe the nature of QED vacuum. We propose an experiment to observe photon-photon scattering in the range 1 MeV – 2 MeV CM energy, i.e., near the peak of the QED cross-section. In addition a low-energy photon-photon collider investigation could lead to the necessary technology developments and prepare the ground for a higher energy complex, while still providing a rich testing ground for QED, and, more generally, QFT.

## Slide 32
g-g Linear Collider
The most striking failing of QFT is the huge mismatch between the measured energy density of vacuum and the energy density of the ground level of the fundamental fields which is wrong by something like 120 orders of magnitude.
a photon-photon scattering experiment with photon energies in the 0.5-0.8 MeV range – where the cross-section is reasonably large, would be an important test of our understanding of the QED vacuum.
This experiment needs a low-energy photon-photon collider, and a photon detection apparatus which is very similar to that current PET scanners

## Slide 33
Luminosity and beam requirements

## Slide 34
CRYO
CRYO
1.5
GeV
1.5
GeV
3
GeV
e+
e+ e- Linear Collider
An electron-positron collider with luminosity of 1032 cm−2s−1 with center of mass energy ranging from the mass of the φ-resonance 1 GeV up to ∼3.0 GeV, would complement high-energy experiment at the LHC and future linear collider (ILC). Such a machine can easily collect an integrated luminosity of about 5 fb−1 in a few years of data taking.
This will allow one to measure the e+e- cross section to hadrons with a total fractional accuracy of 1%, a level of knowledge that has relevant implications for the determination of SM observables, like, the g-2 of the muon and the effective fine-structure constant at the MZ scale. The latter are, through quantum effects, sensitive to possible bSM physics at scales of the order of hundred GeV or TeV.

## Slide 35
A primary effect of the electron-positron interaction is an enhancement of the luminosity due to the pinch effect, i. e. the reduction of the cross section of both beams occurring at the IP due to self focusing forces that is included in the luminosity definition through the factor HD.

## Slide 36
Under the previous condition the positron beam spot size remains constant during the interaction due to the balance between its own defocusing emittance pressure and the counter-propagating electron beam focusing effect.

## Slide 38
For the peak brightness the main advantage of driving the conversion directly with a photon beam relies on the possibility of using thinner targets. The emittance of the positron beam emerging from the target is determined by the source size and the beam divergence.

## Slide 39
Particle Wake Field Acceleration

## Slide 40
Particle Wake Field Acceleration

## Slide 41
THE END

## Slide 43
CRYO
1.5
GeV
n
PWA
e+
Preliminary cost evaluation – step 1 (?)

## Slide 44
Preliminary cost evaluation – step 1

## Slide 45
CRYO
CRYO
1.5
GeV
1.5
GeV
3
GeV
n
e+
PWA
Preliminary cost evaluation – step 2

## Slide 46
Preliminary cost evaluation – step 2

## Slide 47: cluster and nanoparticle
Clusters are small bits of matter composed of anywhere from a few to tens of thousands of atoms.
Small particles are different from bulk matter; finite size effects influence all properties of matter.
Examples are tiny carbon spheres and carbon tubes that are considered promising candidates for use as nanotechnological components.
(17 000 copper atoms in the picture on the right).
Limited photon energy of standard laser systems prevents measuring the full valence electron structure as well or performing photon energy dependent spectroscopy across shallow core edges
The beam intensities available at 3rd generation synchrotron radiation facilities are still far below what is required for meaningful gas phase experiments.
xfel.desy.de

## Slide 48
FIRST FLASH DIFFRACTION IMAGE OF A LIVING CELL
∞
30
60
60
30
Resolution length on the detector (nm)
FLASH soft X-ray laser, Hamburg, Germany
FLASH pulse length: 10 fs
Wavelength: 13.5 nm
RECONSTRUCTED
CELL STRUCTURE
J. Hajdu, I. Andersson, F. Maia, M. Bogan, H. Chapman, and the imaging collaboration
Filipe Maia, Uppsala